Source	Filing Services Canada
Date	06/18/2008
Time	05:31:07 AM

Company	 GOLD SUMMIT CORPORATION
Title	Gold Summit Reports 3.5 Metres of 12.1 G/T Gold in New Shallow Zone at 
Monte Cristo





    CDNX Symbol: GSM











Press Release	




NEWS TRANSMITTED BY FILING SERVICES CANADA
FOR: Gold Summit Corporation
TSX SYMBOL: GSM
Wednesday, June 18, 2008

FSC / Press Release


Gold Summit Reports 3.5 Metres of 12.1 G/T Gold in New Shallow Zone at Monte 
Cristo

Reno, Nevada US, June 18, 2008 /FSC/ - Gold Summit Corporation (GSM - TSX 
Venture), ("GSM") announces receipt of complete assay data from the last three 
of a seven hole core drilling program on the Monte Cristo Property in west 
central Nevada, located approximately 50 km west north west of Tonopah.

International Bethlehem Mining Corp. ("International Bethlehem") (TSX-V: IBC) 
has an option to acquire up to a 50% interest in GSM's Monte Cristo Property by 
incurring exploration expenditures of $3 million over four years. Minimum 
expenditure of $600,000 for 2008 has been met.

The following table shows significant intersections assaying greater than one 
gram per tonne gold in the three drill holes:

-***-

-------------------------------------------------------
Hole No.    From       To         IW       Au      Ag
(metres)  (metres)   (metres)   (g/t)   (g/t)
-------------------------------------------------------
MCC-63     230.2     231.2        1.0      5.7    99.6
-------------------------------------------------------
MCC-64    None above
1 g/t Au
-------------------------------------------------------
MCC-65
Upper Zone  72.5      76.0        3.5     12.1     2.1
-------------------------------------------------------
including   72.5      73.3        0.8     40.4    10.3
-------------------------------------------------------
and         75.0      76.0        1.0     12.5     1.9
-------------------------------------------------------
Main Lode  209.3     210.5        1.2      1.1    51.7
-------------------------------------------------------
216.4     216.9        0.5      1.4    27.6
-------------------------------------------------------
220.0     221.1        1.1      1.4     9.1
-------------------------------------------------------

-****-

The core drill holes were planned to fill in large gaps within the existing 
drill pattern and all three intersected the target McLean Lode. Future plans 
include more systematic core drilling of the McLean Lode in an effort to 
increase and upgrade the present 43-101 compliant inferred resource of 331,000 
tonnes averaging 6.5 g/t gold to indicated and measured status. Significantly, 
drill hole MCC-63 intersected the Lode 50 metres to the north of the resource 
area, thereby demonstrating a potential increase in its size. Drill hole MCC-64 
did not intersect significant mineralization and is outside the resource area.

The shallow high grade intersection in drill hole MCC-65 is evidence of an 
upper mineralized horizon in the system with epithermal characteristics similar 
to the Main Lode.  Sampling of GSM's previous core drill holes within this 
upper zone has not been completed to date. However, assay records from 
historical reverse circulation holes drilled by Cyprus Copper in 1989 show a 
similar higher grade interval.  Cyprus Hole GP-72, drilled 50 metre east of 
hole MCC-65, intersected an interval of 7.6 metres assaying 16.9 g/t gold, 
including a 1.5 metre interval assaying 39.4 g/t gold.  GSM is presently 
examining 22 core previous drill holes in the area to document and sample the 
upper horizon. It has potential to provide another continuous high grade zone 
and could significantly increase the size of the McLean Lode.

The new assays are from half cut HQ core at the Sparks Laboratories of American 
Assay using standard Fire/AA or gravimetric methods with checks provided by 
insertion of blank and standard samples. Quoted assays for Cyprus Hole GP-72 
were from standard 1.3 metre RC splits assayed in Chemex Laboratories in Sparks 
using the Fire/gravimetric method with inserted standards.

Larry Kornze, a GSM Director and a registered Professional Geologist, is 
designated as the Qualified Person under National Instrument 43-101 responsible 
for supervising the technical work on the Monte Cristo Property and has 
approved the contents of this release.

Gold Summit explores mostly in the United States for high grade gold and 
gold/silver deposits that would support underground, low cash cost operations. 
GSM's primary properties, totalling 42 km2, cover four Tertiary epithermal vein 
districts in Nevada. All these have drill ready targets defined by surface 
work, most with bonanza grades in outcrops or discovery drill holes.

The TSX Venture Exchange has not reviewed and does not accept responsibility 
for the adequacy or accuracy of this news release.  This news release includes 
certain "forward looking statements" within the meaning of the United States 
Private Securities Litigation Reform Act of 1995.  Without limitation, 
statements regarding potential mineralization and resources, exploration 
results, and future plans and objectives of the Company are forward looking 
statements that involve various degrees of risk.  The following are important 
factors that could cause the Company's actual results to differ materially from 
those expressed or implied by such forward looking statements: changes in the 
world wide price of mineral commodities, general market conditions, risks 
inherent in mineral exploration, risks associated with development, 
construction and mining operations, the uncertainty of future profitability and 
the uncertainty of access to additional capital.

Shares Outstanding 56,526,241

For further information, contact:

Hillary Vonich
(775) 284-7200
or visit our web site at www.goldsummitcorp.com


Source: Gold Summit Corporation (GSM - TSX-V) http://www.goldsummitcorp.com
Maximum News Dissemination by Filing Services Canada Inc.
Ph: (403) 717-3898  Fx: (403) 717-3896    www.usetdas.com