Source	CANADA NEWSWIRE
Date	04/15/2020
Time	12:08:31 AM

Company	 IsoEnergy Ltd.
Title	IsoEnergy Intersects 7.5m of 22.7% U3O8 in Drill Hole LE20-52 Including
2.5m of 67.2% U3O8





    CDNX Symbol: ISO











Press Release




" BC-IsoEnergy-Hurricane-Z   04-15 2536
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.265532:
^IsoEnergy Intersects 7.5m of 22.7% U3O8 in Drill Hole LE20-52 Including
2.5m of 67.2% U3O8@

Company to Host Conference Call Wednesday April 15, 2020 at 11:00am PST
VANCOUVER, April 15, 2020 /CNW/ - IsoEnergy Ltd. ("IsoEnergy" or the
"Company") (TSXV: ISO; OTCQX: ISENF) is pleased to report final assay results
from the winter 2020 drilling program at the Hurricane zone. Discovered in
2018 at the Larocque East property, the Hurricane zone is a recent discovery
of high-grade uranium mineralization. Larocque East is 100% owned by IsoEnergy
and is located in the prolific Eastern Athabasca Basin of Saskatchewan (Figure
1).
Winter Drilling Selected Highlights:
<<

--  Drill hole LE20-52 assays average 22.7% U3O8 over 7.5m from 318.5 to
326.0m, including 67.2% U3O8 over 2.5m from 322.5 to 325.0m
--  Drill hole LE20-53 assays average 11.7% U3O8 over 10.5m from 317.5 to
328.0m, including 40.4% U3O8 over 3.0m from 324.5 to 327.5m
--  Drill Hole LE20-51 assays average 14.5% U3O8 and 3.5% Ni over 7.5m from
322.5 to 330.0m(x)
--  Drill Hole LE20-40 assays average 20.5% U3O8 over 4.0m from 322.5 to
326.5m(x)
--  Drill Hole LE20-34 assays average 33.9% U3O8 over 8.5m from 326.0 to
334.5m, including 5.0m averaging 57.1% U3O8 from 328.0 to 333.0m(x)
--  Drill Hole LE20-32A assays average 19.6% U3O8 over 8.5m from 329.5 to
338.0m, including 2.5m of 63.6% U3O8 from 334.5 to 337.0m(x)
<>>
(x)Previously released assay
results

Craig Parry, Chief Executive Officer commented: "I'd like to congratulate
our technical team on these latest results and on the highly successful winter
drilling program. Drilling has continued to deliver long intervals of
high-grade pitchblende uranium mineralization, confirming Hurricane as major
discovery. It is worth noting that the Hurricane deposit is in an exceptional
location in the eastern Athabasca close to key infrastructure and only 40km
from Orano's McLean Lake Mill. These latest results from our winter program
come at a crucial time for the uranium exploration and mining sector. In
recent days we have seen the major producers announce extended closures of
their mines and mills which we estimate has reduced global uranium production
volumes by over 50%. Already we have seen the uranium spot price rise over 30%
from $24/lb three weeks ago to $31.50/lb today, breaking the important
psychological barrier of $30/lb in the process. This rise has occurred without
the full impact of physical product being removed from the market and when
these announced supply cuts take full effect in coming weeks, we expect to see
further upward pressure on prices. Against this backdrop IsoEnergy remains
well positioned with $3.5m in cash and we look forward to reporting on plans
for further drilling at our high-grade Hurricane discovery."
Steve Blower, Vice President of Exploration commented: "The last two
drill holes of the campaign have returned very high-grade uranium assays over
long intervals. The southernmost drill holes on all five sections in the
western end of the Hurricane zone are now all strongly mineralized. Clearly
there is room for expansion of this very high-grade area within the larger
Hurricane zone footprint, which now measures 575m long, up to 40m wide and up
to 11m thick."
Investor Conference Call and Webcast
The Company will be hosting a conference call today, April 15, 2020 at
11:00 AM PST (2:00 PM EST), to give a corporate presentation, discuss the
winter drilling program, and host a Q&A for investors and other interested
parties.
Details of the Call:
Participant toll free dial in number: (844) 618-5255
Audience URL:
https://onlinexperiences.com/Launch/QReg/ShowUUID(equal 
sign)3DFB8AE5-B96E-4255-AE54-C68A
D316766F
The presentation to be covered on the call can also be found on the
Company's website: https://www.isoenergy.ca/
Final Assays Received
Drill Hole LE20-52 (Hurricane Section 4435E)
Drill hole LE20-52 was designed to evaluate the potential for additional
high-grade mineralization to the south of drill holes LE20-40 and LE20-34
(Figures 2 and 3). It successfully intersected a thick interval of strong
uranium mineralization at the sub-Athabasca unconformity that averages 22.7%
U3O8 over 7.5m from 318.5 to 326.0m. The interval includes a very high-grade
section that averages 67.2% U3O8 over 2.5m from 322.5 to 325.0m. Within the
very high-grade section is a subinterval of continuous off-scale (>65K CPS on
an RS-125 handheld spectrometer) mineralization that averages 79.9% U3O8 over
1.5m from 322.5 to 324.0m. Figure 4 is a core photo of the mineralized
interval.
Drill Hole LE20-53 (Hurricane Section 4410E)
Drill hole LE20-53 was completed 25m along-strike to the west of drill
hole LE20-52 (Figures 2 and 5). It successfully intersected 10.5m of strong
uranium mineralization at the sub-Athabasca unconformity from 317.5 to 328.0m
that averages 11.7% U3O8 (Figures 2 and 4). The intersection includes a 3.0m
subinterval of very strong uranium mineralization that averages 40.4% U3O8
from 324.5 to 327.5m. Within the very high-grade section is a subinterval of
off-scale (>65K CPS on an RS-125 handheld spectrometer) mineralization that
averages 62.7% U3O8 over 0.5m from 326.0 to 326.5m. Figure 6 is a core photo
of the mineralized interval.
Next Steps
All assays from the 2020 winter drilling program at the Hurricane zone
have now been received. Data compilation and interpretation of the drilling
results are well underway, as is planning for a summer drilling program that
will continue to define the extent of the Hurricane zone. The timing and
amount of summer drilling may be impacted by the COVID-19 pandemic. The
Company continues to monitor the situation will make decisions regarding
future work programs in due course.
The Larocque East Property and the Hurricane Zone
The 100% owned Larocque East property consists of 20 mineral claims
totaling 8,371 ha that are not encumbered by any royalties or other interests.
Larocque East is immediately adjacent to the north end of IsoEnergy's Geiger
property and is 35 km northwest of Orano Canada's McClean Lake uranium mine
and mill.
Along with other target areas, the Property covers a 15-kilometre-long
northeast extension of the Larocque Lake conductor system; a trend of
graphitic metasedimentary basement rocks that is associated with significant
uranium mineralization at the Hurricane zone, and in several occurrences on
Cameco Corp. and Orano Canada Inc.'s neighbouring property to the southwest of
Larocque East. The Hurricane zone was discovered in July 2018 and was followed
up with 29 drill holes in 2019 and an additional 14 drill holes to date in
2020. Dimensions are currently 575m along-strike, 40m wide and up to 11m
thick. The zone is open for expansion along-strike to the east and on most
sections. Mineralization is polymetallic and commonly straddles the
sub-Athabasca unconformity 320 m below surface. The best intersection to date
is 33.9% U3O8 over 8.5m in drill hole LE20-34. Drilling at Cameco Corp.'s
Larocque Lake zone on the neighbouring property to the southwest has returned
historical intersections of up to 29.9% U3O8 over 7.0m in drill hole Q22-040.
Like the nearby Geiger property, Larocque East is located adjacent to the
Wollaston-Mudjatik transition zone - a major crustal suture related to most of
the uranium deposits in the eastern Athabasca Basin. Importantly, the
sandstone cover on the Property is thin, ranging between 140m and 330m in
previous drilling.
Table 1 - 2020 Hurricane Zone Results



Hole-ID  From (m) To (m)  Length (m)

Radioactivity1,2 Chemical Assays    Orientation

Location




(CPS)          U3O8 (%)         Ni (%)            (Azm/Dip)



LE20-30(3)    330.0   335.5          5.5
>500                         7.1             0.9
180/-80
Section 4460E



incl.    331.0   331.5          0.5
>10,000                        3.4             0.1


and incl.    332.0   333.5          1.5
>20,000                       24.0             2.7

---

LE20-32A(3)    329.5   338.0          8.5
>500                        19.6             1.1
180/-80
Section 4510E



incl.    334.5   337.0          2.5
>20,000                       63.6             0.4


incl.    335.0   336.5          1.5
Off-scale5                     76.7             0.3

---

LE20-34(3)    326.0   334.5          8.5
>500                        33.9             0.5
180/-80
Section 4435E



incl.    328.0   333.0          5.0
>20,000                       57.1             0.7


incl.    329.5   331.5          2.0
Off-scale5                     62.8             0.4

---

LE20-36(3)    332.5   333.5          1.0
>500                         3.7             1.0
180/-80
Section 4460E



incl.    332.5   333.0          0.5
>20,000                        5.5             1.3

---

LE20-38(3)    319.5   327.0          7.5
>500                         2.0             0.2
000/-90
Section 4460E



incl.    325.0   325.5          0.5
>20,000                        3.5             0.0


and incl.    326.0   326.5          0.5
>20,000                        9.8             0.1

---

LE20-40(3)    319.5   320.5          1.0
>500                         0.1             0.1
000/-90
Section 4435E



and    322.5   326.5          4.0
>500                        20.5             1.0


incl.    323.0   324.5          1.5
>20,000                       53.8             2.3


incl.    323.0   323.5          0.5
Off-scale5                     64.9             0.2

---

LE20-42(3)    326.0   329.0          3.0
>500                         0.4             0.2
000/-90
Section 4410E

---

LE20-44(3)    325.5   326.0          0.5
>500                         0.2             0.0
000/-90
Section 4460E


and    327.5   329.0          1.5
>500                         0.3             0.6

---

LE20-46(3)    318.0   328.0         10.0
>500                         3.6             1.4
000/-90
Section 4485E



incl.    323.0   325.0          2.0
>20,000                       12.8             1.6


and    326.0   327.0          1.0
>10,000                        4.5             4.9

---

LE20-48(3)    316.0   327.5         11.5
>500                         1.3             0.3
000/-90
Section 4485E


incl.    321.0   321.5          0.5
>10,000                        3.6             1.2


and incl.    324.0   327.0          3.0
>10,000                        3.3             0.2


incl.    324.5   325.0          0.5
>20,000                        5.1             0.2

---

LE20-49(3)    320.5   329.5          9.0
>500                         1.1             0.1
000/-90
Section 4510E



incl.    326.5   327.5          1.0
>10,000                        3.4             0.0

---

LE20-51(3)    322.5   330.0          7.5
>500                        14.5             3.5
000/-90
Section 4510E



incl.    325.5   329.0          3.5
>10,000                       30.9             7.1


Incl.    326.0   329.0          3.0
>20,000                       35.2             8.2

---

LE20-524    318.5   326.0          7.5

>500                  22.7             0.4              000/-90

Section 4435E


incl.    322.5   325.0          2.5

>10,000                67.2             0.7


incl.    322.5   324.0          1.5

Off-scale5               79.9             0.5

---

LE20-534    317.5   328.0         10.5

>500                  11.7             0.3              000/-90

Section 4410E


incl.    324.5   327.5          3.0

>20,000                40.4             0.8


incl.    326.0   326.5          0.5

Off-scale5               62.7             0.3

(equal sign)(equal sign)(equal sign)

Notes:                 1.  Radioactivity is total gamma from
drill core measured with an RS-125
hand-held spectrometer


2.  Measurements of total gamma on
drill core are an indication of
uranium content, but may not
correlate with chemical assays


3.  Radioactivity and chemical assays
previously disclosed


4.  Radioactivity previously
disclosed


5.  Off-scale radioactivity isdefined as exceeding 65,536 cps, the
maximum measurable by an RS-125
spectrometer

Qualified Person Statement
The scientific and technical information contained in this news release
was prepared by Andy Carmichael, P.Geo., IsoEnergy's Senior Geologist, who is
a "Qualified Person" (as defined in NI 43-101 - Standards of Disclosure for
Mineral Projects). Mr. Carmichael has verified the data disclosed. All
radioactivity measurements reported herein are total gamma from an RS-125
hand-held spectrometer. As mineralized drill holes at the Hurricane zone are
oriented very steeply (-80 to -90 degrees) into a zone of mineralization that
is interpreted to be horizontal, the true thickness of the intersections is
expected to be greater than or equal to 90% of the core lengths. This news
release refers to properties other than those in which the Company has an
interest. Mineralization on those other properties is not necessarily
indicative of mineralization on the Company's properties. All chemical
analyses are completed for the Company by SRC Geoanalytical Laboratories in
Saskatoon, SK. For additional information regarding the Company's Larocque
East Project, including its quality assurance and quality control procedures,
please see the Technical Report dated effective May 15, 2019 on the Company's
profile at www.sedar.com.
About IsoEnergy
IsoEnergy is a well-funded uranium exploration and development company
with a portfolio of prospective projects in the eastern Athabasca Basin in
Saskatchewan, Canada. The Company recently discovered the high-grade Hurricane
Zone of uranium mineralization on its 100% owned Larocque East property in the
Eastern Athabasca Basin. IsoEnergy is led by a Board and Management team with
a track record of success in uranium exploration, development and operations.
The Company was founded and is supported by the team at its major shareholder,
NexGen Energy Ltd.
Neither the TSX Venture Exchange nor its Regulations Services Provider
(as that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
This news release shall not constitute an offer to sell or a solicitation
of any offer to buy any securities, nor shall there be any sale of any
securities in any jurisdiction in which such offer, solicitation or sale would
be unlawful. The securities referenced herein have not been, nor will they be,
registered under the United States Securities Act of 1933, as amended (the
"U.S. Securities Act"), and such securities may not be offered or sold within
the United States absent registration under the U.S. Securities Act or an
applicable exemption from the registration requirements thereunder.
Forward-Looking Information
The information contained herein contains "forward-looking statements"
within the meaning of the United States Private Securities Litigation Reform
Act of 1995 and "forward-looking information" within the meaning of applicable
Canadian securities legislation. "Forward-looking information" includes, but
is not limited to, statements with respect to the activities, events or
developments that the Company expects or anticipates will or may occur in the
future, including, without limitation, planned exploration activities.
Generally, but not always, forward-looking information and statements can be
identified by the use of words such as "plans", "expects", "is expected",
"budget", "scheduled", "estimates", "forecasts", "inten

" BC-IsoEnergy-Hurricane-Z   04-15 2536
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.265532:
^IsoEnergy Intersects 7.5m of 22.7% U3O8 in Drill Hole LE20-52 Including
2.5m of 67.2% U3O8@

Company to Host Conference Call Wednesday April 15, 2020 at 11:00am PST
VANCOUVER, April 15, 2020 /CNW/ - IsoEnergy Ltd. ("IsoEnergy" or the
"Company") (TSXV: ISO; OTCQX: ISENF) is pleased to report final assay results
from the winter 2020 drilling program at the Hurricane zone. Discovered in
2018 at the Larocque East property, the Hurricane zone is a recent discovery
of high-grade uranium mineralization. Larocque East is 100% owned by IsoEnergy
and is located in the prolific Eastern Athabasca Basin of Saskatchewan (Figure
1).
Winter Drilling Selected Highlights:
<<

--  Drill hole LE20-52 assays average 22.7% U3O8 over 7.5m from 318.5 to
326.0m, including 67.2% U3O8 over 2.5m from 322.5 to 325.0m
--  Drill hole LE20-53 assays average 11.7% U3O8 over 10.5m from 317.5 to
328.0m, including 40.4% U3O8 over 3.0m from 324.5 to 327.5m
--  Drill Hole LE20-51 assays average 14.5% U3O8 and 3.5% Ni over 7.5m from
322.5 to 330.0m(x)
--  Drill Hole LE20-40 assays average 20.5% U3O8 over 4.0m from 322.5 to
326.5m(x)
--  Drill Hole LE20-34 assays average 33.9% U3O8 over 8.5m from 326.0 to
334.5m, including 5.0m averaging 57.1% U3O8 from 328.0 to 333.0m(x)
--  Drill Hole LE20-32A assays average 19.6% U3O8 over 8.5m from 329.5 to
338.0m, including 2.5m of 63.6% U3O8 from 334.5 to 337.0m(x)
<>>
(x)Previously released assay
results

Craig Parry, Chief Executive Officer commented: "I'd like to congratulate
our technical team on these latest results and on the highly successful winter
drilling program. Drilling has continued to deliver long intervals of
high-grade pitchblende uranium mineralization, confirming Hurricane as major
discovery. It is worth noting that the Hurricane deposit is in an exceptional
location in the eastern Athabasca close to key infrastructure and only 40km
from Orano's McLean Lake Mill. These latest results from our winter program
come at a crucial time for the uranium exploration and mining sector. In
recent days we have seen the major producers announce extended closures of
their mines and mills which we estimate has reduced global uranium production
volumes by over 50%. Already we have seen the uranium spot price rise over 30%
from $24/lb three weeks ago to $31.50/lb today, breaking the important
psychological barrier of $30/lb in the process. This rise has occurred without
the full impact of physical product being removed from the market and when
these announced supply cuts take full effect in coming weeks, we expect to see
further upward pressure on prices. Against this backdrop IsoEnergy remains
well positioned with $3.5m in cash and we look forward to reporting on plans
for further drilling at our high-grade Hurricane discovery."
Steve Blower, Vice President of Exploration commented: "The last two
drill holes of the campaign have returned very high-grade uranium assays over
long intervals. The southernmost drill holes on all five sections in the
western end of the Hurricane zone are now all strongly mineralized. Clearly
there is room for expansion of this very high-grade area within the larger
Hurricane zone footprint, which now measures 575m long, up to 40m wide and up
to 11m thick."
Investor Conference Call and Webcast
The Company will be hosting a conference call today, April 15, 2020 at
11:00 AM PST (2:00 PM EST), to give a corporate presentation, discuss the
winter drilling program, and host a Q&A for investors and other interested
parties.
Details of the Call:
Participant toll free dial in number: (844) 618-5255
Audience URL:
https://onlinexperiences.com/Launch/QReg/ShowUUID(equal 
sign)3DFB8AE5-B96E-4255-AE54-C68A
D316766F
The presentation to be covered on the call can also be found on the
Company's website: https://www.isoenergy.ca/
Final Assays Received
Drill Hole LE20-52 (Hurricane Section 4435E)
Drill hole LE20-52 was designed to evaluate the potential for additional
high-grade mineralization to the south of drill holes LE20-40 and LE20-34
(Figures 2 and 3). It successfully intersected a thick interval of strong
uranium mineralization at the sub-Athabasca unconformity that averages 22.7%
U3O8 over 7.5m from 318.5 to 326.0m. The interval includes a very high-grade
section that averages 67.2% U3O8 over 2.5m from 322.5 to 325.0m. Within the
very high-grade section is a subinterval of continuous off-scale (>65K CPS on
an RS-125 handheld spectrometer) mineralization that averages 79.9% U3O8 over
1.5m from 322.5 to 324.0m. Figure 4 is a core photo of the mineralized
interval.
Drill Hole LE20-53 (Hurricane Section 4410E)
Drill hole LE20-53 was completed 25m along-strike to the west of drill
hole LE20-52 (Figures 2 and 5). It successfully intersected 10.5m of strong
uranium mineralization at the sub-Athabasca unconformity from 317.5 to 328.0m
that averages 11.7% U3O8 (Figures 2 and 4). The intersection includes a 3.0m
subinterval of very strong uranium mineralization that averages 40.4% U3O8
from 324.5 to 327.5m. Within the very high-grade section is a subinterval of
off-scale (>65K CPS on an RS-125 handheld spectrometer) mineralization that
averages 62.7% U3O8 over 0.5m from 326.0 to 326.5m. Figure 6 is a core photo
of the mineralized interval.
Next Steps
All assays from the 2020 winter drilling program at the Hurricane zone
have now been received. Data compilation and interpretation of the drilling
results are well underway, as is planning for a summer drilling program that
will continue to define the extent of the Hurricane zone. The timing and
amount of summer drilling may be impacted by the COVID-19 pandemic. The
Company continues to monitor the situation will make decisions regarding
future work programs in due course.
The Larocque East Property and the Hurricane Zone
The 100% owned Larocque East property consists of 20 mineral claims
totaling 8,371 ha that are not encumbered by any royalties or other interests.
Larocque East is immediately adjacent to the north end of IsoEnergy's Geiger
property and is 35 km northwest of Orano Canada's McClean Lake uranium mine
and mill.
Along with other target areas, the Property covers a 15-kilometre-long
northeast extension of the Larocque Lake conductor system; a trend of
graphitic metasedimentary basement rocks that is associated with significant
uranium mineralization at the Hurricane zone, and in several occurrences on
Cameco Corp. and Orano Canada Inc.'s neighbouring property to the southwest of
Larocque East. The Hurricane zone was discovered in July 2018 and was followed
up with 29 drill holes in 2019 and an additional 14 drill holes to date in
2020. Dimensions are currently 575m along-strike, 40m wide and up to 11m
thick. The zone is open for expansion along-strike to the east and on most
sections. Mineralization is polymetallic and commonly straddles the
sub-Athabasca unconformity 320 m below surface. The best intersection to date
is 33.9% U3O8 over 8.5m in drill hole LE20-34. Drilling at Cameco Corp.'s
Larocque Lake zone on the neighbouring property to the southwest has returned
historical intersections of up to 29.9% U3O8 over 7.0m in drill hole Q22-040.
Like the nearby Geiger property, Larocque East is located adjacent to the
Wollaston-Mudjatik transition zone - a major crustal suture related to most of
the uranium deposits in the eastern Athabasca Basin. Importantly, the
sandstone cover on the Property is thin, ranging between 140m and 330m in
previous drilling.
Table 1 - 2020 Hurricane Zone Results



Hole-ID  From (m) To (m)  Length (m)

Radioactivity1,2 Chemical Assays    Orientation

Location




(CPS)          U3O8 (%)         Ni (%)            (Azm/Dip)



LE20-30(3)    330.0   335.5          5.5
>500                         7.1             0.9
180/-80
Section 4460E



incl.    331.0   331.5          0.5
>10,000                        3.4             0.1


and incl.    332.0   333.5          1.5
>20,000                       24.0             2.7

---

LE20-32A(3)    329.5   338.0          8.5
>500                        19.6             1.1
180/-80
Section 4510E



incl.    334.5   337.0          2.5
>20,000                       63.6             0.4


incl.    335.0   336.5          1.5
Off-scale5                     76.7             0.3

---

LE20-34(3)    326.0   334.5          8.5
>500                        33.9             0.5
180/-80
Section 4435E



incl.    328.0   333.0          5.0
>20,000                       57.1             0.7


incl.    329.5   331.5          2.0
Off-scale5                     62.8             0.4

---

LE20-36(3)    332.5   333.5          1.0
>500                         3.7             1.0
180/-80
Section 4460E



incl.    332.5   333.0          0.5
>20,000                        5.5             1.3

---

LE20-38(3)    319.5   327.0          7.5
>500                         2.0             0.2
000/-90
Section 4460E



incl.    325.0   325.5          0.5
>20,000                        3.5             0.0


and incl.    326.0   326.5          0.5
>20,000                        9.8             0.1

---

LE20-40(3)    319.5   320.5          1.0
>500                         0.1             0.1
000/-90
Section 4435E



and    322.5   326.5          4.0
>500                        20.5             1.0


incl.    323.0   324.5          1.5
>20,000                       53.8             2.3


incl.    323.0   323.5          0.5
Off-scale5                     64.9             0.2

---

LE20-42(3)    326.0   329.0          3.0
>500                         0.4             0.2
000/-90
Section 4410E

---

LE20-44(3)    325.5   326.0          0.5
>500                         0.2             0.0
000/-90
Section 4460E


and    327.5   329.0          1.5
>500                         0.3             0.6

---

LE20-46(3)    318.0   328.0         10.0
>500                         3.6             1.4
000/-90
Section 4485E



incl.    323.0   325.0          2.0
>20,000                       12.8             1.6


and    326.0   327.0          1.0
>10,000                        4.5             4.9

---

LE20-48(3)    316.0   327.5         11.5
>500                         1.3             0.3
000/-90
Section 4485E


incl.    321.0   321.5          0.5
>10,000                        3.6             1.2


and incl.    324.0   327.0          3.0
>10,000                        3.3             0.2


incl.    324.5   325.0          0.5
>20,000                        5.1             0.2

---

LE20-49(3)    320.5   329.5          9.0
>500                         1.1             0.1
000/-90
Section 4510E



incl.    326.5   327.5          1.0
>10,000                        3.4             0.0

---

LE20-51(3)    322.5   330.0          7.5
>500                        14.5             3.5
000/-90
Section 4510E



incl.    325.5   329.0          3.5
>10,000                       30.9             7.1


Incl.    326.0   329.0          3.0
>20,000                       35.2             8.2

---

LE20-524    318.5   326.0          7.5

>500                  22.7             0.4              000/-90

Section 4435E


incl.    322.5   325.0          2.5

>10,000                67.2             0.7


incl.    322.5   324.0          1.5

Off-scale5               79.9             0.5

---

LE20-534    317.5   328.0         10.5

>500                  11.7             0.3              000/-90

Section 4410E


incl.    324.5   327.5          3.0

>20,000                40.4             0.8


incl.    326.0   326.5          0.5

Off-scale5               62.7             0.3

(equal sign)(equal sign)(equal sign)

Notes:                 1.  Radioactivity is total gamma from
drill core measured with an RS-125
hand-held spectrometer


2.  Measurements of total gamma on
drill core are an indication of
uranium content, but may not
correlate with chemical assays


3.  Radioactivity and chemical assays
previously disclosed


4.  Radioactivity previously
disclosed


5.  Off-scale radioactivity isdefined as exceeding 65,536 cps, the
maximum measurable by an RS-125
spectrometer

Qualified Person Statement
The scientific and technical information contained in this news release
was prepared by Andy Carmichael, P.Geo., IsoEnergy's Senior Geologist, who is
a "Qualified Person" (as defined in NI 43-101 - Standards of Disclosure for
Mineral Projects). Mr. Carmichael has verified the data disclosed. All
radioactivity measurements reported herein are total gamma from an RS-125
hand-held spectrometer. As mineralized drill holes at the Hurricane zone are
oriented very steeply (-80 to -90 degrees) into a zone of mineralization that
is interpreted to be horizontal, the true thickness of the intersections is
expected to be greater than or equal to 90% of the core lengths. This news
release refers to properties other than those in which the Company has an
interest. Mineralization on those other properties is not necessarily
indicative of mineralization on the Company's properties. All chemical
analyses are completed for the Company by SRC Geoanalytical Laboratories in
Saskatoon, SK. For additional information regarding the Company's Larocque
East Project, including its quality assurance and quality control procedures,
please see the Technical Report dated effective May 15, 2019 on the Company's
profile at www.sedar.com.
About IsoEnergy
IsoEnergy is a well-funded uranium exploration and development company
with a portfolio of prospective projects in the eastern Athabasca Basin in
Saskatchewan, Canada. The Company recently discovered the high-grade Hurricane
Zone of uranium mineralization on its 100% owned Larocque East property in the
Eastern Athabasca Basin. IsoEnergy is led by a Board and Management team with
a track record of success in uranium exploration, development and operations.
The Company was founded and is supported by the team at its major shareholder,
NexGen Energy Ltd.
Neither the TSX Venture Exchange nor its Regulations Services Provider
(as that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
This news release shall not constitute an offer to sell or a solicitation
of any offer to buy any securities, nor shall there be any sale of any
securities in any jurisdiction in which such offer, solicitation or sale would
be unlawful. The securities referenced herein have not been, nor will they be,
registered under the United States Securities Act of 1933, as amended (the
"U.S. Securities Act"), and such securities may not be offered or sold within
the United States absent registration under the U.S. Securities Act or an
applicable exemption from the registration requirements thereunder.
Forward-Looking Information
The information contained herein contains "forward-looking statements"
within the meaning of the United States Private Securities Litigation Reform
Act of 1995 and "forward-looking information" within the meaning of applicable
Canadian securities legislation. "Forward-looking information" includes, but
is not limited to, statements with respect to the activities, events or
developments that the Company expects or anticipates will or may occur in the
future, including, without limitation, planned exploration activities.
Generally, but not always, forward-looking information and statements can be
identified by the use of words such as "plans", "expects", "is expected",
"budget", "scheduled", "estimates", "forecasts", "intends", "anticipates", or
"believes" or the negative connotation thereof or variations of such words and
phrases or state that certain actions, events or results "may", "could",
"would", "might" or "will be taken", "occur" or "be achieved" or the negative
connotation thereof.
Such forward-looking information and statements are based on numerous
assumptions, including among others, that the results of planned exploration
activities are as anticipated, the price of uranium, the anticipated cost of
planned exploration activities, that general business and economic conditions
will not change in a material adverse manner, that financing will be available
if and when needed and on reasonable terms, that third party contractors,
equipment and supplies and governmental and other approvals required to
conduct the Company's planned exploration activities will be available on
reasonable terms and in a timely manner. Although the assumptions made by the
Company in providing forward-looking information or making forward-looking
statements are considered reasonable by management at the time, there can be
no assurance that such assumptions will prove to be accurate.
Forward-looking information and statements also involve known and unknown
risks and uncertainties and other factors, which may cause actual events or
results in future periods to differ materially from any projections of future
events or results expressed or implied by such forward-looking information or
statements, including, among others: negative operating cash flow and
dependence on third party financing, uncertainty of additional financing, no
known mineral reserves or resources, the limited operating history of the
Company, the influence of a large shareholder, alternative sources of energy
and uranium prices, aboriginal title and consultation issues, reliance on key
management and other personnel, actual results of exploration activities being
different than anticipated, changes in exploration programs based upon
results, availability of third party contractors, availability of equipment
and supplies, failure of equipment to operate as anticipated; accidents,
effects of weather and other natural phenomena and other risks associated with
the mineral exploration industry, environmental risks, changes in laws and
regulations, community relations and delays in obtaining governmental or other
approvals.
Although the Company has attempted to identify important factors that
could cause actual results to differ materially from those contained in the
forward-looking information or implied by forward-looking information, there
may be other factors that cause results not to be as anticipated, estimated or
intended. There can be no assurance that forward-looking information and
statements will prove to be accurate, as actual results and future events
could differ materially from those anticipated, estimated or intended.
Accordingly, readers should not place undue reliance on forward-looking
statements or information. The Company undertakes no obligation to update or
reissue forward-looking information as a result of new information or events
except as required by applicable securities laws
SOURCE IsoEnergy Ltd.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/April2020/15/c1057.html

-0-                           04/15/2020
/For further information: Craig Parry, Chief Executive Officer, IsoEnergy
Ltd., +1 778 379 3211, cparry(at)isoenergy.ca, www.isoenergy.ca; Investor
Relations, Kin Communications, +1 604 684 6730, iso(at)kincommunications.com,
www.isoenergy.ca/
/Web Site: www.isoenergy.ca /
(ISENF ISO.)

CO:  IsoEnergy Ltd.
ST:  British Columbia
IN:  OIL UTI OTC
SU:

-30-