Source	CANADA NEWSWIRE
Date	05/12/2020
Time	11:46:28 PM

Company	 IsoEnergy Ltd.
Title	IsoEnergy Completes Review of Winter Drilling Program at the Hurricane
Uranium Zone





    CDNX Symbol: ISO











Press Release




" BC-IsoEnergyReviewWinter   05-13 2541
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.265532:
^IsoEnergy Completes Review of Winter Drilling Program at the Hurricane
Uranium Zone@

VANCOUVER, May 12, 2020 /CNW/ - IsoEnergy Ltd. ("IsoEnergy" or the
"Company") (TSXV: ISO; OTCQX: ISENF) is pleased to report the results of a
review of the winter 2020 drilling program at the Hurricane zone. A key
highlight is the recognition of several areasxcellent potential to expand the
mineralization. Discovered in 2018 on the Larocque East property, the
Hurricane zone is a recent discovery of high-grade uranium. Larocque East is
100% owned by IsoEnergy and is located in the prolific Eastern Athabasca Basin
of Saskatchewan (Figure 1).
Highlights:
<<

--  The Hurricane zone now measures 575m long, 40m across, and up to 11m
thick
--  Within the overall Hurricane zone footprint, recent drilling on the
western end has intersected a zone of very strong uranium mineralization
that is at least 100m long
--  Previously released highlights from the zone of very strong uranium
mineralization include:
o Drill hole LE20-53 - 11.7% U3O8 over 10.5m, including 40.4% U3O8 over 3.0m
o Drill hole LE20-52 - 22.7% U3O8 over 7.5m, including 67.2% U3O8 over 2.5m
o Drill hole LE20-51 - 14.5% U3O8 over 7.5m, including 30.9% U3O8 over 3.5m
o Drill Hole LE20-40 - 20.5% U3O8 over 4.0m, including 53.8% U3O8 over 1.5m
o Drill Hole LE20-34 - 33.9% U3O8 over 8.5m, including 57.1% U3O8 over 5.0m
o Drill Hole LE20-32A - 19.6% U3O8 over 8.5m, including 63.6% U3O8 over 2.5m
--  Several areas have excellent potential for expansion
--  A summer drilling program is planned that includes the collection of
geotechnical and hydrogeological data
--  With $3.5M in its treasury, the Company is funded through the planned
summer drilling program
<>>
Craig Parry, Chief Executive Officer commented: "Our initial review of
the winter Hurricane zone drilling results has been very positive. Clearly,
there is room for additional mineralization similar to that intersected during
the recently completed program. Given the results of the winter drill program
and proximity to existing uranium mills in the area, we are going to
accelerate the collection of geotechnical and hydrogeological data in order to
optimize and fast-track study and development timelines. An initial mineral
resource estimate for the Hurricane zone will follow when the deposit's
extents are better understood - likely sometime within the next 12 months."
Steve Blower, VP Exploration commented: "The winter drill program has
confirmed that our Hurricane discovery has significant size and high-grade
uranium potential. Additionally, our exploration drilling has confirmed the
fertile and prospective nature of the Larocque conductor trend and we are
enthused by the exploration potential on the property to the east of
Hurricane. While the focus will now be on drilling out Hurricane, we also look
forward to testing targets to the east where past drilling has intersected
uranium mineralization. We have now established a strong set of protocols that
will enable us to operate at the project over the summer despite the Covid-19
pandemic and are well positioned to launch a summer drill campaign that will
deliver news flow over coming months as we move towards delineating an initial
Mineral Resource on Hurricane".
Results
A program of 10,322m of core drilling in 24 drill holes was completed in
March with two drills. One drill rig concentrated on the western end of the
Hurricane zone footprint, expanding the mineralization west to the property
boundary. A second drill rig began evaluating the potential for additional
uranium mineralization well to the east (200m to 1,600m) of the Hurricane zone
footprint. Both of these efforts were successful.
Western Hurricane Zone Expansion
All 14 drill holes completed at the western extension of the Hurricane
zone were mineralized (Table 1). Further, a new zone of very strong uranium
mineralization characterized by very high-grade mineralization over thick
intervals was intersected in several drill holes. The best example is drill
hole LE20-34, which intersected 33.9% U3O8 over 8.5m, including 57.1% U3O8
over 5.0m. The location of the very strong mineralization relative to the rest
of the zone is shown in Figure 2, along with several areas that are considered
prospective for expansion of this material. Importantly, all five of the
westernmost sections are open for expansion to the north and/or to the south.
Figure 3 shows an example of this on section 4435E, where there is excellent
potential for additional mineralization north of drill hole LE20-34, and also
south of drill hole LE20-52.
Eastern Potential
Drilling to the east of the Hurricane zone evaluated the western portion
of a 5km long basement conductive zone mapped by the 2019 DC-resistivity
survey (Figure 4). Strongly graphitic basement gneisses hosting brittle
faulting were intersected in all of the widely spaced reconnaissance drill
holes completed up to 1.6km east of the Hurricane zone during the winter
program. Several of these drill holes also intersected significant sandstone
alteration with elevated sandstone uranium geochemistry and/or illitic
sandstone. Figure 4 shows that IsoEnergy's first pass drilling east of
Hurricane has only covered the westernmost 1.4km of the 5km long
DC-resistivity anomaly, which itself only covers one-third of the 15km of
conductors within the Larocque trend that exists on the Larocque East
property. Further drilling east of the Hurricane zone is required.
Next Steps
Detailed geological and geochemical interpretations are now underway and
will aid planning for a summer 2020 drilling program. Highest priority will be
given to those areas with the greatest potential for expansion of the zone of
very strong mineralization. Based on the results to date and to accelerate
potential development timelines, initial geotechnical and hydrological data
collection will be included in this summer's drilling program. Once the full
extent of the Hurricane zone is defined, an initial Mineral Resource estimate
will follow - likely within the next 12 months. However, the timing and amount
of summer drilling may be impacted by the COVID-19 pandemic, as the safety of
our work crews and our stakeholders in northern Saskatchewan is paramount.
Program plans will be announced in due course as the situation clarifies.
The Larocque East Property and the Hurricane Zone
The 100% owned Larocque East property consists of 25 mineral claims
totaling 14,921ha that are not encumbered by any royalties or other interests.
Larocque East is immediately adjacent to the north end of IsoEnergy's Geiger
property and is 35km northwest of Orano Canada's McClean Lake uranium mine and
mill.
Along with other target areas, the Property covers a 15-kilometre-long
northeast extension of the Larocque Lake conductor system; a trend of
graphitic metasedimentary basement rocks that is associated with significant
uranium mineralization at the Hurricane zone, and in several occurrences on
Cameco Corp. and Orano Canada Inc.'s neighbouring property to the southwest of
Larocque East. The Hurricane zone was discovered in July 2018 and was followed
up with 29 drill holes in 2019 and an additional 14 drill holes to date in
2020. Dimensions are currently 575m along-strike, 40m wide, and up to 11m
thick. The zone is open for expansion along-strike to the east and on most
sections. Mineralization is polymetallic and commonly straddles the
sub-Athabasca unconformity 320 m below surface. The best intersection to date
is 33.9% U3O8 over 8.5m in drill hole LE20-34. Drilling at Cameco Corp.'s
Larocque Lake zone on the neighbouring property to the southwest has returned
historical intersections of up to 29.9% U3O8 over 7.0m in drill hole Q22-040.
Like the nearby Geiger property, Larocque East is located adjacent to the
Wollaston-Mudjatik transition zone - a major crustal suture related to most of
the uranium deposits in the eastern Athabasca Basin. Importantly, the
sandstone cover on the Property is thin, ranging between 140m and 330m in
previous drilling.
Table 1 - Previously Released 2020 Hurricane Zone Drilling Results

Hole-ID From (m) To (m)

Length (m)   Chemical Assays

Orientation

Location


U3O8 (%)            Ni (%)

(Azm/Dip)



LE20-30               330.0   335.5              5.5                
7.1                0.9
180/-80
Section 4460E







incl.    331.0   331.5              0.5                3.4                0.1


and incl.    332.0   333.5              1.5               24.0                
2.7

---

LE20-32A              329.5   338.0              8.5               
19.6                1.1
180/-80
Section 4510E







incl.    334.5   337.0              2.5               63.6                0.4


incl.    335.0   336.5              1.5               76.7                0.3

---

LE20-34               326.0   334.5              8.5               
33.9                0.5
180/-80
Section 4435E







incl.    328.0   333.0              5.0               57.1                0.7


incl.    329.5   331.5              2.0               62.8                0.4

---

LE20-36               332.5   333.5              1.0                
3.7                1.0
180/-80
Section 4460E





incl.    332.5   333.0              0.5                5.5                1.3

---

LE20-38               319.5   327.0              7.5                
2.0                0.2
000/-90
Section 4460E







incl.    325.0   325.5              0.5                3.5                0.0


and incl.    326.0   326.5              0.5                9.8                
0.1

---

LE20-40               319.5   320.5              1.0                
0.1                0.1
000/-90
Section 4435E









and    322.5   326.5              4.0               20.5                1.0


incl.    323.0   324.5              1.5               53.8                2.3


incl.    323.0   323.5              0.5               64.9                0.2

---

LE20-42               326.0   329.0              3.0                
0.4                0.2
000/-90
Section 4410E

---

LE20-44               325.5   326.0              0.5                
0.2                0.0
000/-90
Section 4460E


and    327.5   329.0              1.5                0.3                0.6

---

LE20-46               318.0   328.0             10.0                
3.6                1.4
000/-90
Section 4485E







incl.    323.0   325.0              2.0               12.8                1.6


and    326.0   327.0              1.0                4.5                4.9

---

LE20-48               316.0   327.5             11.5                
1.3                0.3
000/-90
Section 4485E


incl.    321.0   321.5              0.5                3.6                1.2


and incl.    324.0   327.0              3.0                3.3                
0.2


incl.    324.5   325.0              0.5                5.1                0.2

---

LE20-49               320.5   329.5              9.0                
1.1                0.1
000/-90
Section 4510E





incl.    326.5   327.5              1.0                3.4                0.0

---

LE20-51               322.5   330.0              7.5               
14.5                3.5
000/-90
Section 4510E







incl.    325.5   329.0              3.5               30.9                7.1


Incl.    326.0   329.0              3.0               35.2                8.2

---

LE20-52               318.5   326.0              7.5               
22.7                0.4
000/-90
Section 4435E


incl.    322.5   325.0              2.5               67.2                0.7


incl.    322.5   324.0              1.5               79.9                0.5

---

LE20-53               317.5   328.0             10.5               
11.7                0.3
000/-90
Section 4410E


incl.    324.5   327.5              3.0               40.4                0.8


incl.    326.0   326.5              0.5               62.7                0.3

(equal sign)(equal sign)(equal sign)

Qualified Person Statement
The scientific and technical information contained in this news release
was prepared by Andy Carmichael, P.Geo., IsoEnergy's Senior Geologist, who is
a "Qualified Person" (as defined in NI 43-101 - Standards of Disclosure for
Mineral Projects). Mr. Carmichael has verified the data disclosed. All
radioactivity measurements reported herein are total gamma from an RS-125
hand-held spectrometer. As mineralized drill holes at the Hurricane zone are
oriented very steeply (-80 to -90 degrees) into a zone of mineralization that
is interpreted to be horizontal, the true thickness of the intersections is
expected to be greater than or equal to 90% of the core lengths. This news
release refers to properties other than those in which the Company has an
interest. Mineralization on those other properties is not necessarily
indicative of mineralization on the Company's properties. All chemical
analyses are completed for the Company by SRC Geoanalytical Laboratories 
inSaskatoon, SK. For additional information regarding the Company's Larocque
East Project, including its quality assurance and quality control procedures,
please see the Technical Report dated effective May 15, 2019, on the Company's
profile at www.sedar.com.
About IsoEnergy
IsoEnergy is a well-funded uranium exploration and development company
with a portfolio of prospective projects in the eastern Athabasca Basin in
Saskatchewan, Canada. The Company recently discovered the high-grade Hurricane
Zone of uranium mineralization on its 100% owned Larocque East property in the
Eastern Athabasca Basin. IsoEnergy is led by a Board and Management team with
a track record of success in uranium exploration, development, and operations.
The Company was founded and is supported by the team at its major shareholder,
NexGen Energy Ltd.
Neither the TSX Venture Exchange nor its Regulations Services Provider
(as that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
This news release shall not constitute an offer to sell or a solicitation
of any offer to buy any securities, nor shall there be any sale of any
securities in any jurisdiction in which such offer, solicitation or sale would
be unlawful. The securities referenced herein have not been, nor will they be,
registered under the United States Securities Act of 1933, as amended (the
"U.S. Securities Act"), and such securities may not be offered or sold within
the United States absent registration under the U.S. Securities Act or an
applicable exemption from the registration requirements thereunder.
Forward-Looking Information
The information contained herein contains "forward-looking statements"
within the meaning of the United States Private Securities Litigation Reform
Act of 1995 and "forward-looking information" within the meaning of applicable
Canadian securities legislation. "Forward-looking information" includes, but
is not limited to, statements with respect to the activities, events or
developments that the Company expects or anticipates will or may occur in the
future, including, without limitation, planned exploration activities.
Generally, but not always, forward-looking information and statements can be
identified by the use of words such as "plans", "expects", "is expected",
"budget", "scheduled", "estimates", "forecasts", "intends", "anticipates", or
"believes" or the negative connota

" BC-IsoEnergyReviewWinter   05-13 2541
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.265532:
^IsoEnergy Completes Review of Winter Drilling Program at the Hurricane
Uranium Zone@

VANCOUVER, May 12, 2020 /CNW/ - IsoEnergy Ltd. ("IsoEnergy" or the
"Company") (TSXV: ISO; OTCQX: ISENF) is pleased to report the results of a
review of the winter 2020 drilling program at the Hurricane zone. A key
highlight is the recognition of several areasxcellent potential to expand the
mineralization. Discovered in 2018 on the Larocque East property, the
Hurricane zone is a recent discovery of high-grade uranium. Larocque East is
100% owned by IsoEnergy and is located in the prolific Eastern Athabasca Basin
of Saskatchewan (Figure 1).
Highlights:
<<

--  The Hurricane zone now measures 575m long, 40m across, and up to 11m
thick
--  Within the overall Hurricane zone footprint, recent drilling on the
western end has intersected a zone of very strong uranium mineralization
that is at least 100m long
--  Previously released highlights from the zone of very strong uranium
mineralization include:
o Drill hole LE20-53 - 11.7% U3O8 over 10.5m, including 40.4% U3O8 over 3.0m
o Drill hole LE20-52 - 22.7% U3O8 over 7.5m, including 67.2% U3O8 over 2.5m
o Drill hole LE20-51 - 14.5% U3O8 over 7.5m, including 30.9% U3O8 over 3.5m
o Drill Hole LE20-40 - 20.5% U3O8 over 4.0m, including 53.8% U3O8 over 1.5m
o Drill Hole LE20-34 - 33.9% U3O8 over 8.5m, including 57.1% U3O8 over 5.0m
o Drill Hole LE20-32A - 19.6% U3O8 over 8.5m, including 63.6% U3O8 over 2.5m
--  Several areas have excellent potential for expansion
--  A summer drilling program is planned that includes the collection of
geotechnical and hydrogeological data
--  With $3.5M in its treasury, the Company is funded through the planned
summer drilling program
<>>
Craig Parry, Chief Executive Officer commented: "Our initial review of
the winter Hurricane zone drilling results has been very positive. Clearly,
there is room for additional mineralization similar to that intersected during
the recently completed program. Given the results of the winter drill program
and proximity to existing uranium mills in the area, we are going to
accelerate the collection of geotechnical and hydrogeological data in order to
optimize and fast-track study and development timelines. An initial mineral
resource estimate for the Hurricane zone will follow when the deposit's
extents are better understood - likely sometime within the next 12 months."
Steve Blower, VP Exploration commented: "The winter drill program has
confirmed that our Hurricane discovery has significant size and high-grade
uranium potential. Additionally, our exploration drilling has confirmed the
fertile and prospective nature of the Larocque conductor trend and we are
enthused by the exploration potential on the property to the east of
Hurricane. While the focus will now be on drilling out Hurricane, we also look
forward to testing targets to the east where past drilling has intersected
uranium mineralization. We have now established a strong set of protocols that
will enable us to operate at the project over the summer despite the Covid-19
pandemic and are well positioned to launch a summer drill campaign that will
deliver news flow over coming months as we move towards delineating an initial
Mineral Resource on Hurricane".
Results
A program of 10,322m of core drilling in 24 drill holes was completed in
March with two drills. One drill rig concentrated on the western end of the
Hurricane zone footprint, expanding the mineralization west to the property
boundary. A second drill rig began evaluating the potential for additional
uranium mineralization well to the east (200m to 1,600m) of the Hurricane zone
footprint. Both of these efforts were successful.
Western Hurricane Zone Expansion
All 14 drill holes completed at the western extension of the Hurricane
zone were mineralized (Table 1). Further, a new zone of very strong uranium
mineralization characterized by very high-grade mineralization over thick
intervals was intersected in several drill holes. The best example is drill
hole LE20-34, which intersected 33.9% U3O8 over 8.5m, including 57.1% U3O8
over 5.0m. The location of the very strong mineralization relative to the rest
of the zone is shown in Figure 2, along with several areas that are considered
prospective for expansion of this material. Importantly, all five of the
westernmost sections are open for expansion to the north and/or to the south.
Figure 3 shows an example of this on section 4435E, where there is excellent
potential for additional mineralization north of drill hole LE20-34, and also
south of drill hole LE20-52.
Eastern Potential
Drilling to the east of the Hurricane zone evaluated the western portion
of a 5km long basement conductive zone mapped by the 2019 DC-resistivity
survey (Figure 4). Strongly graphitic basement gneisses hosting brittle
faulting were intersected in all of the widely spaced reconnaissance drill
holes completed up to 1.6km east of the Hurricane zone during the winter
program. Several of these drill holes also intersected significant sandstone
alteration with elevated sandstone uranium geochemistry and/or illitic
sandstone. Figure 4 shows that IsoEnergy's first pass drilling east of
Hurricane has only covered the westernmost 1.4km of the 5km long
DC-resistivity anomaly, which itself only covers one-third of the 15km of
conductors within the Larocque trend that exists on the Larocque East
property. Further drilling east of the Hurricane zone is required.
Next Steps
Detailed geological and geochemical interpretations are now underway and
will aid planning for a summer 2020 drilling program. Highest priority will be
given to those areas with the greatest potential for expansion of the zone of
very strong mineralization. Based on the results to date and to accelerate
potential development timelines, initial geotechnical and hydrological data
collection will be included in this summer's drilling program. Once the full
extent of the Hurricane zone is defined, an initial Mineral Resource estimate
will follow - likely within the next 12 months. However, the timing and amount
of summer drilling may be impacted by the COVID-19 pandemic, as the safety of
our work crews and our stakeholders in northern Saskatchewan is paramount.
Program plans will be announced in due course as the situation clarifies.
The Larocque East Property and the Hurricane Zone
The 100% owned Larocque East property consists of 25 mineral claims
totaling 14,921ha that are not encumbered by any royalties or other interests.
Larocque East is immediately adjacent to the north end of IsoEnergy's Geiger
property and is 35km northwest of Orano Canada's McClean Lake uranium mine and
mill.
Along with other target areas, the Property covers a 15-kilometre-long
northeast extension of the Larocque Lake conductor system; a trend of
graphitic metasedimentary basement rocks that is associated with significant
uranium mineralization at the Hurricane zone, and in several occurrences on
Cameco Corp. and Orano Canada Inc.'s neighbouring property to the southwest of
Larocque East. The Hurricane zone was discovered in July 2018 and was followed
up with 29 drill holes in 2019 and an additional 14 drill holes to date in
2020. Dimensions are currently 575m along-strike, 40m wide, and up to 11m
thick. The zone is open for expansion along-strike to the east and on most
sections. Mineralization is polymetallic and commonly straddles the
sub-Athabasca unconformity 320 m below surface. The best intersection to date
is 33.9% U3O8 over 8.5m in drill hole LE20-34. Drilling at Cameco Corp.'s
Larocque Lake zone on the neighbouring property to the southwest has returned
historical intersections of up to 29.9% U3O8 over 7.0m in drill hole Q22-040.
Like the nearby Geiger property, Larocque East is located adjacent to the
Wollaston-Mudjatik transition zone - a major crustal suture related to most of
the uranium deposits in the eastern Athabasca Basin. Importantly, the
sandstone cover on the Property is thin, ranging between 140m and 330m in
previous drilling.
Table 1 - Previously Released 2020 Hurricane Zone Drilling Results

Hole-ID From (m) To (m)

Length (m)   Chemical Assays

Orientation

Location


U3O8 (%)            Ni (%)

(Azm/Dip)



LE20-30               330.0   335.5              5.5                
7.1                0.9
180/-80
Section 4460E







incl.    331.0   331.5              0.5                3.4                0.1


and incl.    332.0   333.5              1.5               24.0                
2.7

---

LE20-32A              329.5   338.0              8.5               
19.6                1.1
180/-80
Section 4510E







incl.    334.5   337.0              2.5               63.6                0.4


incl.    335.0   336.5              1.5               76.7                0.3

---

LE20-34               326.0   334.5              8.5               
33.9                0.5
180/-80
Section 4435E







incl.    328.0   333.0              5.0               57.1                0.7


incl.    329.5   331.5              2.0               62.8                0.4

---

LE20-36               332.5   333.5              1.0                
3.7                1.0
180/-80
Section 4460E





incl.    332.5   333.0              0.5                5.5                1.3

---

LE20-38               319.5   327.0              7.5                
2.0                0.2
000/-90
Section 4460E







incl.    325.0   325.5              0.5                3.5                0.0


and incl.    326.0   326.5              0.5                9.8                
0.1

---

LE20-40               319.5   320.5              1.0                
0.1                0.1
000/-90
Section 4435E









and    322.5   326.5              4.0               20.5                1.0


incl.    323.0   324.5              1.5               53.8                2.3


incl.    323.0   323.5              0.5               64.9                0.2

---

LE20-42               326.0   329.0              3.0                
0.4                0.2
000/-90
Section 4410E

---

LE20-44               325.5   326.0              0.5                
0.2                0.0
000/-90
Section 4460E


and    327.5   329.0              1.5                0.3                0.6

---

LE20-46               318.0   328.0             10.0                
3.6                1.4
000/-90
Section 4485E







incl.    323.0   325.0              2.0               12.8                1.6


and    326.0   327.0              1.0                4.5                4.9

---

LE20-48               316.0   327.5             11.5                
1.3                0.3
000/-90
Section 4485E


incl.    321.0   321.5              0.5                3.6                1.2


and incl.    324.0   327.0              3.0                3.3                
0.2


incl.    324.5   325.0              0.5                5.1                0.2

---

LE20-49               320.5   329.5              9.0                
1.1                0.1
000/-90
Section 4510E





incl.    326.5   327.5              1.0                3.4                0.0

---

LE20-51               322.5   330.0              7.5               
14.5                3.5
000/-90
Section 4510E







incl.    325.5   329.0              3.5               30.9                7.1


Incl.    326.0   329.0              3.0               35.2                8.2

---

LE20-52               318.5   326.0              7.5               
22.7                0.4
000/-90
Section 4435E


incl.    322.5   325.0              2.5               67.2                0.7


incl.    322.5   324.0              1.5               79.9                0.5

---

LE20-53               317.5   328.0             10.5               
11.7                0.3
000/-90
Section 4410E


incl.    324.5   327.5              3.0               40.4                0.8


incl.    326.0   326.5              0.5               62.7                0.3

(equal sign)(equal sign)(equal sign)

Qualified Person Statement
The scientific and technical information contained in this news release
was prepared by Andy Carmichael, P.Geo., IsoEnergy's Senior Geologist, who is
a "Qualified Person" (as defined in NI 43-101 - Standards of Disclosure for
Mineral Projects). Mr. Carmichael has verified the data disclosed. All
radioactivity measurements reported herein are total gamma from an RS-125
hand-held spectrometer. As mineralized drill holes at the Hurricane zone are
oriented very steeply (-80 to -90 degrees) into a zone of mineralization that
is interpreted to be horizontal, the true thickness of the intersections is
expected to be greater than or equal to 90% of the core lengths. This news
release refers to properties other than those in which the Company has an
interest. Mineralization on those other properties is not necessarily
indicative of mineralization on the Company's properties. All chemical
analyses are completed for the Company by SRC Geoanalytical Laboratories 
inSaskatoon, SK. For additional information regarding the Company's Larocque
East Project, including its quality assurance and quality control procedures,
please see the Technical Report dated effective May 15, 2019, on the Company's
profile at www.sedar.com.
About IsoEnergy
IsoEnergy is a well-funded uranium exploration and development company
with a portfolio of prospective projects in the eastern Athabasca Basin in
Saskatchewan, Canada. The Company recently discovered the high-grade Hurricane
Zone of uranium mineralization on its 100% owned Larocque East property in the
Eastern Athabasca Basin. IsoEnergy is led by a Board and Management team with
a track record of success in uranium exploration, development, and operations.
The Company was founded and is supported by the team at its major shareholder,
NexGen Energy Ltd.
Neither the TSX Venture Exchange nor its Regulations Services Provider
(as that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
This news release shall not constitute an offer to sell or a solicitation
of any offer to buy any securities, nor shall there be any sale of any
securities in any jurisdiction in which such offer, solicitation or sale would
be unlawful. The securities referenced herein have not been, nor will they be,
registered under the United States Securities Act of 1933, as amended (the
"U.S. Securities Act"), and such securities may not be offered or sold within
the United States absent registration under the U.S. Securities Act or an
applicable exemption from the registration requirements thereunder.
Forward-Looking Information
The information contained herein contains "forward-looking statements"
within the meaning of the United States Private Securities Litigation Reform
Act of 1995 and "forward-looking information" within the meaning of applicable
Canadian securities legislation. "Forward-looking information" includes, but
is not limited to, statements with respect to the activities, events or
developments that the Company expects or anticipates will or may occur in the
future, including, without limitation, planned exploration activities.
Generally, but not always, forward-looking information and statements can be
identified by the use of words such as "plans", "expects", "is expected",
"budget", "scheduled", "estimates", "forecasts", "intends", "anticipates", or
"believes" or the negative connotation thereof or variations of such words and
phrases or state that certain actions, events or results "may", "could",
"would", "might" or "will be taken", "occur" or "be achieved" or the negative
connotation thereof.
Such forward-looking information and statements are based on numerous
assumptions, including among others, that the results of planned exploration
activities are as anticipated, the price of uranium, the anticipated cost of
planned exploration activities, that general business and economic conditions
will not change in a material adverse manner, that financing will be available
if and when needed and on reasonable terms, that third party contractors,
equipment and supplies and governmental and other approvals required to
conduct the Company's planned exploration activities will be available on
reasonable terms and in a timely manner. Although the assumptions made by the
Company in providing forward-looking information or making forward-looking
statements are considered reasonable by management at the time, there can be
no assurance that such assumptions will prove to be accurate.
Forward-looking information and statements also involve known and unknown
risks and uncertainties and other factors, which may cause actual events or
results in future periods to differ materially from any projections of future
events or results expressed or implied by such forward-looking information or
statements, including, among others: negative operating cash flow and
dependence on third party financing, uncertainty of additional financing, no
known mineral reserves or resources, the limited operating history of the
Company, the influence of a large shareholder, alternative sources of energy
and uranium prices, aboriginal title and consultation issues, reliance on key
management and other personnel, actual results of exploration activities being
different than anticipated, changes in exploration programs based upon
results, availability of third party contractors, availability of equipment
and supplies, failure of equipment to operate as anticipated; accidents,
effects of weather and other natural phenomena and other risks associated with
the mineral exploration industry, environmental risks, changes in laws and
regulations, community relations and delays in obtaining governmental or other
approvals.
Although the Company has attempted to identify important factors that
could cause actual results to differ materially from those contained in the
forward-looking information or implied by forward-looking information, there
may be other factors that cause results not to be as anticipated, estimated or
intended. There can be no assurance that forward-looking information and
statements will prove to be accurate, as actual results and future events
could differ materially from those anticipated, estimated or intended.
Accordingly, readers should not place undue reliance on forward-looking
statements or information. The Company undertakes no obligation to update or
reissue forward-looking information as a result of new information or events
except as required by applicable securities laws
View original content to download
multimedia:http://www.prnewswire.com/news-releases/isoenergy-completes-review-
of-winter-drilling-program-at-the-hurricane-uranium-zone-301058333.html
SOURCE IsoEnergy Ltd.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/May2020/13/c9809.html

-0-                           05/13/2020
/For further information: Craig Parry, Chief Executive Officer, IsoEnergy
Ltd., +1 778 379 3211, cparry(at)isoenergy.ca, www.isoenergy.ca; Investor
Relations: Kin Communications, +1 604 684 6730, iso(at)kincommunications.com,
www.isoenergy.ca/
/Web Site: www.isoenergy.ca /
(ISENF ISO. I01)

CO:  IsoEnergy Ltd.
ST:  British Columbia
IN:  OTC MIN MNG
SU:

-30-