Source	CANADA NEWSWIRE
Date	01/07/2020
Time	05:03:42 AM

Company	 Frontier Lithium Inc.
Title	Frontier Lithium Releases Remaining Phase II Drilling Results of the
Spark Pegmatite





    CDNX Symbol: FL











Press Release




" BC-FrontierDrillingResul   01-07 1439
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention co.122896:
^Frontier Lithium Releases Remaining Phase II Drilling Results of the
Spark Pegmatite@

Highlights
<<

--  Phase II diamond drill program includes four holes drilled totaling
1,159.5m; all intersecting significant zones of spodumene pegmatite;
assay results have been received for all outstanding samples;
--  DDH PL-044-19 intersected 75m of pegmatite averaging 1.4% Li2O,
including 19.0m of 3.4% Li2O;
--  DDH PL-045-19 intersected 144.2m of pegmatite averaging 1.4% Li2O;
--  An additional 52m of channeling was completed on surface averaging 1.5
to 1.77% Li2O;
--  1,600m of intersected pegmatite in 9 drill holes from the first two
phases of drilling and surface channel samples has resulted in an
average grade of 1.53% Li2O.
--  Management initiates Maiden resource estimate on the Spark pegmatite.
<>>
SUDBURY, ON, Jan. 7, 2020 /CNW/ - Frontier Lithium Inc. (TSX.V: FL) (the
"Company) is pleased to announce the remaining results of their second Phase
of drilling on the Spark Pegmatite. Frontier completed four diamond drill
holes totaling 1,159.5 m in July-August 2019 (Table 1). During the drill
program an additional 4 channels totaling 52 m (Table 2) were cut and most of
the exposed outcrop surface in the immediate area of the pegmatite was mapped.
An analysis of the results from the drill program and assay results from the
first two drill holes are included in a Press Release dated September 24th,
2019 and will not be repeated in this Press Release.
"Supported by preliminary modelling, we strongly believe in the potential
for economic viability of the Spark pegmatite." commented Garth Drever, Vice
President of Exploration. "The deposit remains open to the west and has
maintained consistency in both grade and width with depth. The physical data
collected through surface and remote mapping at PAK and Spark has proven
invaluable as a first-pass exploration tool to evaluating the potential of our
mining claims on the Electric Avenue."
Table 1: Summary of Phase 2 Drilling at Spark
https://mailchi.mp/frontierlithium/another-landmark-on-the-electric-avenu
e-2
Table 2: Summary of Channels Cut at Spark in 2019
https://mailchi.mp/frontierlithium/another-landmark-on-the-electric-avenu
e-2
The location of the final two drill holes and surface channels being
reported are highlighted in Figure 1; a location map showing the surface
outline of the Spark pegmatite, location of channels and drill hole traces
with geology overlain on detailed imagery of the outcrop area.
https://mailchi.mp/frontierlithium/another-landmark-on-the-electric-avenu
e-2
Figure 1: Location Map showing Drill Hole and Channel Traces at the Spark
Pegmatite
Table 3 shows a summary of the assay results of holes PL-044-19 and
PL-045-19.
Hole PL-044-19 was designed to step out 50m to 75m to test the extension
of the pegmatite to the west of hole PL-039-19. Three significant pegmatite
zones were intersected with an upper 75m intercept averaging 1.4% Li2O. The
two lower zones of 12 and 27.4m consist of slightly lower grade
spodumene-bearing aplite averaging 0.74% and 0.87% Li2O.
Table 3: Drill hole intersections for PL-044-19 and PL-045-19
https://mailchi.mp/frontierlithium/another-landmark-on-the-electric-avenu
e-2
Figures 2 and 3 are Sections for holes PL-044-19 and PL-045-19
respectively showing Li2O content as histogram plots along the drill hole and
channel traces. The section in Figure 2 was extended to include hole
PL-039-19. Although only scattered remnants of pegmatite were noted on surface
during mapping and prospecting it is apparent that there are two significant
lobes of the pegmatite that extend upward to the surface beneath the
overburden.
https://mailchi.mp/frontierlithium/another-landmark-on-the-electric-avenu
e-2
Figure 2: Section showing Trace Geology and Li2O for DDH Pl-044-19 and
PL-039-19
The final hole of the program, PL-045-19, extended hole PL-037-19 which
had been abandon. Hole PL-045-19 intersected a 17.1m zone of spodumene-bearing
aplite averaging 0.78% Li2O before intersecting a 144.2m zone of predominately
pegmatite from 70.8 to 215m averaging 1.4% Li2O. A 15m zone from 130 to 145m
averages 2.47% Li2O. Anomalous Ta, Sn and Rb occurs over an 11.2m zone from
175 to 186.2m averaging 659 ppm Ta2O5, 520 ppm SnO2 and 0.88% Rb2O. An
analogous zone of enriched Ta is present above in Channel 37 from 63.2 to
69.4m (6.2m) averaging 615 ppm Ta2O5 (see Press Release January 17, 2019).
Figure 3 shows the section of hole PL-045-19 with Channels 37 and 38 plotted
at surface. Both Li2O and Ta2O5 are plotted along the trace of the drill holes
and channels.
Figure 3: Section showing Trace Geology plus Li2O and Ta2O5 for DDH
PL-045-19 and Channels 37 and 38
During the summer drill program an additional 52m of channels (Channels
41 to 43) were cut to complete the section between Channel 38 and start of
Channel 40 and to sample across the western most exposed lobe of the pegmatite
(Channel 44). These channels are highlighted on Figure 1 and displayed in
Figure 4 in a section including hole PL-040-19 and PL-043-19. Assay results
are summarized in Table 4. All channels were logged as spodumene-bearing
Na-aplite with consistent grades between 1.5 and 1.77% Li2O. The aplite is
typically fine to medium grained, light grey to greenish grey locally with
coarser zonations consisting of megacrystic feldspar, fine to coarse-grained
light grey to white spodumene laths, grey quartz and variable amounts of
muscovite.
Table 4: Summary of Channel Results
https://mailchi.mp/frontierlithium/another-landmark-on-the-electric-avenu
e-2


(x) Channels 41, 42 and 43 are staggered, however, represent one continuous 
channel in the gap between Channels 38 and 40

https://mailchi.mp/frontierlithium/another-landmark-on-the-electric-avenu
e-2
Figure 4: Section showing Trace Geology and Li2O for DDH PL-040-19,
PL-043-19 and Channels 40 to 43
During the summer drill program much of what was previously described as
metavolcanics rock has been subdivided into metasedimentary units which are
now recognized to be intercalated within the metavolcanics sequences.
Due Diligence
All scientific and technical information in this release has been
reviewed and approved by Garth Drever, P.Geo., the qualified person (QP) under
the definitions established by National Instrument 43-101. Under Frontier's
QA/QC procedures, all drilling was completed by Chenier Drilling Ltd. of Val
Caron, ON using thin-walled BTW drill rods (4.2 cm core diameter) and a Reflex
ACT III oriented core system. Using the Reflex system, the drill core was
oriented and marked as it was retrieved at the drill. The core was boxed and
delivered to the Frontier core shack where it was examined, geologically
logged and marked for sampling. The core was photographed prior to sampling.
Using a rock saw, the marked sample intervals were halved with one halve
bagged for analysis. Sample blanks along with lithium, rubidium and cesium
certified reference material was routinely inserted into the sample stream in
accordance with industry recommended practices. Field duplicate samples were
also taken in accordance with industry recommended practices. The samples were
placed in poly sample bags and transported to Red Lake by Frontier employees
and then shipped to AGAT Laboratories Ltd. (AGAT) in Mississauga, ON for
quantitative multi-element analysis. AGAT is an ISO accredited laboratory. All
petrographic sample preparation and electron microprobe (EMP) analysis was
completed at the Queen's Facility for Isotope Research (QFIR) at Queen's
University in Kingston, Ontario under the direct supervision of Dr. Steve
Beyer. The core is stored on site at the Pakeagama Lake exploration camp.
About Frontier Lithium
Frontier Lithium is a Canadian junior mining company with the largest
land position in the Electric Avenue, an emerging premium lithium mineral
district located in the Canadian Shield of northwestern Ontario. The company's
PAK Lithium Deposit contains North America's highest concentration of rare
low-iron spodumene. Frontier Lithium's objective is to firstly become a near
term producer of premium technical grade lithium mineral concentrates of 2,000
tonnes of Lithium Carbonate Equivalent ("LCE") for glass producers. Through a
phased approach to scale up to 20,000 tonnes by ramping up production of
concentrates and building a downstream processing facility to produce lithium
chemicals required by glass and battery materials producers.Frontier maintains
a tight share structure with management ownership exceeding 30% of the
Company.
About the PAK deposit
The PAK Deposit is located in the south end of Ontario's Electric Avenue,
a newly emerging premium lithium-metal district. Electric Avenue also hosts
Frontier's newest discovery, Spark showing (2km northwest) and the Pennock
Lake pegmatite occurrence a further 30km along Frontier's PAK Lithium Project.
The PAK deposit has a mineral resource estimate of 9.3 Mt averaging 2.04% Li2O
which has a rare technical/ceramic grade spodumene with low inherent iron
(below 0.1% Fe2O3) as per its NI 43-101 Technical Report, "Preliminary
Feasibility Study" disseminated on April 16, 2018.
Additional information regarding Frontier Lithium is available on SEDAR
at sedar.com under the Company's profile and on its website at
frontierlithium.com, including various pictures of ongoing work at the
project.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
SOURCE Frontier Lithium Inc.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/January2020/07/c7465.html

-0-                           01/07/2020
/For further information: Bora Ugurgel, Manager, Investor Relations, 2736
Belisle Drive Val Caron, ON. P3N 1B3 CANADA, T. +001 705.897.7622, F. +001
705.897.7618/
/Web Site: frontierlithium.com /
(HLKMF FL.)

CO:  Frontier Lithium Inc.
ST:  Ontario
IN:  MNG OTC
SU:

-30-