Source	MARKET NEWS
Date	04/02/2014
Time	07:01:25 AM

Company	 Bullman Minerals Inc.
Title	Inferred 
Resource Of 39.8 Mt Grading 0.94 G/t Go





    CDNX Symbol: BUL











Press Release	





BULLMAN MINERALS INC ("BUL-V")
- Inferred Resource Of 39.8 Mt Grading 0.94 G/t Gold (1.21 Moz)
- On The Balandougouba Project

Bullman Minerals Inc. is pleased to announce the results of the
first independent NI43-101 resource estimate for the Balandougouba
project (Sidikila deposit), located in northeast Guinea, West Africa.
The inferred resource estimate for the Sidikila deposit is 39.8 Mt
grading 0.94 g/t gold (1.21 Moz) at a 0.3 g/t cut-off. No economic
studies have been completed for the Balandougouba project and therefore
a cut-off grade of 0.3 g/t gold was chosen as a possible open pit
cut-off; the resource at various cut-off is shown in Table 1. The
Sidikila deposit is one of several targets the Company is actively
exploring on the Balandougouba project, which comprises three
contiguous exploration concessions for a total area of 265 km2.

Highlights

//st

Maiden NI43-101 resource estimate outlines an inferred resource of 39.8 Mt
grading 0.94 g/t gold (1.21 Moz) at a 0.3 g/t cut-off.

Increasing the cut-off grade to 0.6 g/t gold, the resource grade increases
to 1.17 g/t gold and the total ounces and tonnage decreases to 1.02 Moz and
27.1 Mt, respectively.

Significant potential to increase the resource by drilling down dip of
existing shallow drilling, which mostly intersected the mineralization zone
between surface and 100 m depth, and along strike to the north and
southeast.

Structure hosting the Sidikila deposit can be traced over 15 km to the
north and 6 km to the southeast by geophysics.

Several targets (Niani, Gberekole, Mandiantri, Jade and Fouani) have seen
limited exploration to date, but will be the focus of exploration programs
with the aim to outline satellite deposits that are within a short distance
of Sidikila.

Near surface gold mineralization may be amenable to open pit extraction and
heap leach processing, which Bullman plans to investigate in future mining
and metallurgical studies.

//et

The Sidikila deposit is over 600 m long, up to 100 m wide and has
been intersected in reverse circulation (RC) holes to approximately 100
m below surface, except for four holes that were drilled between 200 to
250 m below surface. The deposit strikes north and dips steeply; the
deposit is open at depth and along strike to the southeast and to the
north. Gold mineralization is hosted in felsic intrusive rocks and
adjacent Birimian-age sedimentary rocks. Gold mineralization occurs in
quartz stockworks and disseminations and is associated with silica,
sericite, biotite and sulphide alteration; sulphide minerals include
pyrite and arsenopyrite with trace pyrrhotite, sphalerite and galena.

Table 1: Balandougouba Project - Inferred Mineral Resource
estimate for the Sidikila deposit.

//st
Grade greater than Cut-off



Tonnes
greater than      Au Cut-off       Cut-off    Au   Contained
(g/t)                               (tonnes)           (g/t)          Ozs Au
----------------------------------------------------------------------------
0.10                              43,980,000            0.87       1,236,000
----------------------------------------------------------------------------
0.20                              42,200,000            0.91       1,228,000
----------------------------------------------------------------------------
0.30                              39,800,000            0.94       1,208,000
----------------------------------------------------------------------------
0.40                              36,180,000            1.00       1,167,000
----------------------------------------------------------------------------
0.50                              31,850,000            1.08       1,104,000
----------------------------------------------------------------------------
0.60                              27,050,000            1.17       1,019,000
----------------------------------------------------------------------------
0.70                              22,690,000            1.27         928,000
----------------------------------------------------------------------------
0.80                              19,090,000            1.37         841,000
----------------------------------------------------------------------------
1.00                              13,690,000            1.56         686,000
//et

Inferred Mineral Resource

"An 'Inferred Mineral Resource' is that part of a Mineral Resource
for which quantity and grade or quality can be estimated on the basis
of geological evidence and limited sampling and reasonably assumed, but
not verified, geological and grade continuity. The estimate is based on
limited information and sampling gathered through appropriate
techniques from locations such as outcrops, trenches, workings and
drill holes.

"Due to the uncertainty that may be attached to Inferred Mineral
Resources, it cannot be assumed that all or any part of an Inferred
Mineral Resource will be upgraded to an Indicated or Measured Mineral
Resource as a result of continued exploration. Confidence in the
estimate is insufficient to allow the meaningful application of
technical and economic parameters or to enable an evaluation of
economic viability worthy of public disclosure. Inferred Mineral
Resources must be excluded from estimates forming the basis of
feasibility or other economic studies."

The Sidikila resource estimate is based on 42 RC holes (5,763 m)
containing 5,163 assays. The drill holes have been drilled on east-west
fences spaced 100 m apart; the holes were mostly drilled towards the
west at -50. The samples (1.0 m lengths) were composited to 2.5 m in
length and interpolated into blocks measuring 10 m by 10 m by 5 m using
ordinary kriging. The kriging exercise was completed in a series of 4
passes using an expanding search ellipse oriented and dimensioned from
the semivariograms. Solid wireframes of the oxide and sulphide
mineralization were used to constrain the estimate. The first pass used
a search ellipse with dimensions equal to 1/4 of the semivariogram
range. A minimum of 4 composites were required to estimate a block with
a maximum of 3 allowed from a given drill hole. In this manner, a
minimum of two drill holes were required to estimate a block. For
blocks not estimated in Pass 1, a second pass using a search dimension
equal to 1/2 the semivariogram range. A third pass using the full range
and a fourth pass using twice the range completed the exercise. In all
cases a maximum of 12 composites were allowed and if more than 12 were
found the closest 12 were used. For all estimated blocks containing
some percentage of external waste, a second kriging exercise was
completed using only composites outside the mineralized solids; the
kriging was completed in a similar manner as described for the
mineralized blocks.

The kriging parameters and number of blocks estimated in each pass
are tabulated below (Table 2).

//st
Number
of Blocks     Az /  Dist.       Az /  Dist.     Az /  Dist.
Domain      Pass Estimated      Dip    (m)        Dip    (m)      Dip   (m)
----------------------------------------------------------------------------
Mineralized
Solids

(9,284
blocks not
estimated)    1         7  353 / 0   35.0  263 / -30  11.25  83/ -60   15.0

-----------------------------------------------------------------
2     4,782  353 / 0   70.0  263 / -30   22.5  83/ -60   30.0

-----------------------------------------------------------------
3    27,215  353 / 0  140.0  263 / -30   45.0  83/ -60   60.0

-----------------------------------------------------------------
4    18,520  353 / 0  280.0  263 / -30   90.0  83/ -60  120.0
//et



Note - The 9,284 blocks within the geologic 3D solid model not
estimated were at depth where the minimum of 4 composites, with a
maximum of 3 from a single hole, were not found.

This maiden resource estimate is based on 42 RC holes with an
average length of 137 m. Considerable potential exists to expand the
existing resource by additional drilling down dip as well as along
strike to the north and southeast. The structure hosting the Sidikila
mineralization can be traced for 6 km to the southeast and over 15 km
to the north as a strong electromagnetic (EM) high. In addition to the
Sidikila deposit, several (5) other targets including Niani, Gberekole,
Mandiantri, Jade and Fouani have seen limited exploration to date (soil
geochemistry, geophysics and shallow drilling), however several of
these targets have extensive, shallow artisanal workings, which will be
the focus of future sampling and drilling programs.

Laboratory Procedures

Reverse circulation drill samples were submitted to ALS Chemex in
Bamako, Mali and the OMAC Stewart laboratory in Ireland. Except for 243
samples from hole GN1, the remainder of samples from this hole and all
the samples for the other 43 holes were prepared and analyzed at ALS
Chemex. Both ALS Chemex and OMAC Stewart are internationally recognized
independent commercial laboratories. The samples were analyzed by fire
assay with an atomic absorption spectrometry (AAS) finish after
digestion in aqua regia. Quality Control - Quality Insurance samples
(standards and duplicates) were inserted to monitor the analytical
results of the laboratory. The standards and duplicates from the
historical drill programs were within acceptable limits, however the
Qualified Persons recommends future programs include use of appropriate
blank control standards and increase the number of standard and
duplicate control samples.

Qualified Persons

Gary Giroux of Giroux Consultants Ltd. completed the resource
estimate and Micheal Gareau of M. Gareau & Associates Geological
Services Inc. and Gary Giroux jointly prepared the NI43-101 Technical
Report titled Mineral Resources of the Sidikila deposit, Balandougouba
Property, Republic of Guinea with an effective date of Dec. 1 2013. Mr.
Gareau and Mr. Giroux have extensive relevant experience and are
Qualified Persons in their respective fields as defined by NI43-101.
Mr. Gareau completed a site visit to the project on November 28, 2012.
The authors are not aware of any known legal, political, environmental,
or other risks that could materially affect the potential development
of the mineral resources or mineral reserves. The NI43-101 Technical
Report will be filed on SEDAR and Bullman Mineral's website within 45
days of this news release.

Andre C. Lambert, B.Sc. (Hons), EurGeol, MIMM is the Exploration
Manager for the Company and a qualified person as defined by National
Instrument 43-101. Mr. Lambert has reviewed and approved the technical
disclosure contained in this News Release.

About Bullman Minerals Inc.

Bullman Minerals Inc. is a Canadian based public company with a
focus on the acquisition, exploration and development of gold
properties in Guinea and neighboring countries of West Africa. The
Company owns two gold projects in the under-explored Siguiri Basin of
northeast Guinea, which is underlain by Birimian age rocks, the host
rock to most of the large gold deposits in West Africa. For details on
the projects, the reader is referred to NI43-101 Technical Report on
the Siguiri and Balandougouba Projects, Guinea, prepared by independent
qualified person Michael B. Gareau with an effective date of April 10,
2013 and available on SEDAR or the company's website.

Some statements in this news release contain forward-looking
information, including without limitation statements as to planned
expenditures and exploration programs. These statements address future
events and conditions and, as such, involve known and unknown risks,
uncertainties and other factors which may cause the actual results,
performance or achievements to be materially different from any future
results, performance or achievements expressed or implied by the
statements. Such factors include without limitation the completion of
planned expenditures, the ability to complete exploration programs on
schedule and the success of exploration programs.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or the accuracy of this news
release.

TSX Venture closing price for BUL-V
Date: 2014/03/28
Closing Price: 0.25

TEL:   +1 604 336-8618  Bullman Minerals Inc.
Peter Yue, CEO and Director
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1409100031TS11409101222-06590920140402