Source	Marketwire
Date	04/02/2014
Time	06:40:43 AM

Company	 CB GOLD INC.
Title	CB Gold's Initial Vetas Gold Project Mineral Resource Estimate





    CDNX Symbol: CBJ











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: CB Gold Inc.

TSX VENTURE SYMBOL: CBJ

April 2, 2014

CB Gold's Initial Vetas Gold Project Mineral Resource Estimate


VANCOUVER, BRITISH COLUMBIA--(Marketwired - April 2, 2014) - CB Gold Inc. (TSX 
VENTURE:CBJ) ("CB GOLD" or the "Company") is pleased to announce an initial 
mineral resource estimate ("Mineral Resource Estimate") on its first three 
targets at its 100% owned Vetas Gold Project, District of Santander, Colombia 
("Vetas Gold Project"). The estimate and resource model define two deposit 
styles: (i) near-surface stockwork and sheeted vein mineralization, and (ii) 
narrow fault-fill veins; and provide the foundation for further exploration and 
initiation of development studies on the Vetas Project.

NI 43-101 Mineral Resource Estimate

Highlights from the initial resource estimate recently completed by SRK 
Consulting (Canada) Inc. ("SRK") of Vancouver, B.C. include:

/T/

--  Steep topography and shallow depth of mineralization: Approximately 70%
of the total resource is above the valley floor (98% within 200 metres
of valley floor), which is anticipated to minimize the mining
infrastructure required to access the mineralization.
--  Excellent metallurgy: Preliminary metallurgical tests indicate potential
recoveries up to 96.1% from combined gravity and flotation processes
(see CB Gold release on August 19, 2013).
--  Strong continuity of mineralization: Modeling has delineated veins with
up to 240 metres of geological continuity along strike and down dip. Due
to gaps in drilling design, the estimated resources do not completely
fill in the modeled veins which highlights the potential for adding new
resources within the footprint of the current resource area.

Table 1: Mineral Resource Statement(i), Vetas Project, Santander Department
- Republic of Colombia, SRK Consulting (Canada) Inc., effective date, March
28, 2014.
----------------------------------------------------------------------------
Category         Tonnage           Grade                     Metal

Au           Ag           Au           Ag
---------------------------------------------------------------
000' t          g/t          g/t       000'oz       000'oz
----------------------------------------------------------------------------
Narrow, Fault-Fill Veins(i)
----------------------------------------------------------------------------
Indicated            118         3.74         8.58           14           33
Inferred           1,681         4.42        17.01          239          920
----------------------------------------------------------------------------
Near Surface, Stockwork Veins(ii)
----------------------------------------------------------------------------
Indicated          1,054         3.20         2.60          108           88
Inferred             941         1.64         1.63           50           49
----------------------------------------------------------------------------
Combined Mining
----------------------------------------------------------------------------
Indicated          1,172         3.25         3.20          123          121
Inferred           2,622         3.42        11.49          289          969
----------------------------------------------------------------------------
(i) Mineral resources are not mineral reserves and do not have demonstrated
economic viability. All figures are rounded to reflect the relative
accuracy of the estimate. Grade outlier restrictions have been used where
appropriate.
(ii) Narrow, Fault-fill vein mineral resources are expected to be mined
using underground methods and are reported at a cut-off of 1.50 g/t Au.
Near Surface, stockwork vein mineral resources are reported in relation to
a conceptual pit shell and are reported at a cut-off grade of 0.50 g/t Au.
Cut-off grades are based on the following assumptions: gold price: US$1,500
per ounce, processing cost: US$16/tonne, G&A: US$2.50/tonne, recovery: 95%,
and mining costs: US$2.50/tonne for open pit and US$50/tonne for
underground. No considerations were given to potential revenues from silver
or other metals.

/T/

Vetas Project Exploration Potential (i):

Due to the high relief of the project area, surface drilling efforts have been 
focused on drilling numerous holes from individual drill platforms to increase 
definition efficiency. This has resulted in significant gaps in drilling 
coverage along interpreted gold-silver veins. SRK considers these gaps, as well 
as the interpreted down-dip extents of the veins, to be significant exploration 
targets. In areas with large gaps in drilling coverage, SRK assessed 
exploration potential for additional tonnes and grade which will be prioritized 
by CB Gold in future drilling campaigns.

SRK estimated exploration potential separately for the El Dorado/San Bartolo 
fault-fill vein systems and the Real Minera, intrusive hosted stockwork system. 
The estimated exploration target for the El Dorado/San Bartolo fault-fill veins 
range between 2.0M and 3.0M tonnes at an estimated grade ranging between 2.7 
g/t to 5.5 g/t Au (approximately, 170 to 530 thousand ounces of gold) and 10 
g/t to 30 g/t Ag (approximately, 640 to 2,890 thousand ounces of silver). The 
estimated exploration target for the Real Mineral stockwork veins range between 
4.5M and 8.0M tonnes at an estimated grade ranging between 0.35 to 0.5 g/t Au 
(approximately, 50 to 130 thousand ounces of gold) and 1 g/t to 1.25 g/t Ag 
(approximately, 140 to 320 thousand ounces of silver).

(i) The potential quantity and grade is conceptual in nature; there has been 
insufficient exploration to define a mineral resource; it is uncertain if 
further exploration will result in discovery of a mineral resource.

Fabio Capponi, President and CEO of CB Gold Inc., said, "We are very pleased 
with the initial resource estimate which involves only the first three targets 
so far tested by the drilling program at the Company's Vetas Gold Project. The 
resource estimate and the geological potential have demonstrated how quickly 
and easily the resource at the Vetas Gold Project can be expanded, in fact, the 
grade estimate model has shown several areas where drilling can be focused to 
significantly increase the resource. We plan to aggressively target these areas 
with future drilling, in conjunction with initiating development studies to 
support a preliminary economic assessment of the project."

Resource Estimation Parameters:

Mineral resource estimates for the Vetas Gold Project were completed using 
Maptek Vulcan(R) software by Guy Dishaw, P.Geo., of SRK. The resource estimate 
incorporates the results of 161 drill holes and 132 surface channel samples 
that have been verified by SRK.

Three dimensional mineralized vein domains were constructed by SRK by 
incorporating drill hole intersections with underground and surface mapping 
data. A total of 34 vein models were designed and are grouped by their vein 
character and orientation into 4 types: El Dorado fault-fill type, San Bartolo 
and Real Minera - San Bartolo fault-fill type, and Real Minera Stockwork type.

Original assays were composited to 1.5 metre lengths within the mineralized 
vein domains. Very few samples were traditionally capped at 100 g/t Au and 200 
g/t Ag. The influence of very high-grade gold and silver values was further 
limited by employing a search distance restriction which prevents a sample, 
with a value above a high-grade threshold, from being used to estimate distant 
blocks. The high-grade threshold values were established by analysis of 
cumulative probability plots and the restriction distance was limited to the 
range of modeled continuity for the type of vein (15m for Fault-fill type veins 
and 30m for Stockwork type veins). Limiting the influence of the very 
high-grade samples results in overall metal losses of 17% for gold and 26% for 
silver.

Ordinary kriging and inverse distance interpolation methods were used to 
estimate Au and Ag grades within each of the Real Minera Stockwork type and 
Fault-Fill type mineralized domains, respectively. Metal values were estimated 
into blocks measuring 5x5x5 metres, sub-blocked to a minimum of 1x1x1 metres. 
Known mined areas were removed, based on available surveys of the existing 
underground development drifts and stopes.

Mineral resources are classified in the Indicated category for all blocks 
estimated by a minimum of 3 samples, where at least 1 sample occurs within a 
maximum of 20m from the block centroid. All remaining estimated blocks were 
assigned to the Inferred category, if at least one sample used to estimate the 
block was found within a maximum distance of 60m from the block centroid.

Qualified Persons

Guy Dishaw, P.Geo., of SRK, Vancouver, B.C., a "Qualified Person" as defined 
under NI 43-101 is responsible for the estimation of the Vetas Gold Project 
mineral resources. The contents of this press release were prepared and 
approved by Marius Mare, M.Sc., P.Geo., Vice President Exploration, CB Gold 
Inc. The complete NI 43-101 technical report will be filed within 45 days of 
this press release and will be available on the Company's website at 
www.cbgoldinc.com and on SEDAR at www.sedar.com.

About CB Gold Inc.:

CB Gold is a mineral exploration company headquartered in Vancouver, British 
Columbia. CB Gold, through its wholly-owned subsidiary, Leyhat Colombia 
Sucursal, is actively pursuing the exploration and development of mineral 
properties in the Republic of Colombia. The Vetas Gold Project consists of a 
number of existing mines (operations currently suspended) and exploration 
concessions, and its exploration and development activities are not affected by 
the declared Regional Natural Park Paramo de Santurban.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this news release.

The securities of CB Gold described herein have not been and will not be 
registered under the United States Securities Act of 1933, as amended (the 
"U.S. Securities Act") or any state securities laws and may not be offered or 
sold within the United States or to U.S. Persons unless registered under the 
U.S. Securities Act and applicable state securities laws or an exemption from 
such registration is available.

Some of the statements contained in this release are forward-looking 
statements, such as estimates and statements that describe the Company's future 
plans, objectives or goals, including words to the effect that the Company or 
management expects a stated condition or result to occur. Since forward-looking 
statements address future events and conditions, by their very nature, they 
involve inherent risks and uncertainties. Actual results in each case could 
differ materially from those currently anticipated in such statements.

- 30 -

CONTACT INFO:

CB Gold Inc.
info@cbgoldinc.com
www.cbgoldinc.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

If you no longer want to receive announcements from us, please do not reply to 
this e-mail.
Instead simply click http://marketwire.com/mw/fmu.jsp?id=475391022