Source	Marketwire
Date	04/01/2014
Time	06:19:39 AM

Company	 INZINC MINING LTD.
Title	InZinc Reports Positive Preliminary Economic Assessment Results For West 
Desert Zinc-Iron-Copper Project





    CDNX Symbol: IZN











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: InZinc Mining Ltd.

TSX VENTURE SYMBOL: IZN

April 1, 2014

InZinc Reports Positive Preliminary Economic Assessment Results For West Desert 
Zinc-Iron-Copper Project


VANCOUVER, BRITISH COLUMBIA--(Marketwired - April 1, 2014) - InZinc Mining Ltd. 
(TSX VENTURE:IZN) is pleased to announce that it has received the results of an 
independent Preliminary Economic Assessment (PEA) of the Company's 
100-per-cent-owned West Desert Project in Utah.

Highlights

/T/

--  after-tax NPV(8%) is US$258.1 million, IRR is 23% and payback is
estimated at 3.7 years assuming a zinc price of US$1/lb and a 14.8 year
mine life at 2.37 million tonnes per year
--  conventional mining and milling
--  average annual zinc production of 107.9 million lbs
--  average annual iron concentrate (magnetite) production of 1.0 million
tonnes
--  average annual copper production of 9.9 million lbs
--  average direct cash costs (C1) of US$-0.04 per pound of zinc and average
fully allocated costs (C3) of US$0.50 per pound of zinc
--  initial project capital costs of US$247.4 million, including
contingencies
--  good potential for resource expansion

/T/

"MDA's preliminary economic assessment is a major re-appraisal of the West 
Desert project", stated Chris Staargaard, President and CEO of InZinc Mining. 
"Over the next several years, a number of the world's more significant zinc 
mines will close, removing a substantial proportion of annual production. The 
PEA confirms that West Desert has the potential to help fill this gap as an 
important zinc and iron producer within the continental USA, one that would be 
in the lowest decile for zinc cash costs globally. With the potential for both 
excellent economics and significant upside remaining in the form of resource 
expansion, this Project represents a very high-quality opportunity for our 
shareholders. We are excited about the conclusions and further opportunities 
identified in the PEA and look forward to advancing West Desert through 
pre-feasibility."

The PEA was prepared by Mine Development Associates ("MDA") with contributions 
from International Metallurgical and Environmental Inc.("IME") in accordance 
with the definitions in Canadian National Instrument 43-101. All dollar amounts 
are US currency. The PEA is considered preliminary in nature. It includes 
Inferred mineral resources that are considered too speculative to have the 
economic considerations applied that would enable classification as mineral 
reserves. There is no certainty that the conclusions within the PEA will be 
realized. Mineral resources that are not mineral reserves do not have 
demonstrated economic viability.

Economics

The table below summarizes base case economic metrics for the project as well 
as its sensitivity to the price of zinc.

/T/

----------------------------------------------------------------------------
After-Tax                       Pre-Tax
----------------------------------------------------------------------------
Zinc
Price             NPV      NPV      IRR      NPV      NPV      IRR  Payback
($/lb)           (5%)     (8%)      (%)     (5%)     (8%)      (%)    (Yrs)
----------------------------------------------------------------------------
0.80             $238M    $146M      17%    $321M    $208M      19%      4.9
----------------------------------------------------------------------------
1.00             $377M    $258M      23%    $507M    $357M      27%      3.7
----------------------------------------------------------------------------
1.20             $507M    $363M      29%    $693M    $506M      34%      3.0
----------------------------------------------------------------------------

Note: US$; base case at Zn=$1 in bold

/T/

Project economics were estimated on the basis of the average of long term metal 
price forecasts periodically published by a number of large banking and 
financial institutions and included zinc at $1/lb, copper at $3/lb, iron ore at 
$105/t (62% Fe, CFR-Tianjin), gold at $1,300/oz and silver at $21/oz. The 
project's iron concentrate (magnetite) is expected to attract a $10/t premium 
to the Tianjin benchmark iron ore price and be priced at $115/t. No long term 
projections were available for the indium price and a price of $600/kg, well 
below the current spot price of about $750/kg, was chosen.

Mineral Resources

The resource base at the West Desert project was re-estimated to include iron. 
MDA constructed a highly detailed, three dimensional block model on the basis 
of both InZinc's and historical drilling. Zinc, iron, copper and indium grades 
were assigned to each block using inverse distance interpolation. The 
percentage of iron occurring as magnetite throughout the resource was modelled 
on the basis of Davis Tube assays from drilling carried out both historically 
and by InZinc in 2007-2008. Gross metal values (GMV) used for cutoff reporting 
were based on a zinc price of US$1/lb, a copper price of US$3/lb, an iron ore 
price of $105/tonne and an indium price of US$600/kg to determine the relative 
value of each metal. The magnetite price of $115/t used in the GMV calculation 
includes the expected $10/t premium to the benchmark iron ore price.

A GMV cutoff value of $50/tonne was used to define resources that would be 
potentially mineable in an underground operation. A GMV cutoff value of 
$15/tonne was used to define oxide resources that would be potentially mineable 
in an open pit operation. All mineralization was diluted to minimum dimensions 
of 2m by 2m by 3m.

Project wide underground resources are summarized in the table below:

/T/

----------------------------------------------------------------------------
Cut-off               Million   GMV    ZnEq     Zn        Zn     Cu       Cu
($GMV)     Category    Tonnes   ($)     (%)    (%)    (Mlbs)    (%)   (Mlbs)
----------------------------------------------------------------------------
50        Indicated      13.0   137    6.22   2.16     691.3   0.23     65.1
----------------------------------------------------------------------------
100       Indicated       8.0   175    7.96   3.18     561.1   0.29     50.9
----------------------------------------------------------------------------
150       Indicated       3.9   232   10.50   5.28     456.1   0.34     29.2
----------------------------------------------------------------------------
50         Inferred      46.0   123    5.57   1.76   1,781.0   0.22    224.6
----------------------------------------------------------------------------
100        Inferred      23.8   168    7.59   3.02   1,583.9   0.32    167.2
----------------------------------------------------------------------------
150        Inferred       9.8   236   10.70   5.88   1,266.5   0.43     92.4
----------------------------------------------------------------------------

----------------------------------------------------------
Cut-off                   In      In  Magnetite  Magnetite
($GMV)     Category    (g/t)     (t)        (%)       (Mt)
----------------------------------------------------------
50        Indicated       33     433         48        6.2
----------------------------------------------------------
100       Indicated       42     340         53        4.2
----------------------------------------------------------
150       Indicated       54     211         53        2.1
----------------------------------------------------------
50         Inferred       24   1,102         48       22.0
----------------------------------------------------------
100        Inferred       32     762         53       12.5
----------------------------------------------------------
150        Inferred       38     375         48        4.7
----------------------------------------------------------
Note: base case in bold; US$; ZnEq based on 100% recovery and Zn=$1/lb,
Cu=$3/lb, Magnetite=$115/t, and In=$600/kg

/T/

Project wide near surface oxide resources are summarized in the table below:

/T/

----------------------------------------------------------------------------
Cut-off               Million   GMV    ZnEq     Zn        Zn     Cu       Cu
($ GMV)    Category    Tonnes   ($)     (%)    (%)    (Mlbs)    (%)   (Mlbs)
----------------------------------------------------------------------------
15        Indicated       1.4   105    4.76   3.44     106.2   0.20      6.2
----------------------------------------------------------------------------
15         Inferred       6.2    97    4.40   2.95     404.8   0.14     19.8
----------------------------------------------------------------------------

----------------------------------------------------------
Cut-off                   In      In  Magnetite  Magnetite
($ GMV)    Category    (g/t)     (T)        (%)       (Mt)
----------------------------------------------------------
15        Indicated        8      11          9        0.1
----------------------------------------------------------
15         Inferred        9      58         15        0.9
----------------------------------------------------------
Note: US$; ZnEq based on100% recovery and Zn=$1/lb, Cu=$3/lb,
Magnetite=$115/t, and In=$600/kg

/T/

Mineralization is open for expansion in three directions and there is very good 
potential for the discovery of additional mineralized zones away from existing 
resources.

Mining and Processing

The PEA contemplates a 5,000 tonne per day underground mining operation ramping 
up to 6,500 tonnes per day in year three using longitudinal and transverse 
long-hole open stoping mining methods based on the underground resource only. 
Near surface oxide resources were not assessed and remain as a future 
opportunity.

Access to the deposit would be via two ramps, one of which would also host a 
conveyor system for ore haulage. A total of 34.0 million tonnes of ore would be 
mined over 14.8 years at an average run of mine mill feed grade of 2.72% Zn, 
0.27% Cu, 44.0% magnetite and 30 gpt In. Indicated and Inferred resources below 
the mining cut-off grade but located inside minable volumes were used to dilute 
the material processed at grade. Internal dilution of non-resource material was 
added at zero grade. Average total dilution in the mineable material is 
approximately 20%.

Run of mine material would undergo crushing and grinding to 65 microns followed 
by separation of a magnetite concentrate using traditional low intensity 
magnetic drum separators. Metallurgical studies have shown better than 95% 
recovery of magnetite into a concentrate grading 63% iron with no deleterious 
elements. The iron up-grading process is effective at removing copper and zinc 
and insignificant levels of these metals remain in the iron concentrate. The 
non-magnetic tails from the separation process, which contain essentially all 
of the copper and zinc minerals, would feed a standard flotation process plant 
with design capacity of 6,500 tonnes per day to accommodate variations in the 
proportion of magnetite in run of mine material. Feed grade to the flotation 
plant is expected to be in the range of 3-6% Zn.

Expected metallurgical recovery for zinc is 92 per cent into a clean 
concentrate grading 55% zinc and containing high levels of indium with no 
deleterious elements. Approximately 74% of the copper is expected to be 
recovered into a clean concentrate grading 29% Cu with payable levels of silver 
and gold and no deleterious elements.

Projected production of payable metals is summarized in the table below:

/T/

----------------------------------------------------------------------------
Annual Average        Life of Mine
----------------------------------------------------------------------------
Zinc (Mlbs)                                        107.9             1,594.3
----------------------------------------------------------------------------
Copper (Mlbs)                                        9.9               146.7
----------------------------------------------------------------------------
Indium (t)                                          38.3               566.1
----------------------------------------------------------------------------
Magnetite (Mt)                                       1.0                14.5
----------------------------------------------------------------------------
Gold (Koz)                                           7.6               113.0
----------------------------------------------------------------------------
Silver (Koz)                                        76.9             1,137.0
----------------------------------------------------------------------------

/T/

Capital and Operating Costs

The projected capital and operating costs for West Desert over a 14.8 year mine 
life are summarized in the tables below.

West Desert Capital Costs (US$ millions)

/T/

----------------------------------------------------------------------------
Underground Development                                                105.4
----------------------------------------------------------------------------
Project Development                                                      7.0
----------------------------------------------------------------------------
Facilities                                                               5.2
----------------------------------------------------------------------------
Mining Equipment                                                        50.9
----------------------------------------------------------------------------
Process Plant                                                          123.1
----------------------------------------------------------------------------
Tailings                                                                33.2
----------------------------------------------------------------------------
Contingency, Indirects, and EPCM                                        64.1
----------------------------------------------------------------------------
Life of Mine Capital Cost                                              388.9
----------------------------------------------------------------------------
Sustaining Capital                                                     141.5
----------------------------------------------------------------------------
Initial Capital Cost                                                   247.4
----------------------------------------------------------------------------

/T/

West Desert Operating Costs (US$ per tonne)

/T/

----------------------------------------------------------------------------
Mining Cost                                                            23.00
----------------------------------------------------------------------------Expe
nsed Development                                                    3.00
----------------------------------------------------------------------------
Processing Cost                                                        12.23
----------------------------------------------------------------------------
Tailings Cost                                                           0.25
----------------------------------------------------------------------------
G&A Costs                                                               2.60
----------------------------------------------------------------------------
Total Operating Cost                                                   41.08
----------------------------------------------------------------------------

/T/

C1, C2 and C3 cash costs (as defined by Brook Hunt) per pound of payable zinc 
are listed in the table below.

West Desert Average Cash Costs (US$) per Lb Payable Zinc

/T/

----------------------------------------------------------------------------
C1 - Direct Cash Cost                                                  -0.04
----------------------------------------------------------------------------
C2 - Production Cost                                                    0.45
----------------------------------------------------------------------------
C3 - Fully Allocated Cost                                               0.50
----------------------------------------------------------------------------

/T/

Opportunities for Enhanced Economics

/T/

--  good potential to increase the resource to the east, west and south
--  potential for the discovery of localized higher-grade areas within the
resource
--  very good potential for the discovery of additional mineralized zones
within the Project area
--  potential for additional recoverable zinc and copper at depth, within
the magnetite resource but beyond the current limits of zinc-copper data
--  transportation costs for iron concentrate (magnetite) could be
significantly reduced through contract negotiations with the railroads
and/or sourcing a domestic consumer(s) in the United States
--  potential to process oxide zinc mineralization
--  potential cost reductions associated with optimization of the tailings
facility

/T/

Future Work

Further work leading to a Pre-Feasibility Study is recommended and will include 
drilling, engineering and marketing studies, hydrological and geotechnical 
analysis, as well as various baseline environmental and archeological studies.

The complete technical report constituting the PEA will be filed within 45 days 
and will be available on InZinc's website and on SEDAR. The technical 
information contained in this news release has been reviewed and approved by 
the Qualified Persons listed in the table below who are independent of InZinc 
Mining Ltd. and responsible for the Preliminary Economic Assessment of the West 
Desert project.

/T/

----------------------------------------------------------------------------
Qualified person     Firm                          Scope of responsibility
----------------------------------------------------------------------------
Paul Tietz, CPG      Mine Development Associates   resource estimation
----------------------------------------------------------------------------
mine planning, financial
Thomas Dyer, P.E.    Mine Development Associates   analysis
----------------------------------------------------------------------------
International Metallurgical
Jeff Austin, P.Eng.  and Environmental Inc.        metallurgy and processing
----------------------------------------------------------------------------

/T/

InZinc Mining Ltd.

Chris Staargaard

Cautionary Note Regarding Forward-Looking Statements

This news release contains forward-looking statements and forward-looking 
information (collectively, "forward-looking statements") within the meaning of 
applicable Canadian and US securities legislation. All statements, other than 
statements of historical fact, included herein including, without limitation, 
statements regarding the potential of the Company's mineral projects and the 
Company's planned drilling and exploration programs. Although the Company 
believes that such statements are reasonable, it can give no assurance that 
such expectations will prove to be correct. Forward-looking statements are 
typically identified by words such as: believe, expect, anticipate, intend, 
estimate, postulate and similar expressions, or are those, which, by their 
nature, refer to future events. The Company cautions investors that any 
forward-looking statements by the Company are not guarantees of future results, 
performance, or actions and that actual results and actions may differ 
materially from those in forward-looking statements as a result of various 
factors, including, but not limited to, those risks and uncertainties disclosed 
in the Company's Management Discussion and Analysis for the year ended December 
31, 2012 filed with certain securities commissions in Canada and other 
information released by the Company and filed with the appropriate regulatory 
agencies. All of the Company's Canadian public disclosure filings may be 
accessed via www.sedar.com and readers are urged to review these materials, 
including the technical reports filed with respect to the Company's mineral 
properties.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

InZinc Mining Ltd.
C.F. Staargaard
President and CEO
(604) 687-7211

or

InZinc Mining Ltd.
Joyce Musial
Corporate Communications
(604) 317-2728
joyce@inzincmining.com
www.inzincmining.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

If you no longer want to receive announcements from us, please do not reply to 
this e-mail.
Instead simply click http://marketwire.com/mw/fmu.jsp?id=475068660