Source	Marketwire
Date	04/15/2014
Time	06:02:59 AM

Company	 MANSON CREEK RESOURCES LTD.
Title	Manson Creek Provides a Corporate and Technical Update





    CDNX Symbol: MCK











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Manson Creek Resources Ltd.

TSX VENTURE SYMBOL: MCK

April 15, 2014

Manson Creek Provides a Corporate and Technical Update


CALGARY, ALBERTA--(Marketwired - April 15, 2014) - Manson Creek Resources Ltd. 
(TSX VENTURE:MCK) ("Manson" or "the Company") is pleased to provide a technical 
overview on its Tell Property, Yukon, in conjunction with its current financing 
and 2014 planned exploration program, including first pass drill testing of the 
Tell target.

The Tell Property, located some 140 kilometers north east of Mayo, Yukon, was 
initially staked by Manson as a high priority target in 2002, following 
extensive field work in the region from 1998 to 2002. The property consists of 
103 claims covering a surface area of roughly 2,150 hectares, 100% owned by 
Manson.

Due to poor market conditions at the time and lack of activity in the region, 
the property did not see significant work except for a number of short field 
programs that occurred in 2005, 2011 and 2012. Surface prospecting and 
geochemical sampling in 2005 and 2011 outlined the presence of 7 significant 
zones of metal bearing gossanous material at surface, occurring either as 
coatings on exposed rocks and talus (Main Tell gossan), as zones of iron oxide 
coated soils and surface materials, or as active sinters/spring sources. The 
uppermost 5 main gossans define a zone oriented east-west, and approximately 
600 meters in strike length.

These gossans all carry high level of various metals including zinc, nickel, 
cobalt, as well as anomalous amounts of tracer materials such as cobalt, 
barium, arsenic, mercury and locally silver. A compilation table of the ranges 
of elements for each gossan is presented below (see NR 12-14, Sept. 14/12).

/T/

----------------------------------------------------------------------------
Number of
Samples and       Zinc       Nickel    Arsenic      Silver
Location                Type         ppm          ppm        ppm         g/t
----------------------------------------------------------------------------
2 Soil    5,795 to greater than    966 to  less than
Roswell              Samples       7,149        1,000      1,114  0.1 to 0.1
----------------------------------------------------------------------------
245 to
6 Soil    6,005 to greater than            less than
Crystal Springs      Samples      23,500        1,000 4.0 to 110  0.1 to 0.8
----------------------------------------------------------------------------
425 to
3 Soil/Silt   10,800 to greater than
Ash Springs          Samples      24,500        1,000 114 to 358           -
----------------------------------------------------------------------------
3 Rock   19,700 to     1,056 to
Ash Springs          Samples      27,500        1,591   10 to 25  0.6 to 1.0
----------------------------------------------------------------------------
164 to
4 Soil/Silt    4,738 to greater than  1,149 to  less than
Area 51              Samples       8,565        1,000      1,816  0.1 to 0.2
----------------------------------------------------------------------------
808 to
7 Soil   12,500 to greater than
Majestic             Samples      17,700        1,000   18 to 33  0.1 to 0.2
----------------------------------------------------------------------------
1 Soil
Corona                Sample      15,600          973         31         0.1
----------------------------------------------------------------------------
Tell Zone
(Historical     4 Soil/Silt   20,020 to     1,545 to             less than
Sampling)           Samples      49,600        2,560  16 to 103  0.2 to 0.2
----------------------------------------------------------------------------
8 Rock
Samples   15,700 to                          less than
Tell Zone       (Ferricrete)      24,900   401 to 604    8 to 30  0.2 to 0.4
----------------------------------------------------------------------------

/T/

Of significance, there is a large zone of abnormally stunted vegetation, also 
known as a "kill zone", which is framed by the known gossans. These zones often 
develop due to high acidity in soils as well as high metal contents that can be 
related to underlying sources of mineralization. The core of this kill zone is 
approximately 1 km long in an east-west direction with widths varying between 
100 to 500 meters.

In 2005, a small grid of soil sampling centered around the main Tell gossan was 
performed, consisting of 4 lines, 100 meters apart and with sampling every 25 
meters along each line. This outlined a zone 400 meters by 400 meters with 
anomalous zinc values above 100 ppm (parts per million), with a core area 
roughly 240 meters by 75 meters with values ranging between 10,000 to 49,600 
ppm (1 to 5%) zinc, and a coincident 250 to 2600 ppm (0.26%) nickel anomaly. 
Barium, cobalt and silver were also found to be anomalous in various parts of 
the grid. (NR-11-11 - August 22/11 and NR 12-14 - September 14/12)

In 2012, an induced polarization surface geophysical survey grid was 
established to cover the area of the main gossan trend and associated kill 
zone. The survey outlined a large zone of low electrical resistivity, or 
conductivity (800 meters in length by 150 to 250 meters in width) with a 
coincident chargeability anomaly (500 meters by 100 meters in width). Both the 
conductivity and chargeability anomalies extend to the maximum survey depth (to 
400 meters), and also extend beyond the actual grid, and remain open (NR-12-14, 
September 14, 2012).

Preliminary field mapping of the target area to date has not identified any 
geological unit at surface that could be responsible for the metal signatures 
or geophysical anomalies revealed by the surveys, and it is interpreted that a 
shallow metal bearing massive sulphide VMS/Sedex type target may be the source 
of the anomalies. This interpretation is supported by extensive historical 
regional work identifying both volcanic rocks and exhalative units in the 
region.

The correlation of the zones of high conductivity and chargeability with known 
gossans, the extensive vegetation kill zone and known metal signatures found in 
all gossans and in the soil grid all support a priority drill target, and also 
suggests that further work regionally should be undertaken to identify 
additional targets. A presentation of the project can be found at www.manson.ca.

In March 2014, Manson Creek entered into an Letter of Intent agreement with 
Guatavita Gold Corp., a private non-arm's length company, to create a Strategic 
alliance to conduct further exploration at the existing Tell property and 
regionally (NR 14-02, March 20, 2014). The Guatavita/Manson (or "Guaman") 
alliance is anticipating a two phase program of regional and focused 
exploration to advance the project to and through the drill stage, subject to 
completion of the previously announced financing. Total program expenditures 
are anticipated to be $1 million dollars in two stages, for which Guatavita may 
earn a 50% interest in the Manson Property by contributing $650,000 of the 
expenditures, at which point a Joint Venture will be formed. The project 
operator is Manson.

The 2014 exploration program consists of a first phase regional airborne 
helicopter supported Mag/EM geophysics aimed at defining the extent of the Tell 
conductor, as well as identifying any similar conductors in the region. This 
work will be followed up with ground checking, mapping and sampling of any new 
conductors, as well as completion of an extensive soil grid over the remainder 
of the Tell target that was not previously fully covered with systematic 
sampling. This first phase of work is currently budgeted at $368,000, and 
subject to financing being in place, is estimated to take place between May and 
June. The second phase of work will consist of drill testing of the large 
untested conductor with a minimum program of 800 meters of diamond drilling, in 
a minimum of four drill holes across the coincident zone of 
conductivity/chargeability and surface gossan formation. This second phase of 
work is currently budgeted at $632,000, and is anticipated to take place 
mid-July to mid-August. The program has been fully permitted.

Pursuant to TSX Venture Exchange policies, Manson will be commissioning an 
independent technical report prepared in accordance with NI 43-101, which will 
be filed on SEDAR once completed. This is required as part of the Exchange 
approvals required for the LOI transaction with Guatavita Gold Corp. on the 
Tell property as announced on March 20th 2014, and subsequent announcement of 
the financing and restructuring of the Company as announced on March 26, 2014. 
This report is to be completed by the end of June, 2014.

It is anticipated that the restructuring announced by the Company will be 
completed within the next week, and the financing closing on a post 
consolidation basis shortly thereafter.

Samples were forwarded to the Eco Tech Laboratory Stewart Group in Whitehorse, 
Yukon for analysis. The Stewart Group Lab are an independent certified 
commercial laboratory All of the soil and rock samples were analyzed using 
inductively coupled plasma (ICP) together with mass spectrometry (MS) finish. 
Gold was analyzed by a fire assay preparation with an atomic absorption 
spectroscopy finish.

The President of Manson Creek Resources Ltd., Jean-Pierre Jutras, P.Geol., is 
the Qualified Person responsible for the preparation of this news release.

On Behalf of the Board of Directors,

Jean-Pierre Jutras, President/Director

The TSX Venture Exchange has neither approved nor disapproved of the contents 
of this press release.

Except for the historical and present factual information contained herein, the 
matters set forth in this news release, including words such as "expects", 
"projects", "plans", "anticipates" and similar expressions, are forward-looking 
information that represents management of Manson Creek's internal projections, 
expectations or beliefs concerning, among other things, future operating 
results and various components thereof or the economic performance of Manson 
Creek. The projections, estimates and beliefs contained in such forward-looking 
statements necessarily involve known and unknown risks and uncertainties, which 
may cause Manson Creek's actual performance and financial results in future 
periods to differ materially from any projections of future performance or 
results expressed or implied by such forward-looking statements. These risks 
and uncertainties include, among other things, those described in Manson 
Creek's filings with the Canadian securities authorities. Accordingly, holders 
of Manson Creek shares and potential investors are cautioned that events or 
circumstances could cause results to differ materially from those predicted. 
Manson Creek disclaims any responsibility to update these forward-looking 
statements.

- 30 -

CONTACT INFO:

Manson Creek Resources Ltd.
Jean-Pierre Jutras
1.403.233.0464
www.manson.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

If you no longer want to receive announcements from us, please do not reply to 
this e-mail.
Instead simply click http://marketwire.com/mw/fmu.jsp?id=477306907