Source	MARKET NEWS
Date	04/15/2014
Time	06:23:16 AM

Company	 Manson Creek Resources Ltd.
Title	Corporate And Technical Update





    CDNX Symbol: MCK











Press Release	





Corporate And Technical Update --->@NEWS RELEASE
MANSON CREEK RESOURCES LTD ("MCK-V;MCKRF-0")
- Corporate And Technical Update

Manson Creek Resources Ltd. ("Manson" or "the Company") is pleased
to provide a technical overview on its Tell Property, Yukon, in
conjunction with its current financing and 2014 planned exploration
program, including first pass drill testing of the Tell target.

The Tell Property, located some 140 kilometers north east of Mayo,
Yukon, was initially staked by Manson as a high priority target in
2002, following extensive field work in the region from 1998 to 2002.
The property consists of 103 claims covering a surface area of roughly
2,150 hectares, 100% owned by Manson.

Due to poor market conditions at the time and lack of activity in
the region, the property did not see significant work except for a
number of short field programs that occurred in 2005, 2011 and 2012.
Surface prospecting and geochemical sampling in 2005 and 2011 outlined
the presence of 7 significant zones of metal bearing gossanous material
at surface, occurring either as coatings on exposed rocks and talus
(Main Tell gossan), as zones of iron oxide coated soils and surface
materials, or as active sinters/spring sources. The uppermost 5 main
gossans define a zone oriented east-west, and approximately 600 meters
in strike length.

These gossans all carry high level of various metals including
zinc, nickel, cobalt, as well as anomalous amounts of tracer materials
such as cobalt, barium, arsenic, mercury and locally silver. A
compilation table of the ranges of elements for each gossan is
presented below (see NR 12-14, Sept. 14/12).

//st
Location     Number of       Zinc         Nickel      Arsenic       Silver
Samples          ppm            ppm          ppm       g/t
and Type

Roswell      2 Soil Samples  5,795 to 7,149  )1,000   966 to 1,114  (0.1 to
0.1
Crystal
Springs     6 Soil Samples  6,005 to 23,500 245 to
)1,000   4.0 to 110    (0.1 to
0.8
Ash Springs  3 Soil/Silt
Samples        10,800 to 24,500 425 to
)1,000   114 to 358     -
Ash Springs  3 Rock Samples 19,700 to 27,500 1,056 to
1,591     10 to 25      0.6 to
1.0
Area 51      4 Soil/Silt
Samples         4,738 to 8,565  164 to   1,149 to
)1,000   1,816        (0.1 to
0.2
Majestic     7 Soil Samples 12,500 to 17,700 808 to
)1,000   18 to 33      0.1 to
0.2
Corona       1 Soil Sample  15,600           973            31      0.1
Tell Zone
(Historical
Sampling)   4 Soil/Silt
Samples        20,020 to 49,600 1,545 to
2,560    16 to 103   (0.2 to
0.2
Tell Zone    8 Rock Samples
(Ferricrete)   15,700 to 24,900   401 to
604     8 to 30    (0.2 to
0.4

//et

Of significance, there is a large zone of abnormally stunted
vegetation, also known as a "kill zone", which is framed by the known
gossans. These zones often develop due to high acidity in soils as well
as high metal contents that can be related to underlying sources of
mineralization. The core of this kill zone is approximately 1 km long
in an east-west direction with widths varying between 100 to 500
meters.

In 2005, a small grid of soil sampling centered around the main
Tell gossan was performed, consisting of 4 lines, 100 meters apart and
with sampling every 25 meters along each line. This outlined a zone 400
meters by 400 meters with anomalous zinc values above 100 ppm (parts
per million), with a core area roughly 240 meters by 75 meters with
values ranging between 10,000 to 49,600 ppm (1 to 5%) zinc, and a
coincident 250 to 2600 ppm (0.26%) nickel anomaly. Barium, cobalt and
silver were also found to be anomalous in various parts of the grid.
(NR-11-11 - August 22/11 and NR 12-14 - September 14/12)

In 2012, an induced polarization surface geophysical survey grid
was established to cover the area of the main gossan trend and
associated kill zone. The survey outlined a large zone of low
electrical resistivity, or conductivity (800 meters in length by 150 to
250 meters in width) with a coincident chargeability anomaly (500
meters by 100 meters in width). Both the conductivity and chargeability
anomalies extend to the maximum survey depth (to 400 meters), and also
extend beyond the actual grid, and remain open (NR-12-14, September 14,
2012).

Preliminary field mapping of the target area to date has not
identified any geological unit at surface that could be responsible for
the metal signatures or geophysical anomalies revealed by the surveys,
and it is interpreted that a shallow metal bearing massive sulphide
VMS/Sedex type target may be the source of the anomalies. This
interpretation is supported by extensive historical regional work
identifying both volcanic rocks and exhalative units in the region.

The correlation of the zones of high conductivity and
chargeability with known gossans, the extensive vegetation kill zone
and known metal signatures found in all gossans and in the soil grid
all support a priority drill target, and also suggests that further
work regionally should be undertaken to identify additional targets. A
presentation of the project can be found at www.manson.ca.

In March 2014, Manson Creek entered into an Letter of Intent
agreement with Guatavita Gold Corp., a private non-arm's length
company, to create a Strategic alliance to conduct further exploration
at the existing Tell property and regionally (NR 14-02, March 20,
2014). The Guatavita/Manson (or "Guaman") alliance is anticipating a
two phase program of regional and focused exploration to advance the
project to and through the drill stage, subject to completion of the
previously announced financing. Total program expenditures are
anticipated to be $1 million dollars in two stages, for which Guatavita
may earn a 50% interest in the Manson Property by contributing $650,000
of the expenditures, at which point a Joint Venture will be formed. The
project operator is Manson.

The 2014 exploration program consists of a first phase regional
airborne helicopter supported Mag/EM geophysics aimed at defining the
extent of the Tell conductor, as well as identifying any similar
conductors in the region. This work will be followed up with ground
checking, mapping and sampling of any new conductors, as well as
completion of an extensive soil grid over the remainder of the Tell
target that was not previously fully covered with systematic sampling.
This first phase of work is currently budgeted at $368,000, and subject
to financing being in place, is estimated to take place between May and
June. The second phase of work will consist of drill testing of the
large untested conductor with a minimum program of 800 meters of
diamond drilling, in a minimum of four drill holes across the
coincident zone of conductivity/chargeability and surface gossan
formation. This second phase of work is currently budgeted at $632,000,
and is anticipated to take place mid-July to mid-August. The program
has been fully permitted.

Pursuant to TSX Venture Exchange policies, Manson will be
commissioning an independent technical report prepared in accordance
with NI 43-101, which will be filed on SEDAR once completed. This is
required as part of the Exchange approvals required for the LOI
transaction with Guatavita Gold Corp. on the Tell property as announced
on March 20th 2014, and subsequent announcement of the financing and
restructuring of the Company as announced on March 26, 2014. This
report is to be completed by the end of June, 2014.

It is anticipated that the restructuring announced by the Company
will be completed within the next week, and the financing closing on a
post consolidation basis shortly thereafter.

Samples were forwarded to the Eco Tech Laboratory Stewart Group in
Whitehorse, Yukon for analysis. The Stewart Group Lab are an
independent certified commercial laboratory All of the soil and rock
samples were analyzed using inductively coupled plasma (ICP) together
with mass spectrometry (MS) finish. Gold was analyzed by a fire assay
preparation with an atomic absorption spectroscopy finish.

The President of Manson Creek Resources Ltd., Jean-Pierre Jutras,
P.Geol., is the Qualified Person responsible for the preparation of
this news release.

On Behalf of the Board of Directors,

Jean-Pierre Jutras, President/Director

The TSX Venture Exchange has neither approved nor disapproved of
the contents of this press release.

Except for the historical and present factual information
contained herein, the matters set forth in this news release, including
words such as "expects", "projects", "plans", "anticipates" and similar
expressions, are forward-looking information that represents management
of Manson Creek's internal projections, expectations or beliefs
concerning, among other things, future operating results and various
components thereof or the economic performance of Manson Creek. The
projections, estimates and beliefs contained in such forward-looking
statements necessarily involve known and unknown risks and
uncertainties, which may cause Manson Creek's actual performance and
financial results in future periods to differ materially from any
projections of future performance or results expressed or implied by
such forward-looking statements. These risks and uncertainties include,
among other things, those described in Manson Creek's filings with the
Canadian securities authorities. Accordingly, holders of Manson Creek
shares and potential investors are cautioned that events or
circumstances could cause results to differ materially from those
predicted. Manson Creek disclaims any responsibility to update these
forward-looking statements.

TSX Venture closing price for MCK-V
Date: 2014/04/08
Closing Price: 0.02

TEL:  1.403.233.0464  Manson Creek Resources Ltd.
Jean-Pierre Jutras
www.manson.ca
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1410400012TS11410401040-06202220140415