Source	Marketwire
Date	04/17/2014
Time	05:01:04 AM

Company	 KAMINAK GOLD CORPORATION
Title	Kaminak Reports Heap Leach Oxide Gold Recoveries of Greater Than 85% on 6 
Inch Crushed Material from Coffee





    CDNX Symbol: KAM











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Kaminak Gold Corporation

TSX VENTURE SYMBOL: KAM

April 17, 2014

Kaminak Reports Heap Leach Oxide Gold Recoveries of Greater Than 85% on 6 Inch 
Crushed Material from Coffee


VANCOUVER, BRITISH COLUMBIA--(Marketwired - April 17, 2014) - Kaminak Gold 
Corporation (TSX VENTURE:KAM) wishes to announce additional, encouraging, 
column leach metallurgical results from bulk, course crush, surface oxide 
samples collected in 2013 at the Coffee Gold Project, 130 km south of Dawson 
City, Yukon. Gold recoveries between 85-88% were returned within a 100-150 day 
leach period from 6" crush samples collected from surface trenches at both 
Supremo and Latte. Corresponding samples crushed to 1" returned gold recoveries 
of 92% over the same period. No agglomeration was required. The 2013 
metallurgical program is now complete and final results are being incorporated 
into a Preliminary Economic Analysis ("PEA"), which is underway and scheduled 
for completion in the second quarter of 2014.

Fred Lightner, Director Mine Development, stated:

"The metallurgical testing results continue to illustrate the amenability of 
the Coffee deposits to heap leaching. Once again, the excellent recovery at the 
1" crush size of over 90% has been demonstrated. The high recoveries 85% to 88% 
at the 6" crush size provide potential for treating lower grade ores by very 
coarse crushing, and even perhaps run-of-mine (ROM) leaching. These final 
results of our 2013 Metallurgical program will provide valuable input for the 
Preliminary Economic Assessment, currently in progress."

Highlights from this work include:

/T/

--  Column leach gold recoveries of 85% and 88% on 6" crushed material from
bulk surface Oxide samples from each of Supremo and Latte

--  Corresponding bulk surface oxide samples crushed to 1" for both Supremo
and Latte produced a recovery of 92%

--  Column leach test work for the 1" samples was conducted under simulated
cold climate conditions. The 6" crush columns were too large to be
contained in the refrigerator and were leached at ambient temperature.
Previous work has shown only a minor (-1%) gold recovery difference
between ambient and cold climate leaching.

--  Bottle roll gold recoveries were not substantially increased compared to
the column leach tests, which is consistent with previous results,
indicating that heap leaching is a more attractive option than agitation
leaching at this stage of the project.

/T/

Results of the recent column leach tests, conducted by Kappes, Cassiday and 
Associates ("KCA") are summarized below in Table 1.

Table 1 April 2014 Column Leach Test Results

/T/

----------------------------------------------------------------------------
Calculated
Sample                 Crush       Head Extracted     Gold  Days Consumption
Descrip-       Temp.  Size(i)     Grade     Grade Recovery    of        NaCN
tion       degrees C  inches     g/t Au    g/t Au        % Leach        kg/t
----------------------------------------------------------------------------
Supremo,
Oxide
(bulk)           22     6.0       4.31      3.68      85%   152        0.91
----------------------------------------------------------------------------
Supremo,
Oxide
(bulk)            4     1.0       3.44      3.17      92%   100        0.93
----------------------------------------------------------------------------
Latte,
Oxide
(bulk)           22     6.0       1.27      1.12      88%   100        0.56
----------------------------------------------------------------------------
Latte,
Oxide
(bulk)            4     1.0       1.12      1.03      92%   100        1.08
----------------------------------------------------------------------------
(i) Crushed to minus 175 mm (80% passing 6 inch) and minus 31.5 mm (80%
passing 1 inch)

/T/

Comparative Bottle Roll Test Work

Results from bottle roll test work undertaken on splits of the same composites 
utilized for column leaching are detailed below in Table 2. Again it was 
observed that at a fine grind, recoveries were not substantially increased over 
the column leach tests, indicating that heap leaching will most probably be 
economically more attractive than agitation leaching.

Table 2 Results of Bottle Roll Leach Tests

/T/

----------------------------------------------------------------------------
Target  Calculated
p80        Head   Extracted      Gold     Leach
Size       Grade       Grade  Recovery      Time
Description                   mm      g/t Au      g/t Au         %     hours
----------------------------------------------------------------------------
Supremo, Oxide (bulk)      0.075        4.08        3.59       96%        96
----------------------------------------------------------------------------
Latte, Oxide (bulk)        0.075        1.47        1.39       94%        96
----------------------------------------------------------------------------

/T/

Bulk Samples for the 2013 Metallurgical Test Program

Locations for collection of metallurgical samples were selected by examination 
of the resource block model for material that would be representative of 
average gold grade. The Supremo Oxide sample was collected from a surface 
trench across the T3 mineralized structure at 6974250mN. The Latte Oxide sample 
was collected from a surface trench across the Latte mineralized structure at 
583250mE. Trenches were excavated to bedrock and sampling was completed on 2m 
intervals. A total of 1500kg of material was collected from each trench and was 
sent to KCA where it was homogenized prior to splits being taken for the 
analytical work presented above.

Kaminak's disclosure of metallurgical data in this press release has been 
reviewed and approved by Fred Lightner, P.E., Director Mine Development of 
Kaminak Gold Corporation, who serves as a Qualified Person under the definition 
of National Instrument 43-101. Disclosure of additional technical or scientific 
information in this press release has been reviewed and approved by Tim Smith, 
P.Geo., Vice President Exploration of Kaminak Gold Corporation, who serves as a 
Qualified Person under the definition of National Instrument 43-101.

On behalf of the Board of Directors of Kaminak

Eira Thomas, President and CEO

Kaminak Gold Corporation

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

Caution Concerning Forward-Looking Statements

Certain disclosures in this release, including management's assessment of the 
future potential of the Coffee Project and future exploration programs, 
constitute forward-looking statements that are subject to numerous risks, 
uncertainties and other factors relating to Kaminak's operations as a mineral 
exploration company that may cause future results to differ materially from 
those expressed or implied in such forward-looking statements, including risks 
as to the completion of the plans and projects. Readers are cautioned not to 
place undue reliance on forward-looking statements. Except as required by law, 
Kaminak expressly disclaims any intention or obligation to update or revise any 
forward-looking statements, whether as a result of new information, future 
events, or otherwise.

The Company has not made a production decision and the Company's strategic plan 
to develop a stand-alone heap leach operation is subject to the results of its 
Feasibility Study. Further, if and when the Company makes any production 
decision, it will disclose the basis of such decision in accordance with the 
requirements of National Instrument 43-101 Standards of Disclosure for Mineral 
Projects ("NI 43-101").

Cautionary Note concerning estimates of Inferred Resources:

This news release uses the term "inferred resources". Inferred resources have a 
great amount of uncertainty as to their existence, and great uncertainty as to 
their economic and legal feasibility. It cannot be assumed that all or any part 
of an Inferred Mineral Resource will ever be upgraded to a higher category. 
Under Canadian rules, estimates of Inferred Resources may not form the basis of 
feasibility or other economic studies. Kaminak advises U.S. investors that 
while this term is recognized and required by Canadian regulations, the U.S. 
Securities and Exchange Commission do not recognize it. U.S. investors are 
cautioned not to assume that part or all of an inferred resource exists, or is 
economically or legally minable.

- 30 -

CONTACT INFO:

Kaminak Gold Corporation
Tony Reda
Vice President of Corporate Development
604.646.4534 or Toll Free: 1.888.331.2269
Fax: 604.646.4526
info@kaminak.com
www.kaminak.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

If you no longer want to receive announcements from us, please do not reply to 
this e-mail.
Instead simply click http://marketwire.com/mw/fmu.jsp?id=477707773