Source	MARKET NEWS
Date	04/17/2014
Time	05:38:50 AM

Company	 Kaminak Gold Corporation
Title	Heap Leach 
Oxide Gold Recoveries Of Greater Than





    CDNX Symbol: KAM











Press Release	





KAMINAK GOLD CORP ("KAM-V;KMKGF-0")
- Heap Leach Oxide Gold Recoveries Of Greater Than
- 85% On 6 Inch Crushed Material From Coffee

Kaminak Gold Corporation wishes to announce additional,
encouraging, column leach metallurgical results from bulk, course
crush, surface oxide samples collected in 2013 at the Coffee Gold
Project, 130 km south of Dawson City, Yukon. Gold recoveries between
85-88% were returned within a 100-150 day leach period from 6" crush
samples collected from surface trenches at both Supremo and Latte.
Corresponding samples crushed to 1" returned gold recoveries of 92%
over the same period. No agglomeration was required. The 2013
metallurgical program is now complete and final results are being
incorporated into a Preliminary Economic Analysis ("PEA"), which is
underway and scheduled for completion in the second quarter of 2014.

Fred Lightner, Director Mine Development, stated:

"The metallurgical testing results continue to illustrate the
amenability of the Coffee deposits to heap leaching. Once again, the
excellent recovery at the 1" crush size of over 90% has been
demonstrated. The high recoveries 85% to 88% at the 6" crush size
provide potential for treating lower grade ores by very coarse
crushing, and even perhaps run-of-mine (ROM) leaching. These final
results of our 2013 Metallurgical program will provide valuable input
for the Preliminary Economic Assessment, currently in progress."

Highlights from this work include:

//st

Column leach gold recoveries of 85% and 88% on 6" crushed
material from bulk surface Oxide samples from each of Supremo and Latte

//et

//st

Corresponding bulk surface oxide samples crushed to 1" for both
Supremo and Latte produced a recovery of 92%

//et

//st

Column leach test work for the 1" samples was conducted under
simulated cold climate conditions. The 6" crush columns were too large to
be contained in the refrigerator and were leached at ambient temperature.
Previous work has shown only a minor (-1%) gold recovery difference between
ambient and cold climate leaching.

//et

//st

Bottle roll gold recoveries were not substantially increased
compared to the column leach tests, which is consistent with previous
results, indicating that heap leaching is a more attractive option than
agitation leaching at this stage of the project.

//et

Results of the recent column leach tests, conducted by Kappes,
Cassiday and Associates ("KCA") are summarized below in Table 1.

//st
Table 1 April 2014 Column Leach Test Results

----------------------------------------------------------------------------
Calculated
Sample                 Crush       Head Extracted     Gold  Days Consumption
Descrip-       Temp.  Size(i)     Grade     Grade Recovery    of        NaCN
tion       degrees C  inches     g/t Au    g/t Au        % Leach        kg/t
----------------------------------------------------------------------------
Supremo,
Oxide
(bulk)           22     6.0       4.31      3.68      85%   152       0.91
----------------------------------------------------------------------------
Supremo,
Oxide
(bulk)            4     1.0       3.44      3.17      92%   100       0.93
----------------------------------------------------------------------------
Latte,
Oxide
(bulk)           22     6.0       1.27      1.12      88%   100       0.56
----------------------------------------------------------------------------
Latte,
Oxide
(bulk)            4     1.0       1.12      1.03      92%   100       1.08
----------------------------------------------------------------------------
(i) Crushed to minus 175 mm (80% passing 6 inch) and minus 31.5 mm (80%
passing 1 inch)
//et

Comparative Bottle Roll Test Work

Results from bottle roll test work undertaken on splits of the
same composites utilized for column leaching are detailed below in
Table 2. Again it was observed that at a fine grind, recoveries were
not substantially increased over the column leach tests, indicating
that heap leaching will most probably be economically more attractive
than agitation leaching.

//st
Table 2 Results of Bottle Roll Leach Tests

----------------------------------------------------------------------------
Target  Calculated
p80        Head   Extracted      Gold    Leach
Size       Grade       Grade  Recovery     Time
Description                   mm      g/t Au      g/t Au         %    hours
----------------------------------------------------------------------------
Supremo, Oxide (bulk)      0.075        4.08        3.59       96%       96
----------------------------------------------------------------------------
Latte, Oxide (bulk)        0.075        1.47        1.39       94%       96
//et



Bulk Samples for the 2013 Metallurgical Test Program

Locations for collection of metallurgical samples were selected by
examination of the resource block model for material that would be
representative of average gold grade. The Supremo Oxide sample was
collected from a surface trench across the T3 mineralized structure at
6974250mN. The Latte Oxide sample was collected from a surface trench
across the Latte mineralized structure at 583250mE. Trenches were
excavated to bedrock and sampling was completed on 2m intervals. A
total of 1500kg of material was collected from each trench and was sent
to KCA where it was homogenized prior to splits being taken for the
analytical work presented above.

Kaminak's disclosure of metallurgical data in this press release
has been reviewed and approved by Fred Lightner, P.E., Director Mine
Development of Kaminak Gold Corporation, who serves as a Qualified
Person under the definition of National Instrument 43-101. Disclosure
of additional technical or scientific information in this press release
has been reviewed and approved by Tim Smith, P.Geo., Vice President
Exploration of Kaminak Gold Corporation, who serves as a Qualified
Person under the definition of National Instrument 43-101.

On behalf of the Board of Directors of Kaminak

Eira Thomas, President and CEO

Kaminak Gold Corporation

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

Caution Concerning Forward-Looking Statements

Certain disclosures in this release, including management's
assessment of the future potential of the Coffee Project and future
exploration programs, constitute forward-looking statements that are
subject to numerous risks, uncertainties and other factors relating to
Kaminak's operations as a mineral exploration company that may cause
future results to differ materially from those expressed or implied in
such forward-looking statements, including risks as to the completion
of the plans and projects. Readers are cautioned not to place undue
reliance on forward-looking statements. Except as required by law,
Kaminak expressly disclaims any intention or obligation to update or
revise any forward-looking statements, whether as a result of new
information, future events, or otherwise.

The Company has not made a production decision and the Company's
strategic plan to develop a stand-alone heap leach operation is subject
to the results of its Feasibility Study. Further, if and when the
Company makes any production decision, it will disclose the basis of
such decision in accordance with the requirements of National
Instrument 43-101 Standards of Disclosure for Mineral Projects ("NI
43-101").

Cautionary Note concerning estimates of Inferred Resources:

This news release uses the term "inferred resources". Inferred
resources have a great amount of uncertainty as to their existence, and
great uncertainty as to their economic and legal feasibility. It cannot
be assumed that all or any part of an Inferred Mineral Resource will
ever be upgraded to a higher category. Under Canadian rules, estimates
of Inferred Resources may not form the basis of feasibility or other
economic studies. Kaminak advises U.S. investors that while this term
is recognized and required by Canadian regulations, the U.S. Securities
and Exchange Commission do not recognize it. U.S. investors are
cautioned not to assume that part or all of an inferred resource
exists, or is economically or legally minable.


TEL:  604.646.4534   Kaminak Gold Corporation
TSX Venture closing price for KAM-V
Date: 2014/04/16
Closing Price: 0.76

TEL:  1.888.331.2269 Tony Reda, Vice President of Corporate
FAX:  604.646.4526   Development
info@kaminak.com
www.kaminak.com
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1410600010TS11410600851-05370120140417