Source	Marketwire
Date	04/11/2014
Time	05:00:38 AM

Company	 TERRAX MINERALS INC.
Title	TerraX Completes Drilling at Homer Lake and Moves Drill #1 to Barney 
Shear, Yellowknife City Gold Project; Drilling Continues With Drill #2 at 
Crestaurum Gold Deposit





    CDNX Symbol: TXR











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: TerraX Minerals Inc.

TSX VENTURE SYMBOL: TXR
FRANKFURT SYMBOL: TX0
PINKSHEETS SYMBOL: TRXXF

April 11, 2014

TerraX Completes Drilling at Homer Lake and Moves Drill #1 to Barney Shear, 
Yellowknife City Gold Project; Drilling Continues With Drill #2 at Crestaurum 
Gold Deposit


YELLOWKNIFE, NORTHWEST TERRITORIES--(Marketwired - April 11, 2014) - TerraX 
Minerals Inc. (TSX VENTURE:TXR)(FRANKFURT:TX0)(PINKSHEETS:TRXXF) has completed 
its planned four hole (1,000 m) drill program at the Homer Lake base 
metal/precious metal target and moved Drill #1 to the Barney Shear (28.32 m @ 
2.97 g/t Au, inclusive of 4.00 m @ 12.59 g/t Au in news release August 14th, 
2013) which is the extension of the Con Mine/Giant Mine shear system that has 
hosted more than 13 Moz of gold production from the two historic mines. The 
Barney Shear Zone is one of TerraX's primary gold targets on the Northbelt 
property of the Yellowknife City Gold Project ("YCGP") in the Northwest 
Territories. Drilling is still underway with a second drill at the nearby 
Crestaurum gold deposit, as announced on April 7, 2014.

The Barney Shear has been delineated over a strike length of 4.5 km by TerraX 
and previous workers and has only been drill tested by prior operators over a 
600 m strike length. Surface mapping in June 2013 indicates that the Barney 
Shear Zone consists of multiple mineralized shears over a greater than 200 m 
width. The 2014 Barney Shear drilling will consist of up to 8 holes following 
the strike extension of the shear up to 300 m north of the mineralization 
defined in drilling carried out by Nebex Resources Ltd. in 1995 and 1996. In 
addition, TerraX will be re-entering the collars of 4 drill holes from the 
1995-96 campaigns. These holes will be surveyed down hole to accurately 
determine the location of previously intersected zones of mineralization, and 
then multiple wedges will be turned off the original holes to generate 
additional mineralized intersections. This work is possible as the previous 
exploration drilling had left the original drill hole collars cased and capped 
to preserve them for future work on this important mineralized zone.

The first hole re-sampled by TerraX, NB95-16, was drilled on the Barney Shear 
by Nebex in 1995. TerraX's assay results include an interval of 20.86 m @ 3.79 
g/t Au, inclusive of 4.00 m @ 12.59 g/t Au (news release of Aug 14, 2013). 
Holes NB-96-02 and NB96-04, drilled in 1996, were also re-logged and re-sampled 
by TerraX with assay results that included 8.16 m @ 5.06 g/t Au and 6.32 g/t Ag 
(NB96-02) and 27.00 m @ 1.9 g/t Au and 6.94 g/t Ag (NB96-04) (news release of 
Nov 14, 2014 ). The assay results from NB96-02 and NB96-04 are very encouraging 
as they confirm the strike continuation and substantial areal extent of the 
Barney Shear Zone. A map indicating the location of this prior drilling is 
available on our web site at www.terraxminerals.com.

Drilling at Homer Lake commenced on March 25, 2014 and targeted a buried 
conductor identified by airborne surveys conducted by TerraX in 2013 that had 
never been drill-tested This target area was within 500 m of a previously 
established ice road which made winter access easier and allowed this drill 
program to be completed quickly with less environmental impact than would have 
been the case with overland access in summer conditions. Logging and sampling 
of drill core from Homer Lake is currently underway with assay results pending.

Homer Lake is not a traditional gold target as would be expected in a major 
gold belt like the Yellowknife Gold Camp. It was originally discovered from 
surface prospecting in the 1930s and six mineralized structures were delineated 
during reconnaissance prospecting by TerraX in the Homer Lake area in 2013. One 
structure has been traced by TerraX for 1,200 m and has chip sample results of 
7 m @ 0.50 g/t Au, 90.2 g/t Ag, 4.25% Pb and 0.89% Zn. A parallel structure 
sampled by TerraX graded 5 m @ 1.54 g/t Au, 95.5 g/t Ag, 3.13% Pb and 1.59% Zn. 
A grab sample by TerraX from a third structure graded 0.60 g/t Au, 529 g/t Ag, 
greater than 20% Pb, and 9.44% Zn.

The technical information contained in this news release has been approved by 
Joseph Campbell, the President of TerraX, who is a Qualified Person as defined 
in "National Instrument 43-101, Standards of Disclosure for Mineral Projects."

About the Yellowknife City Gold Project

The Yellowknife City Gold Project encompasses approximately 8,400 hectares of 
contiguous land immediately north of the City of Yellowknife in the Northwest 
Territories and includes TerraX's wholly-owned Northbelt property acquired in 
February 2013.

The Northbelt gold property encompasses 3,562 hectares on the prolific 
Yellowknife belt, all within 15 km of the city of Yellowknife, and covers 13 km 
of strike on the northern extension of the geology that contained the Giant 
(7.8 Moz) and Con (5.5 Moz) gold mines. The Northbelt property is host to 
multiple shears that are the recognized hosts for gold deposits in the 
Yellowknife camp and it contains innumerable gold showings and historic high 
grade drill results.

TerraX has carried out a strategy of acquiring prospective ground adjacent to 
Northbelt and in October 2013 entered into an option agreement whereby it can 
acquire a 100% interest in the Walsh Lake gold property, which is contiguous 
with and immediately east of Northbelt. The Walsh Lake property consists of 
seven leases and five claims totaling 6,659 acres (2,695 hectares). TerraX has 
also staked and acquired ground to the west of Northbelt to cover prospective 
geology that is on strike from Northbelt structures.

For more information on the Yellowknife City Gold Project, please visit our web 
site at www.terraxminerals.com.

On behalf of the Board of Directors

Joseph Campbell, President

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

This news release contains forward-looking information, which involves known 
and unknown risks, uncertainties and other factors that may cause actual events 
to differ materially from current expectation. Important factors - including 
the availability of funds, the results of financing efforts, the completion of 
due diligence and the results of exploration activities - that could cause 
actual results to differ materially from the Company's expectations are 
disclosed in the Company's documents filed from time to time on SEDAR (see 
www.sedar.com). Readers are cautioned not to place undue reliance on these 
forward-looking statements, which speak only as of the date of this press 
release. The company disclaims any intention or obligation, except to the 
extent required by law, to update or revise any forward-looking statements, 
whether as a result of new information, future events or otherwise.

- 30 -

CONTACT INFO:

Paradox Public Relations
514-341-0408 or Toll Free: 1-866-460-0408
info@paradox-pr.ca

or

Vanguard Shareholder Solutions
604-608-0824 or Toll Free: 855-508-0824
ir@vanguardsolutions.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

If you no longer want to receive announcements from us, please do not reply to 
this e-mail.
Instead simply click http://marketwire.com/mw/fmu.jsp?id=476953497