Source	MARKET NEWS
Date	04/07/2014
Time	06:02:05 AM

Company	 Scorpio Gold Corporation
Title	Final Results 
From 2013 Expansion Drilling At Th





    CDNX Symbol: SGN











Press Release	





SCORPIO GOLD CORP ("SGN-V;SRCRF-0")
- Final Results From 2013 Expansion Drilling At The Oromonte And
- Drinkwater Highwall, Mineral Ridge Project, Nevada

Scorpio Gold Corporation ("Scorpio Gold" or the "Company") reports
final results from its 2013 drilling program at the 70% owned Mineral
Ridge project, located in Nevada. The Oromonte satellite deposit lies
west of the currently producing Drinkwater and Mary pits and the
Drinkwater Highwall zone lies at the northwest end of the Drinkwater
pit.

Previous drilling on the Drinkwater Highwall zone had confirmed
that significant mineralization was left behind in the wall at the
northwest end of the Drinkwater pit (as reported in the Company's
October 30, 2012 and November 26, 2012 news releases). Results from the
2012 and 2013 drilling will be modelled and incorporated into the
Drinkwater mine plan for potential extraction. Additional drilling on
the Drinkwater Highwall is planned in 2014.

Drilling on the Oromonte deposit in 2013 followed up on high-grade
mineralization intersected at depth in 2011-2012 drilling. Drill
results from the first phase of the 2013 drill program at Oromonte were
reported in the Company's September 23, 2013 news release. The
indicated zone of mineralization trends northerly and lies along the
edge of a geophysical magnetic high. It has been intersected at 85 to
115 metres vertical depth and, although not accessible by open pit
mining, may be amenable to underground extraction should further
results support underground development. Historical underground
workings are known to lie approximately 180 meters to the east. The
significance of these drill results in context with their structural
and geophysical setting will be evaluated for follow-up drilling in
2014.

Map links:

Oromonte drill plan:
www.scorpiogold.com/i/maps/mr/Oromonte_DHplan.jpg

Drinkwater Highwall drill plan:
www.scorpiogold.com/i/maps/mr/DrinkwaterHW_DHplan.jpg

Table 1. Significant Drill Results from the Oromonte and
Drinkwater Highwall

//st
Hole      Azm   Dip From   To Width   From     To Width  Gold  Gold
No.     (deg) (deg) (ft) (ft)  (ft)    (m)    (m)   (m) (OPT) (g/t)
Oromonte Deposit
MR13750     0   -90  270  275     5  82.30  83.82  1.52  0.03  0.99
395  400     5 120.40 121.92  1.52  0.02  0.69
MR13751     0   -90   10   15     5   3.05   4.57  1.52  0.01  0.48
200  205     5  60.96  62.48  1.52  0.03  0.93
240  245     5  73.15  74.68  1.52  0.02  0.51
265  320    55  80.77  97.54 16.76  0.03  0.89
MR13752     0   -90  330  335     5 100.58 102.11  1.52  0.04  1.41
395  415    20 120.40 126.49  6.10  0.14  4.82
Northwest Highwall Zone
MR13715   225   -70    5   10     5   1.52   3.05  1.52 0.013  0.45
495  505    10 150.88 153.92  3.05 0.026  0.87
525  530     5 160.02 161.54  1.52 0.044  1.51
MR13716   225   -75  395  410    15 120.40 124.97  4.57 0.051  1.73
500  505     5 152.40 153.92  1.52 0.027  0.93
MR13717   225   -85    0   15    15   0.00   4.57  4.57 0.010  0.34
320  325     5  97.54  99.06  1.52 0.121  4.15
460  470    10 140.21 143.26  3.05 0.032  1.10
600  605     5 182.88 184.40  1.52 0.037  1.27
MR13718   225   -70                          No Significant Results
MR13719   225   -75    0   10    10   0.00   3.05  3.05 0.041  1.39
500  530    30 152.40 161.54  9.14 0.055  1.87
685  690     5 208.79 210.31  1.52 0.013  0.45
MR13745   225   -70    5   10     5   1.52   3.05  1.52 0.013  0.45
515  520     5 156.97 158.50  1.52 0.061  2.09
540  550    10 164.59 167.64  3.05 0.020  0.69
MR13746   225   -70                          No Significant Results
MR13747     0   -90    5   10     5   1.52   3.05  1.52 0.016  0.55
MR13748   225   -70    0   10    10   0.00   3.05  3.05 0.020  0.67
MR13749   225   -60    0   10    10   0.00   3.05  3.05 0.048  1.63

//et

All holes presented in Table 1 were completed by reverse
circulation (RC) drilling. True width is estimated at 90-100% of
downhole width. Analytical results were performed by American Assay
Laboratory Inc. in Sparks, Nevada, an ISO/IEC 17025:2005 accredited
facility. External check assays to verify lab accuracy are routinely
completed by ALS Chemex, an ISO 9001:2000 certified and ISO/IEC
17025:2005 accredited facility. Further details are presented in the
Company's quality assurance and quality control program for the Mineral
Ridge project at: www.scorpiogold.com/i/pdf/reports/QAQC-MR.pdf.
About Scorpio Gold

Scorpio Gold holds a 70% interest in the Mineral Ridge gold mining
operation located in Esmeralda County, Nevada with joint venture
partner Waterton Global Value L.P. (30%), and is currently entitled to
receive 80% of cash flow generated. Mineral Ridge is currently in
production as a conventional open pit mining and heap leach operation.
The Mineral Ridge property is host to multiple gold-bearing structures,
veins and lenses at exploration, development and production stages.
Scorpio Gold also holds a 100% interest in the advanced
exploration-stage Goldwedge property and processing facility in
Manhattan, Nevada. The Company is assessing its exploration plans for
the Goldwedge property as well as the potential for toll milling at the
Goldwedge plant, which is currently permitted for 400 tons per day.

Scorpio Gold's CEO, Peter J. Hawley, PGeo, is a Qualified Person
as defined by National Instrument 43-101 and has reviewed and approved
the content of this release.

ON BEHALF OF THE BOARD SCORPIO GOLD CORPORATION

Peter J. Hawley, CEO

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

The Company relies on litigation protection for forward-looking
statements. This news release contains forward-looking statements that
are based on the Company's current expectations and estimates.
Forward-looking statements are frequently characterized by words such
as "plan", "expect", "project", "intend", "believe", "anticipate",
"estimate", "suggest", "indicate" and other similar words or statements
that certain events or conditions "may" or "will" occur, and include,
without limitation, statements regarding the Company's plans with
respect to the exploration, development and exploitation of its Mineral
Ridge project. Such forward-looking statements involve known and
unknown risks, uncertainties and other factors that could cause actual
events or results to differ materially from estimated or anticipated
events or results implied or expressed in such forward-looking
statements, including risks involved in exploration programs and those
risk factors outlined in the Company's Management Discussion and
Analysis as filed on SEDAR. Any forward-looking statement speaks only
as of the date on which it is made and, except as may be required by
applicable securities laws, the Company disclaims any intent or
obligation to update any forward-looking statement, whether as a result
of new information, future events or results or otherwise.
Forward-looking statements are not guarantees of future performance and
accordingly undue reliance should not be put on such statements due to
the inherent uncertainty thereof.


TEL:  (819) 825-7618 Steve Roebuck, President
EMAIL:  sroebuck@scorpiogold.com
TSX Venture closing price for SGN-V
Date: 2014/04/04
Closing Price: 0.28

TEL:  (858) 456-7300 Investor Relations: Jim Macdonald, Torrey
Hills Capital
EMAIL:  jm@sdthc.com
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1409600015TS11409600775-06003420140407