Source	Marketwire
Date	04/07/2014
Time	05:00:38 AM

Company	 SOURCE EXPLORATION CORP.
Title	Source Intersects 2.70 G/T Gold Equivalent Over 97.2 Metres and, 
Separately, 1.60 G/T Gold Equivalent Over 114.8 Metres at Las Minas





    CDNX Symbol: SOP











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Source Exploration Corp.

TSX VENTURE SYMBOL: SOP

April 7, 2014

Source Intersects 2.70 G/T Gold Equivalent Over 97.2 Metres and, Separately, 
1.60 G/T Gold Equivalent Over 114.8 Metres at Las Minas


THUNDER BAY, ONTARIO--(Marketwired - April 7, 2014) - SOURCE EXPLORATION CORP. 
(the "Company" or "Source") (TSX VENTURE:SOP) is pleased to announce that step 
- out drilling at the Santa Cruz target of its Las Minas project (the "Las 
Minas Project") has intersected a wide mineralized zone extending from the 
surface to 97.2 metres (m) and grading 2.70 g/t Gold Equivalent(1) (Au Eq) in 
diamond drill hole LM-14-SC-03. A high-grade interval assaying 10.06 g/t Au Eq 
over 16.0 metres is contained within the wider intersection.

Hole LM-14-SC-01, collared approximately 32 metres to the southeast of 
LM-14-SC-03, intersected 1.60 g/t Au Eq over a core length of 114.8 metres, 
commencing at the collar. The intersection includes a higher-grade zone of 3.89 
g/t Au Eq over 19.8 metres.

The step-out drilling at Santa Cruz extended the high-grade mineralization cut 
in hole LM-11-SC-45, which returned 19.56 g/t Au Eq over 10.0 metres, by a 
further 75 metres to the northwest.

Delineation drilling at the El Dorado target of the Las Minas Project, which is 
located approximately 550 metres to the north and on strike, cut 3.38 g/t Au EQ 
over 6.0 metres in hole LM-14-ED-12. The higher-grade intersection is contained 
within a wider 20.4 metre interval grading 1.62 g/t Au Eq. Infill hole 
LM-14-ED-08, collared approximately 125 metres southwest of hole LM-14-ED-12, 
cut 28.3 m of mineralized exoskarn and endoskarn grading 1.64 g/t Au Eq.

The drilling has been successful in expanding the high-grade mineralized zone 
at Santa Cruz. In addition, drilling at the El Dorado target continued to 
support earlier results to delineate the down-dip projection of the mineralized 
skarn zone. The El Dorado corridor mineralized skarn zone has been defined over 
a strike length of approximately 840 metres and intersected at about 400 metres 
down-dip, with drill intercepts varying from 20 to 245 metres in thickness - 
see press release dated January 26, 2012.

The Phase 1 drill program totaled 2,737 metres of drilling and is part of a 
planned multiple-phase program to develop an initial mineral resource estimate 
for the Santa Cruz and Eldorado zones. Drill layouts are being prepared for the 
Phase 2 drill program, and the diamond drill remains on site for the 
commencement of drilling.

Santa Cruz Drilling Results:

Step out drilling at Santa Cruz cut wide mineralized zones starting from 
surface and grading up to 2.70 g/t Au Eq over 97.2 metres. The wide zones 
contained high-grade intersections peaking at 10.06 g/t Au Eq over 16.0 metres, 
within a zone of 44.5 metres assaying 5.03 g/t Au Eq.

Highlights include:

/T/

----------------------------------------------------------------------------
From     To Interval  Gold  Silver  Copper Au Eq(1)
Hole No.       (M)    (M)      (M)   g/t     g/t       %       g/t  Comments
----------------------------------------------------------------------------
From
LM-14-SC-01    0.0  114.8    114.8  0.77    3.25    0.46      1.60   Surface
----------------------------------------------------------------------------
including     89.0  108.8     19.8  1.96    8.98    1.05      3.89
----------------------------------------------------------------------------
within        71.7  112.8     43.1  1.19    4.65    0.59      2.27
----------------------------------------------------------------------------

----------------------------------------------------------------------------
From
LM-14-SC-02    0.0   32.0     32.0  1.08    6.53    0.57      2.14   Surface
----------------------------------------------------------------------------

----------------------------------------------------------------------------
From
LM-14-SC-03    0.0   97.2     97.2  1.19    9.42    0.79      2.70   Surface
----------------------------------------------------------------------------
Including     75.2   91.2     16.0  4.39   37.82    2.96     10.06
----------------------------------------------------------------------------
within        52.7   97.2     44.5  2.30   19.07    1.57      5.03
----------------------------------------------------------------------------

/T/

The high-grade gold, silver and copper mineralization at the Santa Cruz target 
is comprised of significant chalcopyrite and bornite, with high magnetite 
content ranging from 40 to 90% by volume. Pictures of the core can be viewed at 
www.sourceexploration.com - see Projects - Photo Gallery - Diamond Drill Core 
Santa Cruz. The zones of massive high-grade magnetite sulphide mineralization 
are located within a large magnetic anomaly outlined by a recent ground based 
high-resolution magnetic survey and measuring approximately 1,300 metres by 700 
metres - see press release dated February 14, 2013.

Brian Robertson, President & CEO, commented: "Drilling continues to expand the 
high-grade mineralized zone at Santa Cruz as well as further delineate the El 
Dorado target. Hole LM-14-SC-03 is an extraordinary drill hole and extends the 
high-grade mineralization outlined in hole LM-11-SC-45 a further 50 metres to 
the north. The spatial relationship between the high-grade mineralized zones 
outlined by the drilling and the strong magnetic anomaly is significant. There 
are several untested magnetic anomalies on the property supported by strong 
surface and underground sampling results that appear to have considerable 
potential for additional high-grade discoveries."

El Dorado Drilling Results:

Infill drilling at the El Dorado target confirmed the results outlined by 
earlier exploration drilling to delineate the down-dip extension of the 
mineralized skarn zone. A total of 12 holes were drilled at El Dorado, 
completing the planned Phase 1 program. Significant assay results are reported 
below.

Highlights include:

/T/

----------------------------------------------------------------------------
From     To  Interval  Gold  Silver  Copper Au Eq(1)
Hole No.       (M)    (M)       (M)   g/t     g/t       %       g/t Comments
----------------------------------------------------------------------------
LM-14-ED-08   54.6   82.9      28.3  0.46    2.66    0.66      1.64
----------------------------------------------------------------------------
including     54.6   64.7      10.1  0.68    4.40    1.13      2.68
----------------------------------------------------------------------------

----------------------------------------------------------------------------
LM-14-ED-12   52.2   73.7      20.4  0.70    3.46    0.51      1.62
----------------------------------------------------------------------------
From     To  Interval  Gold  Silver  Copper Au Eq(1)
Hole No.       (M)    (M)       (M)   g/t     g/t       %       g/t Comments
----------------------------------------------------------------------------
including     54.8   60.8       6.0  1.37    5.10    1.13      3.38
----------------------------------------------------------------------------
within        52.2   76.4      11.1  1.14    5.07    0.89      2.74
----------------------------------------------------------------------------

----------------------------------------------------------------------------
LM-14-ED-15   49.7   80.9      31.2  0.58    2.54    0.06      0.73
----------------------------------------------------------------------------
including     60.7   72.0      11.3  1.42    3.50    0.14      1.72
----------------------------------------------------------------------------

/T/

Table 1 provides a summary of highlight results from the Phase 1 drilling 
program. Drill hole sections can be found at the website - see Projects - Las 
Minas- Drill Sections.

Table 1 Selected Las Minas Phase 1 Drill Results

/T/

----------------------------------------------------------------------------
From       To   Interval     Gold   Silver   Copper    Au Eq
Hole No.         (M)      (M)        (M)      g/t      g/t        %      g/t
----------------------------------------------------------------------------
LM-14-SC-01      0.0    114.8      114.8     0.77     3.25     0.46     1.60
----------------------------------------------------------------------------
including       38.0     52.0       14.0     1.37     4.16     1.25     3.57
----------------------------------------------------------------------------
within           0.0     52.0       52.0     0.69     3.31     0.52     1.64
----------------------------------------------------------------------------
including       89.0    108.8       19.8     1.96     8.98     1.05     3.89
----------------------------------------------------------------------------
within          71.7    112.8       41.1     1.19     4.65     0.59     2.27
----------------------------------------------------------------------------

----------------------------------------------------------------------------
LM-14-SC-02      0.0     32.0       32.0     1.08     6.53     0.57     2.14
----------------------------------------------------------------------------
including        2.0     14.0       12.0     1.31     7.07     0.54     2.41
----------------------------------------------------------------------------

----------------------------------------------------------------------------
LM-14-SC-03      0.0     97.2       97.2     1.19     9.42     0.79     2.70
----------------------------------------------------------------------------
including       75.2     91.2       16.0     4.39    37.82     2.96    10.06
----------------------------------------------------------------------------
within          52.7     97.2       44.5     2.30    19.07     1.57     5.30
----------------------------------------------------------------------------

----------------------------------------------------------------------------
LM-14-SC-04                     Assays pending
----------------------------------------------------------------------------

----------------------------------------------------------------------------
LM-14-SC-05                     Assays Pending
----------------------------------------------------------------------------

----------------------------------------------------------------------------
LM-14-SC-06                     Assays Pending
----------------------------------------------------------------------------

----------------------------------------------------------------------------

----------------------------------------------------------------------------
LM-14-ED-08     54.6     82.9       28.3     0.46     2.66     0.66     1.64
----------------------------------------------------------------------------
Including       54.6     64.7       10.1     0.68     4.40     1.13     2.68
----------------------------------------------------------------------------

----------------------------------------------------------------------------
LM-14-ED-09     18.9     48.2       29.3     0.29     1.54     0.26     0.76
----------------------------------------------------------------------------
including       18.9     26.4        7.5     0.99     4.62     0.97     2.72
----------------------------------------------------------------------------

----------------------------------------------------------------------------
LM-14-ED-10     24.3     34.6       10.3     0.32     2.81     0.19     0.69
----------------------------------------------------------------------------
Including       29.2     32.6        3.4     0.59     4.56     0.30     1.18
----------------------------------------------------------------------------

----------------------------------------------------------------------------

----------------------------------------------------------------------------
LM-14-ED-12     52.2     73.7       20.4     0.70     3.46     0.51     1.62
----------------------------------------------------------------------------
including       54.8     60.8        6.0     1.37     5.10     1.13     3.38
----------------------------------------------------------------------------
within          52.2     76.4       11.1     1.14     5.07     0.89     2.74
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Hole No.       From       To  Interval     Gold   Silver   Copper    Au Eq
(M)      (M)       (M)      g/t      g/t        %      g/t
----------------------------------------------------------------------------
LM-14-ED-14     75.8     85.0       9.2     0.86     3.36     0.46     1.69
----------------------------------------------------------------------------

----------------------------------------------------------------------------

----------------------------------------------------------------------------
LM-14-ED-15     49.7     80.9      31.2     0.58     2.54     0.06     0.73
----------------------------------------------------------------------------
including      60.7     72.0      11.3     1.42     3.50     0.14     1.72
----------------------------------------------------------------------------
----------------------------------------------------------------------------

----------------------------------------------------------------------------
LM-14-ED-
16(i)        88.6     93.0       4.4     0.48     4.25     0.63     1.62
----------------------------------------------------------------------------

----------------------------------------------------------------------------
LM-14-ED-17     84.7     90.3       5.6     0.41     4.68     0.45     1.26
----------------------------------------------------------------------------

----------------------------------------------------------------------------
LM-14-ED-18     28.3     33.9       5.6     0.61     1.23     0.49     1.46
----------------------------------------------------------------------------
(1) Gold equivalent (Au Eq) calculations use metal prices of US$1200/oz. for
gold, US$19.00/oz. for silver and US$3.00/lb. for copper. No adjustments
have been made for potential relative differences in metal recoveries.

Au Eq g/t equals Au g/t + (Ag g/t x 0.016) + (Cu% x1.71).

(i)Intersected old adit.

/T/

All intervals for the El Dorado target are reported as down-hole lengths, and 
based on down-hole structural data, the intervals may be approximately 95% of 
true thickness. Additional information is required to determine true widths for 
the Santa Cruz drilling. Assays are uncut, length weighted average values.

About Las Minas

The Las Minas Project hosts near-surface gold - silver and copper skarn 
mineralization and high-grade gold - silver epithermal vein deposits. The 
project is comprised of six mineral concessions covering approximately 1,616 
hectares (3,995 acres), with several small scale, past-producing mines and 
numerous untested targets.

The district is host to one of the largest under explored gold - silver copper 
skarn systems known in Mexico, and has a production history that extends back 
to the Aztec era. The Las Minas granodiorite intrusive measures approximately 
10 kilometres in diameter and underlies the Las Minas concessions. The 
mineralization controls and association with magnetite appear to be similar to 
the Guerrero Gold belt, which is the site of the Los Filos and Morelos gold 
deposits.

Las Minas is an early-stage exploration project and does not contain any 
mineral resource estimates as defined by National Instrument 43-101 Standards 
of Disclosure for Mineral Projects ("NI 43-101"). The potential quantities and 
grades disclosed herein are conceptual in nature and there has been 
insufficient exploration to define a mineral resource for the targets discussed 
herein. It is uncertain if further exploration will result in these targets 
being delineated as a mineral resource.

Quality Assurance/Quality Control

The technical information in this news release has been reviewed and approved 
by Sonny Bernales, P. Geo., a registered Professional Geoscientist in the 
Province of British Columbia and a qualified person as defined by NI 43-101. 
Mr. Bernales is responsible for logistics and supervision of all exploration 
activity conducted by Source on the property.

The Company has implemented and adheres to a strict Quality Assurance/Quality 
Control program which includes inserting mineralized standards and blanks into 
the sample stream, about 1 for every 10 samples. The standards and blanks were 
obtained from CDN Resource Laboratories Ltd. of Langley, BC, Canada. Each 
sample bag is properly sealed and kept in a secured, restricted storage place 
prior to shipping to the lab. Samples are shipped directly by Source or 
picked-up by the lab vehicle with chain of custody/sample submittal signed and 
dated. The Company sends it samples to SGS Mineral Services (ISO/IEC 17025) at 
Durango, Mexico, an accredited and independent laboratory.

About Source Exploration

Source Exploration is a Canadian based mineral exploration company committed to 
building long-term value through ongoing discoveries and strategic acquisitions 
of prospective precious metals deposits in Mexico. Source is exploring the Las 
Minas Project, which is located in the core of the Las Minas district in the 
Veracruz State, Mexico. The district is host to one of the largest under 
explored skarn systems known in Mexico and has a strong production history that 
dates back to the Aztec era.

CAUTIONARY STATEMENT REGARDING FORWARD-LOOKING INFORMATION: This news release 
includes certain information that may constitute "forward-looking information" 
under applicable Canadian securities legislation. Forward-looking information 
includes, but is not limited to, statements about the magnitude or quality of 
mineral deposits, anticipated advancement of mineral properties or programs, 
future operations, results of exploration, prospects, commodity and precious 
metals prices, future work programs, anticipated financial and operational 
results, capital expenditures and objectives and the completion and timing of 
mineral resource estimates. Forward-looking information is necessarily based 
upon a number of estimates and assumptions that, while considered reasonable, 
are subject to known and unknown risks, uncertainties, and other factors, which 
may cause the actual results and future events to differ materially from those 
expressed or implied by such forward-looking information, including the risks 
identified in the Company's disclosure documents available at www.sedar.com. 
There can be no assurance that such information will prove to be accurate, as 
actual results and future events could differ materially from those anticipated 
in such information. Accordingly, readers should not place undue reliance on 
forward-looking information. All forward-looking information contained in this 
press release is given as of the date hereof and is based on the opinions and 
estimates of management and information available to management as at the date 
hereof. The Company disclaims any intention or obligation to update or revise 
any forward-looking information, whether as a result of new information, future 
events or otherwise, except as required by law.

- 30 -

CONTACT INFO:

Source Exploration Corp.
David Baker
Executive Chairman
604-817-4211
604-970-8052

or

Source Exploration Corp.
Brian Robertson
President & CEO
807-474-4271 or 807-251-1816
Fax: 807-474-4272
info@sourceexploration.com
www.sourceexploration.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

If you no longer want to receive announcements from us, please do not reply to 
this e-mail.
Instead simply click http://marketwire.com/mw/fmu.jsp?id=475980857