Source	Marketwire
Date	04/07/2014
Time	03:00:46 AM

Company	 TIGRAY RESOURCES INC.
Title	Tigray Intersects 28.2 Metres at 8.50 Grams per Tonne Gold at Mato Bula, 
Adyabo Project, Northern Ethiopia





    CDNX Symbol: TIG











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Tigray Resources Inc.

TSX VENTURE SYMBOL: TIG

April 7, 2014

Tigray Intersects 28.2 Metres at 8.50 Grams per Tonne Gold at Mato Bula, Adyabo 
Project, Northern Ethiopia


VANCOUVER, BRITISH COLUMBIA--(Marketwired - April 7, 2014) - Tigray Resources 
Inc. (TSX VENTURE:TIG) ("Tigray" or the "Company") is pleased to announce 
diamond drill results from Phase 2 drilling at the Mato Bula discovery at 
Adyabo (refer to Tigray's news release dated July 16, 2013 for Phase 1 drill 
results). Six additional holes (WMD007 to 012) have been completed, totalling 
1,117 metres. Drilling on 80 metre sections targeted extensions to 
mineralization defined during the Phase 1 diamond drilling campaign (WMD002 to 
006). This drilling has extended Upper Lode mineralization to depth over 150 
vertical metres below surface, and to 80 metres extensions at both the northern 
and southern extents of existing drill intersections. Eleven diamond drill 
holes have now tested the system over a 640 metres strike.

Highlights include;

/T/

--  Section 19880N - WMD007 drilled 100 vertical metres down dip of
mineralization intersected in WMD006 (12.28 metres grading 12.25 grams
per tonne gold and 0.30% copper - refer to Tigray's news release dated
July 16, 2013 ) at Silica Hill, and intersected 28.20 metres at 8.50
grams per tonne gold and 0.24 percent copper including 17.55 metres at
13.18 grams per tonne gold and 0.27 percent copper, from 179.75 metres
drill depth.

--  Section 19960N - WMD009 drilled 80 metres grid north of WMD006 and 007,
and intersected 14.87 metres at 4.49 grams per tonne gold and 0.04
percent copper including 7.90 metres at 7.95 grams per tonne gold and
0.05 percent copper, from 164.20 metres drill depth.

--  Section 19400N - WMD012 drilled the depth extension to previous
mineralization at Mato Bula South (WMD004), and intersected 12.98 metres
at 4.40 grams per tonne gold and 0.87 percent copper from 105.62 metres
drill depth.

--  Section 19320N - WMD011 drilled 80 metres south of previous drilling at
Mato Bula South (WMD004), and intersected 13.98 metres at 2.28 grams per
tonne gold and 0.74 percent copper including 5.43 metres at 4.88 grams
per tonne gold and 0.82 percent copper, from 126.25 metres drill depth.


/T/

At Silica Hill, Upper Lode mineralization and alteration is now defined to 150 
metres vertical depth below surface, remains open at depth, and has been 
defined on two sections 80 metres apart. The tenor (gram-metres) of Upper Lode 
mineralization and intensity and volume of alteration increases to depth on 
both sections. Step out drilling, initially along strike to both the north and 
south at Silica Hill, is required to test the near surface potential of this 
discovery.

At Mato Bula South, Phase 2 drilling has extended the Upper Lode mineralization 
at depth and 80 metres south of previous drilling. The tenor (gram-metres) of 
Upper Lode mineralization increases at depth on section 19400N.

Both Silica Hill and Mato Bula South are part of the Mato Bula Trend, a 
mineralized corridor now defined over 8 kilometres in strike length. 
Gold-copper mineralization is interpreted to be part of a porphyry style Cu-Au 
system containing porphyry-style mineralization, high-grade Au-Cu quartz veins 
and possible replacement styles of mineralization.

Other significant targets previously identified along strike include:

/T/

--  Mato Bula North approximately 1 kilometre northeast of Mato Bula where a
one hole test into the interpreted carapace of a porphyry intrusion
intersected 17.35 metres grading 1.65% copper and 0.40 grams per tonne
gold from 53.80 metres drill depth (WMD001 - hole abandoned before full
test of drill target) (refer to Tigray's news release dated July 16,
2013); and

--  Da Tambuk approximately 4 kilometres northeast of Mato Bula where a four
hole test yielded best results of 12.00 metres at 17.34 grams per tonne
gold and 0.32 percent copper from 52.75 metres drill depth (refer to
Tigray's news release dated March 11, 2014.


/T/

Andrew Lee Smith, President and CEO of Tigray stated, "Our continued success in 
identifying new discoveries and robust drill intersections is a testament to 
the potential for significant discovery that this region of Ethiopia possesses."

Mato Bula Phase 2 Diamond Drill Intercepts

/T/

-------=====================================================================
Gold
grams/
Interval   tonne Copper          Local
Hole ID          From (m)  To (m)   (m)(1)   (2,3)      %   Zone Azimuth Dip
----------------------------------------------------------------------------
WMD007                                                    Upper/
179.75  207.95    28.20    8.50   0.24   Main     274 -46
----------------------------------------
including  189.25  206.80    17.55   13.18   0.27
----------------------------------------
and
including  195.80  206.80    11.00   19.55   0.35
----------------------------------------------------------------------------
WMD008                                                    Upper/
77.20  105.00    27.80    1.81   0.07   Main     279 -50
----------------------------------------
including   94.60   98.60     4.00    5.75   0.04
----------------------------------------------------------------------------
WMD009                                                    Upper/
164.20  179.07    14.87    4.49   0.04   Main     273 -48
----------------------------------------
including  166.40  174.30     7.90    7.95   0.05
----------------------------------------------------------------------------
WMD010              No Significant Intervals                         272 -46
----------------------------------------------------------------------------
WMD011              97.40  101.45     4.05    1.24   0.51   Main     274 -45
-----------------------------------------------
126.25  140.23    13.98    2.28   0.74  Upper
----------------------------------------
including  131.45  136.88     5.43    4.88   0.82
----------------------------------------------------------------------------
WMD012             105.62  118.60    12.98    4.40   0.87  Upper     272 -45
----------------------------------------
including  105.62  108.72     3.10   17.08   3.05
-----------------------------------------------
141.40  142.40     1.00   14.60   0.08
============================================================================
(1) True thicknesses are interpreted as 65-90% of stated intervals.
(2) Intervals use a 0.3 g/t cutoff value.
(3) No top cut has been used on assay values.

/T/

Click here to view a Map of the Mato Bula Drill Hole Locations

Quality Control

The planning, execution and monitoring of Tigray's quality control programs at 
the Harvest project are under the supervision of Jeff Heidema, P.Geo., Tigray's 
Vice President Exploration. Mr. Heidema is a Qualified Person as defined by 
National Instrument 43-101. Diamond drill core samples and trench samples have 
undergone preliminary preparation at the Acme Laboratories facility in Ankara, 
Turkey, and are crushed to 80% passing 10 mesh, and pulverized to 85% passing 
200 mesh (PRP70-1KG package). Analyses are conducted at Acme Laboratories in 
Vancouver, Canada, utilizing Aqua Regia digestion and ICP-ES for base metal and 
silver analyses. Gold analyses are conducted via Fire Assay Fusion with AA 
finish, and gravimetric analyses are completed for over-limit samples. Blanks 
and certified reference standards are inserted into the sample stream to 
monitor laboratory performance. For core, duplicate samples are inserted into 
the sample stream to both monitor laboratory performance and also characterize 
potential mineralization.

Qualified Person

Mr. Heidema has reviewed and approved the scientific and technical information 
contained in this news release.

About Tigray

Tigray is a Canadian mineral exploration company focused on discovery through 
advancing early-stage mineral projects in Ethiopia. Tigray's key property is 
the 70%-owned Harvest polymetallic VMS exploration project, which covers 155 
square kilometres in the Tigray region of Ethiopia, 600 kilometres 
north-northwest of the capital city of Addis Ababa. The company has an option 
to earn an 80% interest in the Adyabo property covering 418 square kilometres 
immediately west of the Harvest project. Tigray's shares trade on the TSX 
Venture Exchange under the symbol TIG.

Tigray and East Africa Metals Inc. ("East Africa") (TSX VENTURE:EAM) have 
jointly announced that they have entered into a definitive agreement pursuant 
to which East Africa has agreed to acquire all of the issued and outstanding 
common shares of Tigray (other than the Tigray shares East Africa currently 
owns). The transaction will be implemented by way of a statutory Plan of 
Arrangement under the Canada Business Corporations Act (refer to Tigray's news 
release dated February 24, 2014).

More information on Tigray Resources Inc. can be viewed at the company's 
website at www.tigray.ca.

On behalf of the Board of Directors:

Andrew Lee Smith, P.Geo.

President, CEO and Director

Cautionary Statement Regarding Forward-Looking Information

This news release contains "forward-looking information" within the meaning of 
applicable Canadian securities legislation. Generally, forward-looking 
information can be identified by the use of forward-looking terminology such as 
"anticipate", "believe", "plan", "expect", "intend", "estimate", "forecast", 
"project", "budget", "schedule", "may", "will", "could", "might", "should" or 
variations of such words or similar words or expressions. Forward-looking 
information is based on reasonable assumptions that have been made by the 
Company as at the date of such information and is subject to known and unknown 
risks, uncertainties and other factors that may cause the actual results, level 
of activity, performance or achievements of the Company to be materially 
different from those expressed or implied by such forward-looking information, 
including but not limited to: risks associated with mineral exploration and 
development; metal and mineral prices; availability of capital; accuracy of the 
Company's projections and estimates, including the initial mineral resource for 
the Harvest Project; interest and exchange rates; competition; stock price 
fluctuations; availability of drilling equipment and access; actual results of 
current exploration activities; government regulation; political or economic 
developments; environmental risks; insurance risks; capital expenditures; 
operating or technical difficulties in connection with development activities; 
personnel relations; the speculative nature of strategic metal exploration and 
development including the risks of diminishing quantities of grades of 
reserves; contests over title to properties; and changes in project parameters 
as plans continue to be refined, as well as those risk factors set out in the 
Company's listing application dated August 18, 2011.

Forward-looking statements are based on assumptions management believes to be 
reasonable, including but not limited to the price of gold, silver, copper and 
zinc; the demand for gold, silver, copper and zinc; the ability to carry on 
exploration and development activities; the timely receipt of any required 
approvals; the ability to obtain qualified personnel, equipment and services in 
a timely and cost-efficient manner; the ability to operate in a safe, efficient 
and effective manner; and the regulatory framework regarding environmental 
matters, and such other assumptions and factors as set out herein. Although the 
Company has attempted to identify important factors that could cause actual 
results to differ materially from those contained in forward-looking 
information, there may be other factors that cause results not to be as 
anticipated, estimated or intended. There can be no assurance that such 
information will prove to be accurate, as actual results and future events 
could differ materially from those anticipated in such information. 
Accordingly, readers should not place undue reliance on forward-looking 
information. The Company does not undertake to update any forward-looking 
information that is included herein, except in accordance with applicable 
securities laws.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this news release.

- 30 -

CONTACT INFO:

Nick Watters, Business Development
604-488-9582
investors@tigray.ca
www.tigray.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

If you no longer want to receive announcements from us, please do not reply to 
this e-mail.
Instead simply click http://marketwire.com/mw/fmu.jsp?id=475968915