Source	Marketwire
Date	04/08/2014
Time	04:00:28 AM

Company	 UNIGOLD INC.
Title	Unigold Provides Exploration Update for the Neita Concession in the 
Dominican Republic





    CDNX Symbol: UGD











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Unigold Inc.

TSX VENTURE SYMBOL: UGD

April 8, 2014

Unigold Provides Exploration Update for the Neita Concession in the Dominican 
Republic


TORONTO, ONTARIO--(Marketwired - April 8, 2014) - Unigold Inc. ("Unigold" or 
the "Company") (TSX VENTURE:UGD) is pleased to provide an update on its ongoing 
exploration work at the Neita Concession and advancement of the Candelones 
deposit.

/T/

1.  Advancing Candelones: building on a solid foundation
On November 12, 2013, the Company announced its maiden mineral resource
estimate for the Candelones Main, Connector and Extension deposits
(collectively "the Candelones deposit"), an inferred mineral resource of
39.5 million tonnes averaging 1.6 g/t gold for 2.0 million ounces of
gold. Work is currently in progress on metallurgical testing, prior to
possible commencement of a Preliminary Economic Assessment later in
2014.


2.  Focus on making new discovery: Neita is target rich
Exploration within the highly prospective Tireo Formation 'belt' in the
Dominican Republic, has recently, identified approximately 5.0 million
gold equivalent ounces. The Tireo Formation 'belt,' is a 40 km wide
sequence of intermediate volcanic and volcanoclastic rocks that bisects
the island of Hispaniola and which has seen limited modern exploration.
Approximately 85% of exploration expenditures to date at Neita have
focused on the Candelones - Guano trend which strikes ENE along the
southern half of the Concession (Figure 2). With the successful
completion of the initial mineral resource estimate at Candelones, the
Company is also focusing its efforts in 2014 towards a "new" discovery.

/T/

Andrew Cheatle, President and CEO of Unigold notes: "We are very excited to 
have a significant land position in what is rapidly emerging as one of the 
premier exploration districts in the world today. With our maiden mineral 
resource estimate completed, and additional metallurgical testing underway we 
can now focus on making a new discovery in the Dominican Republic while 
simultaneously advancing Candelones. We are confident that our field programs 
and data analyses will allow us to effectively prioritize target areas to 
maximize the efficiency of our future drilling, which we expect to resume by 
mid-2014."

To achieve a new discovery, the Company's efforts during the first half of 2014 
is on regional scale mapping of the largely untested northern half of the 
Concession where geochemical and geophysical data define several highly 
prospective areas of copper-gold enrichment. At the same time, results of 
exploration drilling at various gold targets in the southern half of the 
Concession will be critically evaluated with a view to streamlining target 
selection and improving target selection for follow-up drilling.

Once the northern sector mapping is complete, the remaining target areas will 
be evaluated, prioritized and the targets offering the most upside potential 
will be selected for drill testing during H2, 2014.

Exploration Update:

During the fourth quarter of 2013, the Company was focused on delivering its 
maiden mineral resource estimate for Candelones deposit. With that objective 
successfully completed, the Company drill tested select targets along the 
interpreted Candelones - Guano mineralized trend (Figure 1 and 2). In late Q3 
and Q4 2013, the Company drilled the Rancho Pedro, Juan del Bosques and Montazo 
targets (Figure 1 and 2). Wide zones of anomalous gold mineralization were 
intersected and these were associated with IP anomalies. Follow-up work is 
required.

Montazo:

Drilling at Montazo, located 3.0 km to the northeast of the Candelones 
Extension Zone, was targeted to follow up on anomalous results from surface 
mapping and trenching that were coincident with an IP chargeability anomaly 
located along the interpreted contact between andesite volcanoclastics and the 
favourable dacite tuff horizion hosting the mineralization at the Candelones 
Extension.

Significant results include:

/T/

MTZ13-02  50.0 metres averaging 0.60 g/t Au, 9.2 g/t Ag, 0.1% Cu and 0.2% Zn
including 10.5 metres averaging 1.39 g/t Au, 4.8 g/t Ag, 0.0% Cu
and 0.2% Zn and
MTZ13-09  6.75 metres averaging 0.53 g/t Au, 1.3 g/t Ag, 0.0% Cu and 0.3% Zn

/T/

Both MTZ13-02 and 13-09 were drilled on the same section, testing below 
favourable results returned from surface sampling and trenching within a zone 
of intense silicification mapped on surface.

Rancho Pedro:

The Company completed 13 holes (3955 metres) at Rancho Pedro, approximately 6.0 
kilometres east of the Candelones discovery. The drilling targeted a +100 ppb 
gold in soil anomaly coincident with a 500 m x 100 m IP chargeability anomaly, 
both of which occurred at the interpreted boundary between andesite 
volcanoclastics with dacite tuffs, the favourable contact hosting the 
mineralization at Candelones.

Drilling intersected broad intervals of dacite porphyry containing trace 
amounts of finely disseminated pyrite and chalcopyrite cut by minor veinlets 
chalcopyrite, typically less than 2.0 cm in width. Analytical results indicate 
anomalous gold, copper and zinc grade over several tens of metres.

Significant results include:

/T/

DRP-05  68.0 metres averaging 0.05 g/t Au, 1.1 g/t Ag, 0.2% Cu and 0.1% Zn
DRP-11  63.0 metres averaging 0.12 g/t Au, 2.1 g/t Ag, 0.1% Cu and 0.2% Zn
and
DRP-12  73.8 metres averaging 0.13 g/t Au, 2.3 g/t Ag, 0.0% Cu and 0.5% Zn

/T/

The finely disseminated pyrite and chalcopyrite observed in the drill core is 
believed to have generated the chargeability anomaly tested. As a result, 
drilling at Rancho Pedro was suspended pending further review of the data.

Juan del Bosques:

The Company completed 4 holes (1,305 metres) at the Juan del Bosques target, 
2.5 kms northeast of Rancho Pedro. Drilling at Juan del Bosques targeted an 
area of low grade gold results returned from surface trenches.

Significant results include:

/T/

JB13-20  45.3 metres averaging 0.34 g/t Au, 2.8 g/t Ag, 0.0% Cu and 0.0% Zn
and
JB13-21  25.0 metres averaging 0.24 g/t Au, 2.4 g/t Ag, 0.0% Cu and 0.0% Zn

/T/

Results were consistent with the values encountered in the surface trenching. 
Drilling at Juan del Bosques was suspended pending further review and analysis 
of the historical results.

2014 Exploration Plan: detail

Unigold's exploration to date has largely been limited to the southern 25% of 
the Neita Concession, tracing the gold enriched trend defined from Candelones 
to Guano, approximately 10.0 kms to the ENE. While this trend has proven to 
hold significant potential for additional gold discoveries, the Company 
considers it prudent to evaluate the remaining 75% of the Concession which has 
seen limited, if any, follow up exploration on a number of exciting copper and 
gold anomalies defined through soil geochemistry and regional airborne MAG.

The Company is currently focused on regional scale mapping of the northern half 
of the Concession. Current data suggests that the northern portion of the 
Concession is dominated by more mafic volcanic and volcanoclastics rocks, 
interpreted by some to represent the older rocks of the Lower Tireo Formation. 
The southern portion of the Concession is dominated by younger, more felsic 
volcanic and volcanoclastics rocks from the Upper Tireo sequence. The contact 
between the Upper and Lower Tireo is currently interpreted to be a thrust fault 
that trends to the NW and essentially bisects the Concession (Figure 2).

Soil geochemistry indicates a very distinctive break along the mapped contact 
area. Airborne MAG also demonstrates a coincident linear feature that mirrors 
the contact as mapped.

The soil geochemistry clearly indicates that the Lower Tireo has a stronger 
copper response than the Upper Tireo while the gold geochemistry is completely 
opposite, favouring the more felsic volcanic and volcanoclastic rocks of the 
Upper Tireo.

Initial targets of interest that, with the exception of Corozo, have not been 
drill tested to date include:

/T/

--  The northern copper trend - a large, (8.0 km x 2.0 km) copper in soil
anomaly trending NW, parallel to the regional geological fabric located
approximately 11 kms NE of Candelones;
--  Corozo - a coincident copper, gold and molybdenum soil anomaly measuring
approximately 500 m in diameter located in the NW corner of the
Concession approximately 12 km NNW of Candelones and
--  Jiminez, a rock geochemical target demonstrating high grade (+2.0 g/t
Au) located 8.0 kms NNE of Candelones.

/T/

Metallurgy

A composite bulk sample weighing approximately 1,500 kgs, was received by SGS 
Mineral Services ("SGS") in Chile. This composite sample was collected from the 
Candelones Extension deposit. The sample is comprised of more than 220 
individual 2.0 metre half core samples collected from three different drill 
holes on three different sections of the Candelones Extension deposit.

SGS will prepare separate composites that approximate the average grade of the 
deposit as estimated by the inferred mineral resource estimate (approx. 1.6 g/t 
Au). SGS will evaluate the Bond Work Index, grinding and regrinding kinetics, 
rougher and cleaner flotation recovery, gravity recovery and locked cycle 
flotation tests to determine the potential metallurgical recovery at the 
Candelones Extension.

Testing commenced in early February and initial results are expected by June, 
2014.

Dominican Republic

The Dominican Republic is host to world-class gold and base metal mines and 
deposits. The government supports development and exploration in the mining 
sector. In addition, the country has well established Mining Laws and 
Environmental Laws. Unigold's wholly owned flagship property, Neita is 
compliant with all mineral and environmental requirements and work is conducted 
to internationally accepted environmental and social standards. The Neita 
concession exploration license was renewed in 2012 and is in good standing.

Unigold has sufficient funding to meet the goals and objectives established for 
the current exploration program.

QA/QC

Diamond drilling at the Candelones Project included both HQ and NQ diameter 
core for sampling. Holes were typically started with larger diameter HQ core 
and the hole diameter is reduced to NQ at depth. Samples are logged, split by 
wet diamond saw, and half sent for assaying with the other half stored on site. 
Sample lengths typically average 1 m, but vary by geological boundaries. 
Continuous chip samples from trenches are typically 3 m to 5 m in length. QA/QC 
included inserting certified standards and blanks into the sample stream at 
industry standard intervals. Samples are prepped by ACME Analytical Labs in the 
Dominican Republic, with assaying performed through ACME's laboratory in 
Santiago, Chile. Analytical procedures include a 36-element ICP-ES analysis 
(1E) and a 50 g FA AA finish for gold (G6-50).

Wes Hanson P.Geo., Chief Operating Officer of Unigold, has reviewed and 
approved the contents of this press release.

About Unigold Inc.

Unigold is a Canadian based mineral exploration company traded on the TSX 
Venture Exchange under the symbol UGD, focused primarily on exploring and 
developing its gold assets in the Dominican Republic.

For Further Information please visit www.unigoldinc.com.

Forward-looking Statements

Certain statements contained in this document, including statements regarding 
events and financial trends that may affect our future operating results, 
financial position and cash flows, may constitute forward-looking statements 
within the meaning of the federal securities laws. These statements are based 
on our assumptions and estimates and are subject to risk and uncertainties. You 
can identify these forward-looking statements by the use of words like 
"strategy", "expects", "plans", "believes", "will", "estimates", "intends", 
"projects", "goals", "targets", and other words of similar meaning. You can 
also identify them by the fact that they do not relate strictly to historical 
or current facts. We wish to caution you that such statements contained are 
just predictions or opinions and that actual events or results may differ 
materially. The forward -looking statements contained in this document are made 
as of the date hereof and we assume no obligation to update the forward-looking 
statements, or to update the reasons why actual results could differ materially 
from those projected in the forward-looking statements. Where applicable, we 
claim the protection of the safe harbour for forward-looking statements 
provided by the (United States) Private Securities Litigation Reform Act of 
1995.

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

To view the figures associated with this press release, please visit the 
following link: http://media3.marketwire.com/docs/ugd0408figs.pdf.

- 30 -

CONTACT INFO:

Unigold Inc.
Mr. Andrew M. Cheatle, P.Geo
President & CEO
416.866.8157
Fax: 416.866.8674
acheatle@unigoldinc.com

or

Unigold Inc.
Ms. Amanda Dillon
Investor Relations
416.866.8157
Fax: 416.866.8674
adillon@unigoldinc.com
www.unigoldinc.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

If you no longer want to receive announcements from us, please do not reply to 
this e-mail.
Instead simply click http://marketwire.com/mw/fmu.jsp?id=476209861