Source	MARKET NEWS
Date	04/09/2014
Time	05:01:18 AM

Company	 BCGold Corp
Title	Kaiyue Reports 
Exploration Results from Toe Prop





    CDNX Symbol: BCG











Press Release	





KAIYUE INTERNATIONAL INC.  ("KYU-V")
BCGOLD CORP ("BCG-V;BCGOF-0")
- Kaiyue Reports Exploration Results from Toe Property, Yukon

Kaiyue International Inc. ("Kaiyue" or the "Company") and its
option partner BCGold Corp. ("BCGold") are pleased to announce results
from an orientation biogeochemical and VLF geophysical survey conducted
on BCGold's 100%-owned Toe property in October, 2013. The 1,600 ha
property is situated in central Yukon, 7 km northwest of Capstone
Mining Corp.'s Minto Mine, which currently operates at 3,850 tonnes per
day and produces 35.9 million pounds of copper on an annual basis.
The 2013 Toe property exploration program, funded by Kaiyue and
operated by BCGold, was designed to enhance and expand survey coverage
to define "Minto-style" copper-gold drill targets, indicated by
previously defined copper-gold soil geochemical, magnetic and induced
polarization geophysical surveys. The biogeochemical and VLF
geophysical surveys were completed on eight lines, spaced 200 m apart,
with samples and readings collected at 20 m centres. A total of 508 VLF
readings were taken and 442 geochemical samples were collected
(including QA/QC).
Exploration Results
The 2013 biogeochemical sampling and VLF-EM programs defined two
new coincidental and discrete, linear conductors over strike lengths of
approximately 1,300 m and 800 m. Anomaly A was defined over a 1.3 km
distance in a northwest direction. Significant coincidental copper
(Cu), molybdenum (Mo), silver (Ag), tungsten (W), antimony (Sb), and
cerium (Ce) biogeochemical anomalies suggest a robust exploration
target.
Anomaly B lays 200 m to the north and was defined over an 800 m
strike length in an east-west direction. This linear conductor is
defined by a strong Cu response, and weaker W, Sb and Mo biogeochemical
anomalies.
Anomalies A and B are believed to represent discrete, near-surface
copper mineralized structures. A surface trenching program is
recommended to further investigate this possibility. Kaiyue anticipates
that it will be formulating plans for the 2014 exploration season soon.

Exploration work was conducted by Dumas Consulting and Core Assets
Consulting, both independent contractors to Kaiyue. Biogeochemical
samples were submitted to Activation Laboratories Ltd. in Kamloops,
British Columbia, an ISO 9001:2008 accredited laboratory. The work
program was supervised by Darren O'Brien, P.Geo., a Qualified Person as
defined by National Instrument 43-101. Mr. O'Brien has reviewed and
approved the technical contents of this news release.
Toe Property
The Toe property is one of 13 mineral properties that comprise
BCGold's approximately 12,000 ha, 100%-owned Minto/Carmacks copper-gold
property package. All properties are strategically situated proximal
and adjacent to the Minto Mine and Copper North's Carmacks Copper
project, which is located 52 km to the south. BCGold has methodically
advanced this conceptual play and property package through a series of
exploration programs that have included geophysical (airborne magnetic,
radiometric and induced polarization), geochemical (mobile metal ion,
biogeochemical), geological field and diamond drill programs. BCGold
has discovered seven copper zones, including an extension of the
Carmacks Copper deposits on BCGold's adjacent WS property (63.1 m
averaging 0.17% Cu, including 23.6 m averaging 0.34% Cu), and has
advanced seven properties with "Minto-type" exploration targets to the
drill-ready stage.
Kaiyue has the option to acquire a 60% interest in the Toe
property by making $255,000 in cash payments, $1,900,000 in exploration
expenditures and issuing 400,000 shares of Kaiyue to BCGold over a four
year period. Kaiyue can earn an additional 10% interest in the Toe
property by completing a feasibility study, for a total interest of up
to 70% (see August 10, 2012 news release).

On behalf of the Board of Directors,

Hilda Sung
CEO and Director

Neither TSX Venture Exchange nor its Regulation Services Provider (as that
term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.

Some statements in this news release contain forward-looking information or
forward-looking statements. These statements include, but are not limited
to, statements with respect to future expenditures and exploration,
development and production activities. These statements address future
events and conditions, including statement such as "the Company anticipate
that it will be formulating plans for the 2014 exploration season soon"
and, as such, involve known and unknown risks, uncertainties and other
factors, which may cause the actual results, performance or achievements to
be materially different from any future results, performance or
achievements expressed or implied by the statements. Such factors include,
among others, the timing and completion of contemplated financings, the
actual use of proceeds, receipt of regulatory approvals and the timing and
success of future exploration, development and production activities. The
Company expressly disclaims any intention or obligation to update or revise
any forward-looking statements whether as a result of new information,
future events or otherwise except as otherwise required by applicable

























TSX Venture closing price for BCG-V
Date: 2014/04/07
Closing Price: 0.05

TEL:  (604) 831-2114  KAIYUE INTERNATIONAL INC.
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1409700071TS11409703017-20321420140408