Source	Marketwire
Date	04/14/2014
Time	05:00:57 AM

Company	 SCORPIO GOLD CORPORATION
Title	Scorpio Gold Reports Initial Results From 2014 Expansion Drilling at the 
Solberry Satellite Deposit, Mineral Ridge Project, Nevada





    CDNX Symbol: SGN











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Scorpio Gold Corporation

TSX VENTURE SYMBOL: SGN

April 14, 2014

Scorpio Gold Reports Initial Results From 2014 Expansion Drilling at the 
Solberry Satellite Deposit, Mineral Ridge Project, Nevada


VANCOUVER, BRITISH COLUMBIA--(Marketwired - April 14, 2014) - Scorpio Gold 
Corporation ("Scorpio Gold" or the "Company") (TSX VENTURE:SGN) reports initial 
results from its 2014 drilling program at the 70%-owned Mineral Ridge project, 
located in Nevada. The Solberry deposit lies west of the currently producing 
Drinkwater and Mary pits and 600 meters northwest of the heap leach pad.

Pre-2013 drilling on the Solberry deposit outlined a small shallow resource 
based upon a floating cone pit shell (as reported in the Company's August 16, 
2013 news release). Follow-up infill drilling was conducted in 2013 within the 
mineralized wireframe envelope modelled by Telesto, which extended 
east-southeast of the pit shell outline. Drilling in 2014 is targeting the 
extension of mineralization into untested ground outside of the current pit 
shell outline and southeast toward the Oromonte deposit.

The current resource and pit shell at Solberry appear to be constrained by the 
extent of historic drilling rather than any demonstrated termination of the 
mineralized trend. The 2014 drill program is designed to potentially expand and 
enhance the confidence level of the current resource.

Highlights from initial results of the 2014 drilling program on the Solberry 
deposit include:

/T/

--  MR14782: 11.62 grams per tonne ("g/t") gold over 1.52 meters
--  MR14789: 13.82 g/t gold over 1.52 meters
--  MR14792: 9.27 g/t gold over 13.72 meters
--  MR14793: 5.54 g/t gold over 7.62 meters
--  MR14795:.2.01 g/t gold over 10.67 meters
--  MR14796: 4.27 g/t gold over 4.57 meters

/T/

A drill hole location map is available at 
www.scorpiogold.com/i/maps/mr/Solberry_DHplan_2014.jpg.

Table 1. Solberry Deposit - Significant Drill Results

/T/

----------------------------------------------------------------------------
Hole        Azm    Dip  From    To  Width   From     To  Width   Gold   Gold
No.       (deg)  (deg)  (ft)  (ft)   (ft)    (m)    (m)    (m)  (OPT)  (g/t)
----------------------------------------------------------------------------
MR14776       0    -90                     Proposed Hole
----------------------------------------------------------------------------
MR14777       0    -90                     Proposed Hole
----------------------------------------------------------------------------
MR14778       0    -90                     Proposed Hole
----------------------------------------------------------------------------
MR14779     245    -55    45    50      5  13.72  15.24   1.52  0.019   0.65
----------------------------------------------------------------------------
55    60      5  16.76  18.29   1.52  0.020   0.69
----------------------------------------------------------------------------
MR14780       0    -90                     Proposed Hole
----------------------------------------------------------------------------
MR14781       0    -90    60    65      5  18.29  19.81   1.52  0.017   0.59
----------------------------------------------------------------------------
MR14782       0    -90    35    40      5  10.67  12.19   1.52  0.339  11.62
----------------------------------------------------------------------------
50    60     10  15.24  18.29   3.05  0.024   0.81
----------------------------------------------------------------------------
MR14783       0    -90                     Proposed Hole
----------------------------------------------------------------------------
MR14784       0    -90                No Significant Results
----------------------------------------------------------------------------
MR14785       0    -90                No Significant Results
----------------------------------------------------------------------------
MR14785       0    -90                No Significant Results
----------------------------------------------------------------------------
MR14787       0    -90    45    50      5  13.72  15.24   1.52  0.010   0.34
----------------------------------------------------------------------------
70    75      5  21.34  22.86   1.52  0.030   1.03
----------------------------------------------------------------------------
MR14788       0    -90    45    50      5  13.72  15.24   1.52  0.058   2.00
----------------------------------------------------------------------------
110   115      5  33.53  35.05   1.52  0.057   1.94
----------------------------------------------------------------------------
MR14789       0    -90     5    10      5   1.52   3.05   1.52  0.403  13.82
----------------------------------------------------------------------------
MR14790       0    -90   100   110     10  30.48  33.53   3.05  0.015   0.50
----------------------------------------------------------------------------
MR14791       0    -90   120   125      5  36.58  38.10   1.52  0.010   0.34
----------------------------------------------------------------------------
MR14792       0    -90    35    80     45  10.67  24.38  13.72  0.270   9.27
----------------------------------------------------------------------------
95   100      5  28.96  30.48   1.52  0.012   0.42
----------------------------------------------------------------------------
MR14793       0    -90    40    45      5  12.19  13.72   1.52  0.021   0.71
----------------------------------------------------------------------------
85   110     25  25.91  33.53   7.62  0.162   5.54
----------------------------------------------------------------------------
MR14794       0    -90    25    30      5   7.62   9.14   1.52  0.027   0.93
----------------------------------------------------------------------------
35    40      5  10.67  12.19   1.52  0.021   0.72
----------------------------------------------------------------------------
MR14795       0    -90    40    75     35  12.19  22.86  10.67  0.059   2.01
----------------------------------------------------------------------------
95   100      5  28.96  30.48   1.52  0.037   1.28
----------------------------------------------------------------------------
MR14796       0    -90    25    30      5   7.62   9.14   1.52  0.018   0.63
----------------------------------------------------------------------------
80    95     15  24.38  28.96   4.57  0.125   4.27
----------------------------------------------------------------------------
MR14797       0    -90                No Significant Results
----------------------------------------------------------------------------

/T/

All holes presented in Table 1 were completed by reverse circulation (RC) 
drilling. True width is estimated at 80-100% of downhole width. Analytical 
results were performed by American Assay Laboratory Inc. in Sparks, Nevada, an 
ISO/IEC 17025:2005 accredited facility. External check assays to verify lab 
accuracy are routinely completed by ALS Chemex, an ISO 9001:2000 certified and 
ISO/IEC 17025:2005 accredited facility. Further details are presented in the 
Company's quality assurance and quality control program for the Mineral Ridge 
project at www.scorpiogold.com/i/pdf/reports/QAQC-MR.pdf.

About Scorpio Gold

Scorpio Gold holds a 70% interest in the Mineral Ridge gold mining operation 
located in Esmeralda County, Nevada with joint venture partner Waterton Global 
Value L.P. (30%), and is currently entitled to receive 80% of cash flow 
generated. Mineral Ridge is currently in production as a conventional open pit 
mining and heap leach operation. The Mineral Ridge property is host to multiple 
gold-bearing structures, veins and lenses at exploration, development and 
production stages. Scorpio Gold also holds a 100% interest in the advanced 
exploration-stage Goldwedge property and processing facility in Manhattan, 
Nevada. The Company is assessing its exploration plans for the Goldwedge 
property as well as the potential for toll milling at the Goldwedge plant, 
which is currently permitted for 400 tons per day.

Scorpio Gold's CEO, Peter J. Hawley, PGeo, is a Qualified Person as defined by 
National Instrument 43-101 and has reviewed and approved the content of this 
release.

ON BEHALF OF THE BOARD, SCORPIO GOLD CORPORATION

Peter J. Hawley, CEO

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

The Company relies on litigation protection for forward-looking statements. 
This news release contains forward-looking statements that are based on the 
Company's current expectations and estimates. Forward-looking statements are 
frequently characterized by words such as "plan", "expect", "project", 
"intend", "believe", "anticipate", "estimate", "suggest", "indicate" and other 
similar words or statements that certain events or conditions "may" or "will" 
occur, and include, without limitation, statements regarding the Company's 
plans with respect to the exploration, development and exploitation of its 
Mineral Ridge project, including potential further exploration or development 
of the Solberry satellite deposit, any potential expansion of the current pit 
shell outline thereof, and any potential increase in the mineral resource 
estimate in respect thereof. Such forward-looking statements involve known and 
unknown risks, uncertainties and other factors that could cause actual events 
or results to differ materially from estimated or anticipated events or results 
implied or expressed in such forward-looking statements, including risks 
involved in mineral exploration and development programs and those risk factors 
outlined in the Company's Management Discussion and Analysis as filed on SEDAR. 
Any forward-looking statement speaks only as of the date on which it is made 
and, except as may be required by applicable securities laws, the Company 
disclaims any intent or obligation to update any forward-looking statement, 
whether as a result of new information, future events or results or otherwise. 
Forward-looking statements are not guarantees of future performance and 
accordingly undue reliance should not be put on such statements due to the 
inherent uncertainty thereof.

- 30 -

CONTACT INFO:

Scorpio Gold Corporation
Steve Roebuck
President
(819) 825-7618
sroebuck@scorpiogold.com
www.scorpiogold.com

or

Torrey Hills Capital
Jim Macdonald
Investor Relations
(858) 456-7300
jm@sdthc.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

If you no longer want to receive announcements from us, please do not reply to 
this e-mail.
Instead simply click http://marketwire.com/mw/fmu.jsp?id=477126751