Source	MARKET NEWS
Date	04/26/2016
Time	05:34:24 AM

Company	 BonTerra Resources Inc.
Title	Extends 
Main Zone to West with 10 m of 9.3 g/t A





    CDNX Symbol: BTR











Press Release





BONTERRA RESOURCES INC ("BTR-V;BONXF-0")
- Extends Main Zone to West with 10 m of 9.3 g/t Au,
- and Discovers New South Zone with 3.0m of 20.7 g/t Au
- at its Gladiator Gold Project

BonTerra Resources Inc. (the "Company" or "BonTerra") is
pleased to announce that it has received assays on an additional four
(4) holes from its 2016 Exploration and Drill Program on its 100% owned
Gladiator Gold Project located north of Val d'Or, Quebec. To date, 11
of the 19 holes completed have been reported, with eight (8) holes
remaining in the lab. All of the drill holes reported in this press
release are located at or within 50 meters of the known western extents
of the Gladiator deposits.

Nav Dhaliwal, President and CEO of BonTerra, commented: "Once
again we are successful in not only extending the mineralization
further to the west in the Main Zone, but we have discovered additional
high-grade gold with an intersection of 20.7 g/t over 3.0 meters in the
New Zone. Of note, the Main Zone intersected gold at the bottom of the
deepest hole, clearly highlighting the strength and size of the
Gladiator Gold Deposit."

2016 Drilling Program Update and Highlights:

-New South Zone discovery intersects 3.0 m of 20.7 g/t Au in Hole
BA-16-07 at westernmost limits of drilling to date;

-Intersection of 3.0 m of 3.0 g/t Au drilled in New South Zone in
Hole BA-16-08;

-Extends Main Zone further to the west with intersection of 10.0 m
of 9.3 g/t Au, including 3.0 m of 27.5 g/t Au, in Hole BA-16-10;

-Hole BA-16-10 extends mineralization down to 445.5 meters in
deepest and westernmost hole drilled to date;

-8,300 m drilled to date in 19 holes on the western extension of
Gladiator Deposit;

-Visible gold was identified in 16 of the 19 holes;

-The Gladiator Deposits are now outlined to the west by an
additional 200 m long by 450 m deep, where 23 new drill holes (2015 and
2016) have extended the main deposits and discovered 3 new parallel
zones.

-New drill information demonstrates that three zones (Footwall,
Main and Intrusive) continue along strike, while three new zones (North
Shear 1, North Shear 2 and South) have been identified both to the
north and south of the previously known zones.

Dale Ginn, Vice President of Exploration of BonTerra, added: "We
continue to build a very solid, consistent high-grade gold deposit that
is demonstrating continuity in multiple zones. I would like to thank
our Quebec-based exploration team for their hard work and excellent
technical management of the 2015 and 2016 exploration program to date."


Upcoming Program and Next Steps

The western extension of the Gladiator Deposit was targeted based
on interpretation of recent geophysical programs and extension of known
data from the existing Gladiator zones. With the ice drilling program
now complete for the winter season, the project will now focus for the
month of April on gathering and compiling information from the new core
as received to date and pending. The 30-day window is allowing time for
a full interpretation of the initial 19 holes and complete a detailed
report of the winter campaign. Upon completion, BonTerra's technical
team will define, target and prepare the next drilling campaign and
summer surface work. This program is expected to continue with drilling
the main zones, follow up on the recent discoveries, apply drilling in
order to extend the deposits to the east, and to follow up on targets
identified on the Coliseum Property to the west.

See below a summary for all drill results reported to date from
2015 and 2016 including the most recent results from BA-16-07,
BA-16-08, BA-16-10 and BA-16-11:

//st
------------------------------------------------
|Hole     |From |To   |Length|Grade|Zone       |
|         |(m)  |(m)  |(m)   |(g/t |           |
|         |     |     |      |Au)  |           |
|----------------------------------------------|
|BA-15-01A|62.5 |66.0 |3.5   |9.1  |Footwall   |
|----------------------------------------------|
|         |210.6|217.2|6.6   |14.0 |Main       |
|----------------------------------------------|
|Including|215.9|216.7|0.8   |104.5|Main       |
|----------------------------------------------|
|BA-15-02 |107.6|110.2|2.6   |4.7  |Footwall   |
|----------------------------------------------|
|         |224.3|225.2|0.9   |7.6  |Gabbro     |
|----------------------------------------------|
|         |320.5|476.0|155.5 |0.5  |Intrusive  |
|----------------------------------------------|
|         |476.0|483.7|7.7   |7.2  |Main       |
|----------------------------------------------|
|BA-15-03 |187.0|188.5|1.5   |4.3  |Footwall   |
|----------------------------------------------|
|         |200.0|204.0|4.0   |1.3  |Gabbro     |
|----------------------------------------------|
|         |219.0|220.0|1.0   |3.8  |Gabbro     |
|----------------------------------------------|
|         |339.0|379.0|40.0  |0.4  |Intrusive  |
|----------------------------------------------|
|         |392.8|397.0|4.2   |1.6  |Intrusive  |
|----------------------------------------------|
|         |479.0|499.4|20.4  |0.9  |Intrusive  |
|----------------------------------------------|
|BA-15-04 |224.0|235.4|11.4  |1.5  |Main       |
|----------------------------------------------|
|Including|234.1|235.4|1.3   |8.0  |Main       |
|----------------------------------------------|
|BA-16-01 |126.0|127.0|1.0   |5.2  |Footwall   |
|----------------------------------------------|
|         |240.0|378.0|138.0 |0.4  |Intrusive  |
|----------------------------------------------|
|Including|299.0|302.4|3.4   |1.7  |Main       |
|----------------------------------------------|
|Including|353.8|357.0|3.2   |1.9  |Main       |
|----------------------------------------------|
|BA-16-02 |11.0 |55.0 |44.0  |0.4  |New        |
|         |     |     |      |     |(North     |
|         |     |     |      |     |Shear 2)   |
|----------------------------------------------|
|         |79.0 |137.0|58.0  |2.5  |New        |
|         |     |     |      |     |(North     |
|         |     |     |      |     |Shear 1)   |
|----------------------------------------------|
|Including|79.0 |95.0 |16.0  |6.1  |New        |
|         |     |     |      |     |(North     |
|         |     |     |      |     |Shear 1)   |
|----------------------------------------------|
|Including|79.0 |84.0 |5.0   |15.3 |New        |
|         |     |     |      |     |(North     |
|         |     |     |      |     |Shear 1)   |
|----------------------------------------------|
|         |92.5 |95.0 |2.5   |7.5  |New        |
|         |     |     |      |     |(North     |
|         |     |     |      |     |Shear 1)   |
|----------------------------------------------|
|         |103.0|145.0|42.0  |1.0  |Local Shear|
|----------------------------------------------|
|BA-16-03 |4.0  |9.0  |5.0   |9.0  |Footwall   |
|----------------------------------------------|
|Including|4.0  |6.9  |2.9   |13.5 |Footwall   |
|----------------------------------------------|
|BA-16-04 |64.0 |70.0 |6.0   |10.4 |Main       |
|----------------------------------------------|
|BA-16-05 |25.0 |26.5 |1.5   |3.5  |Main       |
|----------------------------------------------|
|         |184.0|186.0|2.0   |12.7 |Main       |
|----------------------------------------------|
|         |290.7|294.0|3.3   |29.0 |New (South)|
|----------------------------------------------|
|BA-16-06 |20.8 |30.0 |9.2   |2.1  |Footwall   |
|----------------------------------------------|
|         |336.0|337.5|1.5   |3.0  |Intrusive  |
|----------------------------------------------|
|         |416.0|420.0|4.0   |1.7  |Main       |
|----------------------------------------------|
|BA-16-07 |142.6|147.0|4.4   |8.0  |Main       |
|----------------------------------------------|
|Including|144.2|147.0|2.8   |11.9 |Main       |
|----------------------------------------------|
|         |155.0|156.0|1.0   |14.9 |Main       |
|----------------------------------------------|
|         |378.0|381.0|3.0   |20.7 |New South  |
|----------------------------------------------|
|BA-16-08 |245.0|332.8|87.8  |0.31 |Intrusive  |
|----------------------------------------------|
|         |368.0|371.0|3.0   |3.0  |New South  |
|----------------------------------------------|
|BA-16-09 |21.7 |27.4 |5.7   |24.3 |Main       |
|----------------------------------------------|
|         |110.1|111.2|1.1   |41.7 |Main       |
|----------------------------------------------|
|         |364.0|369.0|5.0   |1.8  |New (South)|
|----------------------------------------------|
|BA-16-10 |318.0|328.0|10.0  |9.3  |Main       |
|----------------------------------------------|
|Including|321.0|324.0|3.0   |27.5 |Main       |
|----------------------------------------------|
|         |438.0|445.5|7.5   |1.1  |New South  |
|----------------------------------------------|
|BA-16-11 |35.0 |36.7 |1.7   |13.6 |Main       |
|----------------------------------------------|
|         |40.9 |44.0 |3.1   |4.6  |Main       |
|----------------------------------------------|
|         |187.4|187.9|0.5   |24.4 |New South  |
------------------------------------------------

//et

*Stated lengths are core width as drilled, true widths have not
yet been determined.

BonTerra Resources Quick Facts:

-7,563-hectare (Gladiator Project) in the Urban-Barry Camp in
Quebec containing:

-Using a 4 g/t Au cut-off grade, the project currently contains an
inferred resource of 905,000 tonnes, grading 9.37 g/t Au for 273,000
ounces of gold. Of note, ~90% of the worlds operating mines have an
average gold grade less than 8 g/t. Mineral Resource Estimate and
technical report filed July 27, 2012, Snowden Mining Consultants.

-2016 Exploration Program underway - up to 25,000 meters utilizing
minimum of two drill rigs at its 100% owned Gladiator Gold Project to
expand current gold resource.

-2,165-hectare (Larder Property) in the Cadillac-Larder Break camp
in Ontario (refer to March 17, 2016 news release highlighting
historical gold resource).

Dale Ginn, P.Geo. has approved the information contained in this
release. Mr. Ginn is a Director and Vice-President of Exploration for
BonTerra and is a Qualified Person as defined by NI 43-101.

ON BEHALF OF THE BOARD OF DIRECTORS,

Nav Dhaliwal, President & CEO

BonTerra Resources Inc.

For additional information, please contact:




Todd Hanas

Corporate Development

E: todd@bonterraresources.com

T: 866.869.8072

510-744 West Hastings Street, Vancouver, BC V6C 1A1, Canada
Phone: +1 (604) 678-5308  |  Toll-Free: +1 (855) 678-5308
www.bonterraresources.com

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

This press release contains "forward-looking information" that is
based on BonTerra's current expectations, estimates, forecasts and
projections. This forward-looking information includes, among other
things, statements with respect to BonTerra's exploration and
development plans. The words "will", "anticipated", "plans" or other
similar words and phrases are intended to identify forward-looking
information. Forward-looking information is subject to known and
unknown risks, uncertainties and other factors that may cause
BonTerra's actual results, level of activity, performance or
achievements to be materially different from those expressed or implied
by such forward-looking information. Such factors include, but are not
limited to: uncertainties related exploration and development; the
ability to raise sufficient capital to fund exploration and
development; changes in economic conditions or financial markets;
increases in input costs; litigation, legislative, environmental and
other judicial, regulatory, political and competitive developments;
technological or operational difficulties or inability to obtain
permits encountered in connection with exploration activities; and
labour relations matters. This list is not exhaustive of the factors
that may affect our forward-looking information. These and other
factors should be considered carefully and readers should not place
undue reliance on such forward-looking information. BonTerra disclaims
any intention or obligation to update or revise forward-looking
information, whether as a result of new information, future events or
otherwise.





__________________________________________________
_______________________________________________
TSX Venture closing price for BTR-V
Date: 2016/04/25
Closing Price: 0.39
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1611600006TS11611600757-05323720160426