Source	MARKET NEWS
Date	04/11/2017
Time	07:39:18 AM

Company	 Amex Exploration Inc.
Title	Identifies 
High Priority Targets And Starts Dril





    CDNX Symbol: AMX











Press Release





AMEX EXPLORATION INC ("AMX-V;AMXEF-0")
- Identifies High Priority Targets And Starts Drilling On Its
- Eastmain River North Property

Amex Exploration Inc. ("Amex") is pleased to announce the beginning
of an approximately 2000-meter drill program on its 100% owned Eastmain
River North property ("ERN"). This program consists of 13 diamond drill
holes (DDH) that were selected and planned from the combined results of
an airborne Magnetic and Time Domain Electromagnetic (TDEM) survey (see
PR 2016-08-02) and a ground induced polarization survey. (see PR
2017-02-27).

The 26 km-IP survey covered an area of 3.8 km by 1 km of the same
volcano-sedimentary assemblage hosting the newly discovered gold and
base metals showings of SOQUEM's Lac Harbour property. The airborne
geophysical survey demonstrated the continuity of the same magnetic
pattern from SOQUEM to Amex's ERN property, pattern characterized by
NE-SW trending horizons of high and low magnetic conformable anomalies.
Amex has identified 9 high priority targets on the ERN property for
immediate diamond drilling of approximately 2,000 m.

To view the figure associated with this release, please click on
the following link: http://media3.marketwire.com/docs/AMEX_1091479.jpg

This property is situated in the Eeyou Istchee Territory, James
Bay, Quebec, approximately 350 km North of the town of Chibougamau. The
claims are accessible from Chibougamau by the new 243-kilometer-long
all-season road to Stornoway's Renard diamond mine (route 167 extension
from Temiscamie). Amex acquired the property by staking in 2016 and has
carried out in August 2016 an Heliborne airborne Magnetic and Time
-Domain Electromagnetic survey. The 2017 winter IP survey has been
carried by Geophysics TMC of Val D'Or, Quebec while supervision and
interpretation of the survey was under the responsibility of Joel Dube,
P. Eng registered in Quebec.

Amex Exploration Inc. is a junior mining exploration company which
primary objective is to develop and bring into production viable gold
and base metals deposits in mining-friendly jurisdictions. Amex has two
main projects: the 100% owned Perron gold project located 110
kilometres north of Rouyn-Noranda, Quebec, consisting of 116 adjacent
claims covering 4518 hectares; and the 100% owned Eastmain River gold
properties consisting of four distinct properties totalling 135 claims
covering 7,102 hectares.

Alain Vachon, P.Eng., who is a Qualified Person as defined by
Canadian NI 43-101, have approved the technical information reported in
this news release.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

Amex Exploration Inc.
Victor Cantore
President and Chief Executive Officer
514-866-8209
______________________________________
_______________________________________________
TSX Venture closing price for AMX-V
Date: 2017/04/10
Closing Price: 0.19
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1710000037TS11710001368-07360820170411