Source	MARKET NEWS
Date	04/11/2017
Time	12:27:19 PM

Company	 Sunvest Minerals Corp.
Title	Discovers 
New Gold Zone On Mckinnon Hawkins Prop





    CDNX Symbol: SSS











Press Release





SUNVEST MINERALS CORP ("SSS-V")
- Discovers New Gold Zone On Mckinnon-Hawkins Property

Sunvest Minerals Corp. ("Sunvest Minerals" or the "Company") is
pleased to announce an update on the drilling program on the
Mckinnon-Hawkins gold projects located in Hawkins and Walls townships,
Ontario. To date thirteen (13) drill holes have been completed,
comprising 1,624. 4 meters. Drilling has been paused for spring
break-up and is expected to resume in May. To date, complete results
have only been received for four (4) holes with assays pending on the
remaining nine holes.

Most significantly, a new zone has been intersected in two holes
located in the Hanging Wall to the north of the Main Zone. The
McKinnon-Hawkins project Main Zone has a National Instrument 43-101
resource estimate of 239,100 ounces of gold (4,957,000 tonnes at 1.50
grams per tonne gold (g/t Au), at a cut-off grade of 0.5 g/t Au).

The new zone, designated as the "Taylor Extension", located 70 to
90 meters north of the Main Zone, appears to parallel the approximately
east-west strike of the Main Zone, and is open along strike, and at
depth. The Taylor Extension represents a broad new mineralized
environment and if as continuous as the Main Zone, has potential to add
significant resources for the project.

TAYLOR EXTENSION DRILL INTERCEPTS (to date)

Hole HW-17-05, Section 716,050 E, intersected 0.78 g/t Au over 5.0
meters (including 2.29 g/t Au over 1.0 meter) from 51.0 meters.
Anomalous gold values were intersected over 12.0 meters. The total hole
length was 60 meters but will be extended as anomalous gold values were
located at the end of the hole.

Hole HW-17-06, Section 716,000 E, intersected 1.19 g/t Au over 10
meters from 67.0 meters (including 2.28 g/t Au over 3.0 meters). The
Taylor Extension zone values lie within anomalous gold values (+0.10
g/t Au) over a core length of 15. 8 meters. Total hole length is 93.4
meters.

Company CEO Mike England commented, "The discovery of the Taylor
Extension is a significant development for the Mckinnon-Hawkins
project. Further drilling, prospecting and trenching will be directed
at defining this new target. "

Garry Clark, P.Geo, is a qualified person as defined by National
Instrument 43-101 and is the independent qualified person responsible
for reviewing and approving the technical contents of this press
release as they pertain to the McKinnon-Hawkins gold project.

ON BEHALF OF THE BOARD
"Mike England"
Mike England, CEO & DIRECTOR

FOR FURTHER INFORMATION PLEASE CONTACT:
Telephone: 1-604-683-3995
Toll Free: 1-888-945-4770

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Ven ture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

FORWARD LOOKING STATEMENTS: This news release contains
forward-looking statements, which relate to future events or future
performance and reflect management's current expectations and
assumptions. Such forward-looking statements reflect management's
current beliefs and are based on assumptions made by and information
currently available to the Company. Investors are cautioned that these
forward looking statements are neither promises nor guarantees, and are
subject to risks and uncertainties that may cause future results to
differ materially from those expected. These forward -looking
statements are made as of the date hereof and, except as required under
applicable securities legislation, the Company does not assume any
obligation to update or revise them to reflect new events or
circumstances. All of the forward-looking statements made in this press
release are qualified by these cautionary statements and by those made
in our filings with SEDAR in Canada (available at WWW.SEDAR.COM).

Source: Sunvest Minerals Corp.

TEL:  1-604-683-3995
TSX Venture closing price for SSS-V
Date: 2017/04/10
Closing Price: 0.13

TEL:  1-888-945-4770
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1710000056TS11710002146-12235820170411