Source	Marketwire
Date	04/04/2017
Time	06:30:40 AM

Company	 ANGEL GOLD CORP.
Title	Strong Chargeability Anomaly Supports Down Dip Extension of Mineralization 
at the Abejero Prospect of Angel Gold's El Porvenir Project





    CDNX Symbol: ANG











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Angel Gold Corp.

TSX VENTURE SYMBOL: ANG
OTCQX SYMBOL: ANGCF

April 4, 2017

Strong Chargeability Anomaly Supports Down Dip Extension of Mineralization at 
the Abejero Prospect of Angel Gold's El Porvenir Project


VANCOUVER, BRITISH COLUMBIA--(Marketwired - April 4, 2017) - Angel Gold Corp. 
(TSX VENTURE:ANG)(OTCQX:ANGCF) ("Angel" or the "Company"), is pleased to 
provide an update on progress of the geophysical survey program on its Abejero 
Prospect, the third of the three Prospects tested by the current geophysical 
program at its El Porvenir project in the Segovia Mining District of Antioquia, 
Colombia.

Objective and Results

A single line of Induced Polarization geophysics was conducted over the down 
dip extension of the Abejero vein on the Abejero Prospect (Figure 1) in order 
to better define the two ore shoots previously interpreted from historic drill 
core and surface anomalies. Two strong chargeability anomalies were detected 
and corresponded with the down dip direction and extensions of the two known 
ore shoots, Shoots 1 and Shoot 2 as follows:

/T/

--  SHOOT 1, with historic drill intercepts of 5.58m @ 70.35 g/t gold 40.6
g/t silver, and 0.55m @ 14.10 g/t gold 8.90 g/t silver (Foot note(1))
yielded a distinct and discrete chargeability high of around100m in
strike length that appears continuous to depth (Figure 2).The indicated
100m strike length of the high-grade shoot and the historic drill-
indicated thickness and grades are comparable to results recently
reported by Gran Colombia Gold for their Providencia vein
(http://www.grancolombiagold.com/news-and-investors/press-
releases/press-release-details/2017/Gran-Colombia-Gold-Announces-High-
Grade-Drill-Results-From-Its-2016-Infill-Drilling-Campaigns-at-the-
Segovia-and-Marmato-Operations/default.aspx). Angel's Abejero vein
structure has a similar orientation to Gran Colombia Gold's Providencia
Vein, but has a steeper dip. Gran Colombia has traced short strike-
length high-grade shoots at their Segovia mining operations down-dip for
over 1,300m with these shoots remaining open to depth.

--  SHOOT 2, on which the artisanal Abejero Mine is situated and which
formerly produced high grade gold (an Angel sample assayed 117 g/t Au
and 36.5 g/t Ag (see Angel press releases dated February 5 and February
11, 2015)), was expected to yield a geophysical response over a similar
strike length geophysical response to that of Shoot 1, but the anomaly
was far larger and stronger than expected. A strong chargeability
anomaly extending over a distance of more than 400m was detected and
remains open to the southeast (Figure 2). A resistivity anomaly, also
open to the southeast, coincides spatially with the chargeability
anomaly. Higher chargeability usually reflects the presence of sulfides
while higher resistivity typically reflects less conductive rocks such
as intrusives or alteration such as silicification. Sulfides are
associated with the gold mineralization of the Segovia District. The
strength and larger size of the chargeability anomaly is interpreted to
represent a potentially large mineralized target where the Abejero vein
cuts through a brittle body of diorite intruded into the gneiss.
Additional mapping and trenching is needed to better define these drill
targets.

/T/

(1) The results quoted are for Mineros drill holes RBADDH002 & RBADDH003 
respectively. As part of Angel's due diligence program, samples of the assay 
pulps for both of these drill hole intercepts (the core not being in a suitable 
state for meaningful re-sampling) were sent to an ISO accredited laboratory 
along with blanks and standards. There was an excellent comparison between the 
original and check assays. Angel has no reason to doubt the veracity of the 
Mineros results.

"We are excited that the geophysical survey at the Abejero Prospect coincides 
with the known mineralization from historic drilling and presents a much larger 
and stronger conductivity anomaly at the El Porvenir Project. The Induced 
Polarity geophysics program conducted on El Porvenir has now support the 
potential for mineralized targets to exist at depth and along strike of known 
mineralization at all three prospect areas," said Stella Frias, President and 
CEO of Angel Gold Corp.

To view Figure 1, visit the following link: 
http://media3.marketwire.com/docs/1090921-F1.jpg

Figure 1: Abejero Prospect showing the IP line semi-parallel to the Y-shaped 
Abejero structure. The IP line was oriented along the vein with the intent of 
crossing the two known high-grade gold- and sulfide-bearing quartz vein shoots 
identified from shallow historic drilling. Also shown are the historic drill 
hole collars, the better drill intercepts, the interpreted mineralized shoots, 
and a diorite intersected by drill holes at shallow depth. Note that the drill- 
indicated subsurface diorite body coincides with the commencement of the large 
chargeability anomaly. The contact between black sediments to the west and the 
metamorphic gneisses to the east is the deep-crustal Bagre Fault.

Discussion of Results

/T/

--  It is considered likely that the chargeability signature of "SHOOT 2"
was actually overprinted and obscured by a stronger signal caused by
abundant disseminated, veinlet and breccia-fill sulfide coincident with
zones of intense silicification associated with a diorite intrusive body
intersected by the shallow historic drilling. In the area, historic
drill holes RBA019, 022, 023, and 027 intersected wide zones of intense
silica flooding, while drill holes RBA018, 020, 021, 024,025 and 026
intersected more discontinuous patches of intense alteration. Zones of
weak disseminated and fracture-fill pyrite to 1%, over intervals of
between 5 and 20m of down-hole thickness intersected in drill holes
RBA018, 019,020,021,022 and 023 (a strike length of 215m)help to
confirm, but not explain, the size and strength of the chargeability
anomaly shown in the Induced Polarization geophysical line, which
extends more than 400 meters.

--  The extremely brittle intensely silicified rocks encountered by historic
drilling, once subjected to and fractured by tectonic forces, can become
an excellent host for a breccia-hosted style of mineralization. Similar
breccia-hosted mineralization occurs in the intensely silicified
intrusive at Angel's Guayabales prospect
(http://www.angelgoldcorp.com/2017/03/27/angel-gold-geophysical-survey-
encounters-multiple-strong-chargeability-anomalies-at-guayabales-
prospect-at-the-el-porvenir-project/) and at Angel's Iguanacito prospect
(http://www.angelgoldcorp.com/2017/03/20/angel-gold-geophysical-survey-
encounters-strong-chargeability-anomalies-at-the-el-porvenir-project-
ground-induced-polarization-and-magnetic-geophysical-surveys-in-
progress-at-goldsilver-targets-wi/). Both prospects also occur within
Angel's El Porvenir Project and are part of the current geophysical
exploration.

/T/

To view Figure 2, visit the following link: 
http://media3.marketwire.com/docs/1090921-F2.jpg

Figure 2: Section0+00NElooking northeast, showing a shorter and relatively 
weaker chargeability response over Shoot 1(center) and a much stronger and 
longer chargeable response associated with Shoot 2 that is also coincident with 
elevated resistivity.

Historically 2,398.25m of small diameter core (BQ) drilling was completed at 
Abejero, but averaged only 66.6m depth (depths ranged from 38.65 to 85.10m). 
Most of these holes intersected only the host gneiss, but 3 holes (RBA019, 020 
and 022) intersected diorite intrusive at shallow depth. The more significant 
mines within the Segovia mining belt are hosted within similar intrusive rocks.

Intrusive rocks are more homogenous and uniformly brittle than gneiss such as 
that at Abejero, fracture in a wide variety of orientations and the fractures 
are more continuous, thus more suitable to being more continuously mineralized. 
The Abejero structure has the potential to have better continuity as a 
quartz-sulfide zone within the diorite than in the less brittle gneissic rocks.

Interpretation of geophysical responses needs to be placed into context with 
both geology and topography. The electrical current identifies chargeable and 
resistive responses directly under the line being surveyed, but also is 
affected by rocks and mineralization occurring either side of the line. Figure 
3 shows a 3D Google Earth image with the approximate trace of the IP line 
cutting diagonally up a steep slope and along the wall of a gully, such that 
the IP survey is looking into the hill on the northeast side, and thus may plot 
shallow subsurface off-section responses as extending to surface on the pseudo 
section.

Drill Targets

The geophysical anomaly and assay results from historic drilling in the 
vicinity of Shoot 1 combine to make Shoot 1 a priority, drill ready target. The 
target, as defined by the chargeability anomaly, has a length of about 100m. 
The vein to which it corresponds dips 55o to 70o ENE.

At Shoot 2, the down dip extension of the artisanal Abejero mine is also a 
ready drill target, but drilling will need to be based upon current geological 
mapping. The larger and stronger geophysical anomaly over Shoot 2 is also a 
potential drill target for brecciation and gold mineralisation, but prior to 
drill testing geological mapping, a more detailed geophysical survey and 
trenching are warranted.

To view Figure 3, visit the following link: 
http://media3.marketwire.com/docs/1090921F3.jpg

Figure 3:Google Earth 3D topographic image of the Abejero Prospect looking NE, 
showing the approximate position of the IP survey line extending diagonally up 
a hill slope and subparallel to a gully, the major deep crustal Bagre Fault, 
historic Abejero drillhole collars, the Abejero mine and the 
drill-indicated-diorite body.

Qualified Person

Mr. James G. Burns, P. Eng., a Qualified Person under National Instrument 
43-101 standards and a technical advisor to the Company has reviewed and 
approved the technical information contained in this news release.

About Angel Gold Corp.:

Angel is a Canada-based gold and silver exploration company focused on 
responsible development of mineral resources in Colombia, host to some of the 
world's largest gold deposits. Angel's flagship project the El Porvenir is 
located at less than 2 km from Segovia project of Gran Colombia, the El Pino 
West Project is adjacent to the Gramalote project of B2Gold and Anglo Gold 
Ashanti JV and its Heliconia project is located north of the Titiribi district 
along the Cauca fault system.

Angel has been focused on acquiring and validating strategic mineral 
exploration opportunities in Colombia's best mining districts with the highest 
potential for new discoveries.

On Behalf of the Board of Directors of Angel Gold Corp.

Blanca Stella Frias, Director, President and Chief Executive Officer

Neither the TSX Venture Exchange nor the Investment Industry Regulatory 
Organization of Canada accepts responsibility for the adequacy or accuracy of 
this news release.

The TSX Venture Exchange has not reviewed the content of this News Release and 
therefore does not accept responsibility or liability for the adequacy or 
accuracy of the contents of this News Release. This news release contains 
certain "forward- looking statements" within the meaning of Section 21E of the 
United States Securities and Exchange Act of 1934, as amended. Except for 
statements of historical fact relating to the Company, certain information 
contained herein constitutes forward- looking statements. Forward-looking 
statements are based upon opinions and estimates of management at the date the 
statements are made, and are subject to a variety of risks and uncertainties 
and other factors which could cause actual results to differ materially from 
those projected in the forward looking statements. The reader is cautioned not 
to place undue reliance on forward-looking statements. The transaction 
described in this News Release is subject to a variety of conditions and risks 
which include but are not limited to: regulatory approval, shareholder 
approval, market conditions, legal due diligence for claim validity, financing, 
political risk, security risks at the property locations and other risks. As 
such, the reader is cautioned that there can be no guarantee that this 
transaction will complete as described in this News Release. We seek safe 
harbour.

- 30 -

CONTACT INFO:

Angel Gold Corp.
Stella Frias
Investor Relations
+1 (360) 650 1440
www.angelgoldcorp.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=590839788