Source	CANADA NEWSWIRE
Date	04/04/2017
Time	04:03:22 AM

Company	 Azarga Metals Corp.
Title	Azarga Metals Announces Maiden Mineral Resource Estimate for Unkur
Deposit





    CDNX Symbol: AZR











Press Release




" BC-Azarga-Unkur-Estimate   04-04 2437
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business Editors:
^Azarga Metals Announces Maiden Mineral Resource Estimate for Unkur
Deposit@

TSX-V: AZR
VANCOUVER, April 4, 2017 /CNW/ - AZARGA METALS CORP. ("Azarga Metals" or
the "Company") (TSX-V:AZR) announces the results of its maiden Mineral
Resource estimate for its Unkur Copper-Silver Project in the Zabaikalsky
Region of eastern Russia. The estimate is an Inferred Mineral Resource of 42
million tonnes at 0.52% copper and 38g/t silver, containing 220,000 tonnes
(ie, 480 million pounds) of copper and 52 million ounces of silver. This
equates to approximately 380,000 tonnes (ie, 840 million pounds) of copper
equivalent at 0.90% or approximately 124 million ounces of silver equivalent
at 91g/t, assuming a copper price of US$3.00/lb, silver price of US$20/oz and
100% recovery. The Mineral Resource estimate was independently prepared by SRK
Consulting (Russia) Ltd. ("SRK"), in accordance with NI 43-101.
"The maiden Mineral Resource estimate is a very successful result from
just our first few months of physical exploration at Unkur," said Dorian L.
(Dusty) Nicol, the Company's president and CEO. He went on to say,
"importantly, mineralization is open in multiple directions, which supports
growth potential" and "this further stimulates our belief that Unkur has the
potential to be a globally significant copper-silver deposit."
A Technical Report covering the Mineral Resource estimate will be filed
on SEDAR within 45 days of this news release.
SUMMARY
An Inferred Mineral Resource was estimated based on three domains. Zone 1
is the stratigraphically upper zone of mineralization and Zone 2 is the
stratigraphically lower zone, which is divided into a northern (N) and
southern (S) sub-zone. Zone 1 and Zone 2 are further divided into near surface
and underground mineralization.
Table 1: Unkur Copper-Silver Project Inferred Mineral Resource estimate summary 
as at 31 March 2017
--------------------------------------------------------------------------------
-------------------

Tonnage                                                      Copper          
Silver
(million                                                  equivalent      
equivalent
tonnes)                           Copper        Silver    grade (%)    grade 
(g/t)
grade (%)  grade (g/t)
Category / zone
---------------

Near surface (NS)
----------------

- Zone 1                                                          
23                              0.54             40          0.93               
95

- Zone 2 (North)                                                   
9                              0.47             43          0.89               
91

- Zone 2 (South)                                                   
1                              0.42              4          0.46               
47
---                              ----            ---          ----              
---

-Total near
surface                                                          
33                              0.52             39          0.90               
92


Underground (UG)
---------------

- Zone 1                                                           
8                              0.53             34          0.86               
88

- Zone 2 (North)                                                   
1                              0.47             43          0.89               
91
---                              ----            ---          ----              
---

-Total
underground                                                      
10                              0.52             35          0.87               
88


Zone 1 NS + UG                                                     
31                              0.54             38          0.91               
93

Zone 2 NS + UG                                                     
11                              0.46             38          0.84               
85
---                              ----            ---          ----              
---

Total Resource                                                     
42                              0.52             38          0.90               
91
Notes: (1) CIM Definition Standards
were followed for Mineral
Resources; (2) Pit constrained
Mineral Resources are reported
within a conceptual pit shell; (3)
Mineral resources are not Mineral
Reserves and do not have
demonstrated economic viability;
(4) Mineral Resources are reported
at a cut-off grade of 0.3% copper
equivalent for near surface and
0.7% copper equivalent for
underground; (5) copper and silver
equivalent grades were estimated
using US$3.00/lb copper price,
US$20.00/oz silver price and 100%
recovery using the formulae Cu eq (equal sign)
Cu + (0.009722 x Ag) and Ag eq (equal sign) Ag
+ (102.86 x Cu); and (6) numbers
may not add due to rounding.


GROWTH POTENTIAL
Azarga Metals considers that there is strong potential to grow the
Mineral Resource at the Unkur Copper-Silver Project beyond that identified in
this maiden Mineral Resource estimate. The mineralization is open in both
directions along strike and further exploration drilling will aim to extend
mineralization along strike. Of key interest for growth potential is the zone
of thicker and higher grade mineralization in the northern part of the
Inferred Mineral Resource area (see Figure 2). The next phase of work will
focus on using geologic and geophysical exploration to target potential
extensions of this higher grade zone. The mineralization also remains open
down-dip. In addition to this Unkur Copper-Silver Project Inferred Mineral
Resource area and its potential extensions, there are numerous additional
occurrences of copper-silver mineralization and geochemical / geophysical
anomalies within the Company's 5,390 hectare Unkur License.
DETAILS OF MINERAL RESOURCE ESTIMATE DATED 31 MARCH 2017
Details of Mineral Resource estimate dated 31 March 2017
The Mineral Resource estimate was prepared by SRK, under the direction of
Robin Simpson MAIG, an independent Qualified Person as defined by National
Instrument 43-101 ("NI 43-101"). The results are reported in accordance with
NI 43-101 and the 2014 CIM Definition Standards. The Qualified Person visited
the Unkur Copper-Silver Project and SGS Laboratories in Chita during October
2016.
Robin Simpson has approved this written disclosure of the Mineral
Resource estimate.
Data verification
The Qualified Person has verified the database the Mineral Resource
estimate is based on. This verification was done by personal inspection of
drill core, drill sites and trenches during the site visit, and by checking
database content against primary data sources and historical information.
Exploration Information
The estimate is based on 4,580 meters of diamond drilling (from 16
drill-holes) and 186 meters of channel sampling (from four trenches),
completed during Azarga Metals' exploration campaign from August 2016 until
February 2017.
In the opinion of the Qualified Person, the core and channel samples
collected by Azarga Metals are sufficiently accurate and reliable for use in
Mineral Resource estimation, and there are no material data quality issues
related to drilling, sampling, recovery or other factors.
Intervals identified by Azarga Metals' geologists as potentially
mineralized were sampled, typically on one meter lengths. The half-core
samples from drill core, and channel samples from trenches, were sent to SGS
Laboratories in Chita for analysis of copper and silver. Standard QA/QC
protocols were followed, including analysis of duplicates and standards and
check analyses by ALS Laboratories in Chita. The results of this QA/QC
checking will be presented in the forthcoming Technical Report.
The main identified zone of copper-silver mineralization (Zone 1) is
intersected by 13 drill-holes and two trenches. Drill-hole collar and trench
locations are tabulated in Table 2 and the mineralized intersections are
summarized in Table 3. The locations of these intersections are shown in
Figure 3.
Table 2: Drill-hole collar and trench locations from August 2016 to February 
2017 physical exploration program at Unkur Copper-Silver Project
--------------------------------------------------------------------------------
-------------------------------------------------------------

Hole 
or                                                                              
         Y                          Z (RL m)               Maximum     
Starting     Starting
trench 
ID                                                                              
                                                       depth (m)    dip 
(deg)      azimuth
X                                                                               
                                  (deg)
---                                                     
---                                                                             
                                     ----

AM-020                                             
20595906                              6303578                              
902.7                  284.9           -70          249

AM-001                                             
20595871                              6303108                              
929.7                  400.5           -69          241

AM-002                                             
20596077                              6303227                              
919.4                  520.5           -70          248

AM-003                                             
20595911                              6302753                              
930.5                  100.0           -72          242

AM-004                                             
20596093                              6302871                              
935.5                  382.9           -70          242

AM-005                                             
20596247                              6302510                              
913.7                  160.0           -71          241

AM-006                                             
20596388                              6302620                              
955.1                  572.0           -69          221

AM-007                                             
20596411                              6302155                              
927.7                   80.0           -70          222

AM-008                                             
20596611                              6302365                            
1,007.8                  601.3           -72          228

AM-009                                             
20596725                              6301968                              
983.0                  238.0           -69          224

AM-011                                             
20596936                              6301672                              
952.3                  178.5           -68          223

AM-013                                             
20597233                              6301394                              
995.8                  100.0           -68          220

AM-015                                             
20597567                              6301246                             
1042.0                  201.0           -68          217

AM-017                                             
20596211                              6302467                              
916.1                  277.5           -71          230

AM-019                                             
20596639                              6301879                              
938.9                  226.7           -69          224

AM-018                                             
20595635                              6302977                              
937.8                  256.6           -73          241

TR K601                                            
20596492                              6301887                              
969.1                   14.0             0          236

TR K615                                            
20597213                              6301311                            
1,015.4                  115.0             0          222

TR K616                                            
20597472                              6301143                            
1,049.5                   29.0             0          233

Table 3: Intersections used for estimation(1)
--------------------------------------------

From   To  Length      Copper        Silver           Copper             True
(m)  (m)     (m)   grade (%)    grade (%)      equivalent        thickness
Hole or trench 
ID                                                                              
  grade (%)             (m)
-----------------                                                               
                  --------              ---

Zone 1
------

AM-020                                       227.0 241.0       14         
0.51          28.44              0.79             10.6

AM-001(2)                                     82.5 125.5       33         
0.83          79.81              1.61             20.1

AM-002                                       432.5 472.5       40         
0.31          12.77              0.44             33.8

AM-003(3)                                     40.5  77.5       37         
0.43          39.63              0.82             26.9

AM-004(4)                                    319.5 358.5       31         
0.44          27.23              0.70             23.7

AM-006                                       440.5 456.5       16         
0.34          11.02              0.45             14.4
AM-007                                        47.0  60.0       13         
0.25          17.12              0.41             10.9

AM-008                                       352.3 364.3       12         
0.24           6.02              0.30              9.9

AM-011                                       145.5 153.9      8.4         
0.92          61.73              1.52              7.3

AM-013                                        70.0  78.0        8         
0.53          22.62              0.75              6.8

AM-015                                       135.0 145.0       10         
0.29           4.55              0.34              8.7

AM-017                                       189.5 202.5       13         
1.28         103.91              2.29              9.8

AM-019                                        39.0  49.0       10         
0.48          12.39              0.60              8.6

TR K615                                        8.0  17.0        9         
0.30          14.03              0.44              6.9

TR K616                                       18.0  29.0       11         
0.41           6.32              0.47              8.1


Zone 2 (N)
---------

AM-001                                       311.5 346.5       35         
0.47          43.49              0.89

AM-019                                       106.0 119.0       13         
0.17           4.99              0.22


Zone 2 (S)
---------

TR K601                                        0.0  10.0       10         
0.73           2.07              0.75
Notes: (1) copper and silver
equivalent grades were estimated
using US$3.00/lb copper price,
US$20.00/oz silver price and 100%
recovery using the formulae Cu eq 

" BC-Azarga-Unkur-Estimate   04-04 2437
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business Editors:
^Azarga Metals Announces Maiden Mineral Resource Estimate for Unkur
Deposit@

TSX-V: AZR
VANCOUVER, April 4, 2017 /CNW/ - AZARGA METALS CORP. ("Azarga Metals" or
the "Company") (TSX-V:AZR) announces the results of its maiden Mineral
Resource estimate for its Unkur Copper-Silver Project in the Zabaikalsky
Region of eastern Russia. The estimate is an Inferred Mineral Resource of 42
million tonnes at 0.52% copper and 38g/t silver, containing 220,000 tonnes
(ie, 480 million pounds) of copper and 52 million ounces of silver. This
equates to approximately 380,000 tonnes (ie, 840 million pounds) of copper
equivalent at 0.90% or approximately 124 million ounces of silver equivalent
at 91g/t, assuming a copper price of US$3.00/lb, silver price of US$20/oz and
100% recovery. The Mineral Resource estimate was independently prepared by SRK
Consulting (Russia) Ltd. ("SRK"), in accordance with NI 43-101.
"The maiden Mineral Resource estimate is a very successful result from
just our first few months of physical exploration at Unkur," said Dorian L.
(Dusty) Nicol, the Company's president and CEO. He went on to say,
"importantly, mineralization is open in multiple directions, which supports
growth potential" and "this further stimulates our belief that Unkur has the
potential to be a globally significant copper-silver deposit."
A Technical Report covering the Mineral Resource estimate will be filed
on SEDAR within 45 days of this news release.
SUMMARY
An Inferred Mineral Resource was estimated based on three domains. Zone 1
is the stratigraphically upper zone of mineralization and Zone 2 is the
stratigraphically lower zone, which is divided into a northern (N) and
southern (S) sub-zone. Zone 1 and Zone 2 are further divided into near surface
and underground mineralization.
Table 1: Unkur Copper-Silver Project Inferred Mineral Resource estimate summary 
as at 31 March 2017
--------------------------------------------------------------------------------
-------------------

Tonnage                                                      Copper          
Silver
(million                                                  equivalent      
equivalent
tonnes)                           Copper        Silver    grade (%)    grade 
(g/t)
grade (%)  grade (g/t)
Category / zone
---------------

Near surface (NS)
----------------

- Zone 1                                                          
23                              0.54             40          0.93               
95

- Zone 2 (North)                                                   
9                              0.47             43          0.89               
91

- Zone 2 (South)                                                   
1                              0.42              4          0.46               
47
---                              ----            ---          ----              
---

-Total near
surface                                                          
33                              0.52             39          0.90               
92


Underground (UG)
---------------

- Zone 1                                                           
8                              0.53             34          0.86               
88

- Zone 2 (North)                                                   
1                              0.47             43          0.89               
91
---                              ----            ---          ----              
---

-Total
underground                                                      
10                              0.52             35          0.87               
88


Zone 1 NS + UG                                                     
31                              0.54             38          0.91               
93

Zone 2 NS + UG                                                     
11                              0.46             38          0.84               
85
---                              ----            ---          ----              
---

Total Resource                                                     
42                              0.52             38          0.90               
91
Notes: (1) CIM Definition Standards
were followed for Mineral
Resources; (2) Pit constrained
Mineral Resources are reported
within a conceptual pit shell; (3)
Mineral resources are not Mineral
Reserves and do not have
demonstrated economic viability;
(4) Mineral Resources are reported
at a cut-off grade of 0.3% copper
equivalent for near surface and
0.7% copper equivalent for
underground; (5) copper and silver
equivalent grades were estimated
using US$3.00/lb copper price,
US$20.00/oz silver price and 100%
recovery using the formulae Cu eq (equal sign)
Cu + (0.009722 x Ag) and Ag eq (equal sign) Ag
+ (102.86 x Cu); and (6) numbers
may not add due to rounding.


GROWTH POTENTIAL
Azarga Metals considers that there is strong potential to grow the
Mineral Resource at the Unkur Copper-Silver Project beyond that identified in
this maiden Mineral Resource estimate. The mineralization is open in both
directions along strike and further exploration drilling will aim to extend
mineralization along strike. Of key interest for growth potential is the zone
of thicker and higher grade mineralization in the northern part of the
Inferred Mineral Resource area (see Figure 2). The next phase of work will
focus on using geologic and geophysical exploration to target potential
extensions of this higher grade zone. The mineralization also remains open
down-dip. In addition to this Unkur Copper-Silver Project Inferred Mineral
Resource area and its potential extensions, there are numerous additional
occurrences of copper-silver mineralization and geochemical / geophysical
anomalies within the Company's 5,390 hectare Unkur License.
DETAILS OF MINERAL RESOURCE ESTIMATE DATED 31 MARCH 2017
Details of Mineral Resource estimate dated 31 March 2017
The Mineral Resource estimate was prepared by SRK, under the direction of
Robin Simpson MAIG, an independent Qualified Person as defined by National
Instrument 43-101 ("NI 43-101"). The results are reported in accordance with
NI 43-101 and the 2014 CIM Definition Standards. The Qualified Person visited
the Unkur Copper-Silver Project and SGS Laboratories in Chita during October
2016.
Robin Simpson has approved this written disclosure of the Mineral
Resource estimate.
Data verification
The Qualified Person has verified the database the Mineral Resource
estimate is based on. This verification was done by personal inspection of
drill core, drill sites and trenches during the site visit, and by checking
database content against primary data sources and historical information.
Exploration Information
The estimate is based on 4,580 meters of diamond drilling (from 16
drill-holes) and 186 meters of channel sampling (from four trenches),
completed during Azarga Metals' exploration campaign from August 2016 until
February 2017.
In the opinion of the Qualified Person, the core and channel samples
collected by Azarga Metals are sufficiently accurate and reliable for use in
Mineral Resource estimation, and there are no material data quality issues
related to drilling, sampling, recovery or other factors.
Intervals identified by Azarga Metals' geologists as potentially
mineralized were sampled, typically on one meter lengths. The half-core
samples from drill core, and channel samples from trenches, were sent to SGS
Laboratories in Chita for analysis of copper and silver. Standard QA/QC
protocols were followed, including analysis of duplicates and standards and
check analyses by ALS Laboratories in Chita. The results of this QA/QC
checking will be presented in the forthcoming Technical Report.
The main identified zone of copper-silver mineralization (Zone 1) is
intersected by 13 drill-holes and two trenches. Drill-hole collar and trench
locations are tabulated in Table 2 and the mineralized intersections are
summarized in Table 3. The locations of these intersections are shown in
Figure 3.
Table 2: Drill-hole collar and trench locations from August 2016 to February 
2017 physical exploration program at Unkur Copper-Silver Project
--------------------------------------------------------------------------------
-------------------------------------------------------------

Hole 
or                                                                              
         Y                          Z (RL m)               Maximum     
Starting     Starting
trench 
ID                                                                              
                                                       depth (m)    dip 
(deg)      azimuth
X                                                                               
                                  (deg)
---                                                     
---                                                                             
                                     ----

AM-020                                             
20595906                              6303578                              
902.7                  284.9           -70          249

AM-001                                             
20595871                              6303108                              
929.7                  400.5           -69          241

AM-002                                             
20596077                              6303227                              
919.4                  520.5           -70          248

AM-003                                             
20595911                              6302753                              
930.5                  100.0           -72          242

AM-004                                             
20596093                              6302871                              
935.5                  382.9           -70          242

AM-005                                             
20596247                              6302510                              
913.7                  160.0           -71          241

AM-006                                             
20596388                              6302620                              
955.1                  572.0           -69          221

AM-007                                             
20596411                              6302155                              
927.7                   80.0           -70          222

AM-008                                             
20596611                              6302365                            
1,007.8                  601.3           -72          228

AM-009                                             
20596725                              6301968                              
983.0                  238.0           -69          224

AM-011                                             
20596936                              6301672                              
952.3                  178.5           -68          223

AM-013                                             
20597233                              6301394                              
995.8                  100.0           -68          220

AM-015                                             
20597567                              6301246                             
1042.0                  201.0           -68          217

AM-017                                             
20596211                              6302467                              
916.1                  277.5           -71          230

AM-019                                             
20596639                              6301879                              
938.9                  226.7           -69          224

AM-018                                             
20595635                              6302977                              
937.8                  256.6           -73          241

TR K601                                            
20596492                              6301887                              
969.1                   14.0             0          236

TR K615                                            
20597213                              6301311                            
1,015.4                  115.0             0          222

TR K616                                            
20597472                              6301143                            
1,049.5                   29.0             0          233

Table 3: Intersections used for estimation(1)
--------------------------------------------

From   To  Length      Copper        Silver           Copper             True
(m)  (m)     (m)   grade (%)    grade (%)      equivalent        thickness
Hole or trench 
ID                                                                              
  grade (%)             (m)
-----------------                                                               
                  --------              ---

Zone 1
------

AM-020                                       227.0 241.0       14         
0.51          28.44              0.79             10.6

AM-001(2)                                     82.5 125.5       33         
0.83          79.81              1.61             20.1

AM-002                                       432.5 472.5       40         
0.31          12.77              0.44             33.8

AM-003(3)                                     40.5  77.5       37         
0.43          39.63              0.82             26.9

AM-004(4)                                    319.5 358.5       31         
0.44          27.23              0.70             23.7

AM-006                                       440.5 456.5       16         
0.34          11.02              0.45             14.4
AM-007                                        47.0  60.0       13         
0.25          17.12              0.41             10.9

AM-008                                       352.3 364.3       12         
0.24           6.02              0.30              9.9

AM-011                                       145.5 153.9      8.4         
0.92          61.73              1.52              7.3

AM-013                                        70.0  78.0        8         
0.53          22.62              0.75              6.8

AM-015                                       135.0 145.0       10         
0.29           4.55              0.34              8.7

AM-017                                       189.5 202.5       13         
1.28         103.91              2.29              9.8

AM-019                                        39.0  49.0       10         
0.48          12.39              0.60              8.6

TR K615                                        8.0  17.0        9         
0.30          14.03              0.44              6.9

TR K616                                       18.0  29.0       11         
0.41           6.32              0.47              8.1


Zone 2 (N)
---------

AM-001                                       311.5 346.5       35         
0.47          43.49              0.89

AM-019                                       106.0 119.0       13         
0.17           4.99              0.22


Zone 2 (S)
---------

TR K601                                        0.0  10.0       10         
0.73           2.07              0.75
Notes: (1) copper and silver
equivalent grades were estimated
using US$3.00/lb copper price,
US$20.00/oz silver price and 100%
recovery using the formulae Cu eq (equal sign)
Cu + (0.009722 x Ag) and Ag eq (equal sign) Ag
+ (102.86 x Cu); (2) mineralization
begins at base of moraine, possibly
intersection has been truncated by
glacial erosion - composite excludes
barren zone from 104.5 to 114.5; (3)
mineralization begins at base of
moraine, possibly intersection has
been truncated by glacial erosion;
and (4) composite excludes barren
zone from 335.5 to 343.5.

Section lines for drilling are spaced approximately 300m apart. Where
there are two Zone 1 intersections on the same drill section, the spacing
between intersections is typically 200m to 300m.
Estimation methodology and parameters
A wireframe interpretation of Zone 1 was constructed at a nominal
threshold of 0.10% copper. Based on the limits of the current sampling
coverage, the modelled domain has a strike length of 3,400 meters
northwest-southeast, and a down dip extent of up to 550 meters, but this zone
is open down dip and along strike in both directions. The Zone 1 domain
generally dips 50 to 60 degree to the east or northeast, and has an average
true thickness of 19 meters.
Approximately parallel to Zone 1, and 100 to 150m southwest, a second
zone of mineralization has been interpreted, from two drill intersections, one
trench intersection, and one outcrop. This second zone is stratigraphically
below Zone 1.
The Lower Proterozoic sedimentary rocks that host mineralization are
partly covered by Quaternary moraine. The thickness of the moraine cover over
the northern part of the mineralization is up to 100 meters. The moraine cover
generally is thinner to the south, and mineralization in the southern part of
Zone 1 and Zone 2 can be exposed by trenching.
Topography was modelled based on drill collar locations, and using
additional elevation information digitized from topographic maps.
Copper and silver grades within the Zone 1 mineralized domain were
estimated by 2D Ordinary Kriging. A single 2D composite was generated for each
intersection. The true thickness assigned to each composite was calculated
based on the local orientations of the drill intersection and the Zone 1
wireframe. No grade capping was applied to either the samples or the
composites. The block size for 2D Kriging was 100 meters north-south and 100
meters vertically. The results of the estimation were copied into a 3D block
model, with sub-blocking down to 1.5625 meters, in order to achieve a good fit
to the relatively narrow mineralization wireframe.
The copper and silver grades for Zone 2, which contains fewer
intersections than Zone 1, were estimated by a simple average of sample grades
for the northern and southern portions.
For the mineralized domains and the host rocks, a dry bulk density value
of 2.67t/m3 was used for converting volumes into tonnages. This factor is the
average value of samples collected by Azarga. A dry bulk density factor of
2.0t/m3 was assumed for the moraine material.
The portion of the mineralization model that met the CIM definition of a
Mineral Resource ("...reasonable prospects for eventual economic extraction")
was established by using NPV Scheduler software to generate a pit shell to
constrain reporting of the near surface resource. The input parameters for the
pit shell are shown in Table 4. Within the pit (the near surface component of
the resource), no mineralized blocks have an estimated grade of less than 0.4%
(copper equivalent), and no further cut-off grade was applied. Below the pit,
a cut-off grade of 0.7% (copper equivalent) was applied to define an
underground component of the Mineral Resource. This cut-off was estimated
using the same parameters in Table 4, but assuming 20% dilution and an
underground mining production cost of US$20 per tonne.
Table 4: Economic parameters for pit shell
------------------------------------------

Parameters                                    Units    Amount
----------                                    -----    ------

Geotechnical
------------

- Moraine slope                               Deg         30

- Bedrock slope                               Deg         45

Mining factors
--------------

- Dilution (at 0 grade)                        %           5

- Recovery                                     %          95

Processing
----------

- Copper recovery                              %          90

- Silver recovery                              %          90

Operating costs
---------------

- Waste mining cost                        US$/trock    1.20

- Resource mining cost                     US$/trock    1.50

- Incremental mining cost                   US$/1m     0.005

- Reference level                         Z Elevation  1,000

- Processing cost                          US$/tore    10.00

- G&A                                      US$/tore     2.00

- Royalty, selling cost (Cu)                   %         8.0

- Royalty, selling cost (Ag)                   %         6.5

Metal price
-----------

- Copper                                    US$/lb      3.00

- Silver                                    US$/oz     20.00

All Mineral Resources were classified as Inferred, based on the
intersection spacing relative to the interpreted continuity and potential
complexity of the deposit.
Qualified Person
The Company's President and Chief Executive Officer, Dorian L. (Dusty)
Nicol, B.Sc. Geo, MA Geo, a Qualified Person as defined by NI 43-101, has
reviewed and approved the exploration information disclosures contained in
this Press Release.
About Azarga Metals Corp.
Azarga Metals is a mineral exploration and development company that owns
60% of the Unkur Copper-Silver Project in the Zabaikalsky province in eastern
Russia.
AZARGA METALS CORP.
"Dusty Nicol"Dorian L. (Dusty) Nicol, President and CEO
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
Cautionary Statement:This news release contains forward-looking
statements that are based on the Corporation's current expectations and
estimates. Forward-looking statements are frequently characterized by words
such as "plan", "expect", "project", "intend", "believe", "anticipate",
"estimate", "suggest", "indicate" and other similar words or statements that
certain events or conditions "may" or "will" occur. Such forward-looking
statements involve known and unknown risks, uncertainties and other factors
that could cause actual events or results to differ materially from estimated
or anticipated events or results implied or expressed in such forward-looking
statements. Such factors include, among others: the actual results of current
planned exploration activities; conclusions of economic evaluations; changes
in project parameters as plans to continue to be refined; possible variations
in ore grade or recovery rates; accidents, labour disputes and other risks of
the mining industry; delays in obtaining governmental approvals or financing;
and fluctuations in metal prices. There may be other factors that cause
actions, events or results not to be as anticipated, estimated or intended.
Any forward-looking statement speaks only as of the date on which it is made
and, except as may be required by applicable securities laws, the Corporation
disclaims any intent or obligation to update any forward-looking statement,
whether as a result of new information, future events or results or otherwise.
Forward-looking statements are not guarantees of future performance and
accordingly undue reliance should not be put on such statements due to the
inherent uncertainty therein.
SOURCE Azarga Metals Corp.



To view the original version on PR Newswire, visit:
http://www.newswire.ca/en/releases/archive/April2017/04/c7219.html

-0-                           04/04/2017
/For further information: Doris Meyer, at +1 604 536-2711 ext 6, or visit
www.azargametals.com./
/Web Site: https://www.azargametals.com/ /
(AZR.)

CO:  Azarga Metals Corp.
ST:  British Columbia
IN:  MIN MNG
SU:

-30-