Source	Marketwire
Date	04/04/2017
Time	07:00:49 AM

Company	 SAGE GOLD INC.
Title	Sage Gold Drills 5.1 Meters of 1.17 g/t Gold, 190.5 g/t Silver, 0.56% Lead 
and 1.11% Zinc at Onaman





    CDNX Symbol: SGX











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Sage Gold Inc.

TSX VENTURE SYMBOL: SGX

April 4, 2017

Sage Gold Drills 5.1 Meters of 1.17 g/t Gold, 190.5 g/t Silver, 0.56% Lead and 
1.11% Zinc at Onaman


TORONTO, ONTARIO--(Marketwired - April 4, 2017) - Sage Gold Inc. (the 
"Company") (TSX VENTURE:SGX) is pleased to announce the completion of its 
recently announced preliminary drilling program at the historical Headway 
deposit located within the Company's Onaman property in northwestern Ontario 
(please see the Company's news release of February 8, 2017). Six holes were 
drilled for a total of 887 meters over a strike length of 640 meters; holes 
varied from 84 to 201 meters in depth at from 45 to 55 degrees. A total of 226 
samples were taken, including blanks, standards and duplicated that were 
inserted into the sample stream in accordance with industry QAQC standards.

Nigel Lees (President and CEO) stated; "Whereas silver, copper, lead and zinc 
results are generally as anticipated, gold results came as something of a 
surprise, ranging from negligible to fractions of a gram for the most part as 
expected in the peripheries of VMS systems and as reflected in the historical 
results, with outliers ranging up to a high of 14.45 grams per ton ("g/t") in 
hole SG17H01 (87.82-88.21 meters, 0.39 meters drill width, 0.33 meters true 
width). This sample also ran 1,665 g/t silver (53.5 ounces per tonne), 0.15% 
copper, 5.54% lead and 6.89% zinc, within a 5.4 meter (true width) continuously 
mineralized interval running a composite average of 1.17 g/t gold, 190.5 g/t 
silver, 0.56% lead and 1.11% zinc."

Other notable intercepts include the following:

/T/

WIDTH
(TRUE)
HOLE              FROM        TO    meters  GOLD g/t
SG17H01          78.00     79.00      0.90      0.80
"                83.00     89.00      5.40      1.17
including        87.82     88.21      0.33     14.45
SG17H02          31.80     35.00      3.01      0.27
"               148.30    148.90      0.49      2.61
SG17H03          80.86    109.00     23.05      0.26
"               170.00    174.38      3.72      0.41
SG17H04          18.10     19.00      0.74      0.58
"                36.10     37.50      1.21      0.48
"                61.00     71.00       9.1      0.17
SG17H05         115.20    123.00      7.07      0.07
SG17H06          69.00     70.62      1.36      0.14

HOLE         SILVER g/t COPPER ppm    LEAD %    ZINC %
SG17H01             462       1395      3.66      2.98
"                   180         21      0.56      1.11
including          1665       1500      5.54      6.89
SG17H02              11       1325      0.19      2.31
"                    16        304      0.27      0.63
SG17H03           29.20     650.56      0.53      1.61
"                 30.31    2645.68      0.05      2.60
SG17H04            98.3       1260      3.77      5.55
"                    37        410      1.49      4.04
"                 12.70      138.9      0.24      1.46
SG17H05            9.46     348.58      0.12      1.15
SG17H06          100.40     301.36      0.43      1.77

/T/

As conveyed in the Company's previous news release: "Sage geologists believe 
that this zone may be near a zone of focused hydrothermal discharge and 
associated metal concentration, and that the lithological, alteration, 
mineralogical and geochemical data derived from detailed analyses of fresh 
drill core may provide critical clues enabling them to vector in on previously 
undetected VMS targets in the immediate area." The program has proven very 
successful in this regard, particularly given the previously unknown presence 
of gold in the system.

Last drilled between 1949-1952 by Headvue Mines Ltd. along with a half dozen 
holes drilled by Noranda in 1974, the Company's recent drilling program has 
confirmed the presence of fairly persistent base and precious metal 
mineralization within intensely hydrothermally altered and tectonized, mostly 
mafic volcanic rocks and their derivatives over the entire strike length 
tested, often including several mineralized intervals within individual holes. 
Similar to historical results, many mineralized intervals range from under 1, 
up to 2 meters in true thickness, with a smaller number ranging up to and in 
excess of 20 meters in true thickness. Base and precious metal values and 
ratios vary considerably in both. Some of the intervals are suggestive of 
sheared stringer-type VMS mineralization, whereas others appear too thick and 
too massive and are thus more suggestive of more proximal VMS mineralization, 
that which is of primary interest and significance. Overall, the impression is 
that of being on the edge of or near one or more VMS lenses.

The Onaman VMS system is large in scale, long-lived and complex as evidenced by 
several, related mineralized zones of different ages and metal composition, and 
several generations of widespread and often intense hydrothermal 
mineralization. This complexity is amplified by several structural events 
including shearing, which complicates the understanding of the time-space 
relationships integral to VMS deposits and their zonation. It is the 
interpretation of all the lithological and multi-element data provided by this 
new core that will provide Sage geologists with vital information leading to 
the delineation of new, step-out drill targets. This is the current focus of 
Sage's Onaman exploration team.

The Company will provide additional information and updates regarding its 
progress at the Onaman on a timely basis.

Update on Clavos Surface Drilling

Drilling at the Clavos property continues. Sage has completed 7 holes in the 
"Gap" area between the 960 zone and the main mine zone. Sage has also completed 
one of two holes on the western side of the mine zone with the aim of 
increasing the resource in the upper part of the mine. Assay results are 
forthcoming for both the Gap and western drilling and will be released on a 
timely basis.

The technical content of this news release has been reviewed and approved by 
Sage's consulting geologist, Avrom E. Howard, MSc, PGeo, who is a Qualified 
Person ("QP") as defined in National Instrument 43-101.

About Sage Gold

The Company is a mineral exploration and development company which has primary 
interests in near-term production and exploration properties in Ontario Its 
main properties are the Clavos Gold property in Timmins and the 100% owned Lynx 
copper, gold, silver property and other exploration properties in the 
Beardmore-Geraldton Gold Camp. Technical reports and information relating to 
the properties can be obtained from the System for Electronic Document Analysis 
and Retrieval (SEDAR) website at www.sedar.com and www.sagegoldinc.com.

Sage currently plans to complete a reserve estimate and a pre-feasibility study 
on the Clavos property. In the event that a production decision is made that is 
not based on a feasibility study of mineral reserves demonstrating economic and 
technical viability prepared in accordance with National Instrument 43-101, 
readers are cautioned that there is increased uncertainty and higher risk of 
economic and technical failure associated with such a production decision.

CAUTIONARY STATEMENT: Neither the TSX Venture Exchange nor its Regulation 
Services Provider (as that term is defined in the policies of the TSX Venture 
Exchange) accepts responsibility for the adequacy or accuracy of this release. 
This news release may contain forward looking information and the Company 
cautions readers that forward looking information is based on certain 
assumptions and risk factors that could cause actual results to differ 
materially from the expectations of the Company included in this news release. 
This news release includes certain "forward-looking statements", which often, 
but not always, can be identified by the use of words such as "believes", 
"anticipates", "expects", "estimates", "may", "could", "would", "will", or 
"plan". These statements are based on information currently available to the 
Company and the Company provides no assurance that actual results will meet 
management's expectations. Forward-looking statements include estimates and 
statements with respect to the Company's future plans, objectives or goals, to 
the effect that the Company or management expects a stated condition or result 
to occur. Since forward-looking statements are based on assumptions and address 
future events and conditions, by their very nature they involve inherent risks 
and uncertainties. Actual results relating to, among other things, results of 
exploration, metallurgical processing, project development, reclamation and 
capital costs of the Company's mineral properties, and the Company's financial 
condition and prospects, could differ materially from those currently 
anticipated in such statements for many reasons such as, but are not limited 
to: failure to identify mineral resources; failure to convert estimated mineral 
resources to reserves; the preliminary nature of metallurgical test results; 
delays in obtaining or failures to obtain required governmental, environmental 
or other project approvals; political risks; uncertainties relating to the 
availability and costs of financing needed in the future; changes in equity 
markets, inflation, changes in exchange rates; fluctuations in commodity 
prices; delays in the development of projects; capital and operating costs 
varying significantly from estimates and the other risks involved in the 
mineral exploration and development industry; and those risks set out in the 
Company's public documents filed on SEDAR. This list is not exhaustive of the 
factors that may affect any of the Company's forward-looking statements.

These and other factors should be considered carefully and readers should not 
place undue reliance on the Company's forward-looking statements. Although the 
Company believes that the assumptions and factors used in preparing the 
forward-looking information in this news release are reasonable, undue reliance 
should not be placed on such information, which only applies as of the date of 
this news release, and no assurance can be given that such events will occur in 
the disclosed time frames or at all. The Company disclaims any intention or 
obligation to update or revise any forward-looking information, whether as a 
result of new information, future events or otherwise, other than as required 
by law.

- 30 -

CONTACT INFO:

Nigel Lees
President and CEO
416-204-3170
nlees@sagegoldinc.com
www.sagegoldinc.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=590858634