Source	MARKET NEWS
Date	04/05/2017
Time	02:26:36 PM

Company	 Search Minerals Inc.
Title	Achieves 
High Rare Earth Element Extraction From





    CDNX Symbol: SMY











Press Release





SEARCH MINERALS INC ("SMY-V;SHCMF-0")
- Achieves High Rare Earth Element Extraction From Deep Fox
- Mineral Sample

Search Minerals Inc. ("Search" or the "Company") is pleased to
announce the results from a bench-top demonstration test on a Deep Fox
mineral sample using the Search Minerals Direct Extraction Process. The
test was completed at SGS Laboratories in Lakefield, Ontario.

The Deep Fox sample (a surface channel sample) containing 1.59%
TREE including 2,470 g/t Neodymium (Nd), 697 g/t Praseodymium (Pr) and
306 g/t Dysprosium (Dy) was crushed to pass 10 mesh in particle size.
The sample was mixed with sulfuric acid and heated at 190 C for 8 hours
before water leaching for 36 hours at 90 C.

At the end of the water leach, the remaining solids were filtered
and washed. The washed solids, the leachate and the wash solution were
then analyzed.

Test Highlights:

//st

Deep Fox extractions of 90.8% Nd, 90.5% Pr, 81.3% Dy and 82.5%
Terbium (Tb) - (complete extractions shown below in Table 1 below).

The extractions from Deep Fox compare favourably with the extractions from
the Foxtrot recent pilot plant sample of 85% for Nd, 86% for Pr, 68% for Dy
and 71% for Tb, (See Search News Release-October 15, 2015 - Search Minerals
announces expansion of the Deepwater Fox "Critical REE" prospect in the
Port Hope Simpson REE District).

The Deep Fox surface channel sample was approximately 1.65 times higher in
TREE grade compared to the Foxtrot Pilot Plant sample.

//et

Greg Andrews, Search President and CEO states: "We are very
encouraged by these high extraction results from our Deep Fox channel
samples. The metallurgical process refined and verified at pilot plant
scale for our Foxtrot material has, during this bench scale testing,
performed even better with the Deep Fox material. Deep Fox channel
grades are up to 15% higher than those at Foxtrot along a similar
strike length. A primary objective noted in our recently announced
decision to raise $3 million through private placement is to validate
our Port Hope Simpson Critical Rare Earth District concept by drilling
Deep Fox. Obviously, these recovery rates provide an additional
incentive to drill this prospect."

Andrews added: "Search continues to optimize the extraction
recoveries of the key rare earth elements which are crucial for the
permanent magnet market. These elements include: Neodymium,
Praseodymium, Dysprosium, and Terbium. All these elements are
forecasted to be in short supply due to rapidly growing demand for
renewable power generation, electric mobility, and energy-efficient
technologies."

Table 1. Extractions of Rare Earth Elements from the Deep Fox
Sample

//st
Element                                            %
La                                              88.5
Ce                                              90.4
Pr                                              90.5
Nd                                              90.8
Sm                                              89.0
Eu                                              87.8
Gd                                              86.9
Tb                                              82.5
Dy                                              81.3
Ho                                              79.7
Y                                               79.9
Er                                              78.7
Tm                                              71.8
Yb                                              68.5
Lu                                              61.4

//et

Qualified Person:

Dr. David Dreisinger, Ph.D., P.Eng., is the Company's Vice
President, Metallurgy and Qualified Person for the purposes of National
Instrument 43-101 - Standards of Disclosure for Mineral Projects. Dr.
Dreisinger has reviewed and approved the technical disclosure contained
in this news release as applicable. The Company will endeavour to meet
high standards of integrity, transparency, and consistency in reporting
technical content, including geological and assay (e.g., REE) data.

About Search Minerals Inc.

Led by a proven management team and board of directors, Search is
focused on finding and developing resources within the emerging Port
Hope Simpson Critical Rare Earth Element ("CREE") District of South
East Labrador (the "District"). The Company controls a belt 70 km long
and 8 km wide including its 100% interest in the FOXTROT Project which
is road accessible and at tidewater. Exploration efforts have advanced
"Deep Fox" and "Fox Meadow" as significant new CREE prospects very
similar and in close proximity to the original FOXTROT discovery. While
the Company has identified more than 20 other prospects in the
District, its primary objective remains development of FOXTROT with the
clearly demonstrated success of the proprietary processing technology
at the pilot plant level and delineation of prospects that will ensure
competitive-low cost production beyond the 14-year mine life
contemplated in the preliminary economic assessment of FOXTROT
completed in April 2016. The FOXTROT Project has a low capital cost to
bring the initial project into production ($152 M), a short payback
period and is scalable due to Search's proprietary processing
technology. The preliminary economic assessment is preliminary in
nature and includes inferred mineral resources that are considered too
speculative geologically to have the economic considerations applied to
them that would enable them to be categorized as mineral reserves, and
there is no certainty that the preliminary economic assessment will be
realized. The preliminary economic assessment includes the results of
an economic analysis of mineral resources. Mineral resources are not
mineral reserves and do not have demonstrated economic viability.

All material information on the Company may be found on its
website at www.searchminerals.ca and on SEDAR at www.sedar.com

About neo-CREOs (Adamas Intelligence - December 2016)

We consider neodymium, praseodymium, and dysprosium to be
neo-CREOs and they are vital to NdFeB magnets used widely in renewable
power generation, electric mobility, and energy-efficient technologies.
We consider terbium to be a neo-CREO because upon experiencing
shortages of dysprosium, consumers in the magnet industry will rapidly
consume available terbium supplies in its place for applications
involving renewable power generation, electric mobility and energy
efficient technologies. Lanthanum is considered a neo-CREO because it
is widely used in catalytic converters and rechargeable batteries, and
will be increasingly used as a thermal stabilizer by producers of
poly-vinyl chloride (PVC) to minimize lead consumption and improve the
energy efficiency of PVC and other processing equipment.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

Cautionary Statement Regarding "Forward-Looking" Information.

This news release includes certain "forward-looking information"
and "forward-looking statements" (collectively "forward-looking
statements") within the meaning of applicable Canadian and United
States securities legislation including the United States Private
Securities Litigation Reform Act of 1995. All statements, other than
statements of historical fact, included herein, without limitation,
statements relating the future operating or financial performance of
the Company, are forward-looking statements.

Forward-looking statements are frequently, but not always,
identified by words such as "expects", "anticipates", "believes",
"intends", "estimates", "forecasts", "potential", "possible", and
similar expressions, or statements that events, conditions, or results
"will", "may", "could" or "should" occur or be achieved.
Forward-looking statements in this news release relate to, among other
things, forecasts of supplies of elements including Neodymium,
Praseodymium, Dysprosium and Terbium; the Company's plans to endeavour
to meet high standards in its technical reporting; the low costs of
production at FOXTROT; future consumption rates of consumers in the
magnet industry; and future increases in the use of Lanthanum as a
thermal stabilizer by producers of poly-vinyl chloride. Actual future
results may differ materially. There can be no assurance that such
statements will prove to be accurate, and actual results and future
events could differ materially from those anticipated in such
statements. Forward-looking statements reflect the beliefs, opinions
and projections on the date the statements are made and are based upon
a number of assumptions and estimates that, while considered reasonable
by the respective parties, are inherently subject to significant
business, economic, competitive, political and social uncertainties and
contingencies. Many factors, both known and unknown, could cause actual
results, performance or achievements to be materially different from
the results, performance or achievements that are or may be expressed
or implied by such forward-looking statements and the parties have made
assumptions and estimates based on or related to many of these factors.
Such factors include, without limitation, general business, economic
and social uncertainties; litigation, legislative, environmental and
other judicial, regulatory, political and competitive developments; and
those additional risks set out in Search's public documents filed on
SEDAR at www.sedar.com. Although Search believes that the assumptions
and factors used in preparing the forward-looking statements are
reasonable, undue reliance should not be placed on these statements,
which only apply as of the date of this news release and no assurance
can be given that such events will occur in the disclosed time frames
or at all. Except where required by law, Search disclaims any intention
or obligation to update or revise any forward-looking statement,
whether as a result of new information, future events, or otherwise.




Search Minerals Inc.
Greg Andrews
President and CEO
604 998-3432 Ext 2
info@searchminerals.ca

Paul Snow
Investor Relations
709 753-0794
psnow@pilotcom.ca
______________________________
_______________________________________________
TSX Venture closing price for SMY-V
Date: 2017/04/04
Closing Price: 0.07
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1709400070TS11709402106-14235320170405