Source	MARKET NEWS
Date	04/06/2017
Time	09:38:42 AM

Company	 Algold Resources Ltd.
Title	Eleonore 
Mineralization Extended to 150 Meters A





    CDNX Symbol: ALG











Press Release





ALGOLD RESOURCES LTD ("ALG-V;ALGDF-0")
- Eleonore Mineralization Extended to 150 Meters At-Depth -
- Results Continue to Demonstrate

ALGOLD RESOURCES LTD. (the "Corporation") announced preliminary
assay results from its Phase III 20,000-meter drilling campaign carried
out on its Tijirit property ("Tijirit") in Mauritania. Results continue
to demonstrate the high-grade nature of the Eleonore zone, with the
mineralization now extending to a vertical depth of up to 150 meters.

Highlights

//st

Hole T17RC031 (Eleonore Central) - 4 m @ 10.2 g/t Au, a new
mineralized horizon on section S9000.

Hole T17RC032 (Eleonore Central) - 10 m @ 3.19 g/t Au, including 4 m
@ 7.1 g/t Au, situated on section 9080, 28 meters down dip from hole
T16RC121, which intersected 2.02 g/t Au over 1 m (Figure 1).

Hole T17RC013 (Eleonore South) - 3 m @ 7.69 g/t Au, including 1 m @
20.2 g/t Au, hit the main mineralized quartz vein at a vertical depth of
150 meters, thus demonstrating the continuity of this high-grade
mineralized vein at depth in the southern section of Eleonore.

Hole T17RC036 (Eleonore South) - 4 m @ 6.86 g/t Au, situated on
section E7830, 40 meters south of hole T16RC027 (24.4 g/t Au over 6 m) and
50 meters north of hole T16RC133 (2.79 g/t Au over 3 m) (Figure 2).

//et

The results from Eleonore South and Eleonore Central further
validate the continuity of the multiple mineralized structures and
associated gold-bearing quartz veins propagating along regional
structures, and the associated splays identified to date. The
mineralization is associated with pyrite, and to a lesser extent
pyrrhotite and galena within biotite-rich shear zones.

Eleonore Central results are consistent with those from previous
mineralized intersections drilled in 2016 as publish. Results also
demonstrate the strike extension of the high-grade gold mineralized
structure over more than 600 meters at surface and at the 50-meter
vertical level. Drilling to test the 150-meter and 200-meter levels is
ongoing.

On Eleonore South, new results confirm the continuity of the two
sub-parallel gold structures trending north south, which appear offset
in the middle of the zone and then tilt to the northeast, further
delineating an economic gold horizon that stretches over 1.2
kilometers.

The Phase III 20,000-meter reverse-circulation ("RC") and 5,000
meters diamond-drill ("DDH") drilling program was initiated on February
1, 2017 with the objective to further delineate the high-grade gold
deposit. As of March 31, 2017, some 75 RC holes, 11 diamond and 8 RC
pre-collar/diamond tails were completed for 8,749 meters of RC and
2,215 meters of diamond drilling.
Results from Phase III drilling presented in this press release
represent approximately 50% of total drill samples sent to the SGS
Bamako lab facility in February and March 2017. More assay results from
deeper intersections are expected in the coming weeks. Results from
Eleonore North are expected later in the quarter. Algold anticipates
filing an updated National Instrument 43-101 resources estimate by the
end of April 2017.

//st
Table 1: New Assay Result Highlights - Phase III Drilling Program
//et

//st
Vertical Average
Hole Prospect      East   North From  To  Depth* Grade** Width***
ID                  UTM     UTM    m   m     (m)(g/t Au)    (m)
Comments
T17RC034
Eleonore North   482387 2250457  112 114   86.6      3.95    2

T17RC031
Eleonore Central 482179 2249756   62  66   49.0     10.20    4

T17RC032
Eleonore Central 482220 2249827   39  49   33.7      3.19   10
Including 4m @ 7.1g/t Au

T17RC053
Eleonore Central 482354 2249829   84  88   65.9      4.28    4

T17RC013
Eleonore South   481830 2248751  182 184  140.2      1.86    2
197 200  152.1      7.69    3
Including 1m @ 20.2 g/t Au

T17RC036
Eleonore South   481598 2248685   78  82   61.3      6.86    4
*Vertical depth of intersection
below RL collar.
**Weighted average grade,
composite based on
a minimum grade of
0.3 g/t Au with an
internal dilution
of 0.005 g/t Au over
2 m & an edge grade
of 0.25 g/t Au permitted.
***Down-hole length
(believed to be close
to true width)
No capping of higher
values has been applied.
Note: Complete assay
results are available
on Algold's website
(www.algold.com)
//et

Detailed geological descriptions of all mineralized zones can be
found on Algold's website (www.algold.com) and on SEDAR (www.sedar.com)
in the report entitled "Algold 43-101 Technical Report: Tijirit Maiden
Mineral Resources Estimates for the Tijirit Gold Project in
Mauritania".

Quality Assurance / Quality Control (QA/QC)
Analytical work for drill core and chips, geochemical samples and
rock chip samples is being carried out at the independent SGS
Laboratories Ltd. in Bamako, Mali.  The 50 g fire assay with ASS finish
analytical services are accredited by SANAS and are carried out with a
quality assurance protocol in line with ISO 17025:2005. Samples are
stored at the Corporation's field camps and put into sealed bags until
delivered by a geologist on behalf of Algold to the laboratory in
Bamako, Mali, where samples are prepared and analyzed. Until the end of
2016, samples were analyzed at ALS's facility in Loughrea, Ireland.
Beginning in 2017, samples are analyzed at SGS Laboratory, Bamako.
Samples are logged in the tracking system, weighed, dried and finely
crushed to better than 70%, passing a 2 mm (Tyler 9 mesh, US Std.
No.10) screen. A split of up to 1,000 g is taken and pulverized to
better than 85%, passing a 75-micron (Tyler 200 mesh) screen, and a
50-gram split is analyzed by fire assay with an AA finish. Anomalous
samples greater than 5 g/t Au are re-analyzed by 50 g fire assay with
gravimetric finish.  Selected samples may be re-analyzed using a 1 kg
cyanide leach (Bottle Roll) using "LeachWELL" or the 1 kg screen fire
assay method.  Blanks, duplicates and certified reference material
(standards) are inserted to monitor laboratory performance during the
analysis.

This press release has been reviewed for accuracy and compliance
under National Instrument 43-101 by Andre Ciesielski, DSc., PGeo.,
Algold Resources Ltd Lead Consulting Geologist and Qualified Person,
and Alastair Gallaugher, C.Geo. (Chartered Geologist and Fellow of the
Geological Society of London), BSc. Geology, Algold's Exploration
Manager in Mauritania, Qualified Persons as defined by NI 43-101
Standards of Disclosure for Mineral Projects. Andre Ciesielski has
further approved the scientific and technical disclosure in the news
release.

ABOUT ALGOLD
Algold Resources Ltd is focused on the exploration and development
of gold deposits in West Africa. The board of directors and management
team are seasoned resource industry professionals with extensive
experience in the exploration and development of world-class gold
projects in Africa.

Algold is the operator of all of its exploration licenses in
Mauritania. Algold owns 100% of Tijirit, which represents an area of
more than 1,000 km2, situated approximately 25 kilometers southeast of
the Tasiast gold mine as well as the Akjout properties, which were
acquired from Gryphon Minerals (Australia) through a transaction
completed earlier in 2016. Exploration is being carried out on the
Eleonore, Sophie I, Sophie II-III and Lily zones. The Kneivissat
property is 90% owned by Algold and the Legouessi property is being
managed through a 51% earn-in interest agreement with Caracal Gold LLC.
Algold can earn up to a 90% interest in the Legouessi exploration
permit (reference Algold's press release dated October 10, 2013 for
more details), however, Caracal has the right to participate in the
joint venture at either 51% or 75% by funding its share of
expenditures.

CAUTIONARY LANGUAGE REGARDING FORWARD-LOOKING INFORMATION
This press release contains and refers to forward-looking
information based on current expectations. All other statements other
than statements of historical fact included in this release are
forward-looking statements (or forward-looking information). The
Corporation's plans involve various estimates and assumptions and its
business is subject to various risks and uncertainties. For more
details on these estimates, assumptions, risks and uncertainties, see
the Corporation's most recent Annual Information Form and most recent
Management Discussion and Analysis on file with the Canadian provincial
securities regulatory authorities on SEDAR at www.sedar.com. These
forward-looking statements are made as of the date hereof and there can
be no assurance that such statements will prove to be accurate.
Forward-looking statements are subject to significant risks and
uncertainties, and actual results and future events could differ
materially from those anticipated in such statements. Accordingly,
readers should not place undue reliance on forward-looking statements
that are included herein, except in accordance with applicable
securities laws.

SOURCE Algold Resources Ltd.

For further information:  Algold Resources Ltd., 1320, boul. Graham, bureau
132, Mont-Royal, Quebec, H3P 3C8, www.algold.com; Francois Auclair M.Sc.,
PGeo, President & Chief Executive Officer, f.auclair@algold.com, +1 (514)
889 5089; Alex Ball, Executive VP, Finance and Corporate Development,
a.ball@algold,com, +1 (647) 919 2227
______________________________
_______________________________________________
TSX Venture closing price for ALG-V
Date: 2017/04/05
Closing Price: 0.25
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1709500036TS11709501768-09370120170406