Source	MARKET NEWS
Date	04/20/2017
Time	11:04:51 AM

Company	 International Lithium Corp.
Title	Files Technical Report with Indicated Resource E





    CDNX Symbol: ILC











Press Release




[200/News Release]ILCVINTERNATIONAL LITHIUM CORPAPR 20 2017  11:02 AM
Files Technical Report with Indicated Resource Estimate of 1.25Million Tonnes 
LCE at the Mariana Lithium Brine Project, Argentina --->@NEWS RELEASE
INTERNATIONAL LITHIUM CORP ("ILC-V;ILHMF-0")
- Files Technical Report with Indicated Resource Estimate of 1.25
- Million Tonnes LCE at the Mariana Lithium Brine Project, Argentina

International Lithium Corp. (the "Company" or "ILC") is pleased to
announce, with strategic partner Ganfeng Lithium Co. Ltd., ("GFL") and
together the "Companies," the filing of a technical report that
contains a maiden resource estimate for the Mariana lithium brine
project (the "Project") located in Salta, Argentina.

Summary
Further to the Company's news release dated March 8, 2017, ILC has
filed a technical report for the Mariana lithium brine project
containing a maiden resource estimate for the project. ILC requested
Geos Mining Minerals Consultants ("Geos"), based in Sydney, Australia,
to prepare an independent lithium brine resource estimate for the
Companies' Mariana lithium brine deposit in Argentina, and, with Geos
consent, ILC prepared a technical report in accordance with National
Instrument 43-101 - Standards of Disclosure for Mineral Projects (the
"Technical Report").

The Technical Report, entitled, "Technical Report; Mariana Lithium
Project, Salar de Llullaillaco, Argentina," and dated April 10, 2017,
is now available under the Company's profile at www.SEDAR.com. The
effective date for the resource estimate is January 20, 2017, which
represents the date of the most recent data that supports the brine
estimate in the Technical Report.

Report Highlights - Mariana Lithium Brine Project, Argentina

The following highlights taken from the Technical Report, and set
out below, should be considered in the context of the detailed
information given there.

*  Indicated resource contains an estimated 1,248,000 tonnes of
lithium carbonate equivalent (LCE), previously reported with at a 60%
recovery rate to be 747,000 tonnes LCE, which is now calculated as
749,000 tonnes of LCE.
*  Inferred resource contains an estimated 618,000 tonnes of LCE.
*  The indicated resource is estimated at 765 billion litres of
brine grading 306 mg/L lithium ("Li") and 9,457 mg/L potassium ("K").
*  The inferred resource is estimated at 361 billion litres of
brine grading 322 mg/L lithium ("Li") and 10,316 mg/L potassium ("K").
*  Brine resources are tabulated and reported for average specific
yield (SY) of 15% and a cut-off value of 230 mg/L Li. Effective date
for this resource estimate is January 20, 2017.

The preliminary estimates for lithium brine are in the upper end
of the Companies' expectations.

Further Report Details

ILC has completed four drilling campaigns on the Project since
2009: 7 reverse circulation (RC) holes and 16 cored holes. A total of
2,880 m were drilled on the Project during the last 10 months. A final
campaign hole, MA16-24, was in-process as at the effective date of the
Technical Report. Geophysical surveys were conducted downhole for the
completed drill holes, using an electrical probe. Resistivity and
spontaneous potential were measured. As part of a bulk extraction of
lithium from brine bulk testwork undertaken in 2015 a pumping well,
MA15-09-PW, and 2 monitoring wells, MA15-08-MW, MA15-10-MW, were
drilled and constructed. Drill hole MA12-07 was used as a third
monitoring well. The drilling and hydrogeological data indicates that
the Mariana Project at Salar de Llullaillaco is a brine-bearing
sedimentary filled basin complex with unconfined interconnected aquifer
to considerable depth of 328m and possibly deeper. Based on the
preliminary drill information, eight lithological classes were
identified in the drill hole cores, shown in the west, east, and
southern extents of the basin. The aquifer volume is still open at
depth in the majority of the salar, since only two drill holes (MA16-23
and MA16-18) potentially intercepted suspected basement Oligocene to
Pliocene volcanic lithologies.

Brine deposits are unlike the majority of mineral deposits in that
they are fluid. Fluids within a brine deposit can move, and can mix
with adjacent fluids when exploitation of a brine deposit begins.
Evaluation of such deposits therefore requires special considerations
that are not, in general, applied to other style of mineral deposits.

The assessment of brine deposit has been limited to defining
mineral resources at different levels of certainty, varying from
Indicated Resource to Exploration Target, based on the certainty
provided by the data collected during fieldwork. Levels of assessment,
as linked to data certainty are listed below, covering those areas that
fall within the Project tenements only.

Brine resources are tabulated and reported for average specific
yield (SY) of 15% and use a cut-off value of 230 mg/L Li in Table 1.

Table 1: Total indicated and total inferred resource estimates.

//st

Effective  Brine    Li   B  K mg/L  SO42-  Mg     HCO3- Li  LCE#
Volume M Density  mg/L mg/L         mg/L   mg/L   mg/L  K t K t
m3  g/mL

Category
Indicated
766   1.218   306  599 9,456   15,530  4,291 529   234 1,248

Inferred
361   1.222   322  642 10,316  15,315  4,566 535   116 618

//et

The Indicated Resource of 766 Mm)3 at a grade of 306 mg/L Li
equates to 234Kt of lithium as Li ion. Upon conversion of Li to lithium
carbonate (Li(sub)2(/sub)CO(sub)3(/sub)) using a conversion factor of
5.324, gives an equivalent of approximately 1.3 Mt of
Li(sub)2(/sub)CO(sub)3(/sub). However, using a conservative 60%
estimated total recovery return from processing gives a conservative
estimate of 749 Kt of Li(sub)2(/sub)CO(sub)3(/sub) equivalent (LCE).

In preparing this resource estimates, Geos considered and applied
processes to be appropriate for brine style deposits, using the
principles set out in National Instrument 43-101 ("NI 43-101"), Joint
Ore Resources Code JORC (2012) for mineral projects, and CIM Best
Practice Guidelines for Resource and Reserve Estimation for Lithium
Brines.

The Company cautions the reader that no economic studies have been
carried out on the Project. Mineral resources are not mineral reserves
as defined by the Canadian Institute of Mining and Metallurgy, and the
Company cannot guarantee that the resources reported here will be
converted to mineral reserves.

The initial brine resource estimate for the Project is based on
limited knowledge of the geometry of individual aquifer units between
broadly spaced drill holes, and the variation in porosity and brine
grade within these aquifers. Specific yield values are based on
porosity test results from a restricted sample population and compared
with data from analogous salars in the region and technical references.
In order to assess the recoverable brine resource with a higher level
of confidence, further information on the permeability and flow regime
in the aquifer, and watershed basin water balance are necessary.

Conclusions and Recommendations from the Report

The project is moving forward from early stage exploration to
advanced exploration. Work on the following tasks is currently underway
and was originally scheduled to be completed by the end of 2017:

(ol)     *  Detailed pump test;
*  Construction of evaporation ponds;
*  Water balance studies;
*  Transportation studies;
*  Environmental baseline and archaeological study; and
*  Preliminary feasibility study.

Updating of the mineral resources estimated in the Technical
report is another recommendation which will help to support the
preliminary feasibility study. This work will include further
exploration to bring the remaining inferred resource to indicated
stage, and indicated resource to measured resource.

Kirill Klip, Executive Chairman of ILC, stated, "We are very
pleased with the results of the maiden resource estimation at the
Mariana lithium potash brine project, together with our strategic
partner Ganfeng Lithium. This project is now moving from an early
exploration stage to an advanced exploration stage, where it will be
more easily compared to other lithium brine projects in Argentina. We
are looking forward to follow up with Ganfeng Lithium on the
recommendations of this report in order to ensure the rapid advancement
of the project towards the pilot stage and to conduct further
feasibility studies that will investigate the economic viability of the
Mariana project."

The following Qualified Person (QP's) are responsible for
preparation of the Report:

*  Llyle Sawyer, Senior Consultant, Geos Mining;
*  Oliver Willetts, Senior Resource Geologist, Geos Mining; and
*  Afzaal Pirzada, M.Sc., P.Geo.

Llyle Sawyer is a senior geological consultant with over 20 years
of experience in geology, mineral exploration, mineral resource
estimation, and mineral project assessment. He is a Registered
Professional and is currently a Member of the Australia Institute of
Geoscientists (member number 3512). Llyle Sawyer is an independent
technical consultant contracted by Geos Mining and has worked on
similar lithium brine salar deposits in Argentina and other brine style
deposits within Australia. He has the required level of experience and
expertise to qualify as a Qualified Person (QP) as defined in the
National Instrument 43-101 - Standards of Disclosure for Mineral
Projects, Form 43-101F1 Technical Report and related consequential
amendments.

Mr. Sawyer is independent of Litio Minera Argentina S.A. (and
International Lithium Corp.) as independence is described by Section
1.4 of NI 43-101. He has visited the Mariana Project on 4 occasions
during drilling operations since May 2016. Mr. Sawyer has been involved
with the Project since August 2010 in the form of ongoing advice upon
request, discussion of exploration programs and during preparation of
the brine resource estimate and the Report.

Geos Mining is an independent consulting firm recognized for
providing expertise in geological, mineral exploration, resource
modelling, and mining advice; as specialists in the fields of geology,
exploration, mineral resource and mineral reserve estimation and
classification, and project valuation. Litio Minera Argentina S. A.
(the joint venture company formed by the Companies to advance the
Mariana project in Argentina, "LMA") have continued to engage Geos
Mining to prepare this independent preliminary resource report for the
Project.

Oliver Willetts is a senior resource geologist with over 9 years
of experience in geology, mineral exploration, mineral resource
estimation and mineral project assessment. He is a Registered
Professional and is currently a Member of the Australasian Institute of
Mining and Metallurgy (member number 312940). Mr. Willetts is an
independent technical consultant contracted by Geos Mining and has
worked on resource estimation for a variety of minerals (phosphate,
potash (from brines), gold, coal, base metals) within Australia,
Africa, and South America.

Afzaal Pirzada, Geological Consultant of the Company, and a
"Qualified Person" for the purposes of National Instrument 43-101 -
Standards of Disclosure for Mineral Projects, has reviewed and approved
the scientific and technical information contained in this news
release.

About International Lithium Corp.

International Lithium Corp. has a significant portfolio of
projects, strong management, robust financial support, and a strategic
partner and keystone investor, Ganfeng Lithium Co. Ltd., a leading
China-based lithium product manufacturer.

The Company's primary focus is the strategic stake in the Mariana
lithium-potash brine project located within the renowned South American
"Lithium Belt" that is the host to the vast majority of global lithium
resources, reserves and production. The Mariana project, strategically
encompasses an entire mineral rich evaporite basin, totalling 160
square kilometres, that ranks as one of the more prospective salars or
'salt lakes' in the region. Current ownership of the project is through
a joint venture company, Litio Minera Argentina S. A., a private
company registered in Argentina, owned 80% by Ganfeng Lithium Co. Ltd.
("GFL"), and 20% by ILC. In addition, ILC has an option to acquire 10%
in the Mariana project through a back-in right.

Complementing the Company's lithium brine project are three rare
metals pegmatite properties in Canada known as the Mavis, Raleigh, and
Forgan projects, and the Avalonia project in Ireland, which encompasses
an extensive 50km-long pegmatite belt. The Avalonia project is under
option to strategic partner GFL, that currently owns 55% of the
project. The Mavis and Raleigh projects are under option to strategic
partner Pioneer Resources Limited (ASX:PIO) pursuant to which Pioneer
can acquire up to a 51% interest in the projects.

The Mavis, Raleigh and Forgan projects together form the basis of
the Company's newly created Upper Canada Lithium Pool designated to
focus on acquiring numerous prospects with previously reported high
concentrations of lithium in close proximity to existing
infrastructure.

With the increasing demand for high tech rechargeable batteries
used in vehicle propulsion technologies and portable electronics,
lithium is paramount to tomorrow's "green-tech," sustainable economy.
By positioning itself with solid strategic partners and acquiring high
quality assets for the Energy rEVolution supply chain, ILC aims to be
the partner of choice for investors in green-tech and to continue to
build value for its shareholders.

On behalf of the Board of Directors,

Kirill Klip Executive Chairman

For further information concerning this news release, please
contact +1 604-700-8912.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

Cautionary Statement Regarding Forward-Looking Information

Except for statements of historical fact, this news release
contains certain "forward-looking information" within the meaning of
applicable securities law. Forward-looking information is frequently
characterized by words such as "plan," "expect," "project," "intend,"
"believe," "anticipate," "estimate," "will," "could," and other similar
words, or statements that certain events or conditions "may" or "could"
occur. Such forward-looking information is based on a number of
assumptions and subject to a variety of risks and uncertainties,
including but not limited to those discussed in the sections entitled
"Forward-Looking Statements" in the interim and annual Management'sDiscussion 
and Analysis which are available at www.sedar.com. While our
management believes that the assumptions made are reasonable, should
one or more of the risks, uncertainties or other factors materialize,
or should underlying assumptions prove incorrect, actual results may
vary materially from those described in forward-looking information.
Forward-looking information herein, and all subsequent written and oral
forward-looking information are based on estimates and opinions of
management on the dates they are made and are expressly qualified in
their entirety by this cautionary statement. Except as required by law,
the Company assumes no obligation to update forward-looking information
should circumstances or management's estimates or opinions change.

TSX Venture closing price for ILC-V
Date: 2017/04/19
Closing Price: 0.13

TEL: 604-687-7551    INTERNATIONAL LITHIUM CORP
FAX: 604-687-4670
E-mail: info@internationallithium.com
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1710900033TS11710902300-11022420170420