Source	MARKET NEWS
Date	04/26/2018
Time	05:30:55 AM

Company	 Alliance Mining Corp.
Title	Drilling 
Complete On Packsack Property, Bisset,





    CDNX Symbol: ALM











Press Release





ALLIANCE MINING CORP ("ALM-V")
- Drilling Complete On Packsack Property, Bisset, Manitoba

Alliance Mining Corp. ("Alliance" or the "Company") is pleased to
report that drilling is complete on its Packsack property, part of the
Red Rice Lake gold project. All drill core has been logged and core
sawing/sampling is presently underway. Core size was NQ.

The program was completed with four drill holes totaling 792.9
meters. Locations (UTM NAD83 Zone 15) and drill hole orientations are
tabulated below. All technical objectives of the program were
accomplished.

//st

Drill Hole #   Collar Coordinates   Orientation   Total Depth

PK-18-1        310061E / 5652811N   -55 / 205az   80ft / 24.4m

PK-18-2        310018E / 5652760N   -65 / 205az   1247ft / 380.1m

PK-18-3        310037E / 5652739N   -70 / 180az   887ft / 270.4m

PK-18-4        310001E / 5652695N   -48 / 220az   387ft / 118.0m

//et

Drill hole PK-18-1 was abandoned without casing into bedrock when
unexpectedly deep overburden was encountered along the north side of
the Red Rice Lake topographic lineament, which lies immediately north
of the Packsack vein systems. Drilling was then shifted to the south
side of the lineament. Drill setup locations along the south side of
the lineament are constrained by beaver ponds, underground
drifts/crosscuts and rock dumps. Future drilling from the north side of
the lineament will start with HQ to ensure casing to bedrock.

Drill hole PK-18-2 was drilled beneath the Packsack veins and
underground drifts/crosscuts. This drill hole intersected
sericite-altered and quartz-veined feldspar porphyry dike mineralized
with 1% pyrite at 104.84 to 110.48m, as well as chlorite-altered and
quartz-veined mafic dike mineralized with 2% pyrite at 113.35 to
126.42m. These sections are believed to be en echelon northerly
extensions of the Packsack vein systems. Core angles of 35 to 40
suggest true widths will be approximately 60% in these sections (see
photograph below).

To view the graphic in its original size, please click here

PK-18-2 also intersected sericite-altered and quartz-veined dacite
volcanics with 1% pyrite at 316.73 to 318.11m and at 328.57 to 356.20m.
Core angles averaging 20 suggest true widths of about 35% in these
sections. These intersections are believed to be the down-plunge
extension of the Tine veins, which outcrop about 300m south of the
Packsack shaft. The Tine veins were not a primary target of this
program (see photograph below).

To view the graphic in its original size, please click here

Drill hole PK-18-3 was intended to test for a possible east to
northeasterly plunge of the Packsack vein systems. This drill hole
intersected sericite-altered quartz-veined dacite volcanics with 2%
pyrite at 159.58 to 161.95m. Core angles of 30 suggest 50% true width.
This drill hole suggests that the Packsack vein systems do not plunge
significantly to the east or northeast, consistent with observations of
a possible northerly en echelon pattern from hole PK-18-2.

Drill hole PK-18-4 was intended to intersect the Big Dome vein
between the -125ft (38m) level and -250ft (76m) drifts/crosscuts, in
order to provide gold grade/width data on the portion of the vein which
was explored by underground exploration in the 1930s. This drill hole
intersected sericite-altered and silicified dacite volcanics with minor
pyrite at 38.10 to 46.33m (true width 70%), likely the Hargreaves vein.
The Big Dome vein was intersected from 56.80 to 65.38m and was
characterized by a 50% mix of quartz-calcite-ankerite-tourmaline
veining with 1% pyrite and sericite-altered mafic dike wallrock with 3%
pyrite. Core angles on the Big Dome vein varied widely but averaged 30
suggesting a 50% true width (see photo below). Variable sericite
alteration and quartz-calcite-ankerite-tourmaline veining continued in
both altered dacite and altered mafic dikes with 1 to 2% pyrite at
65.38 to 90.09m and 112.61 to 115.59m with core angles averaging 45
suggesting 70% true widths.

To view the graphic in its original size, please click here

"These geological/mineralogical characteristics are indicative of
a very promising environment for gold exploration," stated consulting
geologist William Hood.

Alliance Mining has an option to acquire 100 per cent of the Red
Rice Lake property located in the centre of the Bissett gold camp in
Manitoba. The property is located close to the town of Bissett, Man.,
and just four kilometres south from Klondex Mines' True North gold
mine. The Red Rice Lake gold property claims are located within the
Archean Rice Lake greenstone belt in southeastern Manitoba. This belt
forms part of the Uchi sub province that includes the Red Lake and
Pickle Lake belts in Northwestern Ontario.

Alliance is actively seeking to expand its presence in the Bissett
Gold camp through future property acquisitions and/or potential joint
venture exploration partnerships with neighbouring companies.

William C. Hood, P.Geo, a qualified person as defined by National
Instrument 43-101, is responsible for the technical information
contained in this news release.

ON BEHALF OF THE BOARD
Mr Christopher Anderson
President, CEO and Director

FOR FURTHER INFORMATION PLEASE CONTACT:

Alliance Mining Corp.
(604) 488-3900
Investor Relations:
Antony Claydon: 604-445-5421
E-mail: ir@alliancemining.com

This press release includes certain statements that may be deemed
"forward-looking statements". All statements in this release, other
than statements of historical facts, that address future exploration
drilling, exploration activities and events or developments that the
Company expects, are forward looking statements. Although the Company
believes the expectations expressed in such forward-looking statements
are based on reasonable assumptions, such statements are not guarantees
of future performance and actual results or developments may differ
materially from those in forward-looking statements. Factors that could
cause actual results to differ materially from those in forward-looking
statements include exploitation and exploration successes, continued
availability of financing, and general economic, market or business
conditions.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

TEL:  604-488-3900  ALLIANCE MINING CORP
FAX:  604-488-3910
EMAIL:  office@alliancemining.com
WEBSITE:  http://www.alliancemining.com
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1811500005TS11811500981-05303620180426