Source	MARKET NEWS
Date	04/04/2018
Time	07:17:07 AM

Company	 Amex Exploration Inc.
Title	New Gold 
Rich Polymetallic Drill Results With Gr





    CDNX Symbol: AMX











Press Release





AMEX EXPLORATION INC ("AMX-V")
- New Gold-Rich Polymetallic Drill Results With Grades Up to 6.72
- g/t Au, 24.2 g/t Ag and 0.30% Zn Over 1.5 Meters at Perron

Source:Amex Exploration Inc.

Amex Exploration Inc. ("Amex" or the "Corporation") is very
pleased to report new gold-rich polymetallic drill intersections from
its winter 2017-2018 drilling program at Perron in each of the three
drill holes located in the 'Discovery Hole' polymetallic area with
values of up to 6.72 g/t Au, 24.2 g/t Ag and 0.30% Zn over 1.5 meters
(see Table 1).

//st

Table 1: 2017-18 Winter Drilling results from the Discovery Hole
Polymetallic Area
Hole           From   To     Length  Au    Ag    Cu    Zn
(m)     (g/t) (g/t) (%)   (%)
PE2018-07      131.1  133.5  2.4     3.43  8.88  0.13  0.09
PE2018-07 incl 131.1  132.6  1.5     4.49  9.7   0.11  0.11
PE2018-07      171.85 173.0  1.15    2.43  6.8         0.17
PE2018-07      193.5  198.0  4.5     1.84  9.8         0.30
PE2018-07 incl 195.0  196.5  1.5     4.48  5.3         0.13
PE2018-08      247.5  252.0  4.5     2.06  7.20  0.07  0.11
PE2018-08 incl 247.5  249.0  1.5     4.56  14.2  0.14  0.16
PE2018-10      112.5  114.0  1.5     3.10
PE2018-10      196.0  197.5  1.5     1.59  5.6         1,55
PE2018-10      253.5  261.0  7.5     0.72  18.7
PE2018-10 incl 258.0  261.0  3.0     1.43  23.9        0.27
PE2018-10      282.0  283.5  1.5     6.72  24.2        0.30

//et

Interval intersected along the hole, undetermined true thickness.

These three new drill holes (i.e. PE-2018-07, -08, -10; see Fig.1)
were planned as priority targets from the 3D modelling created in
conjunction with Innovexplo (see PR2017-10-24) as follow up drilling to
the so called 'Discovery Hole' drilled by Amex in 2013 (Hole
PE-2013-03) that returned gold-rich polymetallic values of 3.84 g/t Au,
23.0 g/t Ag, 1.4% Zn and 0.10% Cu over 15.2 meters, including a high
grade intersection of 19.07 g/t Au, 102.0 g/t Ag, 5.0% Zn and 0.38% Cu
(see PR2013-03-19).

Figure 1 Perron 2017/2018 Exploration Drilling
Program:http://www.globenewswire.com/NewsRoom/AttachmentNg/ca828637-62d4-49
53-8d0a-f69b8b7bbda7

The next step is to integrate these drilling results into the 3D
modelling to better understand the geometric and genetic relationship
of these new intersections in order to prepare a new follow up drilling
program that will be focussed not only on the recently identified
'Eastern Gold Zone' (see PR2018-03-02) but also in this very promising
'Discovery Hole Gold-rich Polymetallic Area'.

It is important to note that these are two different mineralised
areas and they are located in two different parts of the Perron
property, geologically and geographically speaking. There is a distance
of about 1.0 Km between these two mineralized areas where relatively
only limited drilling has been done in the past. During this 2017-2018
phase of drilling, Amex tested the one kilometer of strike between the
two mineralized areas and drilled three broadly spaced holes
(PE-2017-02, -04 and PE-2018-06) to evaluate the potential of this 'in
between' ground. Drilling focussed on reactivated syn-volcanic faults
and the contact zone between the Beaupr Rhyolite (acting as host and
footwall rock of both type of mineralization) and the overlying
andesite unit (with some sediments and iron formations that constitute
the hanging wall unit also of both mineralization types).

These three holes intersected gold mineralized intervals with
values up to 9.60 g/t Au over 1.5 meters in hole PE-2018-06 and two
wide intersections of low grade values, one grading 0.62 g/t Au over
9.0 meters, also in hole PE-2018-06, and the other one grading 0.78 g/t
Au over 18.0 meters in hole PE-2017-04 (see table 2). The
interpretation and understanding of these results are yet to be
determined.

Table 2: Gold Intersections Between The Eastern Gold Zone and The
Discovery Hole Polymetallic Area

//st

Hole            From   To     Length (m)  Au (g/t)
PE2017-02       231.0  233.5  2.5         0.64
PE2017-04       246.0  264.0  18.0        0.78
PE2017-04 incl  247.5  249.0  1.5         2.59
PE2017-04 incl  259.5  262.5  3.0         2.12
PE2017-04 incl  304.5  306.0  1.5         2.03
PE2018-06       102    111.0  9.0         0.62
PE2018-06 incl  105    106.5  1.5         2.33
PE2018-06       277.5  279.0  1.5         9.6

//et

Interval intersected along the hole, undetermined true thickness.

Jacques Trottier, PhD, Executive Chairman of Amex said, "Even
though we haven't totally completed the analysis from this last
winter's 2017-2018 drilling campaign, the results are very impressive
and even better than expected. We can already say that this phase of
drilling is a complete success and we achieved our main objectives to
evaluate the gold-rich polymetallic potential of the immediate area of
the 2013 'Discovery Hole' and to potentially identifying new gold
bearing structures. I am very encouraged with the identification of the
new 'Eastern Gold Zone' announced a few weeks ago and now further
confirmation of gold-rich polymetallic zones as described. I am also
very pleased with the results from the drilling between the Eastern
Gold Zone and the Gold-rich Polymetallic Area. There is about one
kilometer of strike length between these two areas and intersecting
gold mineralization in all three widely spaced holes is quite exiting
and opens new ground for further exploration work. Clearly, follow up
drilling is necessary. I am also personally very proud of the work done
by the exploration team that has been involved in the planning and
execution of the winter drill program. Our focussed work on Perron has
already begun to yield tangible results and I believe we have only
scratched the surface of the true potential of this great promising
property."

UPDATE ON CURRENT DRILLING

We have also received the results from hole PE-2017-05 (that was
actually the deepening of hole PE-2013-04) that was drilled to test a
geophysical target and now explained by the presence of finely
laminated iron formations with no significant values and PE-2018-09
drilled to the western limit of the Discovery Hole Gold-rich
Polymetallic Area with no significant values.

Drilling has been terminated on March 6th with hole PE-2018-13 for
a total of 4537 meters. The 2017-2018 program was planned for 4360
meters with 14 targets; we have added one target and reported drilling
on target I and K (refer to PR2017-10-24). As of today, results from
holes PE-2018-11, 12 and 13 are still under processing and review, and
will be communicated when available.

Kelly Malcolm, P.Geo., a Qualified Person as defined by Canadian
NI 43-101, revised and approved the geological information of the
current drilling reported in this news release. The drilling campaign
and the quality control program has been planned and supervised by
Nabil Tarbouche and Amex's management. The QAQC protocol includes
insertion of blanks,standards or duplicates every 10 samples on
average.The gold values are determined by Fire Assay (AU-ICP-21) at ALS
Minerals, Val d'Or. All samples were submitted toALS Mineralsfor gold,
base metals and major and trace element geochemistry. Core Logging and
samplingwascompleted by Lisa Ct, Trainee Geologist of Explo-Logik under
supervision of Nabil Tarbouche.

About Amex

Amex Exploration Inc. is a junior mining exploration company, the
primary objective of which is to develop and bring into production
viable gold and base metals deposits in mining-friendly jurisdictions.
Amex has multiple highly prospective projects: the 100% owned Perron
gold project located 110 kilometres north of Rouyn Noranda, Quebec,
consisting of 116 adjacent claims covering 4518 hectares; the 100%
owned Eastmain River gold properties consisting of 135 claims covering
7,102 hectares and the 100% owned Lebel-sur-Quvillon project in Quebec,
comprising 263 claims covering 14,743 hectares. In addition, Amex has
an option agreement to acquire a 100% interest in the Gowan Property
located near the Kidd Creek Mine.

For further information please contact:
Victor Cantore
President and Chief Executive Officer
Amex Exploration: 514-866-8209

Forward-looking statements:

Except for statements of historical facts, all statements in this
news release regarding, without limitation, future plans and objectives
are forward-looking statements which involve risks and uncertainties.
There can be no assurance that such statements will prove to be
accurate. Actual results and future events could differ materially from
those anticipated in such statements.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1809300025TS11809301255-07154120180404