Source	MARKET NEWS
Date	04/05/2018
Time	05:20:16 AM

Company	 Anfield Energy Inc.
Title	Resource 
Report For Third Of 25 Uranium Projects





    CDNX Symbol: AEC











Press Release





ANFIELD ENERGY INC ("AEC-V")
- Resource Report For Third Of 25 Uranium Projects In Wyoming

Anfield Energy Inc. ("Anfield" or "the Company") is pleased to
announce the receipt of an NI 43-101 compliant mineral resource
technical report for the Nine Mile Lake uranium project, entitled "Nine
Mile Lake Uranium Project, Mineral Resource NI 43-101 Technical Report,
Natrona County, Wyoming, USA" with effective date March 29, 2017 (the
"Nine Mile Report"). Further to Anfield's news release of March 21,
2017, the Nine Mile Report is the third in a series of NI 43-101
technical reports related to Anfield's 25 Wyoming uranium projects. The
report was completed by BRS, Inc., a consulting and engineering firm
with more than 40 years of experience assessing Wyoming uranium
projects.

The resource estimate includes:

*  an Indicated Resource of 2,108,000 tons of mineralized material
with an average grade of 0.059% (equivalent to an Indicated Resource of
2,504,000 pounds of U3O); and

*  an Inferred Resource of 1,297,000 tons of mineralized material
with an average grade of 0.070% (equivalent to an Inferred Resource of
1,804,000 pounds of U3O8).

Corey Dias, Anfield's CEO stated, "We are very pleased to announce
the receipt of this resource report. Since acquiring 24 Wyoming uranium
projects from Uranium One in 2016, we have committed to updating and
confirming resources held on those properties. This report is the third
to have been completed, and there remains a significant opportunity to
delineate further uranium resources on the remaining 21 projects.
Moreover, with the Charlie project resource report expected to be
completed within the next 60 days, we expect to see continued
significant growth in our uranium resource base. Finally, Anfield
remains on course to deliver on its strategy of creating a viable
uranium production complex in Wyoming as it looks to pair its resource
base with the Resin Processing Agreement it has in place with Uranium
One whereby it can process up to 500,000 pounds of uranium per year at
Uranium One's Irigaray Central Processing Plant."

A summary of the Indicated Mineral Resource included in the Nine
Mile Report is presented in Table 1.1. A summary of the Indicated
Mineral Resource included in the Nine Mile Report is presented in Table
1.2.

Table 1.1 Indicated Mineral Resources

//st

GT minimum   Pounds % eU3O8   Tons        Average Grade %eU3O8

0.25         2,504,000        2,108,000   0.059

//et

Table 1.2 Inferred Mineral Resources

//st

GT minimum   Pounds % eU3O8   Tons        Average Grade %eU3O8

0.25         1,804,000        1,297,000   0.070

//et

Mineral resources are not mineral reserves and do not have
demonstrated economic viability in accordance with CIM standards.
Inferred Mineral Resources are too speculative geologically to have the
economic considerations applied to them which would enable them to be
categorized as mineral reserves.

About Nine Mile Lake Project

The Nine Mile Lake project comprises approximately 6,619 acres of
Anfield's mineral rights including mining claims and mineral leases.
and includes 190 unpatented mining lode claims, 1,280 acres of State
mineral leases and 1,538.6 acres of private mineral leases. The data
used in the report consists of radiometric-equivalent data (eU3O8) for
1,100 drill holes; drill intercept data from 26 core holes and 238
rotary drill holes were utilized, along with drill intercepts, chemical
assay certificates and both lithological and geophysical logs.

To the best of our knowledge there are no legal or environmental
matters that could materially affect the potential development of these
resources.

Radiometric equilibrium was assumed, and is considered reasonable
with respect to mineral resources as the mineralization is well below
the ground water table and not subject to surficial oxidation.

A unit weight of 125 pounds per cubic foot or 16 cubic feet per
ton was assumed, based on the report Author's experience working in
operating mines within similar sandstone uranium deposits where reserve
estimates were routinely compared to actual production.

Indicated mineral resources were estimated using the GT contour
method which is considered appropriate for this type of deposit. The GT
was determined for each drill hole, by major stratigraphic horizon, and
the GT was summed for all intercepts meeting the cut-off criteria by
horizon for each hole.

Inferred mineral resources were estimated for those areas where
location of the REDOX front was known based on past drilling but the
available data was not sufficient to estimate Indicated Mineral
Resources.

NI 43-101 Disclosure

The NI 43-101 Resource Technical Report completed for Nine Mile
Lake has been authored by Douglas L. Beahm, P.E., P.G. Principal
Engineer, of BRS Inc. The author has reviewed and approved the
technical content of this news release.

A technical report on the Resource Technical Report will be
published on the System for Electronic Analysis and Retrieval ("SEDAR")
and the Company's website within the 45 days permitted under NI 43-101.


About BRS

BRS, Inc. is an engineering and geology consulting corporation
with expertise in mining and mineral exploration. Of particular note,
it specializes in uranium exploration, mineral resource evaluation,
mine design, feasibility, mine operations, and reclamation. It has
completed numerous uranium projects including technical reports and
feasibility studies for underground, open pit, ISR, and conventional
uranium mills. Representative projects include technical reports and
due diligence for project financing for conventional uranium projects
including the Sheep Mountain and the JAB-RD open pit in Wyoming, the
Cibola Project in New Mexico, the Coles Hill, Virginia open pit and
underground mine, and numerous ISR uranium projects in Wyoming and
Paraguay.

Douglas L. Beahm, P.E., P.G., the principal engineer at BRS, is a
Qualified Person as defined in NI 43-101 with more than 40 years of
professional and managerial experience. Mr. Beahm has a proven track
record in a variety of mining and mine reclamation projects including
surface and underground mining, heap leach recovery, ISR, and uranium
mill tailings projects. Mr. Beahm's experience includes coal, precious
metals, and industrial minerals, but his emphasis throughout his career
has been on uranium.

About Anfield

Anfield is a uranium and vanadium development and near-term
production company that is committed to becoming a top-tier
energy-related fuels supplier by creating value through sustainable,
efficient growth in its assets. Anfield is a publicly-traded
corporation listed on the TSX-Venture Exchange (AEC-V), the OTCQB
Marketplace (ANLDF) and the Frankfurt Stock Exchange (0AD). Anfield is
focused on two production centres, as summarized below:

Wyoming - Irigaray ISR Processing Plant (Resin Processing
Agreement)

Anfield has signed a Resin Processing Agreement with Uranium One
whereby Anfield would process up to 500,000 pounds per annum of its
mined material at Uranium One's Irigaray processing plant in Wyoming.
In addition, the Company can both buy and borrow uranium from Uranium
One in order to fulfill some or all of its sales contracts.

Anfield's 25 ISR mining projects are located in the Black Hills,
Powder River Basin, Great Divide Basin, Laramie Basin, Shirley Basin
and Wind River Basin areas in Wyoming. Anfield's two projects in
Wyoming for which NI 43-101 resource reports have been completed are
Red Rim and Clarkson Hill.

The Charlie Project, acquired from Cotter Corporation, is located
in the Pumpkin Buttes Uranium District in Johnson County, Wyoming. The
Charlie Project consists of a 720-acre Wyoming State uranium lease
which has been in development since 1969.

Arizona/Utah - Shootaring Canyon Mill

A key asset in Anfield's portfolio is the Shootaring Canyon Mill
in Garfield County, Utah. The Shootaring Canyon Mill is strategically
located within one of the historically most prolific uranium production
areas in the United States, and is one of only three licensed uranium
mills in the United States.

Anfield's conventional uranium assets consist of mining claims and
state leases in southeastern Utah and Arizona, targeting areas where
past uranium mining or prospecting occurred. Anfield's conventional
uranium assets include the Velvet-Wood Project, the Frank M Uranium
Project, as well as the Findlay Tank breccia pipe. An NI 43-101
Preliminary Economic Assessment has been completed for the Velvet-Wood
Project. All conventional uranium assets are situated within a 125-mile
radius of the Shootaring Mill.

On behalf of the Board of Directors
ANFIELD ENERGY INC.
Corey Dias, Chief Executive Officer

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

Safe Harbor Statement

THIS NEWS RELEASE CONTAINS "FORWARD-LOOKING STATEMENTS".
STATEMENTS IN THIS NEWS RELEASE THAT ARE NOT PURELY HISTORICAL ARE
FORWARD-LOOKING STATEMENTS AND INCLUDE ANY STATEMENTS REGARDING
BELIEFS, PLANS, EXPECTATIONS OR INTENTIONS REGARDING THE FUTURE.

EXCEPT FOR THE HISTORICAL INFORMATION PRESENTED HEREIN, MATTERS
DISCUSSED IN THIS NEWS RELEASE CONTAIN FORWARD-LOOKING STATEMENTS THAT
ARE SUBJECT TO CERTAIN RISKS AND UNCERTAINTIES THAT COULD CAUSE ACTUAL
RESULTS TO DIFFER MATERIALLY FROM ANY FUTURE RESULTS, PERFORMANCE OR
ACHIEVEMENTS EXPRESSED OR IMPLIED BY SUCH STATEMENTS. STATEMENTS THAT
ARE NOT HISTORICAL FACTS, INCLUDING STATEMENTS THAT ARE PRECEDED BY,
FOLLOWED BY, OR THAT INCLUDE SUCH WORDS AS "ESTIMATE," "ANTICIPATE,"
"BELIEVE," "PLAN" OR "EXPECT" OR SIMILAR STATEMENTS ARE FORWARD-LOOKING
STATEMENTS. RISKS AND UNCERTAINTIES FOR THE COMPANY INCLUDE, BUT ARE
NOT LIMITED TO, THE RISKS ASSOCIATED WITH MINERAL EXPLORATION AND
FUNDING AS WELL AS THE RISKS SHOWN IN THE COMPANY'S MOST RECENT ANNUAL
AND QUARTERLY REPORTS AND FROM TIME-TO-TIME IN OTHER PUBLICLY AVAILABLE
INFORMATION REGARDING THE COMPANY. OTHER RISKS INCLUDE RISKS ASSOCIATED
WITH SEEKING THE CAPITAL NECESSARY TO COMPLETE THE PROPOSED
TRANSACTION, THE REGULATORY APPROVAL PROCESS, COMPETITIVE COMPANIES,
FUTURE CAPITAL REQUIREMENTS AND THE COMPANY'S ABILITY AND LEVEL OF
SUPPORT FOR ITS EXPLORATION AND DEVELOPMENT ACTIVITIES. THERE CAN BE NO
ASSURANCE THAT THE COMPANY WILL BE ABLE TO COMPLETE THE PROPOSED
TRANSACTION, THAT THE COMPANY'S EXPLORATION EFFORTS WILL SUCCEED OR THE
COMPANY WILL ULTIMATELY ACHIEVE COMMERCIAL SUCCESS. THESE
FORWARD-LOOKING STATEMENTS ARE MADE AS OF THE DATE OF THIS NEWS
RELEASE, AND THE COMPANY ASSUMES NO OBLIGATION TO UPDATE THE
FORWARD-LOOKING STATEMENTS, OR TO UPDATE THE REASONS WHY ACTUAL RESULTS
COULD DIFFER FROM THOSE PROJECTED IN THE FORWARD-LOOKING STATEMENTS.
ALTHOUGH THE COMPANY BELIEVES THAT THE BELIEFS, PLANS, EXPECTATIONS AND
INTENTIONS CONTAINED IN THIS NEWS RELEASE ARE REASONABLE, THERE CAN BE
NO ASSURANCE THOSE BELIEFS, PLANS, EXPECTATIONS OR INTENTIONS WILL
PROVE TO BE ACCURATE. INVESTORS SHOULD CONSIDER ALL OF THE INFORMATION
SET FORTH HEREIN AND SHOULD ALSO REFER TO THE RISK FACTORS DISCLOSED IN
THE COMPANY'S PERIODIC REPORTS FILED FROM TIME-TO-TIME.

THIS NEWS RELEASE HAS BEEN PREPARED BY MANAGEMENT OF THE COMPANY
WHO TAKES FULL RESPONSIBILITY FOR ITS CONTENTS.

TEL:  780-920-5044  Clive Mostert, Corporate Communications
Anfield Energy Inc.
EMAIL:  contact@anfieldenergy.com
WEBSITE:  www.anfieldenergy.com
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1809400003TS11809400555-05182920180405