Source	MARKET NEWS
Date	04/05/2018
Time	06:32:17 AM

Company	 West Kirkland Mining Inc.
Title	New 
Target Outlined with Surface Gold Values Nea





    CDNX Symbol: WKM











Press Release





WEST KIRKLAND MINING INC ("WKM-V;WSKKF-0")
- New Target Outlined with Surface Gold Values Near Hasbrouck
- Project, Tonopah, Nevada

West Kirkland Mining Inc. ("West Kirkland", "WKM" or the
"Company") is pleased to report gold assay values in continuous sample
lengths, at surface, further outlining a new target near the Hasbrouck
gold project reserves in Nevada. The objective of the WKM program is to
outline new at surface gold resources that could be combined in a plan
with the Company's heap leach reserves.

New assay results from West Kirkland mapping and channel sampling
at the Gold Mountain area include 340 feet in two nearby sample lengths
that average 1.1 g/t gold.  These sample lines at "South Peak" are
vertically above and near historic underground workings and minor
historic production from veins at Gold Mountain. (Road Cut 4 and
Traverse 1 below). The assay sampling reported includes more
disseminated and broader zones than the historic workings would have
accessed and tested below.

The best channel results of 1.54 g/t Au over 120 feet compares
well with a historic drill intercept 500 feet to the west of 1.1 g/t Au
over a down-hole length of 225 feet.

The true thickness and overall controls of the gold mineralization
at Gold Mountain are still being determined. A steep dipping
fault-break controlled mineralization is mapped as well as a layered
flat-bedded control for some of the mineralization. Additional detailed
surface sampling will be completed in the weeks ahead followed by
drilling targeted on potential for open pit resources near surface.

April 5, 2018 Sample Results - 20 foot continuous chip sample
results

//st

Surface Samples     Length   Gold (g/t)   Silver (g/t)   Location

Road-cut 4          220'     0.88         13.8           South Peak NW
(11 samples)

Outcrop Traverse    120'     1.54         41.7           South Peak N (6
1                                                        samples)

Road-cut 5          180'     0.83         12.1           West Peak N (9
samples)

Outcrop Traverse    215'     0.52         11.2           Sealey Ridge E
2                                                        (14 samples)

Outcrop Traverse    906'     0.40         14.5           Sealey Ridge W
3                                                        (47 samples)

TOTAL               1641'    Avg: 0.61    Avg: 15.7      87 Samples

//et

Results Reported January 29, 2018

//st

Surface Samples   Length   Gold (g/t)   Silver (g/t)   Location

Road-cut 1        441'     0.87         2.4            North Peak NE (26
samples)

Road-cut 2        917'     0.65         13.2           North Peak SW (47
samples)

Road-cut 3        250'     0.68         22.5           North Peak E (16
samples)

TOTAL             1608'    Avg: 0.72    Avg: 11.7      89 Samples

//et

The exploration at Gold Mountain (100% Option Interest) is within
sight of the Hasbrouck Project (75% WKM, 25% Waterton Fund).

The Hasbrouck Gold Project contains Proven & Probable Reserves of
784,000 gold equivalent oz, (45,270,000 tons at 0.017 Au oz/t for
762,000 contained Au oz; 0.233 Ag oz/t for 10,569,000 contained Ag
ounces. NPV5 Post Tax ($1,275/oz Au) estimated at $120M, IRR 43%
(Technical Report and Updated Preliminary Feasibility Study for The
Hasbrouck and Three Hills Gold-Silver Project, Esmeralda County,
Nevada, USA, Report Date: September 14, 2016).



QUALIFIED PERSON

R. Michael Jones P.Eng, CEO of West Kirkland Mining, is a
non-independent Qualified Person as defined by NI 43-101.  He has
reviewed the information contained in this news release and has
verified the data by hiring qualified geologists and engineers and has
completed a review of the detailed technical information.  Mineral
Reserve information in this news release relating to the Hasbrouck Gold
Project has been developed and approved by Thomas L. Dyer, P.E., of MDA
following CIM standards.

QUALITY ASSURANCE/QUALITY CONTROL

West Kirkland Mining utilizes a well-documented system of
inserting blanks and standards into the assay stream and has a strict
chain of custody for samples taken by WKM.  Assays by WKM are completed
at independent laboratories which have internal quality assurance and
quality control systems and procedures.  Assays were performed by ALS
Chemex Labs Ltd., by fire assay and ICP methods.

The historic work was completed by previous property explorers and
developers and provided to WKM in digital form in an extensive
database. The surface assays on road-cuts and grab samples were
performed at ALS labs by standard fire assays with ICP finish methods.
Drill hole assay data for the 1995 and 1990 programs were completed at
Barringer labs, GSI labs, and labs respectively with fire assay methods
and ICP or AA finish.  The 1980 holes do not have assay lab data
available, but the values were part of historic production mine work at
the time and are consistent with the ALS surface data nearby.  Although
the work was completed prior to NI-43101 and was not under WKM control
and chain of custody, the work was completed by qualified professional
geologists and laboratories utilizing standard methods.  The results of
various dates and operators provide similar results to the surface
sample assay work by ALS labs.  For the purpose of general exploration
target generation, the Non-Independent QP has reviewed the data in
detail and has accepted it as verified for general indicative
exploration targeting. The data was verified by ensuring a reasonable
mineralization type and assay tenor comparison, in the same area,
between multiple project exploration companies and labs, along with a
review and acceptance of the quality of the work reported.  Further
confirmation assays under WKM procedures would be required for this
data to be used in Resource calculations.

On behalf of West Kirkland Mining Inc.
"R. Michael Jones"
Chief Executive Officer

For further information, please see the Company's website at
www.wkmining.com or contact us by email at info@wkmining.com.

Disclaimer for Forward-Looking Information

This press release contains forward-looking information or
forward-looking statements (collectively "forward-looking information")
within the meaning of applicable securities laws. Forward-looking
information is typically identified by words such as: "believe",
"expect", "anticipate", "intend", "estimate", "postulate" and similar
expressions, or are those, which, by their nature, refer to future
events.  Forward-looking information in this news release includes,
without limitation, the exploration and project approach of a
Prefeasibility Study.  Historical mineral title also has risk of an
unrecorded claim. The Company cautions investors that any
forward-looking information provided by the Company is not a guarantee
of future results or performance, and that actual results may differ
materially from those in forward-looking information as a result of
various factors, including, but not limited to, the state of the
financial markets for the Company's equity securities, the state of the
market for gold or other minerals that may be produced generally,
variations in the nature, quality and quantity of any mineral deposits
that may be located, the Company's ability to obtain any necessary
permits, consents or authorizations required for its activities, to
raise the necessary capital or to be fully able to implement its
business strategies and other risks associated with the exploration and
development of mineral properties.  The reader is referred to the
Company's public filings for a more complete discussion of such risk
factors and their potential effects which may be accessed through the
Company's profile on SEDAR at www.sedar.com.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

TEL: 604-685-8311    WEST KIRKLAND MINING INC
FAX: 604-484-4710
E-mail: info@wkmining.com
Website: http://www.wkmining.com
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1809400023TS11809400936-06292620180405