Source	MARKET NEWS
Date	04/09/2018
Time	02:16:12 PM

Company	 Nitinat Minerals Corporation
Title	Initiates 
Geological Work Program On Carscallen





    CDNX Symbol: NZZ











Press Release





NITINAT MINERALS CORP ("NZZ-V;NITMF-0")
- Initiates Geological Work Program On Carscallen

Nitinat Minerals Corp. (the "Company") is pleased to announce that
the Company has commenced work on the proposed work program on its 100%
owned Carscallen Gold Property (also known as the Lalonde-Allaire
claims) located in Northern Ontario. The Carscallen Gold Property is
located 25 kms west of the City of Timmins and 7 kilometers north of
the Lakeshore Gold's Timmins Mine, which produced an aggregate of
185,600 ounces in 2014.

Geological Work Program

Historical information suggests the presence of iron carbonate
mafic to intermediate volcanic rock type with the stratigraphic aligned
feature trending NW to SE. This unit has been the target of historical
gold exploration and workings. The geological feature has an
approximate 2km strike length and about 200m wide as exposure on or
near surface.

Previous small scale mining is reported to have occurred towards
the SE of the strike extent. The approximate shaft position (three in
total) are located within and along the same strike as the mafic unit.
Although small scale mining and the remnants of the shafts are found on
the property, the extent of the mining activity is not known.

The Company has initiated an exploration program with the
following activities to be undertaken:

*  Cutting of access lines (shown in the diagram below) that cover
the extent of the property and specifically the target area. A total of
23km of lines are planned to be cut.

A diagram accompanying this announcement is available at
http://resource.globenewswire.com/Resource/Download/43a25df9-d253-4b26-8f69
-d423e85486de

*  A geomagnetic survey will be carried out over the property at
12.5m intervals and at line spacing of 100m.

*  An induced polarization (IP) survey will be carried out over
the property with a pole-dipole electrode array and a dipole spacing of
50m.

*  The total cost of the program is estimated at $60,000.

The program will start immediately and the initial results from
the program are expected by mid-June.

"After this short inexpensive program, the Company should be able
to identify drill targets," stated Herb Brugh, President of the
Corporation, "and with that the Company will initiate an extensive
drill program on all of its claims in order to maximize shareholder
value. The Company's main objective is to find an economical ore body
much the same as Lakeshore (Tahoe) has done."

The Qualified Person for the Carscallen Property is John A. Gould,
B.Sc. University of the Witwatersrand (Geology, Physics and Chemistry)
Potchefstroom University of Higher Christian Education: BSc (Hons)
(Geology) SACNASP Registration: 400022/10.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

Forward-Looking Statements

This news release contains "forward-looking statements" within the
meaning of the United States Private Securities Litigation Reform Act
of 1995 and applicable Canadian securities legislation. Generally,
these forward-looking statements can be identified by the use of
forward-looking terminology such as "plans", "anticipated", "expects"
or "does not expect", "is expected", "budget", "scheduled",
"estimates", "forecasts", "intends", "anticipates" or "does not
anticipate", or "believes", or variations of such words and phrases or
state that certain actions, events or results "may", "could", "would",
"might" or "will be taken", "occur" or "be achieved". Nitinat is
subject to significant risks and uncertainties which may cause the
actual results, performance or achievements to be materially different
from any future results, performance or achievements expressed or
implied by the forward-looking statements contained in this release.
Nitinat cannot assure investors that actual results will be consistent
with these forward-looking statements and Nitinat assumes no obligation
to update or revise the forward-looking statements contained in this
release to reflect actual events or new circumstances.

TEL:  416.216.0964  Herb Brugh, President and Director
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1809800063TS11809802665-14113620180409