Source	MARKET NEWS
Date	04/10/2018
Time	11:37:21 AM

Company	 Cascadero Copper Corporation
Title	Exploration Update





    CDNX Symbol: CCD











Press Release





Exploration Update --->@NEWS RELEASE
CASCADERO COPPER CORP ("CCD-V")
- Exploration Update

Porphyry copper systems show a marked tendency to occur in linear,
typically orogen-parallel belts, which range from a few tens to hundreds
and even thousands of kilometres long, as exemplified by the Andes of
western South America. Cascadero's Sarita Este epithermal gold bearing
high-sulphidation alteration assemblage appears to be perfectly located in
an orogenic belt partly in eastern Chile and partly in western Argentina.
This belt is ~ 500 miles in strike is densely populated with large-scale,
Giant and Super Giant copper and gold deposits. MAP ONE illustrates the
Chilean and Argentine Porphyry Copper and Epithermal Gold Deposits and
Showings

The aphorism Location-Location-Location is well known in urban and
commercial Real Estate. It clearly applies to the porphyry model as stated
and outlined above. Porphyry deposits occur in clusters and frequently with
a linear country - scale structure, controlling the location of the
deposits.

Gold-rich porphyry deposits worldwide conform well to a generalized
descriptive model. This model incorporates six main facies of hydrothermal
alteration and mineralization which are zoned upward and outward with
respect to composite porphyry stocks of cylindrical nature that form atop
much larger parent plutons. This intrusive environment and its overlying
advanced argillic lithocap span about 4 kms vertically, an interval over
which profound changes in the style and mineralogy of gold and associated
copper mineralisation are observed.

The model predicts several geological attributes to be expected in
association with superior gold-rich porphyry deposits. Management believes
that recent ground-based geochemistry, field observations and thin section
work have provided a detailed description of the minerals and alteration
that have focused the Company on Sarita Este as a potential large-scale
gold-rich porphyry prospect.

Exploration for gold-rich porphyry deposits worldwide involves geologic,
geochemical and geophysical work, but generally employs the descriptive
model in an unsophisticated manner and the genetic model rarely. Discovery
of gold-rich porphyry deposits during the last 30 years has resulted mainly
from basic geologic observations and conventional geochemical surveys. A
gold-rich porphyry is described as a deposit that averages )3 g/t Au.  The
tried-and-tested approach is thought likely to provide for the foreseeable
future although more rigorous application of the descriptive and genetic
model can only improve the chances of success. (Excerpt from R. Sillitoe
2000)

Argentina has had significantly less exploration activity than Chile
because of previous government regulations and we believe this will enable
a going forward high - frequency of discoveries in Argentina as the
geological setting has some similarities to eastern Chile.  Cascadero's
property portfolio holds high-potential properties in the right areas at
the right time. Sarita Este is permitted to the trench stage and we expect
work to get underway in late spring.

The contents of this news release have been verified by George Gale, P.Geo.
who is a  'qualified person' as defined in National Instrument 43-101,
Standards of Disclosure for Mineral Projects.

Bill McWilliam, Chairman
Cascadero  Corp
554 Kings Road East
North Vancouver B.C.
604.924.5504

Neither the TSX Venture Exchange nor its Regulation Service Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1809900027TS11809902408-11364720180410