Source	MARKET NEWS
Date	04/11/2018
Time	05:34:29 AM

Company	 Algold Resources Ltd.
Title	High Grade 
Results at Salma Further Corroboratin





    CDNX Symbol: ALG











Press Release





ALGOLD RESOURCES LTD ("ALG-V;ALGDF-0")
- High-Grade Results at Salma Further Corroborating Continuous
- Mineralization Over 10 km

ALGOLD RESOURCES LTD. ("Algold" or the "Corporation") today
announced the results from the first 28 drill holes carried out at the
high-grade Salma Vein System located at the Corporation's Tijirit
Project in Mauritania.

The Salma Vein System, discovered in mid-2017, extends over a
10-kilometer strike and is located only five kilometers northeast of
the Eleonore zone within the prospective granite-greenstone contact
zone.

"The drilling results continue to accentuate the high
prospectivity of Salma and the potential to rapidly add high-grade
ounces and could eventually contribute to growing the resource base at
the Tijirit Project," said Algold Executive Vice-President, Exploration
Francois Auclair. "Tijirit now contains four large mineralized zones
including Eleonore, Lily, Sophie and Salma, all of which are in close
proximity to each other."

Highlights

*  22.77 g/t Au over 2 meters (hole T18RC015), approximately 69
meters below the surface at the southern end of the north Salma Vein
*  12.31 g/t Au over 3 meters (hole T18RC004), approximately 41
meters below the surface at the southern end of the Eleonore East area
*  7.20 g/t Au over 4 meters (hole T18RC006), approximately 46
meters below the surface at the southern end of the Eleonore East area
*  5.59 g/t Au over 3 meters, including 15.9 g/t Au over 1 meter
(hole T18RC020), approximately 34 meters below the surface in the
northern area of the Salma Vein

The 2,634-meter reverse-circulation drilling program, completed in
February 2018, targeted surface mineralization identified during rock
chip panel and channel sampling that was conducted last year.  Fifteen
drill fences were widely spaced over the structure with two holes
drilled on the majority of sections to test down dip continuity
(reference: Figure 1).

Hole T18RC015 intersected high-grade mineralization associated
with a pyrite-bearing quartz vein in granitoid host between 88-90
meters. This hole targeted mineralization seen at surface with panel
sampling returning 25.8 g/t Au and mineralized channel sampling 70
meters north and 100 meters south returning 2.35 g/t Au over one meter
in T17TRS39 and 3.57 g/t Au over 0.65 meters in T17TRS43.

Hole T18RC004 intersected a quartz, pyrite and biotite rich shear
zone (similar to Eleonore) between 51-55 meters within a mafic volcanic
package. The hole was designed to test the surface channel sampling and
rock-chip result of 5.16 g/t Au situated above the drill fence.

Hole T18RC006, 730 meters northeast of T18RC004, intersected three
quartz-biotite rich shear zones between 58-68 meters. The hole was
drilled beneath channel T17TRS02A, which intersected 5.0 g/t Au over
2.4 meters.

Hole T18RC020 intersected an oxidized quartz vein between
43-46-meters at the northern end of the Salma Vein. This hole was
drilled beneath channel T17TRS21, which returned 2.46 g/t Au over 1.5
meters.

Table 1: Salma & Eleonore East Drilling Program Assay Result
Highlights

//st

Hole ID    Prospect   East UTM    North     From   To   Vertical Aver- Width
UTM       (m)    (m)   Depth*   age    ***
(m)    Grade** (m)
(g/t
Au)

T18RC004   Eleonore   485303      2250678   32     33    25         1.46   1
East

52     55    41         12.31  3

Including             53     54               30.72  1

T18RC006   Eleonore   485716      2251283   58     62    46         7.195  4
East

Including             58     60               13.70  2

T18RC010   Salma      486868      2255747   39     46    33         2.44   7

Including             44     45               16.30  1

T18RC014   Salma      486919      2256442   43     44    32         9.46   1

T18RC015   Salma      486868      2256428   88     90    69         22.77  2

Including             88     89               45.00  1

486868      2256428   105    106   82         3.25   1

T18RC020   Salma      487348      2258003   43     46    34         5.59   3

Including             43     44               15.9   1

T18RC021   Salma      487299      2257996   78     82    62         2.75   4

T18RC022   Salma      487355      2258251   44     48    35         2.08   4

T18RC023   Salma      487288      2258252   92     94    71         4.14   2

T18RC025   Salma      487325      2258448   74     75    58         2.52   1

T18RC027   Salma      487197      2258386   58     60    46         1.64   2

T18RC028   Salma      486343      2255510   9      12    8          1.26   3

124    128   96         0.85   4

//et

*Vertical depth of intersection below RL collar. **Weighted
average grade, composite based on a minimum grade of 0.3 g/t Au with an
internal dilution of 0.005 g/t Au over 2 m and an edge grade of 0.25
g/t Au permitted. ***Width, believed to be close to true width. No
capping of higher values has been applied.

Following the discovery of the Salma Vein in May 2017, Algold
successfully completed a limited drilling program. All 28 of the holes
drilled intersected anomalous mineralization ()0.1 g/t Au), and seven
of the 28 holes intersected )1 g/t Au mineralization. This first-pass
drilling program established the validity of the target and confirmed
the ability to prospect the zone effectively.  Results will be used to
help determine where to focus future exploration and resource
development on the Tijirit Mining Licence, complementing the successful
resource drilling at Eleonore, Lily and Sophie.
Several targets remain untested throughout the ten-kilometer-long
corridor. Algold has identified another 15 mineralized zones that have
yet to be tested by drilling at Eleonore East alone. Drilling and
trench results from the Salma and the Eleonore East zone (formerly
known as the Pressure Shadow zone) have not yet been included in
Algold's resource estimates.

Algold has changed the name of the Pressure Shadow target to
Eleonore East. The area lies along strike to the south of the Salma
Vein, but unlike Salma the mineralization predominantly occurs in the
mafic volcanic suite. Being structurally and mineralogically similar to
Eleonore, Eleonore East was deemed a more appropriate name.

Fieldwork is currently underway at the Eleonore Zone where
mechanical trenching is being used to better define surface
mineralization and structural information. Algold looks forward to
providing shareholders with an update in this regard in the near
future.

Filing of a Technical Report Algold reports that the Corporation
today filed a technical report entitled "Tijirit Project NI 43-101
Technical Report with Resource Estimate Update, Tijirit, Mauritania,"
dated April 10, 2018, which was prepared by Yann Camus, P.Eng., SGS
Geostat, Blainville, Canada an independent Qualified Person (as defined
in National Instrument 43-101). The Report supports the disclosure made
in Algold's press release issued on February 26, 2018, entitled
"Eleonore Zone Resources Up: Indicated Total 94,250 oz. @ 4.08 g/t Au,
Inferred at 394,690 oz. @ 4.07 g/t Au". The Report will be available on
SEDAR (www.sedar.com) and on the Corporation's website
(www.algold.com).

Quality Assurance / Quality Control (QA/QC)

Analytical work for drill core and chips, geochemical samples and
rock chip samples is carried out at the independent SGS Laboratories
Ltd. in Bamako, Mali.  The 50 g fire assay with ASS finish analytical
services are accredited by SANAS and are carried out with a quality
assurance protocol in line with ISO 17025:2005. Samples are stored at
the Corporation's field camps and put into sealed bags until delivered
by a geologist on behalf of Algold to the laboratory in Bamako, Mali,
where samples are prepared and analyzed. Until the end of 2016, samples
were analyzed at ALS's facility in Loughrea, Ireland. Beginning in
2017, samples are analyzed at SGS Laboratory, Bamako. Samples are
logged in the tracking system, weighed, dried and finely crushed to
better than 70%, passing a 2 mm (Tyler 9 mesh, US Std. No.10) screen. A
split of up to 1,000 g is taken and pulverized to better than 85%,
passing a 75-micron (Tyler 200 mesh) screen, and a 50-gram split is
analyzed by fire assay with an AA finish.  Anomalous samples greater
than 5 g/t Au are re-analyzed by 50 g fire assay with gravimetric
finish.  Selected samples may be re-analyzed using a 1 kg cyanide leach
(Bottle Roll) using "LeachWELL" or the 1 kg screen fire assay method.
Blanks, duplicates and certified reference material (standards) are
routinely inserted to monitor laboratory performance during the
analysis. The independently inserted Quality Control samples have been
reviewed on receipt of the assay results and fall within the acceptable
limits as defined by Algold's Standard Operating Procedure.

This press release has been reviewed for accuracy and compliance
under National Instrument 43-101 by Andre Ciesielski, DSc., Geo.,
Algold Resources Ltd Lead Consulting Geologist and Qualified Person,
and Alastair Gallaugher, C.Geo. (Chartered Geologist and Fellow of the
Geological Society of London), BSc. Geology, Algold's Exploration
Manager in Mauritania, Qualified Persons as defined by NI 43-101
Standards of Disclosure for Mineral Projects. Andre Ciesielski has
further approved the scientific and technical disclosure in the news
release.

ABOUT ALGOLD Algold Resources Ltd. is focused on the exploration
and development of gold deposits in West Africa. The board of directors
and management team are seasoned resource industry professionals with
extensive experience in the exploration and development of world-class
gold projects in Africa.

FORWARD-LOOKING INFORMATION

This press release contains and refers to forward-looking
information based on current expectations. All other statements other
than statements of historical fact included in this release are
forward-looking statements (or forward-looking information). The
Corporation's plans involve various estimates and assumptions and its
business is subject to various risks and uncertainties. For more
details on these estimates, assumptions, risks and uncertainties, see
the Corporation's most recent Management Discussion and Analysis on
file with the Canadian provincial securities regulatory authorities on
SEDAR at www.sedar.com. These forward-looking statements are made as of
the date hereof and there can be no assurance that such statements will
prove to be accurate. Forward-looking statements are subject to
significant risks and uncertainties, and actual results and future
events could differ materially from those anticipated in such
statements. Accordingly, readers should not place undue reliance on
forward-looking statements that are included herein, except in
accordance with applicable securities laws.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

Algold Resources Ltd.
1320, boul. Graham, bureau 132, Mont-Royal, Quebec, H3P 3C8, www.algold.com

//st

Benoit LaSalle, FCPA, FCA   Alex Ball

Chief Executive Officer     Executive VP, Finance and Corporate
Development

b.lasalle@algold.com        a.ball@algold,com

+1 (514) 951-4411           +1 (647) 919 2227

//et
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1810000005TS11810000845-05330920180411