Source	MARKET NEWS
Date	08/21/2014
Time	07:16:02 AM

Company	 Argentex Mining Corporation
Title	Increases 
Pinguino Silver Gold Project Mineral R





    CDNX Symbol: ATX











Press Release	




[200/News Release]ATXVARGENTEX MINING CORPAUG 21 2014  07:13 AMIncreases 
Pinguino Silver Gold Project Mineral Resource Estimate To26.7 Million Ounces 
Ag Eq. @ 132.3 G/t Ag Eq. Indicated And 7.0Million Ounces Ag Eq. @ 98.0 G/t Ag 
Eq. Inferred --->@NEWS RELEASE
ARGENTEX MINING CORP ("ATX-V;AGXMF-0")
- Increases Pinguino Silver-Gold Project Mineral Resource Estimate
- To 26.7 Million Ounces Ag Eq. @ 132.3 G/t Ag Eq. Indicated
- And 7.0 Million Ounces Ag Eq. @ 98.0 G/t Ag Eq. Inferred

Argentex Mining Corporation ("Argentex"or the "Company") is pleased
to announce the results of the updated National Instrument ("NI")
43-101 compliant Mineral Resource Estimate (the Report) undertaken by
Mine Development Associates ("MDA") of Reno, Nevada. This Report
incorporates drilling and trenching results from 2013 on the Company's
100%-owned Pinguino Silver-Gold Project, located in Santa Cruz
province, Argentina.

Highlights:

//st

Increase in indicated category Ag eq. ounces by 13% (3.0 million additional
Ag Eq. ounces to a total of 26.7 Million Ounces Ag Eq. @ 132.3 g/t Ag Eq)

Increase in inferred category Ag Eq. ounces by 49% (2.3 million additional
Ag Eq. ounces to a total of 7.0 Million Ounces Ag Eq. @ 98.0 g/t Ag Eq.).

Four new veins were added to the resource to bring the total number of
veins included in the updated resource estimate to twelve.

More than sixty veins remain to be fully tested in vein structures that
remain open in all directions

//et

"This significant increase in the resource estimate follows
our latest phase of exploration in the oxidation zone and further
supports our belief in the potential for the future development of the
Pinguino project. The increase resulted from the addition of four veins
to the resource, as well as further drilling and trenching on certain
veins included in the previous resource estimate of January 31st, 2013.
The increase in enriched Ag/Au grade oxide material continues to point
to the potential to evaluate a staged development of the project and
while the long-term future of Pinguino lies in the primary
mineralisation, this high-grade oxide material could make an initial
low-cost oxide operation feasible. The oxide material is enriched in
Ag/Au, whilst the primary mineralisation comprises either Ag-Au or
Ag-Au-Zn-Pb sulphide mineralisation," commented Mike Brown, President
and CEO of Argentex. "These results, coupled with our understanding of
the deposit and its expansion potential, will provide a solid
foundation to our recently announced strategic review.

Table 1: Resource Summary

//st
Indicated       Grade (g/t)     Grade          Ounces (000's) Pounds (000's)
----------------------------------------------------------------------------
Tonnes                        Zn   Pb
('000)   Ag eq.    Ag   Au  (%)  (%)       Ag    Ag eq    Au      Zn     Pb
----------------------------------------------------------------------------
6,281      132.3 103.4 0.58 0.77 0.54 20,877.0 26,717.0 116.8 107,225 74,993
----------------------------------------------------------------------------



----------------------------------------------------------------------------
Inferred        Grade (g/t)     Grade          Ounces (000's) Pounds (000's)
----------------------------------------------------------------------------
Tonnes                        Zn   Pb
('000)   Ag eq.    Ag   Au  (%)  (%)       Ag    Ag eq    Au      Zn     Pb
----------------------------------------------------------------------------
2,207       98.0  65.3 0.66 0.52 0.35  4,632.0  6,957.0  46.5  25,378 17,062
//et



1. Ag equivalent grade = Ag grade + (Au grade * 50) (Rounding may cause
apparent discrepancies).
2. Mineral Resources are not Mineral Reserves and do not have demonstrated
economic viability. There is no certainty that all or any part of the
estimated Mineral Resources will be converted into Mineral Reserves. All
Mineral Resources have been classified in accordance with the Canadian
Institute of Mining, Metallurgy and Petroleum (CIM), CIM Standards on
Mineral Resources and Reserves, Definitions and Guidelines prepared by the
Standards Committee on Reserve Definitions and adopted by the CIM Council
on December 11, 2005 and updated on November 27, 2010 and on May 10, 2014.
3. Two cutoffs are used for reporting the resources: 40g/t AgEq for
elevations above 270m, and 100g/t AgEq for elevations below 270m elevation.
Average surface elevations at Pinguino are around 400 metres above
sea-level.
4. MDA reports resources at cutoffs that are reasonable for deposits of
this nature given anticipated mining methods and plant processing costs,
while also considering economic conditions.
5. For the Luna, Savary and CSV veins, resources were reported only for
those that fell within a floated cone based on reasonable assumptions and
prices for resource reporting for open pit mining.
6. Grades presented are in situ and have been reported to 3m by 6m by 4m
(high) blocks.
7. Tonnes reported are for all veins, as are gold and silver grades and
ounces, but zinc and lead pounds and grades are exclusive of Luna, Savary,
Karina, and CSV veins, which did not have zinc and lead estimated.
8. All equivalent ounces for silver and gold were calculated by Argentex.



The varying cutoffs used in the resource model are given below:

Table 2: Resource estimate by cut-off grades (Ag Eq)

//st
Indicated
----------------------------------------------------------------------------
Cut Off Ag
----------------------------------------------------------------------------
Eq.                 Tonnes    Ag Eq.        Ag        Au        Zn        Pb
----------------------------------------------------------------------------
(g/t)              (000's)     (g/t)     (g/t)     (g/t)         %        %
----------------------------------------------------------------------------
20                  11,635      86.4      66.6      0.40      0.78      0.44
----------------------------------------------------------------------------
40                   6,918     125.7      97.8      0.56      0.94      0.55
----------------------------------------------------------------------------
Reported           6,281.0     132.3     103.4      0.58      0.77      0.54
----------------------------------------------------------------------------
60                   4,552     165.6     130.5      0.70      0.99      0.63
----------------------------------------------------------------------------
80                   3,229     205.2     163.9      0.83      1.02      0.68
----------------------------------------------------------------------------
100                  2,442     242.5     196.0      0.93      0.98      0.72
----------------------------------------------------------------------------
150                  1,401     332.7     276.0      1.14      0.78      0.75
----------------------------------------------------------------------------
200                    912     418.9     355.0      1.28      0.63      0.77
----------------------------------------------------------------------------

----------------------------------------------------------------------------

Indicated
----------------------------------------------------------------------------
Cut Off Ag
----------------------------------------------------------------------------
Eq.                       Ag       Ag Eq          Au          Zn          Pb
----------------------------------------------------------------------------
(g/t)             (000's oz)  (000's oz)  (000's oz) (000's lbs) (000's lbs)
----------------------------------------------------------------------------
20                    24,897      32,327         149     199,614     112,511
----------------------------------------------------------------------------
40                    21,747      27,967         124     142,729      84,365
----------------------------------------------------------------------------
Reported              20,877      26,717         117     107,225      74,993
----------------------------------------------------------------------------
60                    19,102      24,237         103      99,633      63,010
----------------------------------------------------------------------------
80                    17,014      21,304          86      72,514      48,664
----------------------------------------------------------------------------
100                   15,389      19,034          73      52,862      38,549
----------------------------------------------------------------------------
150                   12,432      14,992          51      24,154      23,237
----------------------------------------------------------------------------
200                   10,409      12,284          38      12,756      15,575
----------------------------------------------------------------------------




----------------------------------------------------------------------------
Inferred
----------------------------------------------------------------------------
Cut Off Ag
----------------------------------------------------------------------------
Eq.                 Tonnes    Ag Eq.        Ag        Au        Zn        Pb
----------------------------------------------------------------------------
(g/t)              (000's)     (g/t)     (g/t)     (g/t)         %         %
----------------------------------------------------------------------------
20                   6,043      57.6      39.3      0.37      0.64      0.29
----------------------------------------------------------------------------
40                   2,921      89.1      59.5      0.59      0.85      0.37
----------------------------------------------------------------------------
Reported             2,207      98.0      65.3      0.66      0.52      0.35
----------------------------------------------------------------------------
60                   1,656     119.9      78.5      0.83      0.91      0.43
----------------------------------------------------------------------------
80                   1,059     148.5      96.0      1.05      0.98      0.49
----------------------------------------------------------------------------
100                    699     179.3     114.1      1.30      0.96      0.53
----------------------------------------------------------------------------
150                    341     240.9     157.0      1.68      1.06      0.63
----------------------------------------------------------------------------
200                    173     307.6     216.9      1.81      0.97      0.68
----------------------------------------------------------------------------





----------------------------------------------------------------------------
Inferred
----------------------------------------------------------------------------
Cut Off Ag
----------------------------------------------------------------------------
Eq.                       Ag       Ag Eq          Au          Zn          Pb
----------------------------------------------------------------------------
(g/t)             (000's oz)  (000's oz)  (000's oz) (000's lbs) (000's lbs)
----------------------------------------------------------------------------
20                     7,631      11,206          72      84,880      38,344
----------------------------------------------------------------------------
40                     5,590       8,365          56      54,659      23,733
----------------------------------------------------------------------------
Reported               4,632       6,957          47      25,378      17,062
----------------------------------------------------------------------------
60                     4,181       6,381          44      33,083      15,619
----------------------------------------------------------------------------
80                     3,270       5,055          36      22,910      11,340
----------------------------------------------------------------------------
100                    2,565       4,030          29      14,762       8,141
----------------------------------------------------------------------------
150                    1,722       2,642          18       7,945       4,724
----------------------------------------------------------------------------
200                    1,206       1,711          10       3,694       2,584
//et

The tables below summarise the division of the resource estimate
by oxidation state, as defined from drill logs. Oxidation levels
typically range from 40-60m below the surface, although they can extend
down to approximately 130m below the surface within the veins. These
are reported at the variable cut-off grades (see note 4 above).

Table 3: Resource Composition by Oxidation State

//st
Indicated     Cut-off          Tonnes Ag eq.      Ag      Au      Zn      Pb
----------------------------------------------------------------------------
Zone          (Ag Eq g/t)    (000's)   (g/t)   (g/t)   (g/t)       %       %
----------------------------------------------------------------------------
Oxide         variable         2,802   145.2   114.1    0.62    0.07    0.32
----------------------------------------------------------------------------
Transitional  variable           717   134.5   106.6    0.56    0.23    0.41
----------------------------------------------------------------------------
Sulphide      variable         2,763   118.6    91.7    0.54    1.62    0.80
----------------------------------------------------------------------------
Total                          6,282
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Inferred      Cut-off          Tonnes Ag eq.      Ag      Au      Zn      Pb
----------------------------------------------------------------------------
Zone          (Ag Eq g/t)    (000's)   (g/t)   (g/t)   (g/t)       %       %
----------------------------------------------------------------------------
Oxide         variable           757   101.7    77.7    0.48    0.06    0.30
----------------------------------------------------------------------------
Transitional  variable           163    93.9    72.9    0.42    0.30    0.34
----------------------------------------------------------------------------
Sulphide      variable         1,287    96.5    57.1    0.79    0.77    0.38
----------------------------------------------------------------------------
Total                          2,207
----------------------------------------------------------------------------
----------------------------------------------------------------------------

--------------------------------------------------------------------------------
------------------------------------------------------------------------
Indicated     Cut-off               Ag   Ag eq      Au        Zn          Pb
----------------------------------------------------------------------------
(000's  (000's    (000's
Zone          (Ag Eq g/t)   (000's oz)     oz)     oz)      lbs) (000's lbs)
----------------------------------------------------------------------------
Oxide         variable          10,276  13,081      56     4,324     19,768
----------------------------------------------------------------------------
Transitional  variable           2,458   3,103      13     3,595      6,500
----------------------------------------------------------------------------
Sulphide      variable           8,146  10,536      48    98,550     48,487
----------------------------------------------------------------------------
Total                                   26,720     117   106,469     74,755
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Inferred      Cut-off               Ag   Ag eq      Au        Zn         Pb
----------------------------------------------------------------------------
(000's  (000's    (000's
Zone          (Ag Eq g/t)   (000's oz)     oz)     oz)      lbs) (000's lbs)
----------------------------------------------------------------------------
Oxide         variable           1,890   2,475      12     1,001      5,007
----------------------------------------------------------------------------
Transitional  variable             382     492       2     1,092      1,204
----------------------------------------------------------------------------
Sulphide      variable           2,363   3,993      33    21,907     10,818
----------------------------------------------------------------------------
Total                                    6,960      47    24,000     17,029

See notes for Table 1 for reporting details.

//et

Discussion

The addition of the Karina, Savary, Luna and CSV veins in the
Inferred category follows their discovery in the 2012 exploration
program, and follow up drilling in the oxide zone in late 2013. The
exhibited structural control of high-grade mineralisation by
cross-cutting faults could offer significant potential to identify
high-grade zones at depth. In general only the Marta Centro vein has
been drilled to any significant depth (approximately 350m). The
untested deeper extensions of the veins focusing on zones of
cross-cutting structures for high-grade shoots are targets for resource
expansion.

Of all metals listed and found in the veins, only silver, gold,
zinc, and lead were modelled. Indium occurs at Pinguino associated with
zinc in higher than anomalous grades in the polymetallic veins, but it
was not modelled.

With only 12 of the 70 or more discovered veins included in the
current estimate, the Company continues to believe in the potential of
the mineral resource at Pinguino.

QAQC

A best-practices and increasingly stringent protocol for the
collection, preparation and submission of rock samples for analysis was
followed throughout the phases of exploration at Pinguino. All samples
were analyzed by Acme Analytical Laboratories ("Acme Labs") except for
the 2006 drilling of Phase 2 which were sent to Alex Stewart
(Assayers), Argentina, S.A. The current analytical protocol, which was
largely instituted in 2007 for the Phase V drilling, and which
constitutes the bulk of the assay data that contributed to the resource
model, begins with all field samples being submitted to Acme Labs'
preparation laboratory in Mendoza, Argentina. From there, the sample
pulps were sent to its laboratory in Vancouver for multi-element ICP-MS
analysis (1DX procedure). Samples overlimit in silver, lead, zinc or
copper were rerun by a high- detection limit ICP-ES procedure (Acme
Labs code 7AR). Samples overlimit in silver from that procedure and,
more recently, all gold assays )300 ppb were rerun by fire assay (G6
procedure). Acme Labs is an accredited ISO 9000:2001 full-service
commercial laboratory with its head office in Vancouver. Quality
control was maintained by submitting field blanks and duplicates,
Company standards for the latest phase and by reviewing laboratory
results of its own replicates, duplicates and analytical standards.

About Pinguino

Argentex's 10,000-hectare advanced silver and gold exploration
Pinguino project is located in Argentina's Patagonia region, within the
Deseado Massif of Santa Cruz province. The Deseado Massif is an active
region of mining with four precious metal mines currently in
production, and includes multiple active advanced and early stage
exploration projects.

The Pinguino system has grown to 70+ individual veins, with a
combined strike length approaching ~113 line-kilometers. The Pinguino
project is unique within the Deseado Massif region of Santa Cruz
province in that it contains two different and spatially distinct types
of mineralization, one precious metal and the other sulphide-rich
polymetallic. The Company continues to evaluate the geological model of
sulphide-enriched potentially mineralized intrusives at depth, forming
the probable source for the polymetallic veins exposed on surface.

Pinguino is easily accessible, situated approximately 400
meters above sea level in low-relief topography. An existing system of
all-weather roads provides year-round access to the property.

The mineral resource estimate was prepared by Steven
Ristorcelli, C. P. G., Principal Geologist at Mine Development
Associates in Reno, Nevada in accordance with NI 43-101, and he is an
independent "Qualified Person" as defined by NI 43-101. Mr. S.
Ristorcelli has approved the details of the resource estimate as
contained herewith.

All other content of this press release has been reviewed and
approved by Mr. Mike Brown, MAIG, and he is a "Qualified Person" as
defined by NI 43-101.

The Company expects a complete copy of the Report will be filed
on SEDAR within 45 days of this press release.

About Argentex

Argentex Mining Corporation is an exploration company focused
on advancing its Pinguino silver-gold project in Santa Cruz, Argentina.
In total, Argentex owns 100% of the mineral rights to more than 37
properties located within approximately 136,087 hectares of highly
prospective land located in the Santa Cruz and Rio Negro provinces.

Shares of Argentex common stock trade under the symbol ATX on
the TSX Venture Exchange and under the symbol AGXMF on the OTCQB.
Neither TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

On behalf of Argentex Mining Corporation:

Michael Brown, President and CEO

Statements in this news release that are not historical facts
are forward-looking statements that are subject to risks and
uncertainties. Words such as "expects", "intends", "plans", "may",
"could", "potential", "should", "anticipates", "likely", "believes" and
words of similar import also identify forward-looking statements.
Forward-looking statements in this news release include those
concerning management's belief in the potential for the future
development of the Pinguino project, that the increase in enriched
Ag/Au grade material continues to point to the potential to evaluate a
staged development of the project, that high grade oxide material could
make an initial low cost oxide operation feasible, that these results,
coupled with the Company's understanding of the deposit and its
expansion potential, will provide a solid foundation to the Company's
recently announced strategic review and that the exhibited structural
control of high-grade mineralization by cross-cutting faults could
offer significant potential to identify high-grade zones at depth.

Actual results may differ materially from those currently
anticipated due to a number of factors beyond the Company's control.
These risks and uncertainties include, among other things, the
availability of the Company's consultants and risks that are inherent
in Argentex's operations including the risks that the Company may not
find any minerals in commercially feasible quantity or raise enough
money to fund its exploration and/or plans. These and other risks are
described in the Company's Annual Information Form and other public
disclosure documents filed on the SEDAR website maintained by the
Canadian Securities Administrators and the EDGAR website maintained by
the Securities and Exchange Commission.

TSX Venture closing price for ATX-V
Date: 2014/08/20
Closing Price: 0.07

TEL:  604-568-2496 Argentex Mining Corporation
FAX:  604-568-1540 Michael Brown, President and CEO
info@argentexmining.com
www.argentexmining.com
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1423200033TS11423201020-07140020140821