Source	Marketwire
Date	08/21/2014
Time	06:30:16 AM

Company	 ARGENTEX MINING CORPORATION
Title	Argentex Increases Pingüino Silver-Gold Project Mineral Resource Estimate 
to 26.7 Million Ounces Ag Eq. @ 132.3 g/t Ag Eq. Indicated and 7.0 Million 
Ounces Ag Eq. @ 98.0 g/t Ag Eq. Inferred.





    CDNX Symbol: ATX











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Argentex Mining Corporation

TSX VENTURE SYMBOL: ATX
OTCQB SYMBOL: AGXMF

August 21, 2014

Argentex Increases Pingüino Silver-Gold Project Mineral Resource Estimate to 
26.7 Million Ounces Ag Eq. @ 132.3 g/t Ag Eq. Indicated and 7.0 Million Ounces 
Ag Eq. @ 98.0 g/t Ag Eq. Inferred.


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Aug. 21, 2014) - Argentex Mining 
Corporation ("Argentex" or the "Company") (TSX VENTURE:ATX)(OTCQB:AGXMF) is 
pleased to announce the results of the updated National Instrument ("NI") 
43-101 compliant Mineral Resource Estimate (the Report) undertaken by Mine 
Development Associates ("MDA") of Reno, Nevada. This Report incorporates 
drilling and trenching results from 2013 on the Company's 100%-owned Pinguino 
Silver-Gold Project, located in Santa Cruz province, Argentina.

Highlights:

/T/

--  Increase in indicated category Ag eq. ounces by 13% (3.0 million
additional Ag Eq. ounces to a total of 26.7 Million Ounces Ag Eq. @
132.3 g/t Ag Eq)
--  Increase in inferred category Ag Eq. ounces by 49% (2.3 million
additional Ag Eq. ounces to a total of 7.0 Million Ounces Ag Eq. @ 98.0
g/t Ag Eq.).
--  Four new veins were added to the resource to bring the total number of
veins included in the updated resource estimate to twelve.
--  More than sixty veins remain to be fully tested in vein structures that
remain open in all directions

/T/

"This significant increase in the resource estimate follows our latest phase of 
exploration in the oxidation zone and further supports our belief in the 
potential for the future development of the Pinguino project. The increase 
resulted from the addition of four veins to the resource, as well as further 
drilling and trenching on certain veins included in the previous resource 
estimate of January 31st, 2013. The increase in enriched Ag/Au grade oxide 
material continues to point to the potential to evaluate a staged development 
of the project and while the long-term future of Pinguino lies in the primary 
mineralisation, this high-grade oxide material could make an initial low-cost 
oxide operation feasible. The oxide material is enriched in Ag/Au, whilst the 
primary mineralisation comprises either Ag-Au or Ag-Au-Zn-Pb sulphide 
mineralisation," commented Mike Brown, President and CEO of Argentex. "These 
results, coupled with our understanding of the deposit and its expansion 
potential, will provide a solid foundation to our recently announced strategic 
review.

Table 1: Resource Summary

/T/

----------------------------------------------------------------------------
Indicated       Grade (g/t)     Grade          Ounces (000's) Pounds (000's)
----------------------------------------------------------------------------
Tonnes                        Zn   Pb
('000)   Ag eq.    Ag   Au  (%)  (%)       Ag    Ag eq    Au      Zn     Pb
----------------------------------------------------------------------------
6,281      132.3 103.4 0.58 0.77 0.54 20,877.0 26,717.0 116.8 107,225 74,993
----------------------------------------------------------------------------


----------------------------------------------------------------------------
Inferred        Grade (g/t)     Grade          Ounces (000's) Pounds (000's)
----------------------------------------------------------------------------
Tonnes                        Zn   Pb
('000)   Ag eq.    Ag   Au  (%)  (%)       Ag    Ag eq    Au      Zn     Pb
----------------------------------------------------------------------------
2,207       98.0  65.3 0.66 0.52 0.35  4,632.0  6,957.0  46.5  25,378 17,062
----------------------------------------------------------------------------

1.  Ag equivalent grade = Ag grade + (Au grade (i) 50) (Rounding may cause
apparent discrepancies).
2.  Mineral Resources are not Mineral Reserves and do not have demonstrated
economic viability. There is no certainty that all or any part of the
estimated Mineral Resources will be converted into Mineral Reserves. All
Mineral Resources have been classified in accordance with the Canadian
Institute of Mining, Metallurgy and Petroleum (CIM), CIM Standards on
Mineral Resources and Reserves, Definitions and Guidelines prepared by
the Standards Committee on Reserve Definitions and adopted by the CIM
Council on December 11, 2005 and updated on November 27, 2010 and on May
10, 2014.
3.  Two cutoffs are used for reporting the resources: 40g/t AgEq for
elevations above 270m, and 100g/t AgEq for elevations below 270m
elevation. Average surface elevations at Pinguino are around 400 metres
above sea-level.
4.  MDA reports resources at cutoffs that are reasonable for deposits of
this nature given anticipated mining methods and plant processing costs,
while also considering economic conditions.
5.  For the Luna, Savary and CSV veins, resources were reported only for
those that fell within a floated cone based on reasonable assumptions
and prices for resource reporting for open pit mining.
6.  Grades presented are in situ and have been reported to 3m by 6m by 4m
(high) blocks.
7.  Tonnes reported are for all veins, as are gold and silver grades and
ounces, but zinc and lead pounds and grades are exclusive of Luna,
Savary, Karina, and CSV veins, which did not have zinc and lead
estimated.
8.  All equivalent ounces for silver and gold were calculated by Argentex.

/T/

The varying cutoffs used in the resource model are given below:

Table 2: Resource estimate by cut-off grades (Ag Eq)

/T/

----------------------------------------------------------------------------
Indicated
----------------------------------------------------------------------------
Cut Off Ag
----------------------------------------------------------------------------
Eq.                 Tonnes    Ag Eq.        Ag        Au        Zn        Pb
----------------------------------------------------------------------------
(g/t)              (000's)     (g/t)     (g/t)     (g/t)         %         %
----------------------------------------------------------------------------
20                  11,635      86.4      66.6      0.40      0.78      0.44
----------------------------------------------------------------------------
40                   6,918     125.7      97.8      0.56      0.94      0.55
----------------------------------------------------------------------------
Reported           6,281.0     132.3     103.4      0.58      0.77      0.54
----------------------------------------------------------------------------
60                   4,552     165.6     130.5      0.70      0.99      0.63
----------------------------------------------------------------------------
80                   3,229     205.2     163.9      0.83      1.02      0.68
----------------------------------------------------------------------------
100                  2,442     242.5     196.0      0.93      0.98      0.72
----------------------------------------------------------------------------
150                  1,401     332.7     276.0      1.14      0.78      0.75
----------------------------------------------------------------------------
200                    912     418.9     355.0      1.28      0.63      0.77
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Indicated
----------------------------------------------------------------------------
Cut Off Ag
----------------------------------------------------------------------------
Eq.                       Ag       Ag Eq          Au          Zn          Pb
----------------------------------------------------------------------------
(g/t)             (000's oz)  (000's oz)  (000's oz) (000's lbs) (000's lbs)
----------------------------------------------------------------------------
20                    24,897      32,327         149     199,614     112,511
----------------------------------------------------------------------------
40                    21,747      27,967         124     142,729      84,365
----------------------------------------------------------------------------
Reported              20,877      26,717         117     107,225      74,993
----------------------------------------------------------------------------
60                    19,102      24,237         103      99,633      63,010
----------------------------------------------------------------------------
80                    17,014      21,304          86      72,514      48,664
----------------------------------------------------------------------------
100                   15,389      19,034          73      52,862      38,549
----------------------------------------------------------------------------
150                   12,432      14,992          51      24,154      23,237
----------------------------------------------------------------------------
200                   10,409      12,284          38      12,756      15,575
----------------------------------------------------------------------------



----------------------------------------------------------------------------
Inferred
----------------------------------------------------------------------------
Cut Off Ag
----------------------------------------------------------------------------
Eq.                 Tonnes    Ag Eq.        Ag        Au        Zn        Pb
----------------------------------------------------------------------------
(g/t)              (000's)     (g/t)     (g/t)     (g/t)         %         %
----------------------------------------------------------------------------
20                   6,043      57.6      39.3      0.37      0.64      0.29
----------------------------------------------------------------------------
40                   2,921      89.1      59.5      0.59      0.85      0.37
----------------------------------------------------------------------------
Reported             2,207      98.0      65.3      0.66      0.52      0.35
----------------------------------------------------------------------------
60                   1,656     119.9      78.5      0.83      0.91      0.43
----------------------------------------------------------------------------
80                   1,059     148.5      96.0      1.05      0.98      0.49
----------------------------------------------------------------------------
100                    699     179.3     114.1      1.30      0.96      0.53
----------------------------------------------------------------------------
150                    341     240.9     157.0      1.68      1.06      0.63
----------------------------------------------------------------------------
200                    173     307.6     216.9      1.81      0.97      0.68
----------------------------------------------------------------------------




----------------------------------------------------------------------------
Inferred
----------------------------------------------------------------------------
Cut Off Ag
----------------------------------------------------------------------------
Eq.                       Ag       Ag Eq          Au          Zn          Pb
----------------------------------------------------------------------------
(g/t)             (000's oz)  (000's oz)  (000's oz) (000's lbs) (000's lbs)
----------------------------------------------------------------------------
20                     7,631      11,206          72      84,880      38,344
----------------------------------------------------------------------------
40                     5,590       8,365          56      54,659      23,733
----------------------------------------------------------------------------
Reported               4,632       6,957          47      25,378      17,062
----------------------------------------------------------------------------
60                     4,181       6,381          44      33,083      15,619
----------------------------------------------------------------------------
80                     3,270       5,055          36      22,910      11,340
----------------------------------------------------------------------------
100                    2,565       4,030          29      14,762       8,141
----------------------------------------------------------------------------
150                    1,722       2,642          18       7,945       4,724
----------------------------------------------------------------------------
200                    1,206       1,711          10       3,694       2,584
----------------------------------------------------------------------------

/T/

The tables below summarise the division of the resource estimate by oxidation 
state, as defined from drill logs. Oxidation levels typically range from 40-60m 
below the surface, although they can extend down to approximately 130m below 
the surface within the veins. These are reported at the variable cut-off grades 
(see note 4 above).

Table 3: Resource Composition by Oxidation State

/T/

----------------------------------------------------------------------------
----------------------------------------------------------------------------
Indicated     Cut-off          Tonnes Ag eq.      Ag      Au      Zn      Pb
----------------------------------------------------------------------------
Zone          (Ag Eq g/t)    (000's)   (g/t)   (g/t)   (g/t)       %       %
----------------------------------------------------------------------------
Oxide         variable         2,802   145.2   114.1    0.62    0.07    0.32
----------------------------------------------------------------------------
Transitional  variable           717   134.5   106.6    0.56    0.23    
0.41----------------------------------------------------------------------------
Sulphide      variable         2,763   118.6    91.7    0.54    1.62    0.80
----------------------------------------------------------------------------
Total                          6,282
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Inferred      Cut-off          Tonnes Ag eq.      Ag      Au      Zn      Pb
----------------------------------------------------------------------------
Zone          (Ag Eq g/t)    (000's)   (g/t)   (g/t)   (g/t)       %       %
----------------------------------------------------------------------------
Oxide         variable           757   101.7    77.7    0.48    0.06    0.30
----------------------------------------------------------------------------
Transitional  variable           163    93.9    72.9    0.42    0.30    0.34
----------------------------------------------------------------------------
Sulphide      variable         1,287    96.5    57.1    0.79    0.77    0.38
----------------------------------------------------------------------------
Total                          2,207
----------------------------------------------------------------------------
----------------------------------------------------------------------------

----------------------------------------------------------------------------
----------------------------------------------------------------------------
Indicated     Cut-off               Ag   Ag eq      Au        Zn          Pb
----------------------------------------------------------------------------
(000's  (000's    (000's
Zone          (Ag Eq g/t)   (000's oz)     oz)     oz)      lbs) (000's lbs)
----------------------------------------------------------------------------
Oxide         variable          10,276  13,081      56     4,324      19,768
----------------------------------------------------------------------------
Transitional  variable           2,458   3,103      13     3,595       6,500
----------------------------------------------------------------------------
Sulphide      variable           8,146  10,536      48    98,550      48,487
----------------------------------------------------------------------------
Total                                   26,720     117   106,469      74,755
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Inferred      Cut-off               Ag   Ag eq      Au        Zn          Pb
----------------------------------------------------------------------------
(000's  (000's    (000's
Zone          (Ag Eq g/t)   (000's oz)     oz)     oz)      lbs) (000's lbs)
----------------------------------------------------------------------------
Oxide         variable           1,890   2,475      12     1,001       5,007
----------------------------------------------------------------------------
Transitional  variable             382     492       2     1,092       1,204
----------------------------------------------------------------------------
Sulphide      variable           2,363   3,993      33    21,907      10,818
----------------------------------------------------------------------------
Total                                    6,960      47    24,000      17,029
----------------------------------------------------------------------------
----------------------------------------------------------------------------
See notes for Table 1 for reporting details.

/T/

Discussion

The addition of the Karina, Savary, Luna and CSV veins in the Inferred category 
follows their discovery in the 2012 exploration program, and follow up drilling 
in the oxide zone in late 2013. The exhibited structural control of high-grade 
mineralisation by cross-cutting faults could offer significant potential to 
identify high-grade zones at depth. In general only the Marta Centro vein has 
been drilled to any significant depth (approximately 350m). The untested deeper 
extensions of the veins focusing on zones of cross-cutting structures for 
high-grade shoots are targets for resource expansion.

Of all metals listed and found in the veins, only silver, gold, zinc, and lead 
were modelled. Indium occurs at Pinguino associated with zinc in higher than 
anomalous grades in the polymetallic veins, but it was not modelled.

With only 12 of the 70 or more discovered veins included in the current 
estimate, the Company continues to believe in the potential of the mineral 
resource at Pinguino.

QAQC

A best-practices and increasingly stringent protocol for the collection, 
preparation and submission of rock samples for analysis was followed throughout 
the phases of exploration at Pinguino. All samples were analyzed by Acme 
Analytical Laboratories ("Acme Labs") except for the 2006 drilling of Phase 2 
which were sent to Alex Stewart (Assayers), Argentina, S.A. The current 
analytical protocol, which was largely instituted in 2007 for the Phase V 
drilling, and which constitutes the bulk of the assay data that contributed to 
the resource model, begins with all field samples being submitted to Acme Labs' 
preparation laboratory in Mendoza, Argentina. From there, the sample pulps were 
sent to its laboratory in Vancouver for multi-element ICP-MS analysis (1DX 
procedure). Samples overlimit in silver, lead, zinc or copper were rerun by a 
high- detection limit ICP-ES procedure (Acme Labs code 7AR). Samples overlimit 
in silver from that procedure and, more recently, all gold assays greater than 
300 ppb were rerun by fire assay (G6 procedure). Acme Labs is an accredited ISO 
9000:2001 full-service commercial laboratory with its head office in Vancouver. 
Quality control was maintained by submitting field blanks and duplicates, 
Company standards for the latest phase and by reviewing laboratory results of 
its own replicates, duplicates and analytical standards.

About Pinguino

Argentex's 10,000-hectare advanced silver and gold exploration Pinguino project 
is located in Argentina's Patagonia region, within the Deseado Massif of Santa 
Cruz province. The Deseado Massif is an active region of mining with four 
precious metal mines currently in production, and includes multiple active 
advanced and early stage exploration projects.

The Pinguino system has grown to 70+ individual veins, with a combined strike 
length approaching approx. 113 line-kilometers. The Pinguino project is unique 
within the Deseado Massif region of Santa Cruz province in that it contains two 
different and spatially distinct types of mineralization, one precious metal 
and the other sulphide-rich polymetallic. The Company continues to evaluate the 
geological model of sulphide-enriched potentially mineralized intrusives at 
depth, forming the probable source for the polymetallic veins exposed on 
surface.

Pinguino is easily accessible, situated approximately 400 meters above sea 
level in low-relief topography. An existing system of all-weather roads 
provides year-round access to the property.

The mineral resource estimate was prepared by Steven Ristorcelli, C. P. G., 
Principal Geologist at Mine Development Associates in Reno, Nevada in 
accordance with NI 43-101, and he is an independent "Qualified Person" as 
defined by NI 43-101. Mr. S. Ristorcelli has approved the details of the 
resource estimate as contained herewith.

All other content of this press release has been reviewed and approved by Mr. 
Mike Brown, MAIG, and he is a "Qualified Person" as defined by NI 43-101.

The Company expects a complete copy of the Report will be filed on SEDAR within 
45 days of this press release.

About Argentex

Argentex Mining Corporation is an exploration company focused on advancing its 
Pinguino silver-gold project in Santa Cruz, Argentina. In total, Argentex owns 
100% of the mineral rights to more than 37 properties located within 
approximately 136,087 hectares of highly prospective land located in the Santa 
Cruz and Rio Negro provinces.

Shares of Argentex common stock trade under the symbol ATX on the TSX Venture 
Exchange and under the symbol AGXMF on the OTCQB. Neither TSX Venture Exchange 
nor its Regulation Services Provider (as that term is defined in the policies 
of the TSX Venture Exchange) accepts responsibility for the adequacy or 
accuracy of this release.

On behalf of Argentex Mining Corporation:

Michael Brown, President and CEO

Statements in this news release that are not historical facts are 
forward-looking statements that are subject to risks and uncertainties. Words 
such as "expects", "intends", "plans", "may", "could", "potential", "should", 
"anticipates", "likely", "believes" and words of similar import also identify 
forward-looking statements. Forward-looking statements in this news release 
include those concerning management's belief in the potential for the future 
development of the Pinguino project, that the increase in enriched Ag/Au grade 
material continues to point to the potential to evaluate a staged development 
of the project, that high grade oxide material could make an initial low cost 
oxide operation feasible, that these results, coupled with the Company's 
understanding of the deposit and its expansion potential, will provide a solid 
foundation to the Company's recently announced strategic review and that the 
exhibited structural control of high-grade mineralization by cross-cutting 
faults could offer significant potential to identify high-grade zones at depth.

Actual results may differ materially from those currently anticipated due to a 
number of factors beyond the Company's control. These risks and uncertainties 
include, among other things, the availability of the Company's consultants and 
risks that are inherent in Argentex's operations including the risks that the 
Company may not find any minerals in commercially feasible quantity or raise 
enough money to fund its exploration and/or plans. These and other risks are 
described in the Company's Annual Information Form and other public disclosure 
documents filed on the SEDAR website maintained by the Canadian Securities 
Administrators and the EDGAR website maintained by the Securities and Exchange 
Commission.

- 30 -

CONTACT INFO:

Argentex Mining Corporation
Michael Brown
President and CEO
604-568-2496
Fax: 604-568-1540
info@argentexmining.com
www.argentexmining.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=495656400


NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Argentex Mining Corporation

TSX VENTURE SYMBOL: ATX
OTCQB SYMBOL: AGXMF

August 21, 2014

Argentex Increases Pingüino Silver-Gold Project Mineral Resource Estimate to 
26.7 Million Ounces Ag Eq. @ 132.3 g/t Ag Eq. Indicated and 7.0 Million Ounces 
Ag Eq. @ 98.0 g/t Ag Eq. Inferred.


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Aug. 21, 2014) - Argentex Mining 
Corporation ("Argentex" or the "Company") (TSX VENTURE:ATX)(OTCQB:AGXMF) is 
pleased to announce the results of the updated National Instrument ("NI") 
43-101 compliant Mineral Resource Estimate (the Report) undertaken by Mine 
Development Associates ("MDA") of Reno, Nevada. This Report incorporates 
drilling and trenching results from 2013 on the Company's 100%-owned Pinguino 
Silver-Gold Project, located in Santa Cruz province, Argentina.

Highlights:

/T/

--  Increase in indicated category Ag eq. ounces by 13% (3.0 million
additional Ag Eq. ounces to a total of 26.7 Million Ounces Ag Eq. @
132.3 g/t Ag Eq)
--  Increase in inferred category Ag Eq. ounces by 49% (2.3 million
additional Ag Eq. ounces to a total of 7.0 Million Ounces Ag Eq. @ 98.0
g/t Ag Eq.).
--  Four new veins were added to the resource to bring the total number of
veins included in the updated resource estimate to twelve.
--  More than sixty veins remain to be fully tested in vein structures that
remain open in all directions

/T/

"This significant increase in the resource estimate follows our latest phase of 
exploration in the oxidation zone and further supports our belief in the 
potential for the future development of the Pinguino project. The increase 
resulted from the addition of four veins to the resource, as well as further 
drilling and trenching on certain veins included in the previous resource 
estimate of January 31st, 2013. The increase in enriched Ag/Au grade oxide 
material continues to point to the potential to evaluate a staged development 
of the project and while the long-term future of Pinguino lies in the primary 
mineralisation, this high-grade oxide material could make an initial low-cost 
oxide operation feasible. The oxide material is enriched in Ag/Au, whilst the 
primary mineralisation comprises either Ag-Au or Ag-Au-Zn-Pb sulphide 
mineralisation," commented Mike Brown, President and CEO of Argentex. "These 
results, coupled with our understanding of the deposit and its expansion 
potential, will provide a solid foundation to our recently announced strategic 
review.

Table 1: Resource Summary

/T/

----------------------------------------------------------------------------
Indicated       Grade (g/t)     Grade          Ounces (000's) Pounds (000's)
----------------------------------------------------------------------------
Tonnes                        Zn   Pb
('000)   Ag eq.    Ag   Au  (%)  (%)       Ag    Ag eq    Au      Zn     Pb
----------------------------------------------------------------------------
6,281      132.3 103.4 0.58 0.77 0.54 20,877.0 26,717.0 116.8 107,225 74,993
----------------------------------------------------------------------------


----------------------------------------------------------------------------
Inferred        Grade (g/t)     Grade          Ounces (000's) Pounds (000's)
----------------------------------------------------------------------------
Tonnes                        Zn   Pb
('000)   Ag eq.    Ag   Au  (%)  (%)       Ag    Ag eq    Au      Zn     Pb
----------------------------------------------------------------------------
2,207       98.0  65.3 0.66 0.52 0.35  4,632.0  6,957.0  46.5  25,378 17,062
----------------------------------------------------------------------------

1.  Ag equivalent grade = Ag grade + (Au grade (i) 50) (Rounding may cause
apparent discrepancies).
2.  Mineral Resources are not Mineral Reserves and do not have demonstrated
economic viability. There is no certainty that all or any part of the
estimated Mineral Resources will be converted into Mineral Reserves. All
Mineral Resources have been classified in accordance with the Canadian
Institute of Mining, Metallurgy and Petroleum (CIM), CIM Standards on
Mineral Resources and Reserves, Definitions and Guidelines prepared by
the Standards Committee on Reserve Definitions and adopted by the CIM
Council on December 11, 2005 and updated on November 27, 2010 and on May
10, 2014.
3.  Two cutoffs are used for reporting the resources: 40g/t AgEq for
elevations above 270m, and 100g/t AgEq for elevations below 270m
elevation. Average surface elevations at Pinguino are around 400 metres
above sea-level.
4.  MDA reports resources at cutoffs that are reasonable for deposits of
this nature given anticipated mining methods and plant processing costs,
while also considering economic conditions.
5.  For the Luna, Savary and CSV veins, resources were reported only for
those that fell within a floated cone based on reasonable assumptions
and prices for resource reporting for open pit mining.
6.  Grades presented are in situ and have been reported to 3m by 6m by 4m
(high) blocks.
7.  Tonnes reported are for all veins, as are gold and silver grades and
ounces, but zinc and lead pounds and grades are exclusive of Luna,
Savary, Karina, and CSV veins, which did not have zinc and lead
estimated.
8.  All equivalent ounces for silver and gold were calculated by Argentex.

/T/

The varying cutoffs used in the resource model are given below:

Table 2: Resource estimate by cut-off grades (Ag Eq)

/T/

----------------------------------------------------------------------------
Indicated
----------------------------------------------------------------------------
Cut Off Ag
----------------------------------------------------------------------------
Eq.                 Tonnes    Ag Eq.        Ag        Au        Zn        Pb
----------------------------------------------------------------------------
(g/t)              (000's)     (g/t)     (g/t)     (g/t)         %         %
----------------------------------------------------------------------------
20                  11,635      86.4      66.6      0.40      0.78      0.44
----------------------------------------------------------------------------
40                   6,918     125.7      97.8      0.56      0.94      0.55
----------------------------------------------------------------------------
Reported           6,281.0     132.3     103.4      0.58      0.77      0.54
----------------------------------------------------------------------------
60                   4,552     165.6     130.5      0.70      0.99      0.63
----------------------------------------------------------------------------
80                   3,229     205.2     163.9      0.83      1.02      0.68
----------------------------------------------------------------------------
100                  2,442     242.5     196.0      0.93      0.98      0.72
----------------------------------------------------------------------------
150                  1,401     332.7     276.0      1.14      0.78      0.75
----------------------------------------------------------------------------
200                    912     418.9     355.0      1.28      0.63      0.77
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Indicated
----------------------------------------------------------------------------
Cut Off Ag
----------------------------------------------------------------------------
Eq.                       Ag       Ag Eq          Au          Zn          Pb
----------------------------------------------------------------------------
(g/t)             (000's oz)  (000's oz)  (000's oz) (000's lbs) (000's lbs)
----------------------------------------------------------------------------
20                    24,897      32,327         149     199,614     112,511
----------------------------------------------------------------------------
40                    21,747      27,967         124     142,729      84,365
----------------------------------------------------------------------------
Reported              20,877      26,717         117     107,225      74,993
----------------------------------------------------------------------------
60                    19,102      24,237         103      99,633      63,010
----------------------------------------------------------------------------
80                    17,014      21,304          86      72,514      48,664
----------------------------------------------------------------------------
100                   15,389      19,034          73      52,862      38,549
----------------------------------------------------------------------------
150                   12,432      14,992          51      24,154      23,237
----------------------------------------------------------------------------
200                   10,409      12,284          38      12,756      15,575
----------------------------------------------------------------------------



----------------------------------------------------------------------------
Inferred
----------------------------------------------------------------------------
Cut Off Ag
----------------------------------------------------------------------------
Eq.                 Tonnes    Ag Eq.        Ag        Au        Zn        Pb
----------------------------------------------------------------------------
(g/t)              (000's)     (g/t)     (g/t)     (g/t)         %         %
----------------------------------------------------------------------------
20                   6,043      57.6      39.3      0.37      0.64      0.29
----------------------------------------------------------------------------
40                   2,921      89.1      59.5      0.59      0.85      0.37
----------------------------------------------------------------------------
Reported             2,207      98.0      65.3      0.66      0.52      0.35
----------------------------------------------------------------------------
60                   1,656     119.9      78.5      0.83      0.91      0.43
----------------------------------------------------------------------------
80                   1,059     148.5      96.0      1.05      0.98      0.49
----------------------------------------------------------------------------
100                    699     179.3     114.1      1.30      0.96      0.53
----------------------------------------------------------------------------
150                    341     240.9     157.0      1.68      1.06      0.63
----------------------------------------------------------------------------
200                    173     307.6     216.9      1.81      0.97      0.68
----------------------------------------------------------------------------




----------------------------------------------------------------------------
Inferred
----------------------------------------------------------------------------
Cut Off Ag
----------------------------------------------------------------------------
Eq.                       Ag       Ag Eq          Au          Zn          Pb
----------------------------------------------------------------------------
(g/t)             (000's oz)  (000's oz)  (000's oz) (000's lbs) (000's lbs)
----------------------------------------------------------------------------
20                     7,631      11,206          72      84,880      38,344
----------------------------------------------------------------------------
40                     5,590       8,365          56      54,659      23,733
----------------------------------------------------------------------------
Reported               4,632       6,957          47      25,378      17,062
----------------------------------------------------------------------------
60                     4,181       6,381          44      33,083      15,619
----------------------------------------------------------------------------
80                     3,270       5,055          36      22,910      11,340
----------------------------------------------------------------------------
100                    2,565       4,030          29      14,762       8,141
----------------------------------------------------------------------------
150                    1,722       2,642          18       7,945       4,724
----------------------------------------------------------------------------
200                    1,206       1,711          10       3,694       2,584
----------------------------------------------------------------------------

/T/

The tables below summarise the division of the resource estimate by oxidation 
state, as defined from drill logs. Oxidation levels typically range from 40-60m 
below the surface, although they can extend down to approximately 130m below 
the surface within the veins. These are reported at the variable cut-off grades 
(see note 4 above).

Table 3: Resource Composition by Oxidation State

/T/

----------------------------------------------------------------------------
----------------------------------------------------------------------------
Indicated     Cut-off          Tonnes Ag eq.      Ag      Au      Zn      Pb
----------------------------------------------------------------------------
Zone          (Ag Eq g/t)    (000's)   (g/t)   (g/t)   (g/t)       %       %
----------------------------------------------------------------------------
Oxide         variable         2,802   145.2   114.1    0.62    0.07    0.32
----------------------------------------------------------------------------
Transitional  variable           717   134.5   106.6    0.56    0.23    
0.41----------------------------------------------------------------------------
Sulphide      variable         2,763   118.6    91.7    0.54    1.62    0.80
----------------------------------------------------------------------------
Total                          6,282
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Inferred      Cut-off          Tonnes Ag eq.      Ag      Au      Zn      Pb
----------------------------------------------------------------------------
Zone          (Ag Eq g/t)    (000's)   (g/t)   (g/t)   (g/t)       %       %
----------------------------------------------------------------------------
Oxide         variable           757   101.7    77.7    0.48    0.06    0.30
----------------------------------------------------------------------------
Transitional  variable           163    93.9    72.9    0.42    0.30    0.34
----------------------------------------------------------------------------
Sulphide      variable         1,287    96.5    57.1    0.79    0.77    0.38
----------------------------------------------------------------------------
Total                          2,207
----------------------------------------------------------------------------
----------------------------------------------------------------------------

----------------------------------------------------------------------------
----------------------------------------------------------------------------
Indicated     Cut-off               Ag   Ag eq      Au        Zn          Pb
----------------------------------------------------------------------------
(000's  (000's    (000's
Zone          (Ag Eq g/t)   (000's oz)     oz)     oz)      lbs) (000's lbs)
----------------------------------------------------------------------------
Oxide         variable          10,276  13,081      56     4,324      19,768
----------------------------------------------------------------------------
Transitional  variable           2,458   3,103      13     3,595       6,500
----------------------------------------------------------------------------
Sulphide      variable           8,146  10,536      48    98,550      48,487
----------------------------------------------------------------------------
Total                                   26,720     117   106,469      74,755
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Inferred      Cut-off               Ag   Ag eq      Au        Zn          Pb
----------------------------------------------------------------------------
(000's  (000's    (000's
Zone          (Ag Eq g/t)   (000's oz)     oz)     oz)      lbs) (000's lbs)
----------------------------------------------------------------------------
Oxide         variable           1,890   2,475      12     1,001       5,007
----------------------------------------------------------------------------
Transitional  variable             382     492       2     1,092       1,204
----------------------------------------------------------------------------
Sulphide      variable           2,363   3,993      33    21,907      10,818
----------------------------------------------------------------------------
Total                                    6,960      47    24,000      17,029
----------------------------------------------------------------------------
----------------------------------------------------------------------------
See notes for Table 1 for reporting details.

/T/

Discussion

The addition of the Karina, Savary, Luna and CSV veins in the Inferred category 
follows their discovery in the 2012 exploration program, and follow up drilling 
in the oxide zone in late 2013. The exhibited structural control of high-grade 
mineralisation by cross-cutting faults could offer significant potential to 
identify high-grade zones at depth. In general only the Marta Centro vein has 
been drilled to any significant depth (approximately 350m). The untested deeper 
extensions of the veins focusing on zones of cross-cutting structures for 
high-grade shoots are targets for resource expansion.

Of all metals listed and found in the veins, only silver, gold, zinc, and lead 
were modelled. Indium occurs at Pinguino associated with zinc in higher than 
anomalous grades in the polymetallic veins, but it was not modelled.

With only 12 of the 70 or more discovered veins included in the current 
estimate, the Company continues to believe in the potential of the mineral 
resource at Pinguino.

QAQC

A best-practices and increasingly stringent protocol for the collection, 
preparation and submission of rock samples for analysis was followed throughout 
the phases of exploration at Pinguino. All samples were analyzed by Acme 
Analytical Laboratories ("Acme Labs") except for the 2006 drilling of Phase 2 
which were sent to Alex Stewart (Assayers), Argentina, S.A. The current 
analytical protocol, which was largely instituted in 2007 for the Phase V 
drilling, and which constitutes the bulk of the assay data that contributed to 
the resource model, begins with all field samples being submitted to Acme Labs' 
preparation laboratory in Mendoza, Argentina. From there, the sample pulps were 
sent to its laboratory in Vancouver for multi-element ICP-MS analysis (1DX 
procedure). Samples overlimit in silver, lead, zinc or copper were rerun by a 
high- detection limit ICP-ES procedure (Acme Labs code 7AR). Samples overlimit 
in silver from that procedure and, more recently, all gold assays greater than 
300 ppb were rerun by fire assay (G6 procedure). Acme Labs is an accredited ISO 
9000:2001 full-service commercial laboratory with its head office in Vancouver. 
Quality control was maintained by submitting field blanks and duplicates, 
Company standards for the latest phase and by reviewing laboratory results of 
its own replicates, duplicates and analytical standards.

About Pinguino

Argentex's 10,000-hectare advanced silver and gold exploration Pinguino project 
is located in Argentina's Patagonia region, within the Deseado Massif of Santa 
Cruz province. The Deseado Massif is an active region of mining with four 
precious metal mines currently in production, and includes multiple active 
advanced and early stage exploration projects.

The Pinguino system has grown to 70+ individual veins, with a combined strike 
length approaching approx. 113 line-kilometers. The Pinguino project is unique 
within the Deseado Massif region of Santa Cruz province in that it contains two 
different and spatially distinct types of mineralization, one precious metal 
and the other sulphide-rich polymetallic. The Company continues to evaluate the 
geological model of sulphide-enriched potentially mineralized intrusives at 
depth, forming the probable source for the polymetallic veins exposed on 
surface.

Pinguino is easily accessible, situated approximately 400 meters above sea 
level in low-relief topography. An existing system of all-weather roads 
provides year-round access to the property.

The mineral resource estimate was prepared by Steven Ristorcelli, C. P. G., 
Principal Geologist at Mine Development Associates in Reno, Nevada in 
accordance with NI 43-101, and he is an independent "Qualified Person" as 
defined by NI 43-101. Mr. S. Ristorcelli has approved the details of the 
resource estimate as contained herewith.

All other content of this press release has been reviewed and approved by Mr. 
Mike Brown, MAIG, and he is a "Qualified Person" as defined by NI 43-101.

The Company expects a complete copy of the Report will be filed on SEDAR within 
45 days of this press release.

About Argentex

Argentex Mining Corporation is an exploration company focused on advancing its 
Pinguino silver-gold project in Santa Cruz, Argentina. In total, Argentex owns 
100% of the mineral rights to more than 37 properties located within 
approximately 136,087 hectares of highly prospective land located in the Santa 
Cruz and Rio Negro provinces.

Shares of Argentex common stock trade under the symbol ATX on the TSX Venture 
Exchange and under the symbol AGXMF on the OTCQB. Neither TSX Venture Exchange 
nor its Regulation Services Provider (as that term is defined in the policies 
of the TSX Venture Exchange) accepts responsibility for the adequacy or 
accuracy of this release.

On behalf of Argentex Mining Corporation:

Michael Brown, President and CEO

Statements in this news release that are not historical facts are 
forward-looking statements that are subject to risks and uncertainties. Words 
such as "expects", "intends", "plans", "may", "could", "potential", "should", 
"anticipates", "likely", "believes" and words of similar import also identify 
forward-looking statements. Forward-looking statements in this news release 
include those concerning management's belief in the potential for the future 
development of the Pinguino project, that the increase in enriched Ag/Au grade 
material continues to point to the potential to evaluate a staged development 
of the project, that high grade oxide material could make an initial low cost 
oxide operation feasible, that these results, coupled with the Company's 
understanding of the deposit and its expansion potential, will provide a solid 
foundation to the Company's recently announced strategic review and that the 
exhibited structural control of high-grade mineralization by cross-cutting 
faults could offer significant potential to identify high-grade zones at depth.

Actual results may differ materially from those currently anticipated due to a 
number of factors beyond the Company's control. These risks and uncertainties 
include, among other things, the availability of the Company's consultants and 
risks that are inherent in Argentex's operations including the risks that the 
Company may not find any minerals in commercially feasible quantity or raise 
enough money to fund its exploration and/or plans. These and other risks are 
described in the Company's Annual Information Form and other public disclosure 
documents filed on the SEDAR website maintained by the Canadian Securities 
Administrators and the EDGAR website maintained by the Securities and Exchange 
Commission.

- 30 -

CONTACT INFO:

Argentex Mining Corporation
Michael Brown
President and CEO
604-568-2496
Fax: 604-568-1540
info@argentexmining.com
www.argentexmining.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=495656400