Source	MARKET NEWS
Date	08/01/2014
Time	09:12:10 AM

Company	 Colt Resources Inc.
Title	Encouraging 
Results from the Gap Zone at its Tab





    CDNX Symbol: GTP











Press Release	





COLT RESOURCES INC ("GTP-V;COLTF-0")
- Encouraging Results from the Gap Zone at its Tabuaco Tungsten
- Project, Northern Portugal

Colt Resources Inc. ("Colt" or the "Company") is pleased to
announce positive results from intercepts from two of the first three
holes recently drilled in the Gap Zone at its Tabuaco Tungsten Project
(Figure 1), located in northern Portugal, as part of its resource
expansion drilling program started on June 18th (See press release of
June 16th,2014).

The initial three holes of this latest phase of drilling, DHT-113,
DHT-114 and DHT-115 (Figure 2), have focused on testing the ground
close to an isolated hole completed in December 2012, DHT-88, which
intersected rich tungsten mineralization separate from the Sao Pedro
das Aguias and Aveleira deposits (see press release of January 30th,
2013).  This isolated hole was not included with those used to estimate
resources that formed the basis for the Preliminary Economic Assessment
published in Q3, 2013 (See press release of September 4th, 2013).

Initial visual inspection of the mineralized skarns intersected by
all three holes, both under natural light and short-wave UV-light
indicated that in general they compared very well, both in terms of
mineralogy and texture, with hole DHT-88.  Given the very promising
visual results, sampling and assaying of the mineralized drill core of
holes DHT-113 and DHT-115 was fast-tracked and assay results are
presented on Table 1.  The results for DHT-114 are pending.

The rock mechanics conditions of the entire sequence intersected
by these holes (both the mineralized zones and the hangingwall rocks)
are very good and appear to be superior to those encountered elsewhere
on the project.

The three initial holes of this latest program are located within
100m of DHT-88 and strongly suggest the presence of a previously
undetected zone of mineralization unrelated to either the Sao Pedro das
Aguias or Aveleira deposits.

Table 1

Main WO3 mineralized intervals of hole DHT-88 (assays previously
reported) and assay results from Holes DHT-113, DHT-114 and DHT-115

http://www.newswire.ca/en/story/1393670/colt-resources-reports-encouraging-
results-from-the-gap-zone-at-its-tabuaco-tungsten-project-northern-portugal



Interpretation and Follow-up

Holes DHT-114, DHT-113 and DHT-115 (from SE to NW) appear to have
intersected mineralized skarns similar to that intersected by DHT-88
over a total strike length of greater than 100 meters, located
approximately 300m NW of the Sao Pedro das Aguias resource area, and
approximately 300m south of the Aveleira resource area (Figures 1 and
2).

This mineralization is interpreted to represent a previously
unrecognized deposit at Tabuaco, physically separated from either Sao
Pedro das Aguias or Aveleira deposits. It is suspected that the
separation between these three deposits could be the result of a
combination of Variscan folding with late faulting, but this remains to
be confirmed.

It is hypothesized that the new deposit may extend further along
strike to the NW, as well as down-dip to the SW underneath the granite
body. The program is continuing and a series of follow-up drill holes
are being drilled close by so as to develop a better understanding of
the 3D geometry of this new zone.

"We are very pleased with these results from Tabuaco and look
forward to updating our shareholders in the very near future with
further developments on this ongoing resource expansion program which
is off to an excellent start", stated Nikolas Perrault, Colt President
and CEO

Quality Assurance / Quality Control (QA/QC)

All drill core is transported by Company personnel from drill site
to a nearby secure storage facility for logging and sampling.

Sampling intervals for gold mineralization are defined after core
logging and determination of probable high grade zones based on visible
mineralisation and favourable structure, while the sampling intervals
for the tungsten mineralization are defined after core logging and
determination of scheelite content by examination under short-wave
UV-light.

One half of the core is sent for analysis, while the other half is
retained in the core boxes for future reference.

All samples are sent by courier to ALS Chemex's facility in
Seville, Spain, where they undergo sample preparation.

Gold analysis for all samples is done via method "Au - AA24" (Au
by fire assay and AAS, 50g nominal sample weight). The detection limit
for this method is 5 ppb. For every sample with Au values over 1 ppm,
the pulp is re-analyzed by method "Au - GRA22" (Au by fire assay and
gravimetric finish, 50g nominal sample weight). The detection range for
this method is 0.05-1000 ppm.

Tungsten and tin are analyzed using a metaborate fusion followed
by XRF. Assay results for tungsten are reported by the laboratory as
W%. WO3 values are calculated using a conversion factor of 1.2611.

A set of standards and blanks has been inserted by Colt into the
drill sample stream on a regular basis in addition to the laboratory's
own internal QA/QC standards and duplicates. QA/QC results to date are
well within the accepted norm.

About Colt Resources Inc.

Colt Resources Inc. (www.coltresources.com) is a Canadian mining
exploration and development company engaged in acquiring, exploring,
and developing mineral properties with an emphasis on gold and
tungsten. It is currently focused on advanced stage exploration
projects in Portugal and securing advanced stage mining projects.

SRK (ES) Managing Director - Gareth O'Donovan CEng MSc BA (Hons)
FIMMM FGS, is an independent Qualified Person, as defined in NI 43-101,
for Colt's projects in Portugal. Mr. O'Donovan has reviewed the content
of this press release, and consents to the information provided and the
form and context in which it appears.

The Company's shares trade on the TSX-V, symbol: GTP; the
Frankfurt Stock Exchange, symbol: P01; and, the OTCQX, symbol: COLTF.

SOURCE  Colt Resources Inc.

PDF available at:
http://stream1.newswire.ca/media/2014/08/01/20140801_C9256_DOC_EN_42321.pdf


ENQUIRIES:
Nikolas Perrault, CFA
President & CEO
Colt Resources Inc.
Tel: +351-219-119810
nperrault@coltresources.com

Declan Costelloe, CEng
Executive Vice President & COO
Colt Resources Inc.
Tel: +351-219-119810
dcostelloe@coltresources.com

Additional Information

Figure 1 and figure 2.pdf
TSX Venture closing price for GTP-V
Date: 2014/07/31
Closing Price: 0.22

TEL:  +351-219-119810       Colt Resources Inc.
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1421200024TS11421201059-09091220140801