Source	Marketwire
Date	08/05/2014
Time	07:00:19 AM

Company	 AXE EXPLORATION INC.
Title	Axe Exploration Announces its First Exploration Results on the GoldPeak 
Property





    CDNX Symbol: AXQ











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Axe Exploration Inc.

TSX VENTURE SYMBOL: AXQ

August 5, 2014

Axe Exploration Announces its First Exploration Results on the GoldPeak Property


LAVAL, QUEBEC--(Marketwired - Aug. 5, 2014) - Axe Exploration Inc. (TSX 
VENTURE:AXQ) (the "Corporation") announces that it has received the first assay 
results from the exploration work carried out on its 100%-owned GoldPeak 
Property.

Highlights and Results:

During the last few months, prospecting was carried out on the linecutting in 
order to identify potentially outcrop zones from the anomalies localized and 
defined by the GPS magnetometer survey and OreVision survey (Dipole-Dipole) 
completed on the GoldPeak Property in 2013. One anomalous zone is subcropping 
and was manually stripped and sampled.

Several samples collected by hand with hammer and chisel were sent to the ALS 
Minerals laboratory in Val-d'Or (Quebec) for gold analysis by Atomic Absorption 
(30 g) and to Aqua Regia ICP-AES for the analysis of 35 other elements. Two (2) 
samples turned out to be anomalous in Ag, Cu and Zn (Table below). These 
samples consist of a strongly sheared and oxidized zone with 5 to 10% sulphides 
(pyrite and chalcopyrite).

/T/

----------------------------------------------------------------------------
Sample #          Au (ppm)  Ag (ppm)  Cu (ppm)  Zn (ppm)    Fe (%)     S (%)
----------------------------------------------------------------------------
P225812               0.01       0.5       405      2470      5.74      3.52
----------------------------------------------------------------------------
P225813              0.006       0.3       232      1550      4.24      2.33
----------------------------------------------------------------------------

/T/

Further work, such as mechanical stripping and/or diamond core drilling will be 
evaluated and planned in this area in order to obtain, if possible, a better 
understanding of the structure and mineralizing environment.

QUALIFIED PERSON

Mr. Daniel Gaudreault, Ing., Geo. (OIQ), of Geologica Groupe-Conseil, is the 
Qualified Person as defined by National Instrument 43-101, to supervise the 
preparation of this press release.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

David Mc Donald,
President and CEO,
450.622.5785
info@axeexploration.com
www.axeexploration.com

or

Investor Relations
Patrick Wood,
(416) 473-9133
pat.wood@tormontgroup.com
www.tormontgroup.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=493353063