Source	Marketwire
Date	08/18/2014
Time	06:41:07 AM

Company	 TERRAX MINERALS INC.
Title	TerraX Assays 6.61 g/t Au, 357 g/t Ag, 1.51% Cu, 7.02% Zn and Greater Than 
20% Pb in Grab Samples from Homer Lake Base Metal Target, Yellowknife City Gold 
Project





    CDNX Symbol: TXR











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: TerraX Minerals Inc.

TSX VENTURE SYMBOL: TXR
FRANKFURT SYMBOL: TX0
PINKSHEETS SYMBOL: TRXXF

August 18, 2014

TerraX Assays 6.61 g/t Au, 357 g/t Ag, 1.51% Cu, 7.02% Zn and Greater Than 20% 
Pb in Grab Samples from Homer Lake Base Metal Target, Yellowknife City Gold 
Project


YELLOWKNIFE, NORTHWEST TERRITORIES--(Marketwired - Aug. 18, 2014) - TerraX 
Minerals Inc. (TSX VENTURE:TXR)(FRANKFURT:TX0)(PINKSHEETS:TRXXF) has received 
the assay results from a further 113 samples of the approximately 960 surface 
samples taken during a six week prospecting and mapping program now completed 
at the Yellowknife City Gold Project ("YCGP") just north of Yellowknife in the 
Northwest Territories. Assay results are still pending or being interpreted 
from the remaining samples taken from prospective gold and base metal targets 
at the YCGP, as well as from drilling recently completed at the Crestaurum and 
Barney mesothermal gold targets in the southern portion of the property, and 
will be announced when available.

This sampling reported today was completed by two senior geologists provided by 
Virginia Mines Inc. during mapping of a 1.3 km (N-S) x 650 m (E-W) area 
immediately west of Homer Lake in the northern part of the YCGP, with 99 grab 
and chip samples collected for assay and an additional 14 samples collected for 
whole rock analysis. Assay results ranged from below detection to 6.61 g/t 
gold, below detection to 357 g/t silver, 3 ppm to 1.51% copper, 9 ppm to 7.02% 
zinc, and 5 ppm to greater than 20% lead. Two metal domains are apparent: a 
gold +/- copper domain to the west and a gold-silver-lead-zinc domain to the 
east.

These 113 samples complement the 150 grab and chip samples assayed in 2013 and 
the four holes drilled by TerraX in early 2014. Collectively, this information 
produces a preliminary picture of this prospective area which contains 
widespread mineralization. Of the 249 samples assayed, 102 contain Au greater 
than 0.25 g/t, 46 contain Au greater than 1 g/t; 142 samples contain in excess 
of 5 g/t Ag and 53 have more than 40 g/t Ag; 100 samples have more than 0.25% 
Pb of which 57 have more than 1%; 56 samples have greater than 0.25% Zn and 30 
have greater than 1% Zn. Cu anomalism is much more restricted, with only 7 
samples having greater than 0.25% Cu. Maps showing the distribution of 
mineralization at Homer Lake are available on our website at 
www.terraxminerals.com.

Detailed mapping of the predominantly mafic stratigraphy reveals alternating 
massive and pillowed facies, defining a northwesterly trend which is probably 
the approximate stratigraphic trend. The mafic rocks have been intruded by a 
north-northeast trending quartz porphyry interpreted by the Virginia geologists 
as a variably sericitized and chloritized subvolcanic intrusion. Mineralization 
occurs in bands within and along the edge of the quartz porphyry, associated 
with subparallel structures, and in northwest features along possible flow and 
sill contacts.

A strong metal zonation is apparent, with two discrete domains separated by a 
northeast trending lineament that does not contain any outcrops. This lineament 
also separates dominantly massive flows in the west from pillowed and massive 
flows in the east, and is interpreted by Virginia geologists as a major fault. 
All of the greater than 0.25% zinc values, all but one of the greater than 
0.25% lead values and the vast majority of the greater than 40 g/t silver 
values occur in the eastern domain. The two greater than 1% copper values occur 
in the western domain. Anomalous to ore grade gold is evenly distributed 
between the two domains; the result is a gold-copper domain in the west and a 
gold-silver-lead-zinc domain in the east. These domains were tested by two 
drill holes each in April, 2014, prior to their recognition. Holes TNB14-001 
and 002 tested an electromagnetic anomaly in the western domain. The anomaly 
was determined to be caused by pyrrhotite and lesser chalcopyrite stringers. By 
contrast, holes TNB14-003 and 004 were drilled under the main trench in the 
eastern domain. These holes intersected high grade polymetallic zones 
surrounded by lower grade, but still polymetallic, mineralization. The best 
result was from hole TNB14-004, which returned 3.42 m @ 3.41 g/t Au, 69.3 g/t 
Ag, 3.67% Pb and 3.17% Zn within a wider zone of 71.15 m @ 0.25 g/t Au, 14.0 
g/t Ag, 0.73% Pb and 0.57% Zn (see news release of May 12, 2014).

TerraX thus has two distinct targets at Homer Lake: i) a gold-copper target in 
the west, with known mineralization associated with pyrrhotite and chalcopyrite 
stringers and an electromagnetic signature; and ii) structurally controlled 
gold-silver-lead-zinc mineralization in the eastern part of the area. The high 
grade structural target is enhanced by the presence of a lower grade envelope 
of mineralization. Both targets have good size potential. The origin of the two 
mineralization styles has not yet been determined, but both are considered 
worthy of further drill testing.

Joe Campbell, President of TerraX states, "The Homer Lake mineralization has 
now been traced at surface over a strike length of approximately 1.5 km and has 
been intersected by TerraX drilling to 150 m vertical depth from surface, in 
historical drilling to greater than 300 m vertical depth, and mineralization 
remains open down-dip from this drilling. The nature of the mineralization 
remains unclear (synvolcanic or epigenetic), but the large areal extent and 
high polymetallic grades provides us with an excellent base metal target to 
supplement the numerous gold targets that are the primary focus of TerraX's 
exploration on the YCGP."

Sampling included insertion of certified standards and blanks into the stream 
of samples for chemical analysis. Samples were prepared at ALS Chemex's 
laboratory in Yellowknife and shipped to their Vancouver facility for gold and 
ICP analysis. ALS is a certified and accredited laboratory service. It should 
be noted that, due to their selective nature, assay results from grab samples 
may not be indicative of the overall grade and extent of mineralization in the 
subject area. Technical information contained in this news release has been 
approved by Tom Setterfield, Vice President Exploration of TerraX, who is a 
Qualified Person as defined in "National Instrument 43-101, Standards of 
Disclosure for Mineral Projects."

About the Yellowknife City Gold Project

The Yellowknife City Gold Project encompasses 9,349 hectares of contiguous land 
immediately north of the City of Yellowknife in the Northwest Territories and 
includes TerraX's wholly-owned Northbelt property acquired in February 2013.

The project lies on the prolific Yellowknife greenstone belt, and covers 15 km 
of strike length on the northern extension of the shear system that hosts the 
high-grade Con and Giant gold mines. The project is host to multiple shears 
that are the recognized hosts for gold deposits in the Yellowknife gold 
district and contains innumerable gold showings and historic high grade drill 
results. Since January 2013, TerraX has consolidated the project area by 
acquiring and optioning numerous properties, including: Northbelt, Goodwin, 
Ryan Lake, Walsh Lake, and U-Breccia, as well as staking additional contiguous 
lands. Being all-season road accessible and within 15 km of the City of 
Yellowknife, YCPG is close to vital infrastructure, including: supplies, 
service providers, power, water, and skilled tradespeople.

For more information on TerraX and the Yellowknife City Gold Project, please 
visit our web site at www.terraxminerals.com.

On behalf of the Board of Directors

Joseph Campbell, President

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

This news release contains forward-looking information, which involves known 
and unknown risks, uncertainties and other factors that may cause actual events 
to differ materially from current expectation. Important factors - including 
the availability of funds, the results of financing efforts, the completion of 
due diligence and the results of exploration activities - that could cause 
actual results to differ materially from the Company's expectations are 
disclosed in the Company's documents filed from time to time on SEDAR (see 
www.sedar.com). Readers are cautioned not to place undue reliance on these 
forward-looking statements, which speak only as of the date of this press 
release. The company disclaims any intention or obligation, except to the 
extent required by law, to update or revise any forward-looking statements, 
whether as a result of new information, future events or otherwise.

- 30 -

CONTACT INFO:

Paradox Public Relations
514-341-0408 or Toll Free: 1-866-460-0408
info@paradox-pr.ca

or

Vanguard Shareholder Solutions
604-608-0824 or Toll Free: 855-508-0824
ir@vanguardsolutions.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=495258979