Source	CANADA NEWSWIRE
Date	08/19/2014
Time	06:22:02 AM

Company	 Mundoro Capital Inc.
Title	Mundoro Announces Drilling Results from Tilva Rosh Prospect in Serbia





    CDNX Symbol: MUN











Press Release	




" BC-Mundoro-Drill-Results   08-19 1900
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business  Editors:
^Mundoro Announces Drilling Results from Tilva Rosh Prospect in Serbia@

VANCOUVER, Aug. 19, 2014 /CNW/ - Mundoro Capital Inc. (TSXV: MUN,
www.mundoro.com) ("Mundoro" or the "Company") is pleased to announce drilling
results from its Tilva Rosh prospect within the Savinac exploration license in
northeastern Serbia. The Savinac license covers 90 km2 and is located within
the Timok Magmatic Belt, approximately 20 km southeast of the Bor mining camp.
Teo Dechev, CEO and President of Mundoro commented, "This initial
drilling program at Tilva Rosh was designed to test step-out extensions of the
mineralization down dip and along strike. The initial drilling results have
successfully demonstrated continuation of surface mineralisation at depth,
along strike and are encouraging as management believes the results are
vectoring towards a deeper mineralisation source. The mineralization is open
to the north, south and at depth."
Six inclined diamond drill holes totaling 917.8 m were drilled at the
southern portion of Tilva Rosh system to test the vertical extent of the gold
mineralization, which was previously confirmed by high grade trenching results
of 12 m (at) 33.03 g/t AuEq (30.39 g/t Au, 171.27 g/t Ag) (see October 21, 2013
press release). The drill holes were designed to test the down dip
mineralization to a maximum of 150 m down dip. Collar locations are shown on
Figure 1 -Tilva Rosh Drill Plan. Cross section of interpreted geology shown in
Figure 2 - Tilva Rosh - Cross Section A-A'.
Table 1: Summary of significant results from drill holes SAV01 to SAV06.
___________________________________________________________________
|Drill Hole ID|From | To  |Interval| Au  |Cu (%)|Ag (g/t)|AuEq |CuEq|
|             | (m) | (m) |  (m)   |(g/t)|      |        |(g/t)|(%) |
|_____________|_____|_____|________|_____|______|________|_____|____|
|SAV_01       |  11 |  18 |     7  |7.90 |   _  |  46.74 |8.68 |  _ |
|    Including|_____|_____|________|_____|______|________|_____|____|
|             |  13 |  15 |     2  |24.98|   _  | 128.05 |21.11|  _ |
|    Including|_____|_____|________|_____|______|________|_____|____|
|             |  13 |  14 |     1  |42.90|   _  |   199  |46.22|  _ |
|             |_____|_____|________|_____|______|________|_____|____|
|             | 126 | 133 |     7  |0.35 |   _  |   2.76 |0.40 |    |
|_____________|_____|_____|________|_____|______|________|_____|____|
|SAV_02       |  30 |  40 |    10  |0.34 |   _  |   2.16 |0.38 |  _ |
|             |_____|_____|________|_____|______|________|_____|____|
|             |67.7 |71.8 |   4.1  |0.62 |   _  |   2.36 |0.66 |  _ |
|             |_____|_____|________|_____|______|________|_____|____|
|             |95.6 |100.0|   4.4  |0.54 |   _  |   6.38 |0.65 |  _ |
|_____________|_____|_____|________|_____|______|________|_____|____|
|SAV_03       |71.0 |76.0 |   5.0  |2.54 | 0.59 |  15.54 |3.73 |2.36|
|    Including|_____|_____|________|_____|______|________|_____|____|
|             |74.0 |74.7 |   0.7  |10.35| 1.47 |  50.10 |13.52|8.54|
|_____________|_____|_____|________|_____|______|________|_____|____|
|SAV_04       |42.2 |51.3 |   9.1  |1.24 | 0.33 |   9.00 |1.91 |1.21|
|    Including|_____|_____|________|_____|______|________|_____|____|
|             |43.3 |47.3 |   3.0  |1.45 | 0.58 |  14.60 |2.61 |1.65|
|_____________|_____|_____|________|_____|______|________|_____|____|
|SAV_05       |  29 |50.2 |   21.2 |0.25 |   _  |   1.78 |0.28 |  _ |
|             |_____|_____|________|_____|______|________|_____|____|
|    Including|30.4 |36.0 |   5.6  |0.43 |   _  |   3.30 |0.49 |  _ |
|             |_____|_____|________|_____|______|________|_____|____|
|    Including|46.2 |50.2 |   4.0  |0.35 | 0.14 |   3.88 |0.63 |0.40|
|_____________|_____|_____|________|_____|______|________|_____|____|
|SAV_06       |38.50|42.90|   4.4  |0.59 | 0.21 |  14.95 |1.17 |0.74|
|_____________|_____|_____|________|_____|______|________|_____|____|
Gold Equivalent ("AuEq.") is calculated using the formula AuEq (equal sign) 
(g/t/Au)
+ (g/t/Ag) + ($/ozAu)/65 + [(%Cu) x (22.0462) x ($/lbCu)] ÷ [(1/31.1035) x
($/ozAu)]. Copper equivalent (CuEq%) is calculated using the formula CuEq 
(equal sign)
(%Cu) + [(g/t/AuEq) x (1/31.1035) x ($/ozAu)] ÷ [(22.0462) x ($/lbCu)]. Metal
prices used are: gold price of US$1300/oz, copper price of US$3/lb, and silver
price US$20/oz. All thicknesses from intersections from drill holes are
down-hole drilled thicknesses or outcrop sample length thickness.
The Tilva Rosh drilling program has demonstrated continuation of surface
mineralisation at depth and along strike of a north-west structure responsible
for the high grade gold. The Au-Ag mineralization identified in the in-soil
geochemistry anomaly and confirmed in the trenching, has now been confirmed at
a depth to 76m, along strike for 100 m (50 m to south and 50 m to north) and
remains open in all directions. Copper mineralisation was intersected at depth
in four of the six drill holes (SAV03-SAV06). Management believes copper was
not present at surface due to the highly acidic nature of the lithocap in the
area caused by the high pyrite content in the system. The eastern most drill
holes, SAV02 and SAV05, intersected the highest lead-zinc contents (up to 2.2
% Zn and 0.6 % Pb) suggesting lateral zoning indicative of porphyry style
hydrothermal system.
These initial drill results at Tilva Rosh are encouraging and are
interpreted to be proximal to a Cu-Au porphyry system related to a large area
of advanced argillic lithocaps to the north, highlighted with a central Mo
anomaly rimmed by Cu and followed outwards to zones of Pb-Zn. This is classic
geochemical signatures of porphyry deposit footprints and where the company
believes exist further porphyry drill targets.
Drill Hole Highlights of Tilva Rosh Prospect
Over the past 18 months Mundoro has conducted geochemical, mapping,
trenching, ground magnetic surveys over this license as well as compiling
historic data, targeting epithermal and porphyry Cu-Au systems. This work has
outlined the Savinac mineralised belt (9 km by 2 km) which includes the Tilva
Rosh epithermal system expressed on the surface with a large area of advanced
argillic alteration covering 4km by 1km. Tilva Rosh prospect was explored
previously in late 1970's and early 2000's but significant gold mineralisation
and porphyry Cu-Au potential was identified by Mundoro's exploration in
Q4-2013.
SAV 01 intersected a hydrothermal breccia and veinlet zone similar to the
out-cropping high grade (69.7 m). At 102.3m the hole cut argillic altered
feldspar andesite porphyry with quartz veinlets and pyrite content 2-5%
throughout and minor chalcopyrite mineralisation at 150.9m.
SAV 02 intersected 8.5 meters of iron oxide breccia with silicified
clasts and continued in a hydrothermal breccia with pyrite down to 40.3 m. As
in SAV 01, it then cut andesite feldspar porphyry from 30.9 m to the end of
the hole (158.7 m). SAV 02 is characterized by more faulting and veining of
the andesite porphyry and sphalerite-galena mineralisation in the quartz
veins.
SAV 03 collared in a quartz-iron oxide hydrothermal breccia which
continued down to 48.7 m. From 52.5 m to 82.6 m the drill hole intersected a
fault zone which contains semi-massive pyrite chalcopyrite-chalcocite
mineralisation from 69.9 m to 74.7 m (4.8 m). A-type porphyry veins were noted
from 115.6 m to 121 m (5.4 m) passing to gypsum/anhydrite stockwork veining
and quartz-pyrite veinlets to the end of the hole.
SAV 04 collared in hydrothermal breccia and intersected quartz-pyrite in
andesite and lithic tuff which is moderately argillic altered with rare
pyrite±chalcopyrite veinlets (from 23.8 m to 29.8 m). From 41.3 m, the drill
hole intersected fault breccia with quartz-massive pyrite-sphalerite ± galena
veins containing up to 30% pyrite. From 52.4 m the drill hole intersected
andesite feldspar porphyry, cross cut by quartz-pyrite vein and veinlets,
vuggy texture quartz-pyrite-sphalerite±galena vein with massive pyrite up to
15%) and a hydrothermal breccia zones with quartz-pyrite veins.
SAV 05 collared in argillic altered andesite porphyry with quartz
veinlets with disseminated pyrite and pyrite in fracture fills 1-3% continuing
to the end of hole (149.7 m). From 19.3 m to 94.5 m the drillhole cut through
a fault and quartz vein zone containing irregular pyrite-barite-sphalerite
galena mineralisation.
SAV 06 is the shortest hole drilled (116.3 m). It cut quartz-hydrothermal
breccia from 0 m to 8.6 m hosted in lithic tuff and continued in andesitic
tuff with ~1% pyrite to 38.6 m. From 38.6 m to 67.2 m it entered a fault zone
containing quartz veins with 1-2% pyrite and finished in silicified and
brecciated andesite containing pyrite and anhydrite veining.
Sampling, Analysis and Qualified Person
Drill hole orientations were surveyed at approximately 50 meters
intervals. Drill core was collected from drill sites by the Company's
geologists and processed and sampled at the Company's core shed according to
industry best practice standard procedures. Samples were collected as half PQ
or HQ core at one meter lengths from mineralised intervals and two meter
lengths from none mineralised intervals. Where necessary the sampling lengths
were adjusted to reflect the geological boundaries.
All samples are assayed using 50 gram fire assay with atomic absorption
finish and ME-ICP61 by ALS Romania. The entire sample was crushed to 2mm, then
split off a 1 kg sample and pulverized the split to better than 85% passing 75
microns. Quality Assurance and Quality Control procedures include the
systematic insertion of standards and duplicates into the sample streams.
Duplicate core samples are taken every 25 samples and standards and blanks are
inserted after every 20th sample. All data collected from detailed logging and
assay results from the laboratories are routinely verified and entered in an
Access data base.
Technical information contained in this Press Release has been reviewed
and approved by Mr. G. Magaranov, P. Geo., Qualified Person as defined by
National Instrument 43-101.
On behalf of the Company,
Teo Dechev, Chief Executive Officer, President and Director
About Mundoro Capital Inc.
Mundoro is a well-funded, Canadian based, company focused on mineral
acquisition, exploration, and development. Our primary focus is advancing our
properties on the Tethyan Belt in Southeastern Europe. Mundoro has
methodically acquired a district-scale land position on this prolific mineral
belt which hosts significant Gold-Copper porphyry and related epithermal
deposits. Our strong project pipeline, which also includes assets in Mexico
and China, is positioned to drive long-term, sustainable growth in order to
attain production and shareholder return.
Caution Concerning Forward-Looking Statements
Information included, attached to or incorporated by reference into this
News Release may contain forward-looking statements. All statements, other
than statements of historical fact, included or incorporated by reference in
this News Release are forward-looking statements, including, without
limitation, statements regarding activities, events or developments that the
Board expects or anticipates may occur in the future. These forward-looking
statements can be identified by the use of forward-looking words such as
"will", "expect", "intend", "plan", "estimate", "anticipate", "believe" or
"continue" or similar words or the negative thereof. The material assumptions
that were applied in making the forward looking statements in this News
Release include expectations as to the Company's future strategy and business
plan and execution of the Company's existing plans. There can be no assurance
that the plans, intentions or expectations upon which these forward-looking
statements are based will occur. We caution readers of this News Release not
to place undue reliance on forward looking statements contained in this News
Release, which are not a guarantee of performance and are subject to a number
of uncertainties and other factors that could cause actual results to differ
materially from those expressed or implied by such forward-looking statements.
These factors include general economic and market conditions, changes in law,
regulatory processes, the status of Mundoro's assets and financial condition,
actions of competitors and the ability to implement business strategies and
pursue business opportunities. The forward-looking statements contained in
this News Release are expressly qualified in their entirety by this cautionary
statement. The forward-looking statements included in this News Release are
made as of the date of this News Release and the Board undertakes no
obligation to publicly update such forward-looking statements to reflect new
information, subsequent events or otherwise, except as required by law.
Shareholders are cautioned that all forward-looking statements involve risks
and uncertainties and for a more detailed discussion of such risks and other
factors that could cause actual results to differ materially from those
expressed or implied by such forward-looking statements, refer to the
Company's filings with the Canadian securities regulators available on
www.sedar.com.
Neither TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
SOURCE Mundoro Capital Inc.



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/August2014/19/c7475.html

-0-                           08/19/2014
/For further information:
For further information please contact Teo Dechev, CEO, President and
Director of Mundoro Capital Inc. at +1-604-669-8055 or Michelle Roth, Roth
Investor Relations at +1-732-792-2200.
/
(MUN.)

CO:  Mundoro Capital Inc.
ST:  British Columbia
IN:  MNG
SU:

-30-