Source	MARKET NEWS
Date	08/25/2014
Time	09:06:25 AM

Company	 Highland Copper Company Inc.
Title	Initial 
Resource Estimate For The 543s Deposit,





    CDNX Symbol: HI











Press Release	




[200/News Release]HIVHIGHLAND COPPER CO INCAUG 25 2014  09:04 AMInitial 
Resource Estimate For The 543s Deposit, --->@NEWS RELEASE
HIGHLAND COPPER CO INC ("HI-V")
- Initial Resource Estimate For The 543s Deposit,
- Upper Peninsula, Michigan

Highland Copper Company Inc. ("Highland" or the "Company") is
pleased to announce an initial resource estimate for the 543S copper
deposit part of the Keweenaw Project located in the Keweenaw Peninsula
of Michigan's Upper Peninsula (see Figure 1).

//st
543S Project - Base Case - Underground Scenario
Mineral Resource Estimate - July 5, 2014
---------------------------------------------------------------------------
-
Cut-Off
Grade              Grade Grade             Grade
Resource         Cu Eq.    Tonnage   Cu Eq.   Cu     Copper      Ag   Silver
Category             (%)  ('000 t)      (%)   (%)('000 lbs)   (g/t)('000 oz)
---------------------------------------------------------------------------
-
Indicated            1.9     1,518     3.31  3.27   109,514     5.1      248
---------------------------------------------------------------------------
-
Inferred             1.9       193     3.12  3.08    13,116     4.8       30
---------------------------------------------------------------------------
-
Notes on Mineral Resources
1.  Cu Equivalent = Cu% + (Ag g/t (i) 20$/oz (i) 80% (i) 90%) / (22.0462
lbs/10kg (i) 3$/lb (i) 31.1035 g/oz (i) 90% (i) 96.5%)
2.  Mineral Resources are reported using a copper price of 3$/lb and a
silver price of 20$/oz
3.  A payable rate of 96.5% for copper and 90% for silver was assumed
4.  Preliminary metallurgical testing suggests recovery of 90% for copper
and 80% for silver
5.  Cut-off grade of 1.9% Cu Eq. was used
6.  Underground mining costs are estimated at 57.27$/t of ore
7.  Production costs are estimated at 37.50$/t of ore: 12.00$/t for
processing, 2.50$/t for general and administrative costs, 0.50$/t for
tailings and 22.50$/t for ore transportation to White Pine Complex
8.  A 5% royalty was used (4.99$/t ore)
9.  No mining dilution and mining loss were considered for the Mineral
Resources
10. Rock bulk densities are based on rock types, %Cu and proximity to
specific gravity measurements
11. Assay capping was applied to some mineralized domains
12. Classification of Mineral Resources conforms to CIM definitions
13. The qualified person for the estimate is Mr. Rejean Sirois, eng., Vice
President Geology and Resources of G Mining. The estimate has an
effective date of July 5, 2014
14. Mineral resources, which are not mineral reserves, do not have
demonstrated economic viability. The estimate of mineral resources may
be materially affected by environmental, permitting, legal, title,
taxation, sociopolitical, marketing, or other relevant issues.
15. The quantity and grade of reported inferred resources in this estimation
are uncertain in nature and there has been insufficient exploration to
define these inferred resources as indicated or measured mineral
resources.

//et

The mineral resource estimate was prepared by G Mining Services
Inc. ("G Mining"), a Canadian mining consulting firm. After a detailed
review of different options, Highland and G Mining have opted to report
the mineral resources for potential underground development of the 543S
deposit. This initial mineral resource estimate for the 543S copper
deposit is based on 262 diamond drill holes totaling 45,608 m, of which
220 are NQ size and 42 HQ size, on a drill grid spaced 30.5 by 15 m.

Selection of cut-off grades and base case resource estimate

The table below, prepared by G Mining, shows the sensitivity of
constrained underground resource estimates to the cut-off grade for the
543S resource.

//st
Sensitivity of the 543S Project - Constrained Underground Mineral Resource
Estimate by Cut-Off Grades
---------------------------------------------------------------------------
-
Cut Off Grade
% Cu Eq.                                Indicated

---------------------------------------------------------------
Copper                 Silver
Grade       Contained   Grade      Contained
Tonnage     Grade    Cu           ('000      Ag          ('000
('000 t) Cu Eq.(%)   (%)            lbs)   (g/t)            oz)
---------------------------------------------------------------------------
-
5.0%              163      6.21  6.16          22,166     7.1             37
---------------------------------------------------------------------------
-
4.5%              246      5.71  5.67          30,790     6.4             51
---------------------------------------------------------------------------
-
4.0%              364      5.24  5.20          41,748     6.1             71
---------------------------------------------------------------------------
-
3.5%              508      4.81  4.78          53,532     5.7             94
---------------------------------------------------------------------------
-
3.0%              715      4.36  4.32          68,101     5.4            126
---------------------------------------------------------------------------
-
2.5%              995      3.90  3.87          84,838     5.3            169
---------------------------------------------------------------------------
-
2.0%            1,406      3.41  3.38         104,817     5.1            231
---------------------------------------------------------------------------
-
1.9%            1,518      3.31  3.27         109,514     5.1            248
---------------------------------------------------------------------------
-
1.5%            2,070      2.87  2.84         129,809     4.8            320
---------------------------------------------------------------------------
-
1.0%            3,136      2.31  2.29         158,142     4.4            444
---------------------------------------------------------------------------
-
0.5%            4,993      1.72  1.70         187,130     3.9            621
---------------------------------------------------------------------------
-
Sensitivity of the 543S Project - Constrained Underground Mineral Resource
Estimate by Cut-Off Grades
---------------------------------------------------------------------------
-
Cut Off Grade
% Cu Eq.                                 Inferred

---------------------------------------------------------------
Copper                 Silver
Grade       Contained   Grade      Contained
Tonnage     Grade    Cu           ('000      Ag          ('000
('000 t) Cu Eq.(%)   (%)            lbs)   (g/t)            oz)
---------------------------------------------------------------------------
-
5.0%               14      5.87  5.83           1,776     5.2              2
---------------------------------------------------------------------------
-
4.5%               27      5.30  5.27           3,163     5.1              4
---------------------------------------------------------------------------
-
4.0%               41      4.96  4.93           4,464     5.0              7
---------------------------------------------------------------------------
-
3.5%               59      4.58  4.55           5,960     4.8              9
---------------------------------------------------------------------------
-
3.0%               82      4.21  4.18           7,533     4.6             12
---------------------------------------------------------------------------
-
2.5%              112      3.81  3.78           9,359     4.8             17
---------------------------------------------------------------------------
-
2.0%              173      3.24  3.21          12,290     4.8             27
---------------------------------------------------------------------------
-
1.9%              193      3.12  3.08          13,116     4.8             30
---------------------------------------------------------------------------
-
1.5%              332      2.52  2.49          18,256     4.2             45
---------------------------------------------------------------------------
-
1.0%              751      1.79  1.77          29,267     4.0             97
---------------------------------------------------------------------------
-
0.5%            1,493      1.25  1.23          40,616     3.2            152
---------------------------------------------------------------------------
//et

Mineral Resource Estimate Methodology

G Mining undertook the Mineral Resource estimate based on data
provided by Highland. The estimate was conducted in a block model
limited by eighteen mineralized domains interpreted and modelled as 3D
wireframes. Capped raw assays were composited into regular 2.5-meter
run lengths within each domain. Isotropic cubic blocks of 2.5 meters
were used in the block model. Bulk densities were first estimated in
each block based on regressions calculated from the correlation of
1,100 specific gravity measurements with their copper content, for
three major rock types (flow-tops, dyke and basalt/host rock).
Secondly, blocks within a 50 meter radius from specific gravity
measurements, within the same rock type, were interpolated using those
samples and were given a higher priority. Resulting estimated specific
gravity of blocks inside domains varies from 2.52 g/cm3 to 3.04 g/cm3.
Overburden density was set to a uniform 2.35 g/cm3. Copper and silver
grades were estimated using the Inverse Distance Cube (ID3)
interpolation method in three successive passes, which led to Indicated
and Inferred Resources, limited by mineralized domains. The underground
scenario resources were constrained by blocks with a minimum threshold
value of 1.9% Cu equivalent, where isolated clusters of blocks were
removed and an upper hard boundary was set at 15 m below the bedrock
surface. Mineral Resources were classified according to the CIM
Definition Standards on Mineral Resources and Mineral Reserves.

Metallurgical Work

A.C.A. Howe International first completed historical preliminary
metallurgical studies in 1991 at the Institute of Materials Processing
of Michigan Technological University on three samples of chalcocite
from the 543S deposit. Concentrate grades from conventional flotation
tests demonstrated over 40% Cu and recoveries over 90% were achievable
at grinds between 200 and 270 mesh when combined with cleaning and
re-cleaning of the rougher concentrates. A ball mill grindability work
index of a composite of 19.36 KWh/t was also reported.

In February 2014 seven flotation tests were conducted on composite
samples of drill core from the 543S deposit at SGS Laboratories in
Lakefield, Ontario under the supervision of Ahmed Bouajila, Vice
President, Metallurgy and Ore Processing for G Mining. The composite
grade was 2.61% Cu and 3.9 g/t Ag. Copper recoveries reported for this
work neglect the copper distribution contained in the cleaner tailings.
In a continuous circuit the cleaner tailings would be re-circulated
back to the rougher and cleaner flotation stages, respectively and a
substantial part of it would be recovered in the final concentrate. The
effect of this recirculation cannot be determined without running
locked cycle tests or continuous pilot plant trials. It is concluded
that reasonable expectation from an equivalent optimized and closed
circuit would be:

//st

-- Recoveries: 90% Cu, 80% Ag;

-- Concentrate grades: 44%Cu, 59g/t Ag ; and

-- Mass Pull: 5.5%.

//et

Those numbers are used for the base case reported in this news
release.

Geology of the 543S Deposit.

The 543S copper deposit is located within a zone of
chalcocite-dominated copper mineralization that is unique to the
Keweenaw Peninsula. The known chalcocite deposits in the Keweenaw
region occur in a 30 kilometer long northeast-southwest trending belt
located between the native copper-bearing lodes and the underlying
Keweenaw Fault and hosted by the Portage Lake Lava series. Chalcocite
mineralization primarily occurs as open space fillings in amygdaloidal
and fragmental basalt flow tops. Historically, this type of
mineralization has not been a major exploration target. The 543S
deposit is the largest chalcocite occurrence found to date.

The basalt flows in the area of the 543S deposit are covered by up
to 50 meters of glacial till and do not outcrop in the vicinity of the
deposit. The flows have an average thickness of approximately 33 meters
and are cut by two fine grained sill-like dacitic to andesitic
subvolcanic intrusives (see Fig. 2). At the 543S copper deposit, more
than 99% of the copper occurs in the mineral chalcocite and (1% is
present as bornite, chalcopyrite, or as native copper. Traces of native
silver are also present. Approximately 80 to 90% of chalcocite
mineralization is concentrated in flow top breccias and amygdaloids
where grades are the highest.
Future Plans
The 543S deposit is one of two lava flow top-hosted chalcocite
deposits that have been subject to recent drilling programs by
Highland, the other is the G-2 deposit located about 20 kilometers
northeast of 543S. Highland plans to complete a resource estimate for
G-2 in 2014. Although the possibility of an independent milling complex
at 543S treating mineralization from both 543S and G-2 will be
considered, Highland plans to evaluate alternatives that would treat
mineralization from 543S and other undeveloped copper deposits in the
Western Upper Peninsula of Michigan recently acquired by Highland, in a
single center of metallurgical operations. Planned studies will
evaluate an alternative that would involve transportation to and
processing of mineralization from these deposits in a central mine and
metallurgical complex, the location of which remains to be determined.
Qualified Persons
Rejean Sirois, Vice President of Geology and Resources for G
Mining is the qualified person, as defined in National Instrument
43-101, responsible for the mineral resource estimate for the 543S
deposit as reported herein. He has read and approved the relevant
technical portions of this news release related to the mineral resource
estimate for which he is responsible.
Ahmed Bouajila, Vice President, Metallurgy and Ore Processing for
G Mining is the qualified person, as defined in National Instrument
43-101, responsible for supervising initial metallurgical test work on
samples from the 543S deposit as reported herein. He has read and
approved the relevant technical portions of this news release related
to the metallurgical work for which he is responsible.
The balance of the technical information contained in this
news release has been reviewed and approved by Ross R. Grunwald, PhD.,VP 
Exploration for the Company. Dr. Grunwald is a qualified person as
defined in NI 43-101.
G Mining is completing a National Instrument 43-101
technical report for the mineral resource estimate to be filed on SEDAR
within 45 days of this press release.
Keweenaw Copper Project
The 543S deposit is part of the Keweenaw Copper Project that
covers approximately 9,000 acres of mineral rights and is being
explored under a Mining Venture Agreement between Highland and BRP LLC.
The agreement allows Highland to earn a 65 percent interest by spending
US$11.5 million on the project (which amount has been spent) and
providing a feasibility study by October 26, 2015. The Keweenaw Project
is approximately 180 km northeast of the White Pine North Project and
250 km of the Copperwood Project by road access.
Cautionary Statement
Mineral resources are not mineral reserves and do not have
demonstrated economic viability. The terms "inferred" and "indicated"
resources contains in this press release are recognized and required by
NI 43-101 under Canadian regulations, but not recognized by the U.S.
Securities and Exchange Commission ("SEC"). The SEC requires mining
companies in their filings with the SEC to disclose only those mineral
deposits that a company can economically and legally extract or
produce. "Inferred resources" have a great amount of uncertainty as to
their existence, and great uncertainty as to their economic and legal
feasibility. It cannot be assumed that all or any part of an "inferred
resource" will ever be upgraded to a higher category. Investors are
cautioned not to assume that all or part of an inferred resource
exists, or is economically or legally mineable and that all or any part
of mineral deposits in the "measured" or "indicated" resource
categories will ever be converted into reserves.
This press release contains 'forward-looking information'
within the meaning of applicable Canadian securities legislation.
Forward looking information in this news release includes information
with respect to: the mineral resource estimate; the Company's plans to
complete a mineral resource estimate at the G2 deposit; the timing and
results of future studies; the geological and economic potential of the
Keweenaw Project, including the possibility of developing an
underground operation there; the potential to process mineralization
with other deposits in a central mine; the completion of a feasibility
study to earn 65% of the Keweenaw Project, and other statements and
information regarding anticipated results regarding the Company's
operations and exploration. Actual results may be materially different
from those currently anticipated. Many factors, known and unknown,
could cause the actual results to be materially different from those
expressed or implied by such forward looking statements. Such risks
include, but are not limited to: the volatility of copper price; the
uncertainty of exploration results and mineral resource estimates,
capital expenditure requirements and other costs; the uncertainties
related to the Company's ability to acquire a 65% interest in the
Keweenaw Project; currency fluctuations; the availability of financing
for additional capital requirements, cost of exploration and
development programs; mining risks; risks associated with governmental
and environmental regulation and obtaining all the necessary permits
for the development of the Project; and risks associated with global
economic growth. The Company does not intend, and does not assume any
obligation, to update these forward-looking statements and information,
except as required by law. Accordingly, readers are advised not to
place undue reliance on forward-looking statements.
About Highland
Highland Copper Company Inc. is a Canadian exploration
company focused on exploring and developing copper projects within the
Upper Peninsula of Michigan, U.S.A. Highland has recently completed the
acquisition of the Copperwood Project and the interim closing of the
White Pine Project. The common shares of Highland trade on the TSX
Venture Exchange under the symbol 'HI'. Additional information about
the Company is available on the Company's website at
www.highlandcopper.com and on SEDAR at www.sedar.com.

Figures are available at the following address:
http://file.marketwire.com/release/hi_0825.pdf

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

TSX Venture closing price for HI-V
Date: 2014/08/22
Closing Price: 0.49

TEL:  450-677-2455  David Fennell, Executive Chairman
James Crombie, Interim President and CEO
E-mail: info@highlandcopper.com
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1423600027TS11423601162-09040820140825