Source	MARKET NEWS
Date	08/26/2014
Time	06:29:47 AM

Company	 Appalaches Resources Inc.
Title	287 
G/t Au Drilled Over 1 Meter At Dufferin Mine





    CDNX Symbol: APP











Press Release	





RESSOURCES APPALACHES INC ("APP-V")
- 287 G/t Au Drilled Over 1 Meter At Dufferin Mine

Ressources Appalaches is pleased to announce results from 16 drill
holes totaling 2,022 m made at the Dufferin Mine in Nova Scotia. An
exceptional 287 g/t (9.2 oz/t) gold was intersected over 1 meter in
hole F14-15 at 195 m of the surface corresponding to the vein # 6.

The main purpose of the drilling program is to explore under the
galleries in exploitation mainly the veins 3 to 6 located between 75
and 200 m from the surface but also for the development of galleries
toward east. Drill results are comparable to those of previous drilling
campaigns completed on the property and veins were intersected as
anticipated.

The following table presents the significant results.

//st
Drill Hole   Azimuth        Dip    From      To  Length  Grade Au
#          (degrees)  (degrees)     (m)     (m)     (m)     (g/t)
F14-01           346         75    36,1   36,35    0,25      5,44
F14-03           346         83   32,75    33,5    0,75      6,76
F14-04           166        -83    53,4   54,86    1,46     17,98
67,7    68,5     0,8      4,76
F14-05           166        -88   67,63   70,56    2,93     27,91
Including   67,63    68,1    0,47     25,90
Including      69    70,2     1,2     57,50
F14-06           346         83    28,2    29,1     0,9     12,60
34,95   35,55     0,6      4,67
F14-07           346         78    31,1   32,15    1,05      9,70
F14-10           166        -78    46,4   46,95    0,55     14,60
F14-11           166        -83    17,6      18     0,4      6,67
43,6   44,72    1,12     27,86
F14-12           166        -88    40,7   41,33    0,63      5,13
103,67   104,1    0,43      5,97
F14-13           166        -83      42    43,8     1,8     54,33
Including    42,6    43,4     0,8    122,00
84,5    86,1     1,6     23,37
F14-14           166        -83      96      97       1      4,60
158,33  158,79    0,46      6,55
F14-15           166        -83    39,7    41,9     2,2     11,40
Including    40,3    40,9     0,6     38,10
79,5    80,2     0,7      5,19
Including     195     196       1    287,00
F16-16           166        -83      42    42,5     0,5      5,43
50,65   50,94    0,29      8,02
81,35   86,55     5,2     21,52
Including   81,75    83,2    1,45     54,60
Including    83,2    84,3     1,1     28,40
//et

Note: The length is that of the drilled interval.

Since 2008, more than 18 quartz veins of the "Saddle Reef Vein"
type have now been identified at the Dufferin Mine. The gold-bearing
anticline structure has been followed for 1.4 km and down to a depth of
nearly 400 metres. The veins are sub horizontal juxtaposed one above
the other with 20 to 40 meter spacing.Vein #1, which starts at the mine
portal and plunges 8-10 to the east, was systematically followed over a
distance of 1,200 meters, to a depth of 200 meters. Previous work
indicated twelve other veins beneath the #1 vein, also extending
eastwards. In addition, new veins have been located above the #1 in
eastern part of the property.

Production

The mine currently provides access and operates the first four
veins. For further details on production, see Company's Press Release
of 21-08-2014.

Analysis Procedure

The samples were taken by splitting the core according to industry
standards and they were submitted along with standards, blanks and
duplicates at regular intervals. The analyses were performed by ALS
Laboratory Group for gold using conventional metallic screening. Half
of the drill core has been preserved and all holes are stored at the
site of the Dufferin Mine in Nova Scotia.

About Ressources Appalaches

Since it was created in 1994, the goal of Ressources Appalaches
has been to discover and develop deposits of base and precious metals
in Canada with an expertise targeted towards the Appalachian geological
formation in Quebec and Nova Scotia. The Company is mainly focused on
the exploration and development of the Dufferin Gold Mine in Nova
Scotia.

Photos of the Dufferin Mine and its facilities are available on
the Company's website at: www.ressourcesappalaches.com.

The contents of this press release were prepared and reviewed by
Alain Hupe, Eng. a Qualified Person as defined in NI 43-101. Neither
the TSX Venture Exchange nor its Regulation Service Provider (as that
term is defined in the policies of the TSX Venture Exchange) accepts
any responsibility for the adequacy or accuracy of this release.

This press release may contain certain forward-looking statements
that include elements of risk and uncertainty. Consequently, actual
results may differ substantially from those anticipated in such
statements. These risks and uncertainties are described in the
quarterly and annual reports, and in the documents submitted to the
securities administration.

TSX Venture closing price for APP-V
Date: 2014/08/25
Closing Price: 0.06

TEL: 418-724-0901              Alain Hupe, Eng., President and CEO
info@ressourcesappalaches.com  Ressources Appalaches
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1423700013TS11423700919-06265320140826