Source	Marketwire
Date	08/26/2014
Time	09:02:38 AM

Company	 ATAC RESOURCES LTD.
Title	ATAC Resources Intersects 30.79 m of 9.50 g/t Gold at Conrad, Rackla Gold 
Project-Yukon





    CDNX Symbol: ATC











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: ATAC Resources Ltd.

TSX VENTURE SYMBOL: ATC

August 26, 2014

ATAC Resources Intersects 30.79 m of 9.50 g/t Gold at Conrad, Rackla Gold 
Project-Yukon


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Aug. 26, 2014) - ATAC Resources 
Ltd. ("ATAC") (TSX VENTURE:ATC) is pleased to announce initial results from its 
ongoing 2014 exploration program. The following results are from drilling and 
surface work at the Conrad, Sunrise and Anubis Zones, all located within the 
Nadaleen Trend at the eastern end of ATAC's 100% owned 1,700 sq/km Rackla Gold 
Project in central Yukon.

Highlights:

/T/

--  Conrad Lower Zone step out hole OS-14-277 extends high grade
mineralization -
30.79 m of 9.50 g/t gold;
--  Sunrise drilling extends mineralization to the west of 2013 drilling;
and
--  Anubis area surface exploration outlines pathfinder element+gold
anomalies with 8 km cumulative strike length, similar in size and
intensity to the Osiris area located 10 km to the east.

/T/

Conrad Zone

/T/

----------------------------------------------------------------------------
Conrad Zone                         To
Drill Hole        From (m)         (m)  Interval (m)    Au (g/t)     Section
----------------------------------------------------------------------------

----------------------------------------------------------------------------
OS-14-227           434.12      438.52          4.40        5.50       C475E
----------------------------------------------------------------------------
and                 452.80      483.59         30.79        9.50
----------------------------------------------------------------------------
-  The reported intersections are drilled thicknesses and are believed to
represent approximately 60 to 100% true widths.

/T/

Carlin-type gold mineralization at the Conrad Zone is contained within several 
structural and stratigraphic settings. In the Conrad Upper Zone, gold 
mineralization occurs in an anticline fold hinge. The Upper Zone has been 
continuously traced by shallow drilling over a strike length of 800 m between 
Sections C100E and C900E. A 2012 drill hole (hole OS-12-103) in the Upper Zone 
above hole OS-14-227 returned 46.06 m of 11.24 g/t gold.

Hole OS-14-227 is a step-out from previous holes that intersected the Conrad 
Lower Zone (see news release dated October 9, 2013). Mineralization at the 
Lower Zone is open in all directions and has only been traced with limited 
drilling over a 300 m strike length below the core area of the Upper Zone. The 
Lower Zone is characterized by strong alteration and mineralization localized 
within and adjacent to several flat-lying faults that may be primary 
mineralizing fluid conduits. Drilling is ongoing at the Conrad Zone.

"Step out hole OS-14-227 further demonstrates the continuity and high grade 
nature of the Conrad Zone which remains open in all directions. With only 
limited drilling having been completed at the Lower Zone, significant potential 
exists to find new areas of mineralization and to expand the Lower Zone and 
associated flat-lying mineralized fault breccias." stated Graham Downs, ATAC's 
CEO.

Sunrise Zone

Drilling in 2014 at the Sunrise Zone has successfully expanded the mineralized 
area to the west of two of the final 2013 holes that returned 19.81 m of 5.54 
g/t gold (OS-13-214) and 16.76 m of 6.76 g/t gold (OS-13-217).

/T/

----------------------------------------------------------------------------
Sunrise Zone                        To
Drill Hole        From (m)         (m)  Interval (m)    Au (g/t)     Section
----------------------------------------------------------------------------

----------------------------------------------------------------------------
OS-14-225           190.50      206.35         15.85        2.03       S400E
----------------------------------------------------------------------------
and                 319.13      331.32         12.19        3.09
----------------------------------------------------------------------------
including           319.13      321.16          2.03        9.54
----------------------------------------------------------------------------

----------------------------------------------------------------------------
OS-14-226           288.04      298.70         10.66        3.45       S500E
----------------------------------------------------------------------------
-  The reported intersections are drilled thicknesses and are believed to
represent approximately 60 to 100% true widths.
-  Hole OS-14-224 did not intersect significant mineralization.

/T/

The higher grade part of the Sunrise Zone is a 100 to 150 m long, steeply south 
dipping and southwest-plunging body of stratabound, structurally controlled 
Carlin-type gold mineralization that remains open at depth.

Anubis Zone and Area

The Anubis Zone is located 10 km to the west of the Osiris Zone in an area 
underlain by Paleozoic limestones, shales and calcareous siltstones cut by a 
network of regional-scale fault zones. Three holes were completed at the Anubis 
Zone in 2014 to follow-up on the 2012 discovery hole which intersected 8.51 m 
of 19.85 g/t gold (AN-12-001). Two of the 2014 holes intersected the Anubis 
Fault on strike to the northwest and southeast of the discovery hole, while the 
third hole tested the Anubis Fault at depth. None of the 2014 Anubis holes 
intersected significant gold mineralization or identified the source of 
mineralization in the three previous holes. Additional trenching, test pitting 
and prospecting are ongoing to better understand the Anubis discovery zone 
outcrop and drill intersections in relation to nearby untested gold geochemical 
anomalies.

Elsewhere along the Anubis Fault and the nearby sub-parallel North Fault, 
ongoing soil sampling, overburden drilling and excavator trenching has outlined 
a cumulative strike length of over 8 km of pathfinder element+gold geochemical 
anomalies, most of which are hosted in the favourable limestone units that 
underlie the Anubis shales. Results of this and earlier work in the area are 
being compiled to select targets for diamond drilling.

QA/QC

Samples were forwarded to ALS Minerals in Whitehorse, Y.T. where they were fine 
crushed before a 250 gram split was pulverized to better than 85% passing 75 
microns. The pulverizing circuit was cleaned with quartz sand twice between 
samples. Pulps were then analyzed at ALS Minerals in North Vancouver, B.C. 
where gold determinations were carried out. Splits of the pulverized fraction 
were dissolved using a multi acid digestion and analyzed for 49 elements using 
inductively coupled plasma (ICP) together with mass spectrometry (MS) and 
atomic emission spectroscopy (AES). Gold analyses were by the Au-AA26 procedure 
that involves fire assay preparation using a 50 gram charge with an atomic 
absorption spectroscopy (AAS) finish. Mercury analyses were digested with aqua 
regia and analyzed by inductively coupled plasma mass spectrometry (ICP-MS).

Rigorous procedures are in place regarding sample collection, chain of custody 
and data entry. Certified assay standards, duplicate samples and blanks are 
routinely inserted into the sample stream to ensure integrity of the assay 
process. All of the samples included in this news release have passed the QA/QC 
procedures as described above.

The technical information in this news release has been approved by Julia Lane, 
P.Geo., the Rackla Gold Project manager and a geologist with Archer, Cathro & 
Associates (1981) Limited, and a qualified person for the purposes of National 
Instrument 43-101.

About ATAC

ATAC Resources Ltd. is a Yukon-based exploration company focused on developing 
Canada's only Carlin-type gold district at its 100% owned Rackla Gold Project. 
Recent work on the 1,700 sq/km project has resulted in a positive Preliminary 
Economic Assessment for the Tiger Deposit, drilling of multiple high-grade 
Carlin-type gold zones and the identification of numerous early-stage gold 
exploration targets. The Rackla Gold Project has no underlying royalties or 
third-party interests. ATAC is well financed with approximately $21 million in 
its treasury.

On behalf of Management and the Board of Directors of ATAC Resources Ltd.

Graham Downs, CEO

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES PROVIDER (AS THAT 
TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE EXCHANGE) ACCEPTS 
RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS RELEASE.

This news release may contain forward looking statements based on assumptions 
and judgments of management regarding future events or results that may prove 
to be inaccurate as a result of exploration and other risk factors.

- 30 -

CONTACT INFO:

ATAC Resources Ltd.
Vanessa Pickering
Manager, Corporate Communications
604-687-2522 ext. 260
vpickering@atacresources.com
www.atacresources.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=496042258