Source	MARKET NEWS
Date	08/26/2014
Time	09:24:22 AM

Company	 ATAC Resources Ltd.
Title	Intersects 
30.79 M Of 9.50 G/t Gold At Conrad,





    CDNX Symbol: ATC











Press Release	





ATAC RESOURCES LTD ("ATC-V;ATADF-0")
- Intersects 30.79 M Of 9.50 G/t Gold At Conrad,
- Rackla Gold Project-yukon

ATAC Resources Ltd. ("ATAC") is pleased to announce initial results
from its ongoing 2014 exploration program. The following results are
from drilling and surface work at the Conrad, Sunrise and Anubis Zones,
all located within the Nadaleen Trend at the eastern end of ATAC's 100%
owned 1,700 sq/km Rackla Gold Project in central Yukon.
//st
Highlights:

--  Conrad Lower Zone step out hole OS-14-277 extends high grade
mineralization -
30.79 m of 9.50 g/t gold;
--  Sunrise drilling extends mineralization to the west of 2013 drilling;
and
--  Anubis area surface exploration outlines pathfinder element+gold
anomalies with 8 km cumulative strike length, similar in size and
intensity to the Osiris area located 10 km to the east.

Conrad Zone
-----------------------------------------------------------------------
-----
Conrad Zone                         To
Drill Hole        From (m)         (m)  Interval (m)    Au (g/t)     Section
---------------------------------------------------------------------------
-
---------------------------------------------------------------------------
-
OS-14-227           434.12      438.52          4.40        5.50       C475E
---------------------------------------------------------------------------
-
and                 452.80      483.59         30.79        9.50
---------------------------------------------------------------------------
-
-  The reported intersections are drilled thicknesses and are believed to
represent approximately 60 to 100% true widths.
//et

Carlin-type gold mineralization at the Conrad Zone is contained
within several structural and stratigraphic settings. In the Conrad
Upper Zone, gold mineralization occurs in an anticline fold hinge. The
Upper Zone has been continuously traced by shallow drilling over a
strike length of 800 m between Sections C100E and C900E. A 2012 drill
hole (hole OS-12-103) in the Upper Zone above hole OS-14-227 returned
46.06 m of 11.24 g/t gold.

Hole OS-14-227 is a step-out from previous holes that intersected
the Conrad Lower Zone (see news release dated October 9, 2013).
Mineralization at the Lower Zone is open in all directions and has only
been traced with limited drilling over a 300 m strike length below the
core area of the Upper Zone. The Lower Zone is characterized by strong
alteration and mineralization localized within and adjacent to several
flat-lying faults that may be primary mineralizing fluid conduits.
Drilling is ongoing at the Conrad Zone.

"Step out hole OS-14-227 further demonstrates the continuity and
high grade nature of the Conrad Zone which remains open in all
directions. With only limited drilling having been completed at the
Lower Zone, significant potential exists to find new areas of
mineralization and to expand the Lower Zone and associated flat-lying
mineralized fault breccias." stated Graham Downs, ATAC's CEO.

Sunrise Zone

Drilling in 2014 at the Sunrise Zone has successfully expanded the
mineralized area to the west of two of the final 2013 holes that
returned 19.81 m of 5.54 g/t gold (OS-13-214) and 16.76 m of 6.76 g/t
gold (OS-13-217).

//st
-----------------------------------------------------------------------
-----
Sunrise Zone                        To
Drill Hole        From (m)         (m)  Interval (m)    Au (g/t)     Section
---------------------------------------------------------------------------
-
---------------------------------------------------------------------------
-
OS-14-225           190.50      206.35         15.85        2.03       S400E
---------------------------------------------------------------------------
-
and                 319.13      331.32         12.19        3.09
---------------------------------------------------------------------------
-
including           319.13      321.16          2.03        9.54
---------------------------------------------------------------------------
-
---------------------------------------------------------------------------
-
OS-14-226           288.04      298.70         10.66        3.45       S500E
---------------------------------------------------------------------------
-
-  The reported intersections are drilled thicknesses and are believed to
represent approximately 60 to 100% true widths.
-  Hole OS-14-224 did not intersect significant mineralization.

//et

The higher grade part of the Sunrise Zone is a 100 to 150 m long,
steeply south dipping and southwest-plunging body of stratabound,
structurally controlled Carlin-type gold mineralization that remains
open at depth.

Anubis Zone and Area

The Anubis Zone is located 10 km to the west of the Osiris Zone in
an area underlain by Paleozoic limestones, shales and calcareous
siltstones cut by a network of regional-scale fault zones. Three holes
were completed at the Anubis Zone in 2014 to follow-up on the 2012
discovery hole which intersected 8.51 m of 19.85 g/t gold (AN-12-001).
Two of the 2014 holes intersected the Anubis Fault on strike to the
northwest and southeast of the discovery hole, while the third hole
tested the Anubis Fault at depth. None of the 2014 Anubis holes
intersected significant gold mineralization or identified the source of
mineralization in the three previous holes. Additional trenching, test
pitting and prospecting are ongoing to better understand the Anubis
discovery zone outcrop and drill intersections in relation to nearby
untested gold geochemical anomalies.

Elsewhere along the Anubis Fault and the nearby sub-parallel North
Fault, ongoing soil sampling, overburden drilling and excavator
trenching has outlined a cumulative strike length of over 8 km of
pathfinder element+gold geochemical anomalies, most of which are hosted
in the favourable limestone units that underlie the Anubis shales.
Results of this and earlier work in the area are being compiled to
select targets for diamond drilling.

QA/QC

Samples were forwarded to ALS Minerals in Whitehorse, Y.T. where
they were fine crushed before a 250 gram split was pulverized to better
than 85% passing 75 microns. The pulverizing circuit was cleaned with
quartz sand twice between samples. Pulps were then analyzed at ALS
Minerals in North Vancouver, B.C. where gold determinations were
carried out. Splits of the pulverized fraction were dissolved using a
multi acid digestion and analyzed for 49 elements using inductively
coupled plasma (ICP) together with mass spectrometry (MS) and atomic
emission spectroscopy (AES). Gold analyses were by the Au-AA26
procedure that involves fire assay preparation using a 50 gram charge
with an atomic absorption spectroscopy (AAS) finish. Mercury analyses
were digested with aqua regia and analyzed by inductively coupled
plasma mass spectrometry (ICP-MS).

Rigorous procedures are in place regarding sample collection,
chain of custody and data entry. Certified assay standards, duplicate
samples and blanks are routinely inserted into the sample stream to
ensure integrity of the assay process. All of the samples included in
this news release have passed the QA/QC procedures as described above.

The technical information in this news release has been approved
by Julia Lane, P.Geo., the Rackla Gold Project manager and a geologist
with Archer, Cathro & Associates (1981) Limited, and a qualified person
for the purposes of National Instrument 43-101.

About ATAC

ATAC Resources Ltd. is a Yukon-based exploration company focused
on developing Canada's only Carlin-type gold district at its 100% owned
Rackla Gold Project. Recent work on the 1,700 sq/km project has
resulted in a positive Preliminary Economic Assessment for the Tiger
Deposit, drilling of multiple high-grade Carlin-type gold zones and the
identification of numerous early-stage gold exploration targets. The
Rackla Gold Project has no underlying royalties or third-party
interests. ATAC is well financed with approximately $21 million in its
treasury.

On behalf of Management and the Board of Directors of ATAC
Resources Ltd.

Graham Downs, CEO

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES
PROVIDER (AS THAT TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE
EXCHANGE) ACCEPTS RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS
RELEASE.

This news release may contain forward looking statements based
on assumptions and judgments of management regarding future events or
results that may prove to be inaccurate as a result of exploration and
other risk factors.

TSX Venture closing price for ATC-V
Date: 2014/08/25
Closing Price: 0.91

TEL:  604-687-2522 ext. 260  ATAC Resources Ltd.
Vanessa Pickering
Manager, Corporate Communications
E-mail: vpickering@atacresources.com
Internet: www.atacresources.com
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1423700034TS11423701641-09223920140826