Source	Marketwire
Date	08/29/2014
Time	09:45:00 AM

Company	 NV GOLD CORPORATION
Title	NV Gold Discovers New Gold Zone at Rattlesnake Hills





    CDNX Symbol: NVX











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: NV Gold Corporation

TSX VENTURE SYMBOL: NVX

August 29, 2014

NV Gold Discovers New Gold Zone at Rattlesnake Hills


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Aug. 29, 2014) -

NOT FOR DISTRIBUTION TO U.S. NEWS WIRE SERVICES OR FOR DISSEMINATION IN THE U.S.

NV Gold Corporation (TSX VENTURE:NVX) ("the Company") announced today that the 
14-hole drill program recently completed on its newly-acquired Rattlesnake 
Hills Project in Natrona County, Wyoming has intercepted significant gold 
mineralization at Blackjack, a previously undrilled target on the property.

Hole NVJ 001 intercepted 33.5 m grading 1.33 grams per tonne (or 1.33 ppm or 
110 feet @ 0.039 ounces per ton (opt)). Hole NVJ 001 was mineralized throughout 
its entire length of 152 meters (500 feet), with an average grade for the 
entire hole of 0.556 g/t. The hole is the western-most hole in the program and 
therefore this new zone is open in that direction. The Company has not received 
the silver assays for Hole NVJ 001 and will report them separately when 
received. Hole NVJ 001 was transected by Hole NVJ 008 (-45 degrees), which 
passed Hole NVJ 001 at approximately 85 meters from its collar (60m south of 
Hole NVJ 001). Several intercepts were present in Hole NVJ 008, confirming the 
results in Hole NVJ 001. (See table below)

Two additional holes were completed to the east of Hole NVJ 001 to test lateral 
continuity. Holes NVJ 005 and NVJ 007 were drilled 50 meters and 90 meters east 
of Hole NVJ 001, respectively. Both holes were angle holes drilled to test the 
structure at 60-80 meters depth. Both holes encountered multiple intercepts of 
gold and silver mineralization. Importantly, mineralization is increasing in 
intensity and grade from east to west. Significant results from the Blackjack 
program are as follows:

/T/

----------------------------------------------------------------------------
Au      Ag    Au Eq
Intercept  Length   Grade   Grade    Grade
Hole         TD (m)        (m)     (m)   (g/t)   (g/t)    (g/t) Area or Zone
----------------------------------------------------------------------------
----------------------------------------------------------------------------
NVJ 001         152      0-152     152   0.556     (i)      (i)    Blackjack
----------------------------------------------------------------------------
----------------------------------------------------------------------------
inc                     0-33.5    33.5   1.332     (i)      (i)
----------------------------------------------------------------------------
----------------------------------------------------------------------------
43-60      17   0.518     (i)      (i)
----------------------------------------------------------------------------
----------------------------------------------------------------------------
65.5-152      87   0.342     (i)      (i)
----------------------------------------------------------------------------
----------------------------------------------------------------------------
NVJ 002          76     0-12.2    12.2   0.384    1.33     0.40    Blackjack
----------------------------------------------------------------------------
----------------------------------------------------------------------------
NVJ 003         116     0-12.2    12.2   0.423    1.33     0.44    Blackjack
----------------------------------------------------------------------------
----------------------------------------------------------------------------
NVJ 004          76       0-20      20   0.201    1.39     0.22    Blackjack
----------------------------------------------------------------------------
----------------------------------------------------------------------------
NVJ 005         152       0-12      12   0.446    1.10     0.46    Blackjack
----------------------------------------------------------------------------
----------------------------------------------------------------------------
46-58      12   0.545    3.63     0.60
----------------------------------------------------------------------------
----------------------------------------------------------------------------
64-98      34   0.315    6.75     0.42
----------------------------------------------------------------------------
----------------------------------------------------------------------------
NVJ 007         152    111-122      11   0.860   11.44     1.04    Blackjack
----------------------------------------------------------------------------
----------------------------------------------------------------------------
NVJ 008         136       0-14      14   0.352    1.09     0.37    Blackjack
----------------------------------------------------------------------------
----------------------------------------------------------------------------
38-46       8   0.286    6.86     0.39
----------------------------------------------------------------------------
----------------------------------------------------------------------------
67.1-80.8    13.7   0.721   33.26     1.23
----------------------------------------------------------------------------
----------------------------------------------------------------------------
81-96      15   0.235    7.18     0.35
----------------------------------------------------------------------------
----------------------------------------------------------------------------
105-119      14   0.316   14.08     0.53

----------------------------------------------------------------------------
----------------------------------------------------------------------------
(i) Sample results not yet received
Notes: True widths of these intercepts cannot be determined with the
information currently available. Au Equivalent is calculated using
gold:silver of 1:65.

/T/

Key observations are as follows:

/T/

--  Seven of eight holes at Blackjack returned gold values of significance.
Six of eight holes, so far, report silver values of interest, with Hole
1 remaining to report.
--  Hole NVJ 001 was collared in strong mineralization and was mineralized
throughout its entire length.
--  Gold mineralization encountered in this drill program represents the
first discovery of gold outside the two previously drilled deposits at
North Stock and Antelope basin, located nearly 8 kilometers to the east,
supporting the concept that Rattlesnake Hills could be a district-scale
gold play.
--  Results indicate that the Blackjack Zone is increasing in grade and
intensity in an east to west direction. The strongest hole was on the
western edge of the drilling and is open to the west and north and at
depth.

/T/

Additionally, 6 holes were drilled at the Baldy Prospect, located on the 
northwestern portion of the property. Although there was no significant 
mineralization encountered in these holes, the alteration and structure was of 
interest and additional follow-up work will be undertaken.

John E. Watson, the Company's President, said "This was the Company's first 
exploration drilling program at Rattlesnake Hills and it has succeeded in its 
primary objective of discovering a new gold zone outside the two known, 
previously drilled deposits. The mineralization remains open to the west along 
strike and to the north. Both directions have geochemical sampling supportive 
of a successful follow-up program. We are very excited by these results and 
will be planning additional drilling at Blackjack and other targets in 2015."

Exploration activities at the Rattlesnake Hills Gold project were conducted 
under the supervision of Michael B. Ward, P.Geo., a contract geologist of NV 
Gold who is not independent but is a Qualified Person under NI 43-101. Mr. Ward 
has approved this news release. Assays reported were conducted by ALS Chemex 
(Reno, Nevada and Vancouver, BC, Canada) using fire assay with an AA finish and 
ICP. The data verification procedures and QA/QC procedures followed for the 
recent drilling program involved inserting certified standards and blanks into 
the sample stream. Rig duplicates have been collected.

NVX is a Vancouver-based company, whose objective is to create shareholder 
value by the acquisition, exploration, and development of gold projects located 
within the major gold producing areas of the western United States and in 
Switzerland.

On behalf of the Board of Directors,

John E. Watson, President

This news release includes certain forward-looking statements or information. 
All information other than statements of historical fact included in this 
release, including, without limitation, statements regarding future plans and 
objectives of the Company, is forward-looking information that involve various 
risks and uncertainties. In certain cases, forward-looking information can be 
identified by the use of words such as "plans", "expects" or "does not expect", 
"is expected", "budget", "scheduled", "estimates", "forecasts", "intends", 
"anticipates" or "does not anticipate", or "believes", or variations of such 
words and phrases or statements that certain actions, events or results "may", 
"could", "would", "might" or "will be taken", "occur" or "be achieved". 
Statements regarding the Rattlesnake Hills property being a district scale gold 
play and follow-up exploration are considered forward-looking information. 
Forward-looking information involves known and unknown risks, uncertainties and 
other factors which may cause the actual results, performance or achievements 
of the Company to be materially different from any future results, performance 
or achievements expressed or implied by the forward-looking information. There 
can be no assurance that such statements will prove to be accurate and actual 
results and future events could differ materially from those anticipated in 
such statements. Important factors that could cause actual results to differ 
materially from the Company's plans or expectations include availability of 
capital and financing, general economic, market or business conditions, 
regulatory changes, timeliness of government or regulatory approvals, risks 
inherent in the mineral exploration and production industry, and other risks 
detailed from time to time in the filings made by the Company with securities 
regulators. The Company expressly disclaims any intention or obligation to 
update or revise any forward-looking information whether as a result of new 
information, future events or otherwise except as otherwise required by 
applicable securities legislation.

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

NV Gold Corporation
John E. Watson
303-674-9400
john@watson-assoc.com
www.NVGoldCorp.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=496576542