Source	MARKET NEWS
Date	08/29/2014
Time	09:59:33 AM

Company	 NV Gold Corporation
Title	Discovers New Gold 
Zone At Rattlesnake Hills





    CDNX Symbol: NVX











Press Release	





NV GOLD CORP ("NVX-V")
- Discovers New Gold Zone At Rattlesnake Hills

NOT FOR DISTRIBUTION TO U.S. NEWS WIRE SERVICES OR FOR
DISSEMINATION IN THE U.S.

NV Gold Corporation ("the Company") announced today that the
14-hole drill program recently completed on its newly-acquired
Rattlesnake Hills Project in Natrona County, Wyoming has intercepted
significant gold mineralization at Blackjack, a previously undrilled
target on the property.

Hole NVJ 001 intercepted 33.5 m grading 1.33 grams per tonne (or
1.33 ppm or 110 feet @ 0.039 ounces per ton (opt)). Hole NVJ 001 was
mineralized throughout its entire length of 152 meters (500 feet), with
an average grade for the entire hole of 0.556 g/t. The hole is the
western-most hole in the program and therefore this new zone is open in
that direction. The Company has not received the silver assays for Hole
NVJ 001 and will report them separately when received. Hole NVJ 001 was
transected by Hole NVJ 008 (-45 degrees), which passed Hole NVJ 001 at
approximately 85 meters from its collar (60m south of Hole NVJ 001).
Several intercepts were present in Hole NVJ 008, confirming the results
in Hole NVJ 001. (See table below)

Two additional holes were completed to the east of Hole NVJ 001 to
test lateral continuity. Holes NVJ 005 and NVJ 007 were drilled 50
meters and 90 meters east of Hole NVJ 001, respectively. Both holes
were angle holes drilled to test the structure at 60-80 meters depth.
Both holes encountered multiple intercepts of gold and silver
mineralization. Importantly, mineralization is increasing in intensity
and grade from east to west. Significant results from the Blackjack
program are as follows:

//st
Hole     TD  Intercept Length   Au      Ag      Au Eq   Area or Zone
Grade   Grade   Grade
(m)       (m)    (m)   (g/t)   (g/t)   (g/t)
NVJ 001  152     0-152    152   0.556       *       *       Blackjack
inc             0-33.5   33.5   1.332       *       *
43-60     17   0.518       *       *
65.5-152     87   0.342       *       *
NVJ 002   76    0-12.2   12.2   0.384    1.33    0.40       Blackjack
NVJ 003  116    0-12.2   12.2   0.423    1.33    0.44       Blackjack
NVJ 004   76      0-20     20   0.201    1.39    0.22       Blackjack
NVJ 005  152      0-12     12   0.446    1.10    0.46       Blackjack
46-58     12   0.545    3.63    0.60
64-98     34   0.315    6.75    0.42
NVJ 007  152   111-122     11   0.860   11.44    1.04       Blackjack
NVJ 008  136      0-14     14   0.352    1.09    0.37       Blackjack
38-46      8   0.286    6.86    0.39
67.1-80.8   13.7   0.721   33.26    1.23
81-96     15   0.235    7.18    0.35
105-119     14   0.316   14.08    0.53

//et

//st
* Sample results not yet received
Notes:            True widths of these intercepts cannot be determined with
the information currently available. Au Equivalent is calculated using
gold:silver of 1:65.

//et

Key observations are as follows:

//st

Seven of eight holes at Blackjack returned gold values of
significance. Six of eight holes, so far, report silver values of interest,
with Hole 1 remaining to report.

Hole NVJ 001 was collared in strong mineralization and was mineralized
throughout its entire length.

Gold mineralization encountered in this drill program represents the first
discovery of gold outside the two previously drilled deposits at North
Stock and Antelope basin, located nearly 8 kilometers to the east,
supporting the concept that Rattlesnake Hills could be a district-scale
gold play.

Results indicate that the Blackjack Zone is increasing in grade and
intensity in an east to west direction. The strongest hole was on the
western edge of the drilling and is open to the west and north and at
depth.

//et

Additionally, 6 holes were drilled at the Baldy Prospect, located
on the northwestern portion of the property. Although there was no
significant mineralization encountered in these holes, the alteration
and structure was of interest and additional follow-up work will be
undertaken.

John E. Watson, the Company's President, said "This was the
Company's first exploration drilling program at Rattlesnake Hills and
it has succeeded in its primary objective of discovering a new gold
zone outside the two known, previously drilled deposits. The
mineralization remains open to the west along strike and to the north.
Both directions have geochemical sampling supportive of a successful
follow-up program. We are very excited by these results and will be
planning additional drilling at Blackjack and other targets in 2015."

Exploration activities at the Rattlesnake Hills Gold project were
conducted under the supervision of Michael B. Ward, P.Geo., a contract
geologist of NV Gold who is not independent but is a Qualified Person
under NI 43-101. Mr. Ward has approved this news release. Assays
reported were conducted by ALS Chemex (Reno, Nevada and Vancouver, BC,
Canada) using fire assay with an AA finish and ICP. The data
verification procedures and QA/QC procedures followed for the recent
drilling program involved inserting certified standards and blanks into
the sample stream. Rig duplicates have been collected.

NVX is a Vancouver-based company, whose objective is to create
shareholder value by the acquisition, exploration, and development of
gold projects located within the major gold producing areas of the
western United States and in Switzerland.

On behalf of the Board of Directors,

John E. Watson, President

This news release includes certain forward-looking statements or
information. All information other than statements of historical fact
included in this release, including, without limitation, statements
regarding future plans and objectives of the Company, is
forward-looking information that involve various risks and
uncertainties. In certain cases, forward-looking information can be
identified by the use of words such as "plans", "expects" or "does not
expect", "is expected", "budget", "scheduled", "estimates",
"forecasts", "intends", "anticipates" or "does not anticipate", or
"believes", or variations of such words and phrases or statements that
certain actions, events or results "may", "could", "would", "might" or
"will be taken", "occur" or "be achieved". Statements regarding the
Rattlesnake Hills property being a district scale gold play and
follow-up exploration are considered forward-looking information.
Forward-looking information involves known and unknown risks,
uncertainties and other factors which may cause the actual results,
performance or achievements of the Company to be materially different
from any future results, performance or achievements expressed or
implied by the forward-looking information. There can be no assurance
that such statements will prove to be accurate and actual results and
future events could differ materially from those anticipated in such
statements. Important factors that could cause actual results to differ
materially from the Company's plans or expectations include
availability of capital and financing, general economic, market or
business conditions, regulatory changes, timeliness of government or
regulatory approvals, risks inherent in the mineral exploration and
production industry, and other risks detailed from time to time in the
filings made by the Company with securities regulators. The Company
expressly disclaims any intention or obligation to update or revise any
forward-looking information whether as a result of new information,
future events or otherwise except as otherwise required by applicable
securities legislation.

Neither TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

NV Gold Corporation
TSX Venture closing price for NVX-V
Date: 2014/08/28
Closing Price: 0.33

TEL:     303-674-9400 John E. Watson
E-mail:  john@watson-assoc.com
Website: www.NVGoldCorp.com
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1424000036TS11424000940-09582220140829