Source	Filing Services Canada
Date	09/02/2014
Time	04:30:17 AM

Company	 ENDURANCE GOLD CORPORATION
Title	Endurance Reports 140 Metres of 5.2 Grams per Tonne Gold from the Godzilla 
Zone, Pardo Joint Venture, Ontario





    CDNX Symbol: EDG











Press Release	




SOURCE: Filing Services Canada
Date: 09/02/2014
Time: 07:30:00

Company: ENDURANCE GOLD CORPORATION
Title:Endurance Reports 140 Metres of 5.2 Grams per Tonne Gold from the 
Godzilla Zone, Pardo Joint Venture, Ontario (EDG - TSXV) 
TSXV SYMBOL: EDG


NEWS TRANSMITTED BY FILING SERVICES CANADA
FOR: Endurance Gold Corporation
TSXV SYMBOL: EDG
Tuesday, September 02, 2014 - 7:30 AM

Original Source Location: 
http://www.fscwire.com/newsrelease/endurance-reports-140-metres-52-grams-tonne-g
old-godzilla-zone-pardo-joint-venture

Endurance Reports 140 Metres of 5.2 Grams per Tonne Gold from the Godzilla 
Zone, Pardo Joint Venture, Ontario


Vancouver, British Columbia (FSCwire) - Endurance Gold Corporation (EDG  TSX.V, 
Endurance) announces that the operator of the Pardo Joint Venture property 
(Pardo JV Property), Ginguro Exploration Inc. (Ginguro), has today provided new 
encouraging results from the Godzilla Zone on the Pardo JV Property. The Pardo 
JV Property is comprised of 16 claims located approximately 65 km northeast of 
Sudbury, Ontario. Ginguro is the operator of the Pardo JV Property (Operator) 
and holds a 64.5% ownership interest and Endurance owns a 35.5% ownership 
interest.



The Operator reports assays have been received for three additional saw-cut 
channel samples taken at the recently discovered Godzilla Zone. Channel 14-34 
returned an average of 5.2 grams per tonne gold (g/t Au) over 140 metres. 
Channel 14-35, which was cut sub-parallel to channel 14-34 at a slightly higher 
elevation, averaged 2.6 g/t Au over 18.5 metres. Channel 14-36, which was cut 
approximately perpendicular to channel 14-34 and channel 14-35 averaged 1.5 g/t 
Au over 21.5 metres. Channel 14-34 is comprised of a 95 metre long north 
section that averaged 4.5 g/t Au, and a south section that averaged 6.5 g/t Au 
over 45 metres. The two sections of the channel include minor offsets where 
necessary to cross covered areas and are separated by a five-metre section 
where no rock is exposed. The gold-bearing conglomerate sampled at the Godzilla 
Zone appears to have an average true thickness of approximately 4 metres.



All of the channel sampling at the Godzilla Zone is now complete. A total of 
527 metres of channel sample were cut across the zone. Assay results for 294 
metres of channel samples remain outstanding. The exposed outcrop area which 
contains the Godzilla Zone mineralization measures 175 metres north-south by up 
to 125 metres east-west.



Maps illustrating the geology and channel sample locations can be found on the 
Companys website at www.endurancegold.com (http://www.endurancegold.com).



Due to the near flat lying nature of the sedimentary strata, it is not always 
possible to cut samples across the gold-bearing strata. Samples are usually 
collected either parallel or perpendicular to the interpreted paleochannel 
direction. Therefore,the channel lengths reported in this release represent the 
gold distribution over the surface area sampled and do not represent true 
thicknesses of the mineralized unit. The known gold mineralization within the 
nearly flat-lying near-surface basal conglomerate on the Pardo JV Property now 
extends approximately 3 kilometres north-south by approximately 1.1 kilometres 
east-west.



Both Ginguro and Endurance are funding the 2014 program on a pro rata basis, 
based on ownership. The Operator reports that the next two months remaining in 
the field season will be directed towards prospecting other prospective areas 
as well as targets generated by the recently completed radon gas survey on the 
Pardo JV Property.



In the preparation of this news release, Endurance has relied on data collected 
and compiled by the Operator of exploration programs, and summarized to the 
Company for this release. Robert T. Boyd, P.Geo. is a qualified person as 
defined in National Instrument 43-101 and supervised the compilation of the 
technical information provided by the Operator and forming the basis for this 
release. Potential quantity and grade is conceptual in nature. There has been 
insufficient exploration to define a mineral resource on the Pardo JV Property 
to date, and it is uncertain if further exploration will result in the target 
being delineated as a mineral resource. The Operator reports that Pardo JV 
samples are transported in security sealed bags for preparation at AGAT Prep 
Lab located in Sudbury, Ontario. Prepped samples are shipped for analysis to 
the AGAT Assay Laboratory in Mississauga, Ontario. AGAT Laboratories Ltd. is an 
ISO 17025 registered laboratory. The Operator reports that the channel samples 
summarized in this release for channel 14-43 north were assayed using a 
modified pulp metallic assay procedure. The entire sample was crushed and 
pulverized to 85% passing 100 mesh. The +100 mesh material was fluxed and 
assayed in its entirety, while two 50 g aliquots of the -100 mesh undersize 
pulp were cut out and fire assayed. Results were reported as a weighted average 
of gold in the three fractions. The operator reports that samples for channels 
14-34 south, 14-35 and 14-36 were also crushed in their entirety, with a 1kg 
split then pulverized. Two 50 g aliquots of the pulp were cut out and fire 
assayed. Results were reported as a weighted average of gold in the two 
fractions. In instances where the averages exceed 10 g/t, the sample is re-run 
with a gravimetric finish and the gravimetric result is reported. The Operator 
reports that they insert a certified reference standard or an analytical blank 
in every batch of 20 samples and that validation parameters are established in 
the database to ensure quality control. The operator reports that validation 
parameters are established in the database to ensure quality control.



About Endurance

Endurance Gold Corporation is a company focused on the acquisition, exploration 
and development of highly prospective North American mineral properties with 
the potential to develop world-class deposits. The Company's exploration focus, 
for projects operated by Endurance, is intrusive-related mineral systems with 
potential for discovery of major new precious or rare metals deposits, and its 
business plan offers shareholders exposure to several majority-owned 
exploration projects with significant discovery potential such as the Elephant 
Gold Property in Alaska, the Rattlesnake Hills Gold Property in Wyoming, and 
the Bandito Rare Earth-Niobium Property in the Yukon. Please visit 
www.endurancegold.com (http://www.endurancegold.com).



ENDURANCE GOLD CORPORATION



Robert T. Boyd

Per: 

President & CEO



FOR FURTHER INFORMATION, PLEASE CONTACT

Endurance Gold Corporation

(604) 682-2707, info@endurancegold.com (mailto:info@endurancegold.com)

www.endurancegold.com (http://www.endurancegold.com/)



Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this news release. This news 
release may contain forward looking statements based on assumptions and 
judgments of management regarding future events or results that may prove to be 
inaccurate as a result of factors beyond its control, and actual results may 
differ materially from the expected results.



NEWS RELEASE 14-16


To view this press release as a PDF file, click onto the following link:
http://www.fscwire.com/sites/default/files/news_release_pdf/EnduranceSept22014.p
df
Source: Endurance Gold Corporation (TSX Venture:EDG) 
http://www.endurancegold.com



Maximum News Dissemination by FSCwire. http://www.fscwire.com



Copyright(C)2014 Filing Services Canada Inc.