Source	Marketwire
Date	09/02/2014
Time	05:30:23 AM

Company	 KAMINAK GOLD CORPORATION
Title	Kaminak Drills New Gold Discovery 3.55g/t Au over 28m at Coffee and 
Announces Phase II Exploration Program





    CDNX Symbol: KAM











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Kaminak Gold Corporation

TSX VENTURE SYMBOL: KAM

September 2, 2014

Kaminak Drills New Gold Discovery 3.55g/t Au over 28m at Coffee and Announces 
Phase II Exploration Program


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Sept. 2, 2014) - Kaminak Gold 
Corporation (TSX VENTURE:KAM) today announced results for 27 drill holes from 
the recently completed, $3.5 million, 2014 Phase I exploration drilling 
campaign at the Coffee Gold Project, Yukon Territory. The objective of the 
program was to drill test priority gold-in-soil anomalies situated proximal to 
the current resource that have the potential to contribute high-value, open-pit 
oxide resources to the existing mine plan. Kaminak recently announced the 
results from a preliminary economic assessment (PEA) at Coffee demonstrating a 
robust, high-margin, rapid pay-back, 11-year open pit mining project using a 
US$1250/oz. gold price.

Phase I exploration drilling in 2014 successfully identified shallow, 
predominately oxidized gold-bearing structures within the Kona North zone 
returning 3.55 grams per tonne gold (g/t Au) over 28 metres (m), extended 
mineralization 900 metres along strike on the Supremo T3 trend and intersected 
high-grade gold mineralization at Cappuccino. A $2 million, Phase II 
exploration program has been approved by the Board of Directors and is underway 
targeting Kona North primarily and other additional priority gold-in-soil 
anomalies proximal to the current resource. The Phase II program will proceed 
in conjunction with the recently commenced Feasibility Program (see news 
release 28 July, 2014).

Kaminak President and CEO, Eira Thomas, commented: "Ongoing exploration of the 
numerous high-tenor geochemical anomalies remaining at Coffee continues to 
demonstrate the resource upside of the project and has the potential to enhance 
the already positive, high-margin economics at Coffee as demonstrated in the 
recently completed PEA. Delineation drilling at Kona North is underway with the 
goal of defining a near surface, oxide resource that may be incorporated into 
the Coffee Feasibility Study."

Exploration Highlights

/T/

--  Kona North Discovery: Drilling intersected 3.55 g/t Au over 28m from 14m
downhole and 2.66g/t Au over 9m from 53m downhole (CFD376), and 4.05g/t
Au over 8m from 38m downhole and 3.79g/t Au over 8m from 51m downhole
(CFD379). Additional drilling is underway to determine the structural
orientation and geometry of the zone and to delineate near-surface oxide
ounces that may be incorporated into the Feasibility Study.
--  Drilling also extended the Supremo T3 mineralized zone northwards to at
least 3.5km strike length and returned best drill results at the
intersection of the T3 and Macchiato trends. Drill results include: 1.95
g/t over 14m (from 81m) and 2.21 g/t over 9m (from 128m). The T3
structure remains open to the north along strike and to depth.
--  The Phase II exploration program is budgeted at $2M with the goal of
augmenting the global resource inventory, which will be incorporated
into the final Feasibility Study. The Phase II program has commenced and
the initial $12 million feasibility program previously announced is
ongoing.

/T/

Phase I Exploration Drilling Results

The objective of the 2014 Phase I Coffee Exploration Program was to explore 
primarily untested gold-in-soil anomalies and geophysical targets, which occur 
in close proximity to the existing Coffee Mineral Resource Estimate of 719,000 
ounces Indicated (14 Mt grading at 1.56g/t Au), and 3,434,000 ounces Inferred 
(79 Mt grading at 1.36g/t Au) using a base case cut-off of 0.5g/t Au for Oxide 
and Transitional material and a 1g/t Au cut-off for Sulphide material. The 
targeted zones, which occur within 1-2 kilometres of the existing resources, 
included T3 North, Macchiato, Cappuccino, Arabica, Latte West, and Kona North. 
Exploration comprised trenching, infill soil sampling, prospecting and drilling 
targeting near-surface oxide mineralization. Drilling results are tabulated 
below.

Kona North consists of 1.5km x 0.5km gold-in-soil anomaly peaking at 1.6g/t Au, 
which straddles the contact between Permian gneisses and schists (host rocks to 
Latte-Supremo) and the Cretaceous Coffee Creek Granite. The gold-in-soil 
anomaly is coincident with topographic and magnetic lineaments interpreted to 
represent the extensions of the Latte and Americano structures and a possible 
third NNW trending structure. The highest tenor gold-in-soils occur at the 
interpreted intersection zone of the three structures. Drilling in 2010 
intersected highly deformed and altered Permian schist with gold mineralization 
peaking at 1.46g/t Au over 4m from 32m downhole, but did not intersect the 
schist-granite contact. Drilling in 2014 was oriented south to north, with the 
intent to drill orthogonally to the lithological contact and the interpreted 
Latte and Americano structures. At the Latte-Americano intersection zone, 
drilling intersected gold mineralization primarily hosted in granite in the 
hanging-wall to the contact with Permian basement rocks. Mineralization 
comprises disseminated sulphide and stockwork sulphide veinlets accompanied by 
strong silicification and clay alteration. Intercepts of completely to 
partially oxidized mineralized granite included 3.55g/t Au over 28m from 14m 
downhole in CFD0376, 4.05g/t Au over 8m from 38m downhole and 3.79g/t Au over 
8m from 51m downhole in CFD0379. Gold-in-soils, lineament mapping and 
geophysical data support a strike approximately orthogonal to drilling; 
however, an alternative orientation is that the drilling may be oblique to the 
strike of mineralization. Additional drilling is planned to investigate the 
geometry of the oxide mineralization intersected in CFD376 & 379.

At Supremo, previous drilling defined Inferred and Indicated resources on the 
T3 structure over a 2.5km strike length. 2014 trenching and drilling targeted 
the northward extension of the gold-in-soil anomalism and the T3 magnetic 
lineament and extended mineralization an additional 900m along strike to a 
total strike length of 3.4km. Magnetics and geochemistry suggest T3 may extend 
an additional 1km further northwards to a potential total strike length of 
4.5km. The best drilling intercepts occurred at the intersection of T3 and the 
Macchiato trends, comprising 1.95g/t Au over 14m from 81m and 2.21 g/t over 9m 
from 128m in CFD356. The results warrant additional systematic step-out 
drilling northward along strike on Supremo T3 with the objective to extend open 
pit oxide resources.

The Cappuccino geochem anomaly occurs over 900m x 600m, and with a peak assay 
of 26.5g/t Au in soil, is the highest tenor soil anomaly on the Coffee property 
found to date. Trenching and drilling intersected bedrock mineralization on N, 
NE and NW trending structures. CFD0362 intersected 6.63g/t Au over 5m from 68m 
downhole, which included 17.76g/t Au over 1.15m from 71m downhole.

Drilling Results

/T/

----------------------------------------------------------------------------
Weighted
Average
From        To     Width     grade
Prospect              Drill Hole           (m)       (m)    (m)(i)  (g/t Au)
----------------------------------------------------------------------------
T3 North              CFD0353               43        45         2      2.56
----------------------------------------------------------------------------
T3 North              CFD0353               60        62         2      1.12
----------------------------------------------------------------------------
T3 North              CFD0354                6        10         4      3.57
----------------------------------------------------------------------------
T3 North              CFD0354               65        69         4      4.10
----------------------------------------------------------------------------
T3 North/Macchiato    CFD0355               67        78        11      1.48
----------------------------------------------------------------------------
T3 North/Macchiato    CFD0355               84        89         5      1.38
----------------------------------------------------------------------------
T3 North/Macchiato    CFD0356               52        54         2      1.99
----------------------------------------------------------------------------
T3 North/Macchiato    CFD0356               81        95        14      1.95
----------------------------------------------------------------------------
T3 North/Macchiato    CFD0356              102       107         5      1.73
----------------------------------------------------------------------------
T3 North/Macchiato    CFD0356              128       137         9      2.21
----------------------------------------------------------------------------
No significant result - dike intersected
Macchiato             CFD0357                    in target zone
----------------------------------------------------------------------------
Supremo T3 North      CFD0358               18        19         1      1.83
----------------------------------------------------------------------------
Supremo T3 North      CFD0359               19        22         3      1.05
----------------------------------------------------------------------------
Supremo T3 North      CFD0359               34        39         5      1.26
----------------------------------------------------------------------------
Supremo T3 North      CFD0359              114       116         2      4.82
----------------------------------------------------------------------------
Supremo T3 North      CFD0360               32        34         2      1.34
----------------------------------------------------------------------------
Macchiato             CFD0361              113       114         1      1.18
----------------------------------------------------------------------------
Cappuccino            CFD0362               32        38         6      0.85
----------------------------------------------------------------------------
Cappuccino            CFD0362               46        50         4      2.66
----------------------------------------------------------------------------
Cappuccino            CFD0362               68        73         5      6.63
----------------------------------------------------------------------------
Including             71     72.15      1.15     17.76
----------------------------------------------------------------------------
Cappuccino            CFD0362              147       149         2      1.83
----------------------------------------------------------------------------
Cappuccino            CFD0363               77        82         5      1.27
----------------------------------------------------------------------------
Cappuccino            CFD0363               99       101         2      5.47
----------------------------------------------------------------------------
Cappuccino            CFD0363              137       140         3       1.5
----------------------------------------------------------------------------
French Press          CFD0364              127       128         1      3.85
----------------------------------------------------------------------------
Cappuccino            CFD0365               29        30         1      3.03
----------------------------------------------------------------------------
Cappuccino            CFD 366              147       152         5      3.98
----------------------------------------------------------------------------
French Press          CFD0366               94        99         5      0.81
----------------------------------------------------------------------------
French Press          CFD0367                 No Significant Result
----------------------------------------------------------------------------
French Press          CFD0368                 No Significant Result
----------------------------------------------------------------------------
Cappuccino            CFD0369               36        39         3      2.34
----------------------------------------------------------------------------
Cappuccino            CFD0369               48        51         3       1.1
----------------------------------------------------------------------------
Cappuccino            CFD0370               97        98         1      2.54
----------------------------------------------------------------------------
Cappuccino            CFD0370              114       124        10      1.52
----------------------------------------------------------------------------
Cappuccino            CFD0371                 No Significant Result
----------------------------------------------------------------------------
Supremo T7            CFD0372               83        88         5       3.4
----------------------------------------------------------------------------
Cappuccino            CFD0373                 No Significant Result
----------------------------------------------------------------------------
Latte                 CFD0374               45        46         1      4.00
----------------------------------------------------------------------------
Latte                 CFD0374               56        58         2      2.33
----------------------------------------------------------------------------
Latte                 CFD0374              111       113         2      1.03
----------------------------------------------------------------------------
Kona North            CFD0375               36        40         4      0.86
----------------------------------------------------------------------------
Kona North            CFD0376               14        42        28      3.55
----------------------------------------------------------------------------
Kona North            CFD0376               53        62         9      2.66
----------------------------------------------------------------------------
Kona North            CFD0376               65        77        12      0.89
----------------------------------------------------------------------------
Kona North            CFD0377                 No Significant Result
----------------------------------------------------------------------------
Kona North            CFD0378               15        17         2      1.15
----------------------------------------------------------------------------
Kona North            CFD0378               20        21         1      2.69
----------------------------------------------------------------------------
Kona North            CFD0379               38        46         8      4.05
----------------------------------------------------------------------------Kona
 North            CFD0379               51        59         8      3.79
----------------------------------------------------------------------------
Kona North            CFD0379               71        74         3      4.19
----------------------------------------------------------------------------
Kona North            CFD0379               79        83         4      5.78
----------------------------------------------------------------------------
Kona North            CFD0379              127       131         4      2.13
----------------------------------------------------------------------------

(i) True width estimated at approximately 2/3 down-hole length except for
Kona North, where the orientation of the structure has yet to be determined.

/T/

All maps, sections and assay sheets associated with this news release can be 
viewed by clicking the following link: 
http://kaminak.com/news_releases/index.php?&content_id=591

Field Program Updates: Feasibility and Exploration

As recently announced (28 July, 2014), in conjunction with the closing of a 
$13.52M private placement (23 July, 2014), the Company has commenced a 
Feasibility Study the Coffee Gold Project. Drilling and related field programs 
have been extended into the fall of 2014 with the objective to complete 
critical path and long lead time work programs. Four diamond core drills and 
two RC percussion drill are now turning on the property, undertaking resource 
delineation infill, condemnation, geotechnical, hydrological and metallurgical 
drilling. Environmental and heritage baseline studies and engineering studies 
into the optimal route and design of the access road are also advancing as 
planned.

On the back of the positive exploration results from Kona North, T3 North and 
Cappuccino, the Company also approved a Phase II Exploration Program at the 
Kona North zone and other high priority exploration targets. The Company is 
debt-free and fully-financed to complete its 2014 objectives.

QA / QC

Kaminak's disclosure of a technical or scientific nature in this press release 
has been reviewed and approved by Tim Smith, P.Geo., Vice President Exploration 
of Kaminak Gold Corporation, who serves as a Qualified Person under the 
definition of National Instrument 43-101. Quality assurance and quality control 
procedures include the systematic insertion of blanks and standards into the 
drill sample string. Samples are placed in sealed bags and shipped directly to 
the ALS Minerals preparatory laboratory in Whitehorse prior to gold fire assay.

On behalf of the Board of Directors of Kaminak

Eira Thomas, President and CEO

Kaminak Gold Corporation

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accept 
responsibility for the adequacy or accuracy of this release.

Caution Concerning Forward-Looking Statements

Certain disclosures in this release, including management's assessment of the 
future potential of the Coffee Project and future exploration programs, 
constitute forward-looking statements that are subject to numerous risks, 
uncertainties and other factors relating to Kaminak's operations as a mineral 
exploration company that may cause future results to differ materially from 
those expressed or implied in such forward-looking statements, including risks 
as to the completion of the plans and projects. Readers are cautioned not to 
place undue reliance on forward-looking statements. Except as required by law, 
Kaminak expressly disclaims any intention or obligation to update or revise any 
forward-looking statements, whether as a result of new information, future 
event, or otherwise.

The Company has not made a production decision, and the Company's strategic 
plan to develop a stand-alone heap leach operation is subject to the results of 
its Feasibility Study. Further, if and when the Company makes any production 
decision, it will disclose the basis of such decision in accordance with the 
requirements of National Instrument 43-101 Standards of Disclosure for Mineral 
Projects ("NI 43-101").

Cautionary Note concerning estimates of Inferred and Indicated Resources:

This news release uses the terms "Inferred Resources" and "Indicated 
Resources", which have a great amount of uncertainty as to their existence, and 
great uncertainty as to their economic and legal feasibility. It cannot be 
assumed that all or any part of an Inferred and/or Indicated Mineral Resource 
will ever be upgraded to a higher category. Under Canadian rules, estimates of 
Inferred Resources may not form the basis of feasibility or other economic 
studies. Kaminak advises U.S. investors that while this term is recognized and 
required by Canadian regulations, the U.S. Securities and Exchange Commission 
does not recognize it. U.S. investors are cautioned not to assume that part or 
all of an Inferred and Indicated resource exists, or is economically or legally 
minable.

- 30 -

CONTACT INFO:

Kaminak Gold Corporation
Tony Reda
Vice President of Corporate Development
Toll-Free: 1.888.331.2269 or direct: 604.646.4534
info@kaminak.com
www.kaminak.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=496642333