Source	Marketwire
Date	08/06/2015
Time	05:02:27 AM

Company	 KAPUSKASING GOLD CORP.
Title	Kapuskasing Gold Identifies 2 Gold Mineralization Settings at Rollo 
Sampling Up to 8.59 g/t and 11.41 g/t as It Readies for Diamond Drilling





    CDNX Symbol: KAP











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Kapuskasing Gold Corp.

TSX VENTURE SYMBOL: KAP

August 6, 2015

Kapuskasing Gold Identifies 2 Gold Mineralization Settings at Rollo Sampling Up 
to 8.59 g/t and 11.41 g/t as It Readies for Diamond Drilling


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Aug. 6, 2015) - Kapuskasing Gold 
Corp. (TSX VENTURE:KAP) (the "Company" or "KAP") reports the results of 
prospecting and channel sampling at its Rollo Property located in northern 
Ontario. Sampling at the high-grade Racicot Gold Showing (previously reported 
as the Hanson Occurrence, see news release June 11, 2015) has identified two 
different gold bearing relationships - a north bearing quartz vein system 
sampled in three locations over 30 meters of strike which returned up to 8.59 
g/t over 0.6 meters and a syenite/porphyry dike system crosscutting the quartz 
vein system which sampled up to 11.41 g/t along its contact with east-west 
trending mafic metavolcanics. A drill program is now being designed to further 
test these two gold mineralization relationships.

Garry Clark, KAP's exploration manager comments: "We will be conducting a 
series of short (approx. 50 meter) diamond drill holes to test both styles of 
gold mineralization and attempt to add a third dimension to the high grade 
sampling encountered so far. Drill permits are anticipated to be in place by 
late August and drilling contracts are currently being evaluated. The Company 
also continues its discussions with First Nations in the area and expects to 
sign early exploration agreements in the very near term."

The recent program was comprised of prospecting, mapping and sampling (grab and 
channels). A total of 12 channel samples and 3 grab samples were taken from the 
Racicot gold showing (see website for map). The channel saw-cuts and grab 
samples focused on two exposed areas at the Racicot gold showing and determined 
that there are two principal gold bearing relationships.

Gold mineralization associated with:

1) A north bearing quartz, quartz carbonate vein system that cross cuts the 
east-west trending mafic metavolcanics and

2) A syenite/porphyry dike system that trends sub parallel to the metavolcanics.

From observations of the limited geological exposure, the dike system seems to 
crosscut the quartz vein system. The sampling of the quartz vein system in 
three locations over an approximate 30 meter strike length included 8.82 g/t 
gold over 0.6 metres. The grab samples were taken at the south contact of the 
Syenite/Metavolcanics where channel sampling was not possible. The grab samples 
highlighted the gold concentration along the contact with assays of 1.0, 1.89 
and 11.41 g/t gold.

/T/

SAMPLING OF RACICOT SHOWING

----------------------------------------------------------------------------
Grams
Sample   Location   Sample    Sample                  Gold  Length   Average
No.       Racicot     Type Direction  Description  per Ton  Metres    GGPT/M
----------------------------------------------------------------------------
South             East -
284701      Strip  Channel      West  Quartz Vein    2.454     0.5
----------------------------------------------------------------------------
South             East -
284702      Strip  Channel      West  Quartz Vein    1.106     0.4
----------------------------------------------------------------------------
South             East -
284703      Strip  Channel      West  Quartz Vein    0.825     0.3  1.60/1.2
----------------------------------------------------------------------------
South             East -
284704      Strip  Channel      West  Quartz Vein     0.27     0.7  1.12/1.9
----------------------------------------------------------------------------
Syenite /
North                      Volcanic /
284677      Strip     Grab                Contact   11.414
----------------------------------------------------------------------------
Syenite /
North                      Volcanic /
284678      Strip     Grab                Contact     1.01
----------------------------------------------------------------------------
Syenite /
North                      Volcanic /
284679      Strip     Grab                Contact    1.885
----------------------------------------------------------------------------
North             North-
284705      Strip  Channel     South      Syenite    0.331     0.9
----------------------------------------------------------------------------
North             North-
284706      Strip  Channel     South      Syenite    0.114     0.7
----------------------------------------------------------------------------
North             North-
284707      Strip  Channel     South      Syenite     0.43     0.9
----------------------------------------------------------------------------
Syenite /
North             North-   Volcanic /
284708      Strip  Channel     South      Contact    6.752     0.5
----------------------------------------------------------------------------
North             North-        Mafic
284709      Strip  Channel     South     Volcanic    0.048     0.7
----------------------------------------------------------------------------
Quartz vein
North             East -    and Mafic
284710      Strip  Channel      West     Volcanic    1.237     0.7
----------------------------------------------------------------------------
Quartz vein
North             East -    and Mafic
284711      Strip  Channel      West     Volcanic    0.036     0.6
----------------------------------------------------------------------------
North             East -
284712      Strip  Channel      West  Quartz Vein    8.594     0.6
----------------------------------------------------------------------------

/T/

Ongoing prospecting/sampling at other locations on Rollo:

Concurrent with the work at the Racicot showing, 53 grab samples were collected 
at various areas of the property as part of an ongoing program to advance known 
gold showings at Rollo. Prospecting focused on any potential gold bearing 
environments. Samples are illustrated on the company website.

/T/

Rollo Prospecting Sampling
----------------------------------------------------------------------------
Number of Samples                                                 Range Gold
----------------------------------------------------------------------------
27                                                Below detection limit (DL)
----------------------------------------------------------------------------
11                                                 greater than DL to 49 ppb
----------------------------------------------------------------------------
5                                                               50 to 99 ppb
----------------------------------------------------------------------------
3                                                             100 to 199 ppb
----------------------------------------------------------------------------
4                                                             200 to 499 ppb
----------------------------------------------------------------------------
greater than 500 ppb
2                                       (0.639 and 1.309 grams gold per ton)
----------------------------------------------------------------------------

/T/

Previous sampling of the Coppell Lake area had located an anomalous gold sample 
associated with a quartz feldspar porphyry within sheared mafic metavolcanics. 
The examination indicates a shallow blast or pit on the quartz feldspar 
porphyry. A total of 11 samples were taken with 5 greater than 100 ppb gold 
with one assaying 1.309 g/t gold. All samples were from quartz feldspar 
porphyry with variable amounts of quartz veinlets and pyrite. The 1.309 g/t 
gold sample contains 3-5 mm quartz veinlets and greater than 1% pyrite.

The Rollo property is situated along a projected extension of the 
Destor-Porcupine fault zone, which hosts several multi-million-ounce gold 
producers in the nearby Timmins camp, and sits between IAMGOLD's Cote Lake gold 
deposit and Goldcorp's Borden Gold project.

Kapuskasing Gold has 6 gold properties located along extensions of the 
Destor-Porcupine or Borden Gold project. All of the properties, with the 
exception of Rollo, are situated within the Kapuskasing structural zones and 
have potential similarities to Goldcorp's Borden Gold project. A detailed map 
and property descriptions can be viewed on the Company's website: 
www.kapgold.com.

On behalf of the Board of Directors of Kapuskasing Gold Corp.,

Dean Nawata, President & CEO, Director

Qualified Person

Mr. Garry Clark P.Geo, the Exploration Manager and a director of the Company, a 
Qualified Person ("QP") as defined by National Instrument 43-101, has reviewed 
the technical content of this release.

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

Forward-Looking Statements and Cautionary Notes

Statements in this document which are not purely historical are forward-looking 
statements, including any statements regarding beliefs, plans, expectations or 
intentions regarding the future. Forward-looking statements contained in this 
document are based on certain key expectations and assumptions made by 
Kapuskasing, including, without limitation, expectations and assumptions 
respecting the outlook of exploration activity on the Borden and Rollo 
properties and the impact on Kapuskasing's business and management assessment 
of future operations. Although the forward-looking information contained in 
this press release is based upon what Kapuskasing's management believes to be 
reasonable assumptions, the Company cannot assure investors that actual results 
will be consistent with such information. Forward-looking information reflects 
current expectations of management regarding future events and operating 
performance as of the date of this press release.

It is important to note that actual outcomes and the Company's actual results 
could differ materially from those in such forward-looking statements. Risks 
and uncertainties include, but are not limited to, economic, competitive, 
governmental, environmental and technological factors that may affect the 
Company's operations, markets, products and prices. Readers should refer to the 
risk disclosures outlined in the Company's Management Discussion and Analysis 
of its audited financial statements filed with the British Columbia Securities 
Commission.

The forward-looking information contained herein is expressly qualified in its 
entirety by this cautionary statement. Forward-looking information reflects 
management's current beliefs and is based on information currently available to 
the Company. The forward-looking information is made as of the date of this 
press release and Kapuskasing assumes no obligation to update or revise such 
information to reflect new events or circumstances, except as may be required 
by applicable law.

This news release contains information with respect to adjacent or similar 
mineral properties in respect of which the Company has no interest or rights to 
explore or mine. Readers are cautioned that the Company has no interest in or 
right to acquire any interest in any such properties, and that mineral deposits 
on adjacent or similar properties are not indicative of mineral deposits on the 
Company's properties.

- 30 -

CONTACT INFO:

Kapuskasing Gold Corp.
Dean Nawata
President & CEO, Director
1(647) 360-0897
www.kapgold.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=538649726