Source	Marketwire
Date	08/24/2015
Time	05:01:07 AM

Company	 INDEPENDENCE GOLD CORP.
Title	Independence Gold Intercepts 7.23 g/t Gold Across 12.2 m on the Boulevard 
Project, Yukon





    CDNX Symbol: IGO











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Independence Gold Corp.

TSX VENTURE SYMBOL: IGO

August 24, 2015

Independence Gold Intercepts 7.23 g/t Gold Across 12.2 m on the Boulevard 
Project, Yukon


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Aug. 24, 2015) - Independence Gold 
Corp. (TSX VENTURE:IGO) (the "Company") is pleased to announce two new gold 
discoveries on its 100% owned Boulevard Project, located in the White Gold 
District 135 kilometers (km) south of Dawson City, Yukon and contiguous to the 
Coffee Gold Project currently being advanced by Kaminak Gold Corporation. The 
Company completed a total of 1,746 metres (m) (13 holes) of reverse circulation 
(RC) drilling to evaluate previously untested geochemical soil anomalies. The 
best intercepts are 7.23 grams per tonne (g/t) gold across 12.2 m at the new 
Sunrise Zone, and 4.25 g/t gold across 6.10 m at the Denali Zone, located 13 km 
to the northwest of Sunrise. A follow-up program including ground magnetic 
surveying, geological mapping and additional RC drilling has been initiated.

Sunrise Zone

The 2015 RC drill program was designed to test multiple northeast-trending 
multi-element soil geochemical anomalies coincident with magnetic low features. 
These anomalies parallel mineralized trends at Kaminak's Coffee deposit located 
9 km northeast of the Sunrise Zone. Eight RC drill holes totaling 819 m were 
completed, with significant drill results presented below:

/T/

============================================================================
Drill Hole             From (m)         To (m)  Length (m)(i)       Au (g/t)
----------------------------------------------------------------------------
BV15-31                   18.29          19.81           1.52           8.80
----------------------------------------------------------------------------
and                       41.10          70.10          29.00           3.21
----------------------------------------------------------------------------
incl.                     41.10          53.34          12.24           7.23
----------------------------------------------------------------------------
incl.                     41.10          44.20           3.10          26.27
----------------------------------------------------------------------------
BV15-32                    9.14          12.19           3.05           0.38
----------------------------------------------------------------------------
BV15-33                   24.38          25.91           1.53           0.63
----------------------------------------------------------------------------
TG15-01                   44.20          48.77            4.6           0.22
============================================================================

/T/

(i)True thickness estimated to be 60-70% of drill intercepts

The mineralized intercept from 41.10 m to 53.34 m depth in hole BV15-31 assayed 
7.23 g/t gold across 12.2 m, with assay values ranging from 0.025 g/t to 47.70 
g/t gold over 1.52 m sample intervals. The hole ended in mineralization at 
70.10 m depth with mineralization open in all directions. Mineralization is 
hosted within silicified quartzite crosscut by quartz veins containing pyrite 
and pyrrhotite, along an inferred northeast trending fault structure. Hole 
BV15-31 is centrally located within a 550 m long gold- and arsenic-in-soil 
anomaly which will be further tested during the follow-up program.

Denali Zone

The Denali Zone is a 700 m long multi-element soil geochemical anomaly where 
4.56 g/t gold over 10 m was discovered during the 2012 trenching program (see 
the Company's news releases dated September 25 and December 18, 2012). The 
Denali Zone was tested by five RC drill holes, for a total of 927 m, during the 
2015 program. Significant results are presented below:

/T/

============================================================================

Drill Hole             From (m)         To (m)  Length (m)(i)       Au (g/t)
----------------------------------------------------------------------------
YCS15-01                  18.29          21.34           3.05           3.33
----------------------------------------------------------------------------
YCS15-02                  71.63          74.68           3.05           0.50
----------------------------------------------------------------------------
and                      185.93         187.45           1.52           1.30
----------------------------------------------------------------------------
YCS15-03                   9.14          15.24           6.10           4.25
----------------------------------------------------------------------------
incl.                     13.72          15.24           1.52          12.10
============================================================================

/T/

(i)True thickness estimated to be 80-90% of drill intercepts

Figures of the Sunrise Zone and Denali Zone can be viewed on the Company 
website.

Drill holes YCS15-01 and YCS15-03 together define a 130 m long northwest 
trending, northeast dipping zone that confirms surface trench mineralization 
and is open along strike and at depth. The gold mineralization is variably 
hosted within quartzite or quartz biotite schist and, similar to other 
mineralized zones in the White Gold District, is associated with elevated 
arsenic and antimony.

The Company has increased its total 2015 exploration and project evaluation 
budget to $2.0 million (see the Company's news release dated May 20, 2015). The 
diamond drilling previously announced for the Company's Henderson Project has 
been postponed due to the follow-up program on the Boulevard Project.

David Pawliuk, P.Geo., the Company's Qualified Person as defined by National 
Instrument 43-101 for the Boulevard Project, has reviewed the technical 
information in this news release. Quality assurance and quality control 
procedures include systematic insertion of blanks and standards into the sample 
sequence. Samples are placed in sealed bags and shipped directly to SGS Canada 
Inc.'s analytical facility in Burnaby, BC for preparation, aqua regia 
inductively coupled plasma (ICP) element analysis and fire assay analysis.

Independence Gold Corp. (TSX VENTURE:IGO) is a well-financed mineral 
exploration company listed on the TSX Venture Exchange. With multiple projects 
in the Yukon, and the 3Ts Project located in British Columbia, the portfolio 
ranges from early stage grassroots exploration to advanced-stage resource 
expansion. For additional information please visit the Company's website 
www.ingold.ca.

INDEPENDENCE GOLD CORP.

Randy Turner, President & CEO

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Investor Relations
604-687-3959
info@ingold.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=540048854